## Slide 1: Overview of MACCS Status and Development – Sep 2022
Dan Clayton
Sandia National Laboratories
Notes: Hello!
Intro
Thank you
New users: Advertise MACCS Workshop and videos
Questions: Monitors

## Slide 2: Contents
Current versions
MACCS background
MACCS version 4.0
MACCS version 4.1
Planned MACCS version 4.2
Supporting documents
Auxiliary and supporting files
MACCS modernization
Summary
Notes: History - predecessor codes leading up to the MACCS we know today
New Animation tool! Allows users to animate results from MACCS. You can make videos and screenshots, over a map background. Greatly helps to visualize results. and demo during the workshop.
You can still register for the workshop.

## Slide 3: Current Versions
  MACCS/WinMACCS
  Current version is v4.1 (July 2021)
  Version 4.2 planned for release in December 2022
  MACCS-HYSPLIT tools
  Current version is v1.0 (April 2019)
  Version 1.1 planned for release in December 2022
  SecPop
  Current version is v4.3.0 (June 2014)
  Planning to update with new US census data and programming language in 2023
  MelMACCS
  Current version is v2.0.1 (February 2016)
  In the process of rewriting in more modern programming language
  Version 4.0 planned for release in September 2022
  AniMACCS
  Current version is v1.3.1 (January 2022)

## Slide 4: Purpose for MACCS
  Created by Sandia to support NRC research and regulatory applications
  Origins go back to the mid-1970s
  Typically used for prospective analyses, e.g.,
  Probabilistic risk assessments (NUREG-1150 and NRC’s Level 3 PRA)
  Probabilistic consequence assessments (SOARCA)
  Cost/benefit analyses (required for environmental analyses in licensing)
  Very versatile with a large set of user inputs
  Intended to run rapidly for PRA applications
  Large set of weather trials (hundreds or thousands)
  Significant set of source term categories (ten or twenty) plus additional sensitivity studies
Notes: Discuss the background…why was MACCS created.
WASH 1400: Reactor Safety study – which ____
Level 3 PRA – Assess the consequences (both biological and economic) of a potential release of radioactive material into the atmosphere for a whole range of accident scenarios.
More specific probabilistic safety assessments like SOARCA which focused on a select few severe accidents
Help influence design decisions – also can be used following realized accident scenarios to evaluate the addition of extra protections. (filtered vent).
Emphasize the rapidly portion:
How many user inputs (depending on how complicated your run – simple run (100-ish) to 1000s)
Weather trials (about a thousand, max of 8760 hrs/year)
Source terms categories? Normally around 10-20 something for typical PRA

## Slide 5: MACCS Lineage
  Calculation of Reactor Accident Consequences (CRAC) Code (1975)
  Developed for the Reactor Safety Study (WASH-1400)
  CRAC2 (1982)
  Primarily used in 1982 siting study (NUREG/CR-2239)
  MACCS (MELCOR Accident Consequence Code System) (1990)
  Primarily used in NUREG-1150
  MACCS2 (1998)
  Developed to support DOE documented safety analyses of nuclear facilities
  WinMACCS/MACCS (2011)
  Enhance user friendliness
  Reduce likelihood of user errors
  Enable routine examination of uncertainty
Notes: As mentioned on the previous slide.
  CRAC and Reactor Safety Study – first U.S. systematic attempt to search out large spectrum of accidents
  first to use quantitative techniques to estimate the following in an integrated manner:
    probabilities: 1/20,000 core melt per reactor per year
    source terms
    public consequences
    Nine PWR and five BWR release categories defined and frequencies quantified
  Assign probability distribution to key variables
    release magnitude
    weather conditions
    population
1982 Siting Study –
NUREG-1150 – First full PRA? Five assessed plants
Five principle steps of risk analysis:
  Accident (frequency) analysis
  Accident progression, containment loadings, and structural response analysis
  Radioactive material transport (source term) analysis
  Offsite consequence analysis
  Risk Integration - combines and analyzes the first four steps
MACCS2 - Improvements in dose conversion data base, decay chains, emergency response model, and food pathway model
WinMACCS – what we have today
Sampling for uncertainty analyses

## Slide 6: Phenomena Treated by MACCS
Representation of source term
Atmospheric dispersion
  Statistical sampling of archived weather data
  Wet and dry deposition
Exposure pathways to humans
  Inhalation
  Cloudshine
  Groundshine
  Resuspension
  Ingestion
Emergency actions
  Sheltering
  Evacuation
  KI ingestion
  Relocation
Long-term remedial actions
  Decontamination
  Temporary or permanent interdiction of property
  Crop disposal
Economic losses
  Evacuation and relocation per diem costs
  Long-term relocation cost
  Decontamination costs
  Loss of property use
  Depreciation during interdiction
  Property value for permanent interdiction
Notes: Source term – imported as a file from MELCOR or similar application, or input directly into MACCS itself by specifying the release characteristics. Magnitude and timing, to include buoyancy (heat), height, initial timing, release rate by radionuclide by chemical group, particle size distribution by chemical group…items like that to characterize your release.
Models Atmospheric transport and dispersion – weather is a key part of that – options for statistical sampling of your weather data
(120 hour, bin sampling)
Deposition – deposited on the ground, or washed out by interactions with clouds or rain.
Exposure pathways – and ultimately the biological impacts and resulting risks
Broken down into multiple time domains:
Emergency – sheltering, biological impacts and potential shielding effects
Evacuation – speed and timing of evacuation for example. You can also modify this for certain groups of people, or modify speeds (weather)
Potassium Iodine Ingestion –
Relocation
Long Term effects:
Impacts on the land – work associated with decontaminating land, possible interdition, and crop disposal
Economic Losses:
Mentioned biological impacts, but a key part of MACCS is also calculating economic impacts to have a full picture of the risk.

## Slide 7: MACCS Code Modules
  ATMOS
  Calculates transient air and ground concentrations
  Option for Gaussian Plume Segment or Lagrangian Particle models
  EARLY
  Treats emergency phase (up to 40 days, usually one week)
  Models emergency response actions
  Estimates doses from exposure pathways
  Estimates health effects
  CHRONC
  Treats intermediate phase (up to 30 years, usually one year)
  Treats long-term phase (up to 300 years, usually 50 years)
  Estimates long-term doses from exposure pathways
  Estimates health effects
  Estimates economic losses
Notes: Atmos:
Models atmospheric transport and dispersion. MACCS utilizes the Gaussian plume model, however with MACCS 4.0 you now have the option to use HYSPLIT (Lagrangian particle tracking).
Models the movement of your plume, accounts for weather effects, buoyancy, advection downwind, dispersion, turbulence, and deposition of particles from the plume. This ultimately informs the user on air and ground concentrations.
Early:
Also looking at your biological impacts
Time period up to 40 days (usually one week)
Doses from those exposure pathways we just talked about (inhalation, cloudshine, groundshine, resuspension) – resulting health effects. Early (acute) radiation effects.
Chronc:
Much longer time frame
Treats both the intermediate phase and long term phase (up to over 300, usually 50)
NO CLOUDSHINE OR INHALATION!
Long term exposure pathways – health effects – chronic effects like cancer
Economic losses (contamination, interdiction, loss of property value)
Emergency response actions – breaks your population into cohorts and assigns evacuation times
Acute symptoms, like early fatalities and injuries
CHRONC:
Long term effects-
Cancer
Economic effects

## Slide 8: Animation of Plume Segments
Notes: Taken from sample problem?

## Slide 9: Animation of Ground Deposition (Gaussian)
Notes: Sample problem?
Ground Concentration
Cs-137
nCi/m2

## Slide 10: Animation of Ground Deposition (Lagrangian)
Notes: Not a sample problem – but a animation for Fukushima using MACCS coupled with HYSPLIT
Also ground concentration, also Cs-137, map legend and units are different.
I think this is integrated?

## Slide 11: MACCS 4.0 Improvements
  Optional capability to perform high-fidelity atmospheric transport modeling with HYSPLIT (Lagrangian)
  Optional state-of-practice, GDP-based model (RDEIM) to account for economic losses (database currently supports contiguous USA)
  Support for special files needed by animation tool, AniMACCS
  Limits extended on a large set of input parameters
  Convenience enhancements added for cyclical file management
  Qualifiers can be tab-separated in reports to facilitate importing into a spreadsheet
  Input parameters can be exported, including distribution definitions
  Results for each weather trial are used to define quantile results

## Slide 12: MACCS 4.1 Improvements
  Near-field modeling improvements:
  Comparison of several near-field atmospheric transport and dispersion codes including QUIC, ARCON96, and AERMOD concluded MACCS provides a conservatively bounding assessment in the near-field
  MACCS v4.1 enhancements added for plume meander and trapping and downwash to simulate or bound near-field assessments of other codes
  New projective peak dose output option
  Documentation added to help menu in WinMACCS
  Updates to the RDEIM economic model
  Mixing layer information for each time period
  Time synchronization between local time and UTC
  Pop-up window for converting previous version
  Linux version of MACCS 4.1

## Slide 13: New Licensing Process
  MACCS 4.0/4.1 contains new licensing features
  Software is locked to a specific computer
  Licenses are for one-year duration
  Steps to activate license
  Run WinMACCS 4.X.0 Setup.exe (no installation key required)
  Open WinMACCS 4.X.0
            A popup screen briefly describes the licensing process
            Readme file provides more details on licensing process
  Run CreateLicenseRequestFile.exe in folder C:\Users\Public\WinMACCS to create license.request
  Send a copy of license.request to wg-maccs-entity@sandia.gov
  Once approved, Sandia sends MACCS_license.key to user
  License key is linked to WinMACCS
Notes: Product.key?
Order is switched

## Slide 14: Linking License Key
  File Specifications/License File is used to link MACCS_license.key
  WinMACCS provides the number of days left on license
  User should be proactive in updating license key

## Slide 15: Planned MACCS 4.2 Improvements
  Remove node locking from license
  Only time limit for licenses
  Available from download site
  Removes three steps from process
  Up to 999 radionuclides
  Still limited to six member decay chain length
  Need dose coefficient data for radionuclides
  Split indirect costs in economic model
  Dual dose criteria
  Relocation dose projection and timing
  Decontamination in habitable areas
  Skin pathway standardization

## Slide 16: Supporting Documents
  All MACCS related documents can be found at https://maccs.sandia.gov/maccs.aspx
  WinMACCS & MACCS User Guides
  4.1 WinMACCS Enhancements document
  MACCS User’s Guide and Reference Manual Report (consistent with Version 4.0) (SAND 2022-7112)
  MACCS Theory Manual (consistent with Version 3.10)
  Other legacy guides
  Guidance for MACCS input parameters
  MACCS-HYSPLIT Tools documentation
  Benchmark, verification and validation report
  Complete set of published SOARCA reports
Notes: Question – technical bases document not in there?
Describe how to get to these
User Guide – very descriptive
SOARCA reports – good description of a consequence analysis – when starting a new project makes a good reference
Input Parameter Guidance? In Process.

## Slide 17: Auxiliary and Supporting Files
  Dose coefficient (DCF) files for LNT and non-LNT applications
  FGR-13 (based on FGR-13 using standard radiation weighting factors)
  FGR-13 Gray Equivalent (Rev. A) (based on FGR-13 using relative biological effectiveness (RBE) factors consistent with FGR-13 cancer induction modeling and with all SOARCA analyses)
  Updated versions to accompany MACCS 4.2
  COMIDA2 files to go with each type of dose coefficient file
  Created with COMIDA2 2.0.0.3
  Exposure duration (LASTACUM) set to 50 years
  NRC and DOE sample problems
  Tutorials based on NRC sample problems
  Fogbugz used for problem reporting and corrective actions – https://ersdt.fogbugz.com/

## Slide 18: MACCS Modernization
  Working collaboratively with the US NRC to determine the future vision for MACCS
  Effectively tackle the consequence analysis challenges of the future
  Incorporate modern programming languages and techniques
  Be compatible with modern computing platforms
  Increased flexibly and modularity
  Support advanced reactor consequence analysis and future model updates
And we want your feedback!
Please complete survey following IMUG

## Slide 19: Summary
MACCS performs prospective consequence analysis of potential atmospheric releases of nuclear materials
Multiple supporting documents and auxiliary files
MACCS 4.1 was released in July 2021
MelMACCS 4.0 planned for release September 2022
MACCS 4.2 planned for release December 2022
  Removal of node locking
  Increase in number of radionuclides that can be included
  Increased flexibility in projected dose
  Additional output for RDIEM (economic model)
MACCS modernization underway!

## Slide 20: List of Acronyms
ATD Atmospheric Transport and Dispersion
CRAC Calculation of Reactor Accident Consequences
DCF Dose Conversion Factor
DOE Department of Energy
FGR Federal Guidance Report
GDP Gross Domestic Product
HYSPLIT Hybrid Single Particle Lagrangian Integrated Trajectory
LNT Linear No Threshold
MACCS Accident Consequence Modeling Code
NOAA National Oceanographic and Atmospheric Administration
NRC Nuclear Regulatory Commission
PRA Probabilistic Risk Assessment
RBE Relative Biological Effectiveness
RDEIM Regional Disruption Economic Impact Model
SOARCA State-of-the-Art Reactor Consequence Analyses