## Slide 1: Developing a Method to Quantitatively Screen Advanced Reactor Radionuclides Using a Heat Pipe Reactor Inventory
SAND2022-12467 C
Kyle Clavier, PhD, SNL
Dan Clayton, PhD, SNL
Keith Compton, PhD, US NRC
2022 International MACCS User Group (IMUG) Conference
September 19-21, 2022

## Slide 2: Outline
Introduction and Background
Screening Methodology
Important Findings
Conclusions, Limitations and Opportunities for Future Work

## Slide 3: WASH-1400 identifies a subset of radionuclides to be included in a consequence analysis
Section 3.3 and 8.2.1 of Appendix VI
This methodology includes consideration of:
  Radionuclide half-life
  Emitted radiation type and energy
  Inventory
  Release fraction
  Elemental chemistry

## Slide 4: Alpert et al. (1986) updated the list of radionuclides identified in WASH-1400
Estimation of release fractions was subject of considerable uncertainty at the time
Alpert et al. developed a method to consider relative importance of individual elements to reactor accident consequences assuming equal release fractions
Ultimately resulted in a list of 60 radionuclides
SOARCA updated this list even further
  Explicitly includes short lived decay progeny
  71 radionuclides in total identified for LWR consequence analysis
Alpert et al., 1986

## Slide 5: 71 radionuclides were identified as important for LWRs based on inventory, half-life and potential biological hazard of radionuclides expected to be present in a large LWR
Chemical Group | Isotope | T1/2
Noble Gas | Kr-85 | 10.72 yr
 | Kr-85m | 4.48 hr
 | Kr-87 | 76.3 min
 | Kr-88 | 2.84 hr
 | Xe-133 | 5.25 d
 | Xe-135 | 9.09 hr
 | Xe-135m | 15.3 min
Alkali Metals | Rb-86 | 18.7 d
 | Rb-88 | 17.8 min
 | Cs-134 | 2.062 yr
 | Cs-136 | 13.1 d
 | Cs-137 | 30.0 yr
Alkaline Earths | Sr-89 | 50.5 d
 | Sr-90 | 29.1 yr
 | Sr-91 | 9.5 hr
 | Sr-92 | 2.71 hr
 | Ba-137m | 2.55 min
 | Ba-139 | 82.7 min
 | Ba-140 | 12.74 d
Halogens | I-131 | 8.04 d
Halogens | I-132 | 2.30 hr
 | I-133 | 20.8 hr
 | I-134 | 52.6 min
 | I-135 | 6.61 hr
Chemical Group | Isotope | T1/2
Chalcogens | Te-127 | 9.35 hr
 | Te-127m | 109 d
 | Te-129 | 69.6 min
 | Te-129m | 33.6 d
 | Te-131 | 25.0 min
 | Te-131m | 30.0 hr
 | Te-132 | 78.2 hr
Platinoids | Ru-103 | 39.3 d
 | Ru-105 | 4.44 hr
 | Ru-106 | 368.2 d
 | Rh-103m | 56.1 min
 | Rh-105 | 35.4 hr
 | Rh-106 | 29.9 sec
Early Transition Elements | Co-58 | 70.8 d
 | Co-60 | 5.271 yr
 | Nb-95 | 35.1 d
Early Transition Elements | Nb-97 | 72.1 min
 | Nb-97m | 1.0 min
 | Mo-99 | 66.0 hr
 | Tc-99m | 6.02 hr
Tetravalents | Zr-95 | 64.0 d
 | Zr-97 | 16.9 hr
 | Ce-141 | 32.5 d
 | Ce-143 | 33.0 hr
 | Ce-144 | 284.3 d
 | Np-239 | 2.35 d
 | Pu-238 | 87.74 yr
 | Pu-239 | 2.41E4 yr
 | Pu-240 | 6.54E3 yr
 | Pu-241 | 14.4 yr
Chemical Group | Isotope | T1/2
Trivalents | Y-90 | 64.0 d
 | Y-91 | 58.5 d
 | Y-91m | 49.7 min
 | Y-92 | 3.54 hr
 | Y-93 | 10.1 hr
 | La-140 | 40.3 hr
Trivalents | La-141 | 3.9 hr
 | La-142 | 92.5 min
 | Pr-143 | 13.56 d
 | Pr-144 | 17.3 min
 | Pr-144m | 7.2 min
 | Nd-147 | 11.0 d
Trivalents | Am-241 | 432.2 y
 | Cm-242 | 162.8 d
 | Cm-244 | 18.11 yr
Cadmium Group | Sb-127 | 3.85 d
 | Sb-129 | 4.32 hr
Source: State of the Art Reactor Consequence Analysis (SOARCA)

## Slide 6: Advancing reactor technology has motivated an investigation into developing a similar subset of radionuclides relevant to advanced non-LWRs
High-temperature gas reactors (HTGR)
Fluoride-salt-cooled high-temperature reactor (FHR)
Molten-salt reactors (MSR)
Sodium fast reactor (SFR)
Liquid metal fast reactors (LMR)

## Slide 7: The NRC Vision and Strategy Document (Vol. 3) outlines a radionuclide screening effort
Calls for the identification of a subset of radionuclides to be included in MACCS calculations for non-LWRs
Radionuclide selection should be based upon factors such as:
  Core inventory
  Nature of radioactivity
  Specific organ effects
Expand upon previous qualitative efforts to screen advanced reactor radionuclides in Preliminary Radioisotope Screening for Off-site Consequence Assessment of Advaned Non-LWR Systems (Andrews et al., 2021)
  Developed a preliminary, qualitative list of radionuclides for these reactors (57 radionuclides)
  Identified knowledge gaps that still exist regarding reactor chemistry and system behavior

## Slide 8: 57 radionuclides identified in preliminary qualitative screening assessment
Chemical Group | Isotope | T1/2 | Reactor Type
New Proposed Group | H-3 | 12.3 y | HTGR, FHR, MSR, SFR
 | C-14 | 5,730 y | HTGR, FHR
Alkali Metals | Na-22 | 2.6 y | SFR
 | Na-24 | 15 h | SFR
Alkaline Earths | Ra-224 | 3.66 d | MSR
Noble Gas | Ar-41 | 110 m | SFR
 | Kr-83m | 1.83 hr | MSR
 | Xe-131m | 11.9 d | MSR
 | Xe-133m | 2.2 d | MSR
Early Transition Elements | Cr-51 | 27.7 d | SFR
 | Mn-54 | 312.3 d | SFR
 | Fe-59 | 44.5 d | SFR
 | Nb-93m | 16.13 yr | MSR
 | Ta-182 | 114.4 d | SFR
Cadmium Group | As-77 | 38.5 hr | MSR
 | Cd-113m | 14.1 yr | MSR
 | Cd-115m | 44.5 d | MSR
 | Sb-125 | 2.8 y | HTGR, FHR
 | Sb-126 | 12.3 d | MSR
 | Sb-128 | 9.01 hr | MSR
Chalcogens | Se-81 | 18.4 m | MSR
 | Se-81m | 57.3 m | MSR
 | Se-83 | 22.3 m | MSR
 | Te-125m | 57.5 d | MSR
 | Te-133m | 55.4 min | MSR
 | Te-134 | 41.8 min | MSR
Chemical Group | Isotope | T1/2 | Reactor Type
Halogens | Br-83 | 2.4 hr | MSR
 | Br-84 | 31.8 min | MSR
Platinoids | Pd-109 | 13.7 h | MSR
 | Pd-112 | 21.0 hr | MSR
Tin Group | Ag-110m | 250 d | HTGR, FHR
 | Ag-111 | 7.45 d | MSR
 | Sn-117m | 13.7 d | MSR
 | Sn-119m | 293 d | MSR
 | Sn-121m | 43.9 yr | MSR
 | Sn-123 | 129 d | MSR
Trivalents | Pr-146 | 24.2 hr | MSR
 | Pm-147 | 2.6 y | HTGR, FHR, MSR
 | Pm-148m | 41.3 d | MSR
 | Pm-149 | 53.1 hr | MSR
Trivalents | Pm-151 | 28.4 hr | MSR
 | Sm-151 | 88.8 y | HTGR, FHR, MSR
 | Sm-153 | 46.3 hr | MSR
 | Eu-154 | 8.6 y | HTGR, FHR, MSR
 | Eu-155 | 4.8 y | HTGR, FHR, MSR
 | Eu-156 | 15.2 d | MSR
 | Eu-157 | 15.2 hr | MSR
 | Cm-243 | 29 y | MSR, LMR
 | Cm-245 | 8,500 y | HTGR, FHR, MSR, LMR
Trivalents | Cm-246 | 4700 y | MSR, LMR
 | Am-242m | 150 y | MSR, LMR
 | Am-243 | 7400 y | MSR, LMR
Chemical Group | Isotope | T1/2 | Reactor Type
Tetravalents | Th-228 | 1.91 y | MSR
 | Pa-233 | 27.0 d | MSR, MSR, LMR
 | Pu-242 | 373,300 y | HTGR, FHR, MSR, LMR
Uranium Group | U-232 | 68.9 y | MSR
 | U-237 | 6.75 d | MSR, LMR
Source: Andrews et al., 2021. Preliminary Radioisotope Screening for Off-site Consequence Assessment of Advanced Non-LWR Systems, SAND2021-11703

## Slide 9: Advanced reactor research is still underway, but some preliminary information does exist
Information on half-life and potential biological hazard for 825 radionuclides in MACCS is available
Still need reliable information for advanced reactors:
  Inventories
  Transport pathways
  Chemistries
Some preliminary inventories are available
  INL Heat Pipe Reactor Design
  See Walker et al. (2022) SCALE Modeling of the Fast-Spectrum Heat Pipe Reactor
Available inventories allow us to illustrate a method that can be applied to identify a list of radionuclides for any advanced reactor technology, provided that a quantitative inventory is available
  Method analogous to Alpert et al. to estimate relative importance assuming equal release fraction
  Identify “most important” contributors based on relative importance
  Consider doses to multiple organs, scaled to that of I-131 (early phase) and Cs-137 (long-term phase)

## Slide 10: MACCS 4.1 was used to assess the relative importance of advanced reactor radionuclide suite
Step 1: calculate an activity-normalized dose of combined list of 57 preliminary radionuclides and heat pipe reactor suite
  Screen heat pipe reactor by eliminating radionuclides with short half-lives (<1 hour) and low contribution to the total inventory (<0.0001%)
    > 1200 radionuclides reduced to 108
  EARLY and CHRONC doses from a unit 1-Ci release were modeled for each of these radionuclides and normalized to equivalent releases of I-131 and Cs-137, respectively
  In this manner, a relative biological hazard list was developed
Step 2: illustrate using a heat pipe reactor inventory to scale these “hazard rankings” by the inventory (relative to I-131 or Cs-137 as appropriate)
  Identify radionuclides that, if released in sufficient quantities, may be important to early or long-term dose
Step 3: additionally screen this list by eliminating radionuclides with effective and organ doses less than 1% of those of I-131 (early phase) and Cs-137 (late phase doses)

## Slide 11: The MACCS assumptions used for this analysis mirrored those in previous studies
L-ICRP60ED dosimetric quantity used as surrogate for potential latent health effects from both EARLY and CHRONC phase doses. A-RED MARR and A-LUNG used for surrogates of early health effects from early phase doses
Constant, “typical” weather conditions – D stability, 4 m/s windspeed, no rain
Release occurs outside of the growing season
Doses from elements/isotopes include the effect of radioactive decay and in-growth or decay progeny during transport.
Nonbuoyant release from a single plume at 40 m elevation. Uniform 1-hour release immediately after accident initiation
0.002 m/sec dry dep. velocity, radiation protection factors of 0.75, 0.22, and 0.46 for cloudshine, groundshine, and inhalation and skin, respectively
Uniform population distribution of approximate CONUS average
No emergency protective actions, exposure duration of 7 days for EARLY, CHRONC duration of 1 year, no intermediate phase

## Slide 12: Analysis suggests that 69 heat pipe reactor radionuclides may be of importance if released in sufficient quantities
48 of these radionuclides are already considered for LWR analyses
21 new radionuclides listed here
Note: decay progeny not listed here
Isotope | EARLY Relative ICRP60 Effective Dose | EARLY Relative Red Marrow Dose | EARLY Relative Lung Dose | CHRONC Relative ICRP60 Effective Dose | CHRONC Relative Red Marrow Dose | CHRONC Relative Lung Dose
Ag-111 |  |  | 0.04 |  |  | 
Ag-112 |  |  | 0.01 |  |  | 
Cd-115 |  |  | 0.03 |  |  | 
Eu-155 |  |  | 0.017 |  |  | 
Eu-156 |  | 0.031 | 0.063 |  |  | 
Nb-95m |  |  | 0.06 |  |  | 
Nd-149 |  | 0.014 | 0.22 |  |  | 
Pd-109 |  |  | 0.09 |  |  | 
Pm-147 | 0.34 |  | 1.57 |  |  | 0.03
Pm-148m |  |  | 0.015 |  |  | 
Pm-149 | 0.035 |  | 0.97 |  |  | 
Pm-151 | 0.012 | 0.043 | 0.396 |  |  | 
Pr-145 | 0.03 |  | 1.58 |  |  | 
Sb-125 |  | 0.02 | 0.017 | 0.04 | 0.04 | 0.04
Sm-153 |  |  | 0.173 |  |  | 
Sn-121 |  |  | 0.011 |  |  | 
Sn-125 |  |  | 0.0301 |  |  | 
Sn-127 |  |  | 0.028 |  |  | 
Te-125m |  |  | 0.0107 |  |  | 
U-234 | 0.40 |  | 0.663 |  |  | 0.03
U-237 | 0.035 | 0.041 | 0.663 |  |  | 

## Slide 13: Summary and Limitations
A method for the identification of radionuclides of potential for advanced reactors – based on half-life, biological hazard, and relative abundance in a core – is provided and illustrated using a radiological inventory developed for a heat pipe reactor
  Provide a traceable and transparent basis for selecting radionuclides for inclusion in advanced reactor consequence analysis
Radionuclides were progressively screened, first based on half-life and relative inventory, and then further based upon relative biological hazard to develop a list of 21 new radionuclides to consider for the heat pipe reactor
In theory, this method can be applied to any advanced reactor inventory as they become available
Some radionuclides did not have dose coefficients in MACCS
Complexities of H-3 and C-14 are generally unaccounted for in MACCS
Food ingestion ignored
Normalizing to doses of volatile isotopes of iodine and cesium means that large releases not associated with high elemental volatility may need to be reassessed
Other thresholds for half-life, relative abundance, or relative biological hazard may be used

## Slide 14: Thank you!
Kyle Clavier, PhD, Sandia National Laboratories
kaclavi@sandia.gov
Dan Clayton, PhD, Sandia National Laboratories
djclayt@sandia.gov
Keith Compton, US Nuclear Regulatory Commission
Keith.Compton@nrc.gov
Authors would like to acknowledge the members of the larger MACCS team at SNL: Mariah Smith, Jennifer Leute, Joshua Dise, and John Fulton. Authors would like to additionally acknowledge the following NRC staff for their technical and programmatic contributions to this effort: Salman Haq, AJ Nosek and Nazila Tehrani.

## Slide 15: References
United States Nuclear Regulatory Commission (US NRC) 2019. NRC Non-Light Water Reactor (Non-LWR) Vision and Strategy: Volume 3: Computer Code Development Plans for Severe Accident Progression, Source Term, and Consequence Analysis.
WASH-1400 Reactor Safety Study: An Assessment of Accident Risks in U.S. Commercial Nuclear Power Plants. NUREG-75/014.
Alpert, D.J., Chanin, D.I., Ritchie, L.T. 1986. Relative Importance of Individual Elements to Reactor Accident Consequences Assuming Equal Release Fractions. NUREG/CR-4467, SAND85-2575.
Chang, R., Schaperow, J., Ghosh, T., Barr, J., Tinkler, C., Stutzke, M. November 2012. State-of-the-Art Reactor Consequence Analysis (SOARCA) Report. NUREG-1935
Andrews, N.C., Higgins, M., Taconi, A., Leute, J. 2021. Preliminary Radioisotope Screening for Off-site Consequence Assessment of Advanced Non-LWR Systems, SAND2021-11703
2022 SCALE Non-LWR Models for NRC Volume 3. https://code.ornl.gov/scale/analysis/non-lwr-models-vol3
Walker, E., Skutnik, S., Wieselquist, W., Shaw, A., Bostelmann, F., 2022. SCALE Modeling of the Fast-Spectrum Heat Pipe Reactor. ORNL/TM-2021/2021
Nosek, A.J., Bixler, N. 2021. MACCS Theory Manual. SAND2021-11535
Naegeli, R.E. 2003. A MACCS2 Single Nuclide Downwind Dose Database for Sandia National Laboratories, Technical Area V. SAND2003-0883
Leute, J., Walton, F., Mitchell, R., Eubanks, L. 2021. MACCS (MELCOR Accident Consequence Code System) User Guide – Version 4.0. SAND2021-8998