## Slide 1: Qualitatively Reviewing MACCS Capabilities for Assessing Variable Radionuclide Physical/Chemical Forms and Tritium
SAND2022-12468 C
Kyle Clavier, PhD, SNL
Dan Clayton, PhD, SNL
Keith Compton, PhD, US NRC
2022 International MACCS User Group (IMUG) Conference
September 19-21, 2022

## Slide 2: Outline
Introduction to radionuclide chemical/physical forms
The MACCS dosimetry and deposition models
Dose coefficient development and MACCS dosimetry lineage
Clearance class and f1 development
Deposition model state of practice
Opportunities for additional research
Tritium overview
Tritium transformation processes
Existing tritium models
Recommendations for potential MACCS upgrades

## Slide 3: In a nuclear accident scenario, it is possible that there are multiple chemical and physical forms of a given radionuclide released
NRC non-LWR Vision and Strategy calls for an investigation into how MACCS handles radionuclide size, shape and chemical form in atmospheric and dosimetry calculations
  Inform potential improvements to MACCS capabilities for atmospheric transport and dosimetry
MACCS has robust, flexible modeling capabilities that are generally well-suited to accommodate diverse forms of a given isotope
  Understanding existing capabilities will help to inform improvements
It is pertinent to investigate MACCS variables relevant to chemical and physical form modeling and how MACCS functionality facilitates the analysis of accident consequences from varying forms of a given isotope
  Look into dosimetry and transport assumptions relative to state of practice
  Technology neutral fashion

## Slide 4: The MACCS dosimetry model
EARLY: cloudshine, groundshine, direct/resuspension inhalation and skin deposition
  Difference dose coefficients for each pathway read from the DC file supplied with MACCS
  Generally, dose is a product of exposure and dose coefficient
CHRONC: MACCS additionally considers food and water ingestion (in addition to groundshine and resuspension inhalation doses)
  Indirect late-phase doses from ingestion may occur in different spatial elements than where the deposition processes occurred
  Food ingestion doses will depend on farmable land area and ground concentration
  Water ingestion will depend on direct deposition and washoff to freshwater bodies (simple secondary transport equation)
MACCS currently does not allow for multiple chemical forms for the same isotope
  Each isotope of a given element is attributed the same dose coefficient (for a given organ/pathway)

## Slide 5: The MACCS deposition model
MACCS allows user to assign radionuclides to various high-level chemical groups based on physical and chemical properties that are assumed to be identical
  Typically defined to be consistent with accident progression codes like MELCOR
Assuming every isotope in a group behaves the same ignores the unique physical/chemical properties of radioactive molecules
  Particle size
  Transformation in the environment
  Hygroscopicity
  Agglomeration
  Density
Aerosol size distribution is used to assign a dry deposition velocity
  Dry deposition a function of ground level air concentration and dry deposition velocity
  Particle size distribution are binned and each assigned dry deposition velocity
Wet deposition functions independently of particle size

## Slide 6: Other summary observations regarding the MACCS conceptual models
The dose calculation for a given radioisotope in MACCS assumes chemical form does not change following release to the atmosphere
No secondary environmental transport is assumed after deposition
Risk coefficient uncertainty can vary considerably across applications
  E.g., inhalation risk may depend strongly on availability of information on the chemical/physical form inhaled
FGR 13: “the biokinetic, dosimetric, and radiation risk models generally have been derived from much less detailed and sometimes inconsistent databases (with) substantial uncertainties”
Default absorption types are recommended, but information regarding this selection is often limited and, in many cases, reflects occupational rather than environmental experience
An analyst should consider the timescale in which chemical transformations are expected to happen
  Environmental transformation processes happen slowly
  E.g., is a given radionuclide expected to oxidize before substantially decaying?

## Slide 7: Conceptual accounting for alternate physical/chemical forms in dose coefficient development
EPA regularly publishes federal guidance reports to assist with radiation protection programs
  FGR13 provides technical accounting for risk coefficients, dependent on age, gender, metabolism, dosimetry, radiogenic risk, and competing causes of death
  A supplement to FGR provides the basis for dose coefficients in MACCS
  Effective dose coefficients based on ICRP60 recommendations for tissue weighting
Absorption type/clearance class in MACCS consistent with Runkle and Ostmeyer (1985), a study discussing dosimetric data for accidental radionuclide release from nuclear reactors
  Runkle and Ostmeyer (1985): “the most probable chemical forms of the inhaled radionuclides are used to assign clearance classes…except for Cs and I isotopes, most of the important inhaled radionuclides will be in the form of insoluble compounds (principally oxides and hydroxides)”

## Slide 8: More on the MACCS dosimetry lineage
FGR 12 and ICRP 72 informed external and internal dose coefficients, respectively, included in FGR 13
  External considered radionuclides with a half-life of at least 10 minutes or occurring in the decay chain of a radionuclide that does
  Internal excluded radionuclides with half-life less than 10 minutes and isotopes of noble gases
  No practical differences between ICRP72 dose coefficients and those used to developed FGR 13 for isotopes of interest for consequences analysis

## Slide 9: Clearance class and f1 development dates back to the 1950s
ICRP 2 (1959) – provided a foundational, single compartment model for the lung to predict deposition, retention and clearance of inhaled aerosols
ICRP 30 (1979) – supersedes ICRP 2, improved estimations of deposition in and clearance from the respiratory tract
  3 anatomical compartments were used: nasopharyngeal, tracheobronchial and pulmonary
  Introduced the “D, W, Y” shorthand
ICRP 66 (1994) – further revises ICRP 30 model and includes morphometry, respiratory physiology, radiation biology, deposition, clearance, and dosimetry
  Changed the “D,W,Y” clearance class convention to “F,M,S”
  Broad nature of clearance class timelines means the risk associated with some radionuclides may be over/underestimated (actual clearance times are on lower/upper end of clearance time bin)

## Slide 10: Other relevant, newer documentation exists for dosimetry but are often associated with occupational intakes
ICRP 68 supersedes ICRP 61 and provides dose coefficients for occupational intake of radionuclides
  Used the lung model from ICRP 66
  Tabulates effective dose coefficients for inhalation for varying isotopes, clearance classes, and particle sizes
  Provides recommendations for clearance types and f1 values for various chemical compounds
Beginning in 2015, Occupational Intakes of Radionuclides (OIR) reports published by ICRP to replace the ICRP 30 series, ICRP 54, 68, and 78
  Contains more up-to-date and detailed information than ICRP 68
  Detailed information on chemical forms commonly encountered in an occupational setting and associated clearance class and f1 values
  An update to FGR 13 may logically include a reference to the OIR series

## Slide 11: Other deposition models exist, but MACCS is consistent with state-of-practice specifically for modeling variable chemical/physical forms
EPA AERMOD model includes algorithms for both dry and wet deposition for particulates and gaseous emissions and relies on the resistance model
  Particulate deposition calculation method based on particle size
  Wet deposition depends on washout coefficient and precipitation rates
NOAA HYSPLIT uses either a user specified velocity or calculated using a known particle diameter, air density and particle density
  Users can optionally select the resistance model
  Wet deposition model assumes a scavenging ratio to account for rainout and washout (removal constant)
Generally, the impact of chemical form on wet and dry deposition is not currently account for in any state-of-practice model for particulate deposition, including MACCS

## Slide 12: Additional work may be warranted to produce data necessary to inform model improvements
Identify whether non-LWR accident releases contain chemical forms other than insoluble oxide or hydroxide forms, and what those forms are
Conduct a sensitivity analysis for dose coefficients for variable chemical forms
Expand the dose coefficient file and allow the user to define which chemical form should be used
Enhance MACCS to allow a user to specify release fractions for different chemical forms of the same isotope
Review non-LWR accident progression analyses to determine whether significant gaseous releases are likely
Benchmark the MACCS dry and wet deposition models against alternate state of practice models

## Slide 13: Tritium has highly unique chemical behavior in the environment and may become important for advanced reactor consequence analyses
If released in large enough quantities, it may be warranted to update MACCS capabilities to model tritium fate and transport more effectively in an accident scenario
Updates may be informed by existing modeling capabilities from other tritium models
MACCS has been used in previous studies to model tritium releases

## Slide 14: Tritium behaves similarly to hydrogen in the environment and biological processes
Weak beta emitter – primary radiological hazard is through ingestion of tritiated organic molecules
Chemical form can heavily influence radiological risk posed by tritium
  Inhaling gaseous tritium poses relatively limited radiological risk (low absorption, significant exhale). Dermal contact also limited
  Ingestion and dermal contact with HTO poses a comparatively larger risk (high biological uptake)
  Meaningful concentrations of HTO can also be absorbed through the skin at a rate approximately half that of inhalation
  Can also bind to carbon through photosynthetic processes and create OBT
Tritium Form | Dose Coefficient (Sv/Bq)
Organically Bound Tritium (Ingestion) | 4.2 E-11
Tritiated Water (Ingestion) | 1.8 E-11
Tritium Gas (Inhalation, Moderate Absorption) | 1.8E-15
Organically Bound Tritium (Inhalation) | 4.1E-11
Tritiated Water (Inhalation) | 1.8E-11

## Slide 15: Complex environmental processes govern tritium transformation processes
Gaseous tritium oxidation in the atmosphere (slow process)
  Photochemical oxidation in the air
  Isotopic exchange
  Depends on gas mixture and tritium concentration
Oxidation via soil microbes
  Air to soil transfer governed by diffusion, depends on soil humidity and/or concentration gradients
  Oxidation depends on soil type, moisture and temperature
Transformation in plants
  Tritium expected to naturally take part in the water cycle and thus subject to a great number of changing environmental conditions at any time and physiological processes of vegetation
  Air to plant transfer depends on leaf exchange between vapor and free water in leaf organs
  Timing of release (day vs. night) may strongly influence the transfer of tritium through plants
  Eventually incorporated into plant organic matter (OBT)
Transfer to animals
  Animals ingest grass or other plants containing exchangeable OBT
  Consider relocating animals to uncontaminated grass
  Milk and meat likely not a major exposure pathway (fast biological turnover of HTO and OBT)

## Slide 16: Existing tritium models
UFOTRI – the most comprehensive model regarding tritium releases, dispersion, deposition and the subsequent movement and transformation through the environment
  Similar Gaussian dispersion model to MACCS
  Differentiates between different forms of tritium in the environment, has a detailed reemission physics model, accounts for the conversion of tritium to HTO, uptake by plants, and conversion into OBT
GENII – well documented dose and risk assessment model developed by EPA
  Utilizes special tritium models for acute and chronic exposures
  Chronic module depends on hydrogen content of plant/animal being contaminated
  Also accounts for OBT generation
RSAC – Radiological Safety Analysis Computer program
  Uses different equations for calculating ingestion doses from tritium
  Assumed ratios of plant water and tritium concentration in plant water vs atmospheric water
Other less documented/research models

## Slide 17: Multiple pathways may exist for updates to MACCS to accommodate acute tritium releases
The atmospheric transport processes are largely similar, but MACCS may benefit from updates to longer-term environmental process models
Multiple pathways for updates:
  Simply continue to use the most conservative dose coefficient for HTO in the existing MACCS code with no changes to the atmospheric transport or longer-term processes. Reduces the need to have an exact accounting of the chemical form of tritium releases
  Develop the capabilities for MACCS to identify multiple different chemical forms of tritium and associated transformation. Variable tiers of complexity for which this might be accomplished (e.g., incorporating a simple transfer rate model)
  Introduce tritium accounting capabilities similar to those in UFOTRI and the more complex capabilities of other models. This would require substantial effort but would provide more detailed estimations of tritium in an accident scenario
Consider examining advanced reactor inventories first to determine if model updates are worthwhile (i.e., is tritium even an issue?)

## Slide 18: Thank you!
Kyle Clavier, PhD, Sandia National Laboratories
kaclavi@sandia.gov
Dan Clayton, PhD, Sandia National Laboratories
djclayt@sandia.gov
Keith Compton, US Nuclear Regulatory Commission
Keith.Compton@nrc.gov
Authors would like to acknowledge the members of the larger MACCS team at SNL: Mariah Smith, Jennifer Leute, Joshua Dise, and John Fulton. Authors would like to additionally acknowledge the following NRC staff for their technical and programmatic contributions to this effort: Salman Haq, AJ Nosek and Nazila Tehrani.

## Slide 19: References
U.S Nuclear Regulatory Commission (NRC), 2020. NRC Non-Light Water Reactor (Non-LWR) Vision and Strategy, Volume 3- Computer Code Development Plans for Severe Accident Progression, Source Term, and Consequence Analysis, Revision 1.
Nosek, A.J., Bixler, N, 2021. MACCS Theory Manual. SAND2021-11535
Eckerman, K.F., Leggett, R.W., Nelson, C.B., Puskin, J.S., Richardson, A.C.B., 1999. Federal Guidance Report No. 13, Cancer Risk Coefficients for Environmental Exposure to Radionuclides. EPA 402-R-99-001
Haaker, R.F., Bixler, N.E., 2019. FGR 13 Dose Conversion Factor Files. SAND2019-13422R.
Runkle, G.E., Ostmeyer, R.M., 1985. An Assessment of Dosimetry Data for Accidental Radionuclide Releases from Nuclear Reactors. NUREG/CR-4185, SAND85-0283
International Commission on Radiological Protection (ICRP), 1991. ICRP Publication 60, 1990 Recommendations of the International Comission on Radiological Protection. Vol. 21, 1-3. ISSN 0146-6453.
Eckerman, K.F., Ryman, J.C., 1993. Federal Guidance Report No. 12, External Exposure to Radionuclides in Air, Water and Soil. EPA-402-R-93-081.
International Commission on Radiological Protection (ICRP), 1996. ICRP Publication 72, Age-dependent Doses to Members of the Public from Intake of Radionuclides: Part 5 Compilation of Ingestion and Inhalation Dose Coefficients. Vol. 26, 1. ISSN 0146-6453
International Commission on Radiological Protection (ICRP), 1995. ICRP Publication 71, Age-dependent Doses to Members of the Public from Intake of Radionuclides: Part 4 Inahlation Dose Coefficients. Vol. 25, 3-4. ISSN 0146-6453.
International Commission on Radiological Protection (ICRP), 1994. ICRP Publication 66, Human Respiratory Tract Model for Radiological Protection. Vol. 24, 1-3. ISSN 0146-6453.
International Commission on Radiological Protection (ICRP), 1959. ICRP Publication 2, Permissible Dose for Internal Radiation. Pergamon Press.
International Commission on Radiological Protection (ICRP), 1979. ICRP Publication 30, Limits for Intakes of Radionuclides by Workers. Vol. 2, 3-4. Pergamon Press.
International Commission on Radiological Protection (ICRP), 1994. ICRP Publication 68, Dose Coefficients for Intakes of Radionuclides by Workers. Vol 24, 4. ISSN 0146-6453. Pergamon Press

## Slide 20: References (cont.)
International Commission on Radiological Protection (ICRP), 2022. ICRP Publication 151, Occupational Intakes of Radionuclides: Part 5. Vol 51, 1-2.
International Commission on Radiological Protection (ICRP), 2019. ICRP Publication 141, Occupational Intakes of Radionuclides: Part 4. Vol 48, 2-3.
International Commission on Radiological Protection (ICRP), 2017. ICRP Publication 137, Occupational Intakes of Radionuclides: Part 3. Vol 46, 3-4.
International Commission on Radiological Protection (ICRP), 2016. ICRP Publication 134, Occupational Intakes of Radionuclides: Part 2. Vol 45, 3-4.
International Commission on Radiological Protection (ICRP), 2015. ICRP Publication 130, Occupational Intakes of Radionuclides: Part 1. Vol 44, 2.
United States Environmental Protection Agency (EPA), 2021. User’s Guide for the AMS/EPA Regulatory Model (AERMOD). EPA-454/B-21-001.
Wesely, M.L., Doskey, P.V., Shannon, J.D., 2002. Deposition Parameterizations for the Industrial Source Complex (ISC3) Model. ANL/ER/TR-01/003.
United States Environmental Protection Agency (EPA), 2004. AERMOD Deposition Algorithms – Science Document (Revised Draft). Published online at https://www.epa.gov/scram/air-quality-dispersion-modeling-preferred-and-recommended-models
Stein, A.F., Draxler, R.R., Rolph, G.D., Stunder, B.J.B., Cohen, M.D., Ngan, F. 2015. NOAA’s HYSPLIT Atmospheric Transport and Dispersion Modeling System. Bulletin of the American Meteorological Society. 96 (12), 2059-2077
Draxler, R.R., Hess, G.D. 1998. An Overview of the HYSPLIT_4 Modelling System for Trajectories, Dispersion, and Deposition. Australian Meteorological Magazine. 47, 295-308.

## Slide 21: References
International Atomic Energy Agency (IAEA), 2014. IAEA-TECDOC-1738, Transfer of tritium in the environment after accidental releases from nuclear facilities: report of working group 7. Environmental Modelling for Radiation Safety (EMRAS II) Programme. Vienna, Austria.
Murphy Jr., C.E., Wortham, G.R., 1995. An atmospheric tritium release database for model comparisons (U). WSRC-TR-91-671, Rev 2 (Revision Date: September 15, 1997).
International Commission on Radiological Protection (ICRP), 2012. ICRP Publication 119, Compendium of Dose Coefficients Based on ICRP Publication 60. Volume 41, Supplement 1, Annals of the ICRP, ISSN 0146-6453, ISBN 978-1-4557-5430-4.
United States Department of Energy, March 1999. Final environmental impact statement for the production of tritium in a commercial light water reactor. DOE/EIS-0288.
Napier, B.A., Peloquin, R.A., Strenge, D.L., Ramsdell, J.V., 1988. GENII- The Hanford Environmental Radiation Dosimetry Software System. PNL-6584 Vol. 1 UC-600.
U.S. Nuclear Regulatory Commission (NRC), 2019. Tritium, Radiation Protection Limits, and Drinking Water Standards.
Barry, P.J., Watkins, B.M., Belot, Y., Davis, P.A., Edlund, O., Galeriu, D., Raskob, W., Russell, S., Togawa, O., 1999. Intercomparison of model predictions of tritium concentrations in soil and foods following acute airborne HTO exposure. Journal of Environmental Radioactivity, 42, 191-207.

## Slide 22: References (cont.)
Raskob, W., Hasemann, I., 1991. User guide for UFOTRI: A Program for Assessing the Off-Site Consequences from Accidental Tritium Releases. KfK 4853
Raskob, W., 1990. UFOTRI: Program for Assessing the Off-Site Consequences from Accidental Tritium Releases. KfK 4605
Garland, J.A., Cox, L.C., 1980. The absorption of tritium gas by English soils, plants and the sea. Water, Air, and Soil Pollution. 14, 103-114.
Raskob, W., 1994. Description of NORMTRI: a computer program for assessing the off-site consequences from air-borne releases of tritium during normal operation of nuclear facilities. KfK 5364.
Napier, B.A.., Strenge, D.L., Ramsdell Jr., J.V., Eslinger, P.W., Fosmire, C., 2009. GENII Version 2 software design document. PNNL-14584 Rev. 3.
Schrader, B.J., 2010. Radiological Safety Analysis Computer (RSAC) Program Version 7.2 Users Manual. INL/EXT-09-15275.
Ogram, G.L., 1991. Improved ETMOD modules for HTO exchange, HT deposition, and vegetation HTO. Canadian Fusion Fuels Technology Project, CFFTP G-9188, OHRD No. 91-191-K
BIOMOVS II Technical Report No.8 Tritium in the Food Chain Intercomparison of Model Predictions of Contamination in Soil, Crops, Milk and Beef after a Short Exposure to Tritiated Water Vapour in Air.
International Atomic Energy Agency, 2022. Modelling and Data for Radiological Impact Assessments (MODARIA) Programme, Report of Working Group 7. Harmonization and intercomparison of models for accidental tritium releases to the atmosphere. IAEA-TECDOC-1991