## Slide 1: HYSPLIT-based Emissions Inverse Modeling System for nuclear power plants: Applications to South Korea and East Asian domain
Hyun Cheol Kim 1,2, Tianfeng Chai 1,2, Fantine Ngan 1,2, Mark Cohen 1, Juyeop Kim 3, and Chunsil Jin 4
1 Air Resources Laboratory, National Oceanic and Atmospheric Administration
2 Cooperative Institute for Climate and Satellites, University of Maryland
3 FNC Technology, Co., Ltd, South Korea
3 Korea Institute of Nuclear Safety, South Korea

## Slide 2: Outline
HYSPLIT
Emission Inverse modeling
  HYSPLIT-based Emissions Inverse Modeling System (HEIMS)
Dispersion simulation & source term estimation
  Korean Nuclear Power Plants
  ADAMO, ESTES & HEIMS-n
  Validation
    Twin experiments / Pseudo observations
    Fukushima NPP application
  Sensitivity tests
Conclusion

## Slide 3
HYSPLIT Model
Continuous development at NOAA Air Resources Laboratory (ARL) for more than 40 years
ARL HYSPLIT modeling group (~10 scientists)
Trajectories and Dispersion
Forward and Backward
3-D Dispersion (generally > ~1 km):
  Puffs (top-hat or Gaussian)
  “Particles” (i.e., computational points)
  Eulerian grid
Dry and Wet deposition
Chemical and Radiological Transformations
Simulation Modes:
  Run online (READY)
  Download – run via Graphical User Interface
  Download – run via command line and scripts
  Windows, Mac, Linux
Users:
  Emergency response & science at NOAA
  Emergency response & science - other agencies (e.g., MACCS)
  Scientific community: e.g., Stein et al. 2015 ~ 3000 citations
3
z
+ y
- y
x
Dispersion via 3-D puffs that grow and split horizontally and vertically as they are transported downwind
Dispersion via assembly of 3-D computational particles that undergoing turbulent transport
Notes: I’m going to be providing a very brief overview of the HYSPLIT model and some of its new features and applications, but am not going to be going into any detail about exactly how it is currently used in MACCS
Collaborative exchanges between ARL and applications – e.g., MACCS – is a very important way that the HYSPLIT model is evaluated and improved.
===========================================
3D particle-based dispersion:
To simulate a plume from a source, we release many particles at a time, and this cloud of particles is transported downwind
Each computational point particle gets additional motion based on the amount of turbulence in the atmosphere.
Here we are showing just a few particles released at one time. In a real HYSPLIT run, you would release 100’s or 1000’s or even more particles at any given time.
If the pollutant release was ongoing, you would keep releasing particles from the source as long as you wanted to simulate the emissions.
As the wind changes speed and direction, and as the turbulence in the atmosphere changes, the plume will be dispersed in different directions and will be dispersed to different extents.

## Slide 4: Emission inverse modeling
Estimation of emissions using observation(s)
Unknowns: Strength, location, time, vertical allocation
Inverse modeling with Forward dispersion simulation
  Single source single receptor
  Multi source multi receptor
  Transfer Coefficient Matrix
  Cost function minimization
Uncertainties: meteorology, physical configuration & observations
Validation
  Twin experiment / Perfect model experiment
  Fukushima NPP incident

## Slide 5: TCM and Cost function
Transfer Coefficient Matrix (TCM)
c: nuclide concentration
q: emission rate
D: decay
TCM: dispersion coefficient
Cost function configuration (Chai et al. 2015)
c: nuclide concentration
q: Emission rate
ε, σ: Error variances
h: model, o: observation, b: background
N: site number M: sampling number
Emissions inverse modeling is to find emissions (q) that minimizes the defined cost function
Initial guess
Background
concentration
Temporal
smoothness
Hi,j

## Slide 6: HYSPPLIT-based Emissions Inverse Modeling System (HEIMS)
Fire emissions (HEIMS-f): Smoke forecasts have been challenged by high uncertainty in fire emission estimates. The HEIMS-f is designed to assimilate wildfire emissions based on the GOES Aerosol/Smoke Product (GASP) and HYSPLIT dispersion simulations
Volcanic emissions (HEIMS-v) : The effects of eruption of large volcanoes to regional environment include short-term damages, such as the flow of crushed stone to adjacent areas, long-range damages, such as aviation difficulty by deteriorated visibility and volcanic ash deposition, and long-term effect such as climate changes in a global scale. The HEIMS-v has been developed to estimate volcanic emissions based on aerosol (e.g. MODIS AODs) and/or gaseous properties (e.g. TROPOMI SO2). A case study has been conducted using the Nishinoshima (Japan) volcano eruptions that happened in August 2020

## Slide 7: Inverse modeling for Fukushima NPP incident
Source term estimation using air concentration measurements and a Lagrangian dispersion model–Experiments with pseudo and real cesium-137, T Chai, R Draxler, A Stein – Atmos. Environ., 2015

## Slide 8: Korean Nuclear Power Plants

## Slide 9: Flow patterns near Korean NPPs

## Slide 10: Integrated Environmental Radiation Monitoring Network (IERNet)
High Pressurized Ion Chamber (HPIC) – managed by KINS (296 sites, dose only)
NaI(Tl) Sodium iodide scintillation detector – managed by Korea Hydro & Nuclear Power (KHNP) Co., Ltd (91 sites, nuclide concentration)
387 sites

## Slide 11: ADAMO & ESTES
(T. Kim et al., 2019)
Domestic/Global
UM, GFS, CMC
FLEXPART, HYSPLIT
Accident Dose Assessment and Monitoring (ADAMO)
Environmental monitoring based Source Term Estimation System (ESTES)
Incident Detection
IERNet
Monitoring
HYSPLIT
Initiate Scenario-based
unit-emission Simulation
Emission estimation
Dispersion
Simulation
w/ Emission
Comparison
Rapid response
Impact Assessment
Conc. to dose
conversion
Power Plant
Source term estimation (Direct)
Inventory
PSA
RASCAL
Scenario
Nuclide profiles
& release time
NFEM
HPIC
NaI(Tl)
Domestic/Global
UM, GFS, CMC
HYSPLIT only

## Slide 12: PSEUDO observations

## Slide 13: Case study (1) (July 15, 2019)
Hanbit NPP
6 hour release
5 min PSEUDO observations

## Slide 14: Case study (2): Kori NPP (May 2022)
Cs-137 5E13 Bq/h
(6 hour)
Cs-137 5E13 Bq/h
(15 hour)
Actual
Estimated

## Slide 15: Case study: Kori NPP (May 2022)

## Slide 16
Cs-137 5E13 Bq/h
(6 hour)
Cs-137 5E13 Bq/h
(15 hour)
How to resolve these issues
Remove low quality observations
Constrain release time
Add foreign monitors

## Slide 17: Application to Fukushima NPP incident
WRF simulations for Fukushima
Model configuration
WRF version: v3.8.1
Grid spacing: D01 (36-km), D02 (12-km) and D03 (4-km)
LCC projection with projection center at 35N/135 E
Standard latitude at 35N/35N
Vertical layer: 34 layers
Period: March 10th - 31st, 2011
IC/BC: GFS 6-hourly
Nudging: analysis nudging
Nesting: one-way nesting
Surface – http://rda.ucar.edu/data/ds461.0
Upper level – http://rda.ucar.edu/data/ds351.0
Initialization: daily at 06 UTC, 36-hr run and 12-hr spin-up
extracting output 18UTC (3am local time) – next day 17 UTC
Physical options
microphysics: WSM 6-class graupel scheme
radiation scheme: RRTM scheme for longwave radiation (radt=30)
Dudhia scheme for shortwave radiation
cumulus scheme: Grell-Freitas ensemble scheme (cudt=5)
surface scheme: Revised MM5 Monin-Obukhov scheme
land surface model: Unified NOAH LSM
PBL scheme: YSU scheme
time step: 120 sec, 90 sec and 15 sec

## Slide 18: Fukushima observations from SPM monitors

## Slide 19: Unit emission simulation & TCM construction

## Slide 20: Estimated FNPP emissions

## Slide 21: Sensitivity test (1): temporal resolution
FNPP sensitivity tests
Unit emission temporal resolution

## Slide 22: Sensitivity test (2): meteorology
WRF (27km)
WRF (9km)
WRF (3km)
GDAS (1degree)
FNPP sensitivity tests: Meteorology

## Slide 23: Sensitivity test (3): release height
FNPP sensitivity tests: release heights
Release = 10m
Release = 100m

## Slide 24
Comparison between the observed Cs-137 concentrations from SPM monitors during the Fukushima NPP incident and the reconstruction of Cs-137 concentrations from HIEMS-n system.

## Slide 25: Chinese and Japanese NPPs
Chinese nuclear power plants
Japanese nuclear power plants

## Slide 26: Ukraine NPPs

## Slide 27: Improved efficiency: TCM reconstruction method
Unit emission runs (120h run, 3-hourly)
Time
Time+3h
Time+6h
Time+111h
Time+114h
Time+117h
Summation of 40 files
Emis 0
Emis 1
Emis 2
Emis 37
Emis 38
Emis 39

## Slide 28: Operational ESTES
ERMS collection & processing
NFEM data processing
Routine TCM simulation (3 hourly TCM w/ 15 CNPP): ~ 30 min
Inverse model & TCM reconstruction can be conducted: < 1 min

## Slide 29: Conclusion and future direction
ESTES system is designed to estimate emissions from domestic or foreign nuclear power plant incident
TCM and cost function minimization method are adopted in the system.
Quality control of observations will be critical to the robustness of the system.
For rapid response, a TCM-based reconstruction method can provide very efficient dispersion modeling output for varying emissions scenarios.