## Slide 1: A Decision Support Tool for Radiological/Nuclear Mitigation and Recovery
Michael D. Kaminski, Scott Parent, Douglas E. Johnson
Strategic Security Sciences, Argonne National Laboratory
Matthew Magnuson
*Center for Environmental Solutions and Emergency Response, Office of Research and Development, U.S. Environmental Protection Agency.

## Slide 2: When in incident timeline can the tool be used?
After immediate lifesaving phase is complete, expect the following activities in the impacted area:
People, vehicles, and objects have moved and are moving in and out of the contaminated areas
Urgent mitigation or remediation is needed for critical infrastructure
Response/recovery missions are underway
Remediation is being planned
2
Clean-up phase
Timeframe: days-years
Includes: local, state, tribal, contractors, EPA, etc.
Early phase
Timeframe: less than ~72 hrs
Includes: mostly local responders
Photo provided by the USEPA.

## Slide 3: Support Goals
Mitigation of received dose to first responders: Reduce the radiation dose burden to response and recovery personnel.
Containment of wastewater: Water may be used by first responders and it may also be used to reduce radiation levels to early responders and subsequent response teams. Natural rain events.
Decontamination (gross and final): Decontamination methods can be more effective if implemented within days of a release rather than waiting months or years.
Solid waste management: Large amounts of contaminated, solid waste will be generated over a wide area from businesses and residences.
Survey and monitoring: Monitor the radiological contamination levels in affected areas for an extended period.
A collection of response/recovery missions

## Slide 4: Approach
To develop a list of answers to the scenarios posed
  Solicited responses from various subject matter experts across the country and the United Kingdom.
  Reviewed citywide all-hazards response documents and radiologically-specific response documents.
  Obtained preferred methods from local and regional emergency management and response personnel from around U.S.
  Held workshops with various national and local SMEs.
  Held teleconferences and meetings to brainstorm and discuss potential options and identify gaps in our approach.
The information collected
  Contains a description of the equipment and its potential use, primary advantages and limitations, and opportunities for gathering additional data on its efficacy.

## Slide 5
TOOL DEMONSTRATION

## Slide 6: Sign-In Page

## Slide 7: dashboard
Navigation and Search Bar
Subject Pane –
Shows the options available to the user for inclusion into the Active Plan.
Active Plan Pane –
Keeps a running tab on those items selected in the Subject pane. Organizes your effort and equipment choices.

## Slide 8: Organization of Concepts
System concepts
The Subject Pane displays key system concepts in hierarchical order from left to right, as illustrated here.

## Slide 9: Subject pane - highlighted
The Subject Pane allows the user to explore the database of Support Goals , Scenarios , Recovery Methods , and Equipment Types supported by the Tool.
The baseline window provides the list of Support Goals as a timeline in the response and recovery.
  Mitigating dose and infrastructure operations might be initiated in the Response phase
  Wastewater related operations may be initiated in the Response or Recovery phases
  Solid waste, Decontamination, and Survey and Monitoring likely will occur in the Recovery phase only.

## Slide 10: Hypothetical Use case
As part of a planning section meeting during a discussion-based exercise, a hypothetical objective is established in the Incident Action Plan that requires reducing generation and containing spread of radioactively contaminated water.
  A radiological release has occurred in a downtown area that requires firefighting operations.
  The contamination has been determined to be localized to several square blocks surrounding the release site.
  The city has a combined sewer system that directs all sewer flow to the local wastewater treatment plant.

## Slide 11: Hypothetical Use case (cont.)
  Treatment plant operators have expressed strong concern that ingress of contaminated water into the treatment plant will force a shutdown of the plant due to an absence of policies, procedures, equipment, and expertise to safely operate the plant under such conditions.
The objective established in the response phase is to prevent ingress of contaminated water into the sewer system in time to minimize the contamination of the sewer system and water treatment plant.
The tool is used in the planning section to help organize the response effort (strategies and tactics) and understand the equipment options to successfully meet the objective.

## Slide 12: Support Goal selected
Since the objective is related to wastewater, we click on next to the corresponding support goal - “Wastewater containment during the response and recovery phases,” adding it into the Active Plan pane.
The Subject pane now refreshes to show the inferences that the Tool has made based on your limited input.
The seven scenarios related to Wastewater are now shown in the Subject pane.

## Slide 13: scenario selected
We add the scenario “Prevent ingress to sewers” into the Active Plan pane.
The Tool now infers that we are concerned with an Outdoor Area.
  This may come into play when we pare down equipment because the Tool will recommend those equipment better designed for outdoor activities rather than those designed for use indoors. We will ignore this for now.
The Tool shows us the Recovery Methods associated with “Prevent ingress to sewers” scenario.

## Slide 14: Recovery method selected
We add “Divert Water” from the sewer to the Active Plan pane rather than collecting, filtering, or transferring the water.
The Tool now asks for measurable data to help select equipment.
  If the user has an Equipment Budget, it can be entered and the Tool will recommend more strongly equipment that meets the budget constraints.
  If the user can express a level of Urgency for the equipment, then the Tool will recommend more strongly equipment that can be obtained more readily than others that require a lead time.

## Slide 15: Side note -Recovery methods
By clicking on the Recovery Methods tab, one can view the entire list of ~75 Recovery Methods supported by the Tool
Clicking on the recovery method name or information button shows more specific information regarding that recovery method (next slide).
Click here

## Slide 16: Side note - Exploring a recovery method
Recovery method
Associated equipment types
Associated scenarios

## Slide 17: Equipment selected
Based on the equipment listed by the Tool for our hypothetical use case, we chose to add to the Active Plan
  Sandbags,
  Gutter and downspouts,
  Modular flood wall,
  Floor bunding, and
  Drain covers and diverters
If we are satisfied with our choices, we can click on the Equipment List to view our output file.

## Slide 18: The Equipment list
We can view the attributes of any piece of equipment at any time while using the Tool by clicking on the equipment name.
The attributes also will be displayed when the user clicks on the Equipment List button.
To help the user understand how the equipment may be used to accomplish the objective, the Equipment List report contains:
  Listing of aliases (alternative names),
  A description of the equipment and its use,
  Guidance on best practices for its use,
  Required skill,
  Cost, etc.

## Slide 19: Summary
The Tool output will be a list of recommended methods and equipment to accomplish the specified goal complete with important information and guidance on use and best practices.
Potential uses:
  Tabletop exercises
  Identification of equipment needs prior to incident
  By Planning Section of Incident Command Structure (ICS) following incident
Current effort focuses on
  Gathering beta testing feedback
  Preparing the Tool for transfer to EPA for live deployment
  Identifying and including any missing information
Could be adapted for biological and chemical incidents
Deployment scheduled for September 2022.

## Slide 20: Acknowledgments
The research in this presentation was conducted under support from the U.S. Department of Homeland Security (DHS) Science and Technology Directorate (S&T) under IAA No. 70RSAT18KPM000188. Any opinions contained herein are those of the authors and do not necessarily reflect those of DHS S&T.
The U.S. Environmental Protection Agency, through its Office of Research and Development, partially funded and collaborated in the research described here under Interagency Agreement 92380201 with Argonne National Laboratory. This document was reviewed in accordance with EPA policy prior to publication. Note that approval for publication does not signify that the contents necessarily reflect the views of the Agency. Mention of trade names or commercial products does not constitute endorsement or recommendation for use of a specific product.
The submitted presentation has been created by UChicago Argonne, LLC, Operator of Argonne National Laboratory (“Argonne”). Argonne, a U.S. Department of Energy Office of Science laboratory, is operated under Contract No. DE-AC02-06CH11357. The U.S. Government retains for itself, and others acting on its behalf, a paid-up nonexclusive, irrevocable worldwide license in said article to reproduce, prepare derivative works, distribute copies to the public, and perform publicly and display publicly, by or on behalf of the Government.
All images courtesy of Shutterstock or personal archives unless stated otherwise.