## Slide 1: Overview of U.S. NRC Level 3 PRA Project Offsite Consequence Analysis Reactor At-Power Level 3 PRA for Internal Events and Floods
International MACCS User’s Group
September 19-21, 2022
K. Compton, A. Hathaway Office of Nuclear Regulatory Research
U.S. Nuclear Regulatory Commission (NRC)

## Slide 2: NRC Site Level 3 PRA
As directed in SRM-SECY-11-0089, the staff is developing a Level 3 PRA that:
  Addresses risk contributors not previously considered.
  Reflects technical advances since NUREG-1150 study, including application of methods developed by the State- of-the-Art Reactor Consequence Analyses (SOARCA) project within a full risk context.
  Allows extraction of new risk insights.
  Enhances NRC staff’s PRA capability and expertise.
Potential uses of the Level 3 PRA project are discussed in SECY-12-0123 and include research to:
  Enhance the technical basis for the use of risk information
  Improve the PRA state-of-practice
  Identify safety and regulatory improvements
  Support knowledge management
The first set of draft project reports were released for public comment on April 22, 2022 (87 FR 24205).
2

## Slide 3: NRC Site Level 3 PRA
Some of the information used in the preparation of the NRC Site Level 3 PRA reports was voluntarily provided by a licensee based on one of the nuclear power plants it is licensed to operate.
The information provided by the licensee reflects the plant as it was designed and operated as of 2012 and does not reflect the plant as it is currently designed, licensed, operated, or maintained.
In addition, the information provided by the licensee for the reference plant was changed based on additional information, assumptions, practices, methods, and conventions used by the NRC in the development of plant-specific PRA models used in its regulatory decision-making.
Use of the NRC Site Level 3 PRA reports to assess the risk from the reference plant is not appropriate and these reports will not be the basis for any regulatory decision associated with the reference plant.
3

## Slide 4: Documentation of MACCS Input Parameters
Technical discussion of input parameters
  Identification of analysis assumptions
  Description of conceptual models based on MACCS model description documents
  Discussion of technical bases for input parameters reflecting state of practice analysis
  Technical bases drawn from site specific information and SOARCA best practice recommendations such as those documented in NUREG/CR-7009
Tabular summary of input parameters with references to applicable discussion section for traceability
Identification of uncertainties and recommended sensitivity analyses to address potentially significant uncertainties
4

## Slide 5: Site Characteristics
The reference site for this study contains two four-loop Westinghouse PWRs with large dry containments.
The surrounding area consists of low rolling hills with primarily rural undeveloped forested land with a few homes and small farms.
The 3169-acre site is located on a bluff adjacent to the bank of a large river.
A large industrial complex with restricted access is located immediately across the river from the site.
The site is approximately 15 mi east-northeast of the county seat and 26 mi southeast of a larger city.
Distance (mi) | General Public | Industrial | Total
0.75 | - | - | -
1.75 | 25 | - | 25
5 | 592 | - | 592
10 | 3,226 | 2,000 | 5,226
15 | 15,902 | 11,000 | 26,902
20 | 42,961 | 11,000 | 53,961
25 | 133,099 | 11,000 | 144,099
50 | 746,243 | 11,000 | 757,243
100 | 3,350,283 | 11,000 | 3,361,283
Land Cover | Fraction
Woodlands (forest and scrubland) | 72%
Cropland | 19%
Open developed land | 4%
Low- to high intensity developed land | 4%
2013 land cover within 25 miles of the site
2015 cumulative population distribution

## Slide 6: Release Categories Source: NRC 2022f
Release Category | Description
V-F | Interfacing systems LOCA with auxiliary building failure (unscrubbed)
V-F-SC | Interfacing systems LOCA with auxiliary building failure (scrubbed)
V | Interfacing systems LOCA without auxiliary building failure
SGTR-O | Steam generator tube rupture with open secondary-side relief valves (unscrubbed)
SGTR-O-SC | Steam generator tube rupture with open secondary-side relief valves (scrubbed)
SGTR-C | Steam generator tube rupture with closed secondary-side relief valves
ISGTR | Induced steam generator tube rupture
CIF | Containment isolation failure (unmitigated)
CIF-SC | Containment isolation failure (mitigated)
ECF | Early containment failure
LCF | Late containment failure due to long-term quasi-static overpressure (unscrubbed)
LCF-SC | Late containment failure due to long-term quasi-static overpressure (scrubbed)
ICF-BURN | Intermediate containment failure due to deflagration/detonation (unscrubbed)
ICF-BURN-SC | Intermediate containment failure due to deflagration/detonation (scrubbed)
BMT | Containment failure due to basemat ablation
NOCF | No containment failure with releases from design-basis containment leakage

## Slide 7: Source Terms Source: NRC 2022f
Cesium release fractions, relative to accident initiation time
Note: Bypass scenarios are plotted with a dotted line. Release categories with no containment failure to the atmosphere are plotted with dashed lines
Chart: Time since Accident initiation (hr)
Release Category | Frequency (/rcy) | GE (hr) | Onset of Major Release (hr) | Cs Release Fraction | I Release Fraction
V-F | 1ˣ10-7 | 1.25 | 3.2 | 1.40E-01 | 1.30E-01
V-F-SC | 2ˣ10-7 | 1.25 | 3.2 | 1.20E-01 | 9.20E-02
V | <7ˣ10-8 | 7.5 | 10 | 1.10E-03 | 6.40E-04
SGTR-O | <7ˣ10-8 | 47 | 51 | 3.40E-01 | 2.50E-01
SGTR-O-SC | 2ˣ10-7 | 47 | 51 | 9.10E-03 | 1.00E-02
SGTR-C | <7ˣ10-8 | 47 | 52 | 1.20E-02 | 1.10E-02
ISGTR | 6ˣ10-7 | 8 | 11 | 2.30E-01 | 9.20E-02
CIF | <7ˣ10-8 | 3 | 21 | 4.20E-02 | 3.40E-02
CIF-SC | <7ˣ10-8 | 3 | 18 | 3.30E-02 | 2.50E-02
ECF | <7ˣ10-8 | 8 | 22 | 1.50E-01 | 1.60E-01
LCF | 2.9ˣ10-5 | 3 | 55 | 1.20E-02 | 9.90E-03
LCF-SC | 3ˣ10-6 | 8 | 128 | 6.00E-04 | 1.70E-03
ICF-BURN | 9ˣ10-6 | 3 | 28 | 4.30E-02 | 3.20E-02
ICF-BURN-SC | 2ˣ10-6 | 3 | 28 | 6.90E-05 | 5.90E-05
BMT | 8ˣ10-7 | 13 | Never | 6.40E-05 | 5.40E-05
NOCF | 2.4ˣ10-5 | 8 | Never | 8.50E-05 | 7.40E-05
Source Term Summary Note: rcy: reactor-critical-year; GE: General Emergency declaration time; Cs: Cesium; I: Iodine

## Slide 8: Meteorology
Five years of hourly observations from site were evaluated.
Weather file based on hourly observations from 1998
Base case model used all 8760 hourly observations, rather than sampling a subset of observations

## Slide 9: Evacuation Model
Cohort Number | Short Name | Description
1-3 | 1GP1/2/3 | 0–10 mile general public, first/second/third 30%
4 | 1GPT | 0–10 mile general public, final 10% (tail)
5 | IND | Industrial facility workers
6 | 1GPS | 10-15 mile general public shadow evacuees, 20%
7-9 | 2GP1/2/3 | 10-15 mile general public, first/second/third 30%
10 | 2GPT | 10-15 mile general public, final 10% (tail)
11 | SCH | 10-15 mile schools
12 | 2GPS | 15-20 mile general public shadow evacuees, 20%
13-15 | 3GP1/2/3 | 15-20 mile general public, first/second/third 30%
16 | 3GPT | 15-20 mile general public, final 10% (tail)
17 | 3GPS | 20-25 mile general public shadow evacuees, 20%
18 | NE | Non-evacuees
ETE mobilization and evacuation curve showing the 30, 60, 90 and 100 percent evacuation of the full 0–10 mile EPZ
Source: adapted from site evacuation time estimate report.
Region | 90% Evacuation Time (hh:mm) | 100% Evacuation Time (hh:mm)
0-10 mile (EPZ) | 1:40 | 3:20
10-15 mile | 6:00 | 7:30
15-20 mile | 8:45 | 10:45
Evacuation times defined in model
Early-phase cohorts used in model

## Slide 10: Tabulated Consequence Measures
Measure | MACCS Output Type | Spatial Interval | Units
Collective total effective dose | 5 | 0–50 and 0-100 mi | person-rem
Total latent fatality cases | 1 | 0–50 and 0-100 mi | persons
Population-weighted individual latent fatality risk | 8 | 0–10 mi | individual risk (unitless)
Total early fatality cases | 1 | 0–50 mi | persons
Population-weighted individual early fatality risk | 8 | 0–1.8 mi | individual risk (unitless)
Area exceeding 555 kBq/m2 Cs-137 | D | 0–50 and 0-100 mi | mi2
Population relocated during intermediate phase | 14 | 0–50 and 0-100 mi | persons
Total economic costs | 10 | 0–50 and 0-100 mi | 2015$
MACCS can produce many types of consequence measures (see Section 3.7 of NRC 2022g).
A diverse set of consequence measures spanning a variety of impacts is tabulated for use in the risk integration analyses documented in Section 5 of NRC 2022g.
Additional intermediate results related to these measures are included in each subsection of Section 4 of NRC 2022g for interpretative purposes.

## Slide 11: Treatment of Uncertainty
Uncertainty was addressed by
Including a qualitative discussion of uncertainties in input parameters.
Developing lists of candidate sensitivity analyses.
Performance of selected sensitivity analyses.
Sensitivity cases selected for quantification include:
ME_2: Meteorological Sampling
  Examines the effect of sampling only a subset of weather trials
  Provides a reference comparison case for sensitivity cases RE_4 and HE_2
RE_4: Accident Termination Time
  Examines the impact of terminating radiological releases 36 hours after SAMG entry
HE_2: Low-Dose Cancer Risk Estimation
  Examines the cancer risks arising only from moderate or high doses
  Uses a model that estimates cancer risk based only on annual individual doses greater than 0.05 Sv (5 rem) or lifetime individual doses greater than 0.1 Sv (10 rem)

## Slide 12: Impact of Weather Year Selection
Figures showing relative contribution of weather bins and release categories to mean suggest that for all impacts except early health effects, no weather conditions contribute disproportionately to mean values.
See section 6.5.3 of NUREG/CR-7245, which showed variations of less than 10% in individual latent fatality risk with variations in the weather year chosen for sampling.
Relative contribution of weather bins and release categories to mean (across all weather trials) population-weighted individual latent fatality risk within 10 miles
Relative contribution of weather bins and release categories to mean (across all weather trials) population-weighted individual early fatality risk within 1.8 miles
12

## Slide 13: Mean Size of Population Receiving Individual Early Phase Total Effective Dose Levels
Release Category | Low Dose (1-10 rem) | Moderate Dose (10-100 rem) | High Dose (> 100 rem)
V-F | 52,000 | 860 | 1.2
V-F-SC | 43,000 | 650 | 1.1
V | <1 | <1 | -
SGTR-O | 70,000 | 260 | <1
SGTR-O-SC | 280 | <1 | <1
SGTR-C | 90 | <1 | <1
ISGTR | 41,000 | 66 | <1
CIF | 2,300 | <1 | <1
CIF-SC | 2,200 | <1 | <1
ECF | 33,000 | 22 | <1
LCF | 310 | <1 | -
LCF-SC | <1 | - | -
ICF-BURN | 10,000 | <1 | -
ICF-BURN-SC | <1 | - | -
BMT | <1 | - | -
NOCF | <1 | - | -
The potential for moderate or high individual doses is largely associated with events with large releases that bypass containment (interfacing system LOCAs and, to a lesser extent, steam generator tube ruptures).
The population receiving high individual acute doses is very small (at most, less than one person on average), even for the most severe scenarios.
Values of less than a single person may occur as the result of weighting small populations by low values, usually arising from the combination of low values for the likelihood of being in a specific cohort and relatively infrequent weather conditions

## Slide 14: Collective Dose Within 50 Miles by Cohort
Chart: Mean population dose (person-rem) by cohort type
| V-F | V-F-SC | V | SGTR-O | SGTR-O-SC | SGTR-C | ISGTR | CIF | CIF-SC | ECF | LCF | LCF-SC | ICF-BURN | ICF-BURN-SC | BMT | NOCF
All Evacuating Cohorts | 15620 | 13470 | 8.7055 | 12322 | 687.4 | 461 | 9010 | 853 | 812 | 5200 | 10.72 | 0.00089 | 514 | 0.00024 | 0.065052 | 0.00043
NON-EVAC (<20 MI) | 170 | 140 | 0.79 | 210 | 9.8 | 11 | 160 | 50 | 44 | 100 | 2100 | 0.5 | 41 | 0.046 | 0.15 | 0.081
NON-EVAC (>20 MI) | 140000 | 120000 | 2000 | 150000 | 9200 | 9300 | 140000 | 59000 | 52000 | 150000 | 24000 | 1200 | 83000 | 90 | 390 | 160
CHRONC | 260000 | 210000 | 12000 | 500000 | 59000 | 100000 | 430000 | 360000 | 290000 | 570000 | 160000 | 29000 | 330000 | 1900 | 2800 | 3100
Over 95 percent of the collective effective dose within 50 miles is associated with the combination of
the late-phase exposures represented by the CHRONC cohort and
the early-phase exposures to the non-evacuating individuals beyond the 20-mile evacuation zone.

## Slide 15: Individual Peak Total Effective Dose
Mean value (across all weather trials) of peak total effective dose (rem) from early-phase exposure to non-evacuees
Mean value (across all weather trials) of peak total effective dose (rem) from late-phase exposure
Non-evacuees beyond 20 miles, as well as late phase individual doses, are characterized by low or very low (<10 rem) mean peak total effective doses to individuals
Values in figures below represent peak dose at distance; off-centerline doses may be much lower

## Slide 16: Total Latent Fatalities
Release Category | EVAC (0-50 mi) | NONEVAC (0-20 mi) | NONEVAC (20-50 mi) | CHRONC (0-50 mi) | OVERALL (0-50 mi) | OVERALL (ME_2) | OVERALL (HE_2)
V-F | 7 | <1 | 53 | 140 | 200 | 200 | 26
V-F-SC | 6 | <1 | 42 | 110 | 160 | 150 | 22
V | <1 | <1 | <1 | 6 | 6 | 6 | <1
SGTR-O | 5 | <1 | 60 | 260 | 320 | 320 | 18
SGTR-O-SC | <1 | <1 | 4 | 31 | 35 | 35 | <1
SGTR-C | <1 | <1 | 4 | 53 | 57 | 58 | <1
ISGTR | 3 | <1 | 52 | 220 | 280 | 270 | 6
CIF | <1 | <1 | 30 | 190 | 220 | 220 | <1
CIF-SC | <1 | <1 | 27 | 150 | 180 | 180 | <1
ECF | 2 | <1 | 72 | 300 | 370 | 380 | 3
LCF | <1 | 1 | 12 | 84 | 98 | 96 | <1
LCF-SC | <1 | <1 | <1 | 15 | 15 | 15 | <1
ICF-BURN | <1 | <1 | 43 | 180 | 220 | 220 | <1
ICF-BURN-SC | <1 | <1 | <1 | <1 | <1 | <1 | <1
BMT | <1 | <1 | <1 | 1 | 1 | 1 | <1
NOCF | <1 | <1 | <1 | 1 | 1 | 1 | <1
Latent fatality cases, 0–50 mi (persons): Base case with 0–50-mile totals for sensitivity cases ME_2 and HE_2
Most projected latent fatality cases arise in the late phase
Most early-phase contributions associated with populations beyond the 20-mile evacuation zone
Therefore, most latent fatalities are computed to arise from low or very low doses
Dose truncation significantly reduces consequences
Values of less than a single person may occur as the result of weighting small populations by low values, usually arising from the combination of low values for the likelihood of being in a specific cohort and relatively infrequent weather conditions

## Slide 17: Individual Latent Fatality Risk
Release Category | 1GPT (6.1%) | NON-EVAC (0.3%) | EARLY (wtd) | CHRONC | OVERALL (BASE) | OVERALL (ME_2) | OVERALL (RE_4) | OVERALL (HE_2)
V-F | 7.3E-04 | 2.2E-03 | 1.4E-04 | 3.2E-04 | 4.6E-04 | 4.7E-04 | 4.5E-04 | 1.3E-04
V-F-SC | 6.3E-04 | 1.8E-03 | 1.2E-04 | 2.2E-04 | 3.4E-04 | 3.6E-04 | 3.5E-04 | 1.3E-04
V | 2.6E-06 | 2.1E-05 | 4.8E-07 | 5.3E-05 | 5.4E-05 | 5.5E-05 | 5.5E-05 | 6.1E-09
SGTR-O | 1.8E-05 | 2.4E-03 | 9.7E-06 | 6.5E-04 | 6.6E-04 | 6.5E-04 | 5.5E-04 | 8.5E-06
SGTR-O-SC | 1.0E-06 | 7.0E-05 | 3.4E-07 | 1.2E-04 | 1.2E-04 | 1.3E-04 | 1.3E-04 | 1.5E-07
SGTR-C | 1.6E-06 | 7.1E-05 | 4.2E-07 | 2.1E-04 | 2.1E-04 | 2.1E-04 | 1.8E-04 | 1.2E-07
ISGTR | 7.6E-05 | 1.7E-03 | 1.7E-05 | 8.2E-04 | 8.4E-04 | 8.4E-04 | 6.8E-04 | 1.3E-05
CIF | 1.6E-07 | 3.7E-04 | 1.2E-06 | 7.9E-04 | 7.9E-04 | 8.0E-04 | 5.0E-04 | 5.1E-07
CIF-SC | 1.4E-07 | 3.2E-04 | 1.1E-06 | 6.0E-04 | 6.0E-04 | 6.0E-04 | 3.1E-04 | 4.2E-07
ECF | 2.0E-07 | 7.7E-04 | 2.5E-06 | 8.5E-04 | 8.6E-04 | 8.6E-04 | 6.4E-04 | 2.1E-06
LCF | 7.5E-08 | 1.3E-04 | 4.3E-07 | 6.1E-04 | 6.1E-04 | 6.1E-04 | 6.9E-06 | 6.7E-09
LCF-SC | 1.1E-10 | 1.7E-05 | 5.2E-08 | 1.4E-04 | 1.4E-04 | 1.5E-04 | 5.7E-06 | 1.3E-10
ICF-BURN | 2.4E-08 | 1.1E-04 | 3.6E-07 | 6.7E-04 | 6.7E-04 | 6.8E-04 | 5.0E-04 | 2.6E-08
ICF-BURN-SC | 2.8E-11 | 1.3E-06 | 4.0E-09 | 7.8E-06 | 7.8E-06 | 7.8E-06 | 7.8E-06 | -
BMT | 1.3E-08 | 5.8E-06 | 2.0E-08 | 1.3E-05 | 1.3E-05 | 1.3E-05 | 4.8E-06 | -
NOCF | 5.8E-11 | 2.7E-06 | 8.3E-09 | 1.4E-05 | 1.4E-05 | 1.4E-05 | 8.2E-06 | -
Mean value of the population-weighted individual latent cancer fatality risk within 10 miles, by release category and cohort or phase (fraction of 10-mile population provided in parentheses)
Individual latent fatality risk for population within 10 miles is dominated by late-phase exposure
Early phase individual latent fatality risk for population within 10 miles is limited by protective actions
Risks for late-evacuating cohorts higher than weighted-average early phase risk
Overall risk arises from low-dose exposures

## Slide 18: Individual Latent Fatality Risk Source Term Magnitude
Individual latent fatality risk for population within 10 miles is dominated by late-phase exposure for all release categories
Risk appears to plateau at release fractions greater than approximately 1%, illustrating the effect of late phase protective actions at limiting exposure
Mean (across all weather trials) early- and late-phase population-weighted individual fatality risk within 10 miles as a function of cesium release fraction

## Slide 19: Individual Latent Fatality Risk Warning Time
Only those releases having warning times on the order of 2 hours yield early-phase risks comparable to the late-phase risks.
Because early phase exposures are generally much less than modeled long-term exposures, factors affecting only early phase exposure (such as delayed or prolonged evacuations) are not expected to be a major contributor to total exposures unless they are so delayed that they result in high early phase exposures
Mean (across all weather trials) early- and late-phase population-weighted individual latent fatality risk within 10 miles, relative to warning time

## Slide 20: Early Health Effects
Early fatalities arise primarily among delayed evacuees under low wind speed, slightly stable, or stable conditions at distances of less than a few miles.
Release Category | 1GPT | Non-Evac
V-F | 2.9E-06 (0.92 mi) | 3.6E-04 (2.1 mi)
V-F-SC | - (0.78 mi) | 7.9E-05 (1.9 mi)
V | - | -
SGTR-O | - | 5.0E-05 (1.7 mi)
SGTR-O-SC | - | -
SGTR-C | - | -
ISGTR | - | 1.1E-05 (1.2 mi)
CIF | - | - (0.53 mi)
CIF-SC | - | - (0.53 mi)
ECF | - | - (0.58 mi)
LCF | - | -
LCF-SC | - | -
ICF-BURN | - | -
ICF-BURN-SC | - | -
BMT | - | -
NOCF | - | -
Relative contribution of weather bins to mean population-weighted individual early fatality risk within 1.8 miles
Cohort-specific mean population-weighted individual early fatality risk within 1.8 miles (95th percentile distance range of non-zero risk is provided in parentheses)

## Slide 21: Early Health Effects Sensitivity Analyses
Release Category | Base Case | ME_2 | Fraction of Base Case | RE_4 | Fraction of Case ME_2
V-F | 2.10E-06 | 5.40E-07 | 26% | 5.40E-07 | 100%
V-F-SC | 4.00E-07 | 4.30E-07 | 108% | 4.30E-07 | 100%
V | - | - | - | - | -
SGTR-O | 2.50E-07 | 2.40E-08 | 10% | 2.40E-08 | 100%
SGTR-O-SC | - | - | - | - | -
SGTR-C | - | - | - | - | -
ISGTR | 5.60E-08 | 2.30E-08 | 41% | 2.30E-08 | 101%
CIF | - | - | - | - | -
CIF-SC | - | - | - | - | -
ECF | - | - | - | - | -
LCF | - | - | - | - | -
LCF-SC | - | - | - | - | -
ICF-BURN | - | - | - | - | -
ICF-BURN-SC | - | - | - | - | -
BMT | - | - | - | - | -
NOCF | - | - | - | - | -
Sampling a subset of weather conditions can affect early fatality risk
Truncation of the release 36 hours after SAMG entry has no impact on early fatality risk
Individual early fatality risk, 0–1.8 mi (mean value across all weather trials)

## Slide 22: Land Contamination
A Cs-137 deposition level of 15 Ci/km2 is chosen as a reference level for risk integration because that level is likely to require some level of restriction during the intermediate and recovery phases.
Magnitude of affected area depends on magnitude of source term and operational definitional of contamination
Chart: Cesium Release Fraction
| 0.13 | 9.1999999999999998E-2 | 6.4000000000000005E-4 | 0.25 | 0.01 | 1.0999999999999999E-2 | 9.1999999999999998E-2 | 3.4000000000000002E-2 | 2.5000000000000001E-2 | 0.16 | 9.9000000000000008E-3 | 1.6999999999999999E-3 | 3.2000000000000001E-2 | 5.8999999999999998E-5 | 5.3999999999999998E-5 | 7.3999999999999996E-5
Cs-137 deposition > 15 Ci/km2 | 760 | 501 | 5 | 2620 | 49 | 103 | 1050 | 285 | 204 | 1540 | 63 | 10 | 207 | 0.5 | 0.2 | 0.6
Cs-137 deposition > 40 Ci/km2 | 255 | 172 | 2 | 1080 | 18 | 39 | 361 | 104 | 74 | 516 | 22 | 3 | 77 | 0.16 | 0.05 | 0.16
Farmland Interdiction | 1350 | 1130 | 73 | 2040 | 498 | 692 | 2940 | 2060 | 1430 | 2870 | 930 | 101 | 2010 | 6 | 4 | 7
Non-Farmland Decontamination/Interdiction | 330 | 220 | 3.9 | 1300 | 21 | 46 | 470 | 240 | 220 | 1100 | 93 | 8.5 | 380 | 0.48 | 0.65 | 0.94
Farmland Condemnation | 121 | 80 | 2 | 477 | 8 | 18 | 173 | 51 | 36 | 252 | 11 | 3 | 37 | 0.12 | 0.04 | 0.16
Non-Farmland Condemnation | 2.5 | 1.7 | 0.03 | 11.3 | 0.05 | 0.5 | 4.4 | 1.3 | 0.9 | 5.6 | 0.2 | 0.03 | 0.7
Non-Farmland Condemnation | 2.5 | 1.7 | 0.03 | 11.3 | 0.05 | 0.5 | 4.4 | 1.3 | 0.9 | 5.6 | 0.2 | 0.03 | 0.7
22

## Slide 23: Affected Population
Chart: Cesium Release Fraction
| 0.13 | 9.1999999999999998E-2 | 6.4000000000000005E-4 | 0.25 | 0.01 | 1.0999999999999999E-2 | 9.1999999999999998E-2 | 3.4000000000000002E-2 | 2.5000000000000001E-2 | 0.16 | 9.9000000000000008E-3 | 1.6999999999999999E-3 | 3.2000000000000001E-2 | 5.8999999999999998E-5 | 5.3999999999999998E-5 | 7.3999999999999996E-5
Evacuees Affected By Plume | 58000 | 58000 | 13000 | 67000 | 27000 | 65000 | 69000 | 69000 | 69000 | 67000 | 31000 | 15000 | 66000 | 3300 | 16000 | 16000
Early Phase Relocation | 67300 | 56200 | 1.01 | 90400 | 170.4 | 20.3 | 59600 | 1501.5 | 1201.4 | 30320 | 57.2 | 9e-05 | 2102.3 | 0.0003 | 0.0006 | 0
Late Phase - Interdicted | 46030 | 32420 | 39.74 | 172500 | 1737.5 | 3105 | 55010 | 17000 | 16000 | 110000 | 4000 | 53.6 | 40000 | 0.8 | 0.4 | 1.2
Late Phase - Condemnation | 37 | 20 | 310 | 0.04 | 1.3 | 36 | 2.1 | 1.8 | 61 | 0.7
Early-phase protective actions are largely confined to the area within 50 miles of the site
The size of the affected population drops as a function of the time since the accident
Most of the affected population in the late (recovery) phase is due to those requiring a relatively limited level of decontamination (no more than a decontamination factor [DF] of 3)
Values of less than a single person may occur as the result of weighting small populations by low values, usually arising from the combination of low values for the likelihood of being in a specific cohort and relatively infrequent weather conditions

## Slide 24: Economic Consequences
Majority of economic impacts occur within 50 miles for the types of source terms considered here
Mean (across all weather trials) total economic costs (2015$) within 50 and 100 miles as a function of cesium release fraction

## Slide 25: Economic Consequences
Total economic costs are generally dominated by population-dependent costs such is intermediate phase relocation and long-term recovery costs
Different cost components exhibit a different sensitivity to total release magnitude
Chart: Cesium Release Fraction
| 0.13 | 9.1999999999999998E-2 | 6.4000000000000005E-4 | 0.25 | 0.01 | 1.0999999999999999E-2 | 9.1999999999999998E-2 | 3.4000000000000002E-2 | 2.5000000000000001E-2 | 0.16 | 9.9000000000000008E-3 | 1.6999999999999999E-3 | 3.2000000000000001E-2 | 5.8999999999999998E-5 | 5.3999999999999998E-5 | 7.3999999999999996E-5
Total Emergency Phase | 230000000 | 210000000 | 25000000 | 280000000 | 51000000 | 120000000 | 230000000 | 130000000 | 130000000 | 180000000 | 59000000 | 28000000 | 130000000 | 6200000 | 31000000 | 31000000
Total Population Dependent - Late Phase | 6841000000 | 4766100000 | 3260000 | 24998000000 | 248010000 | 424380000 | 8220000000 | 2364600000 | 2126510000 | 18078000000 | 452500000 | 4430000 | 4647190000 | 66600 | 24300 | 112400
Milk and Crop Disposal | 437200000 | 366100000 | 20400000 | 753000000 | 153000000 | 205000000 | 918000000 | 624000000 | 431000000 | 926000000 | 269100000 | 24910000 | 612000000 | 1330000 | 920000 | 1560000
Farmland Interdiction | 630000000 | 480000000 | 19400000 | 1550000000 | 128000000 | 209000000 | 1090000000 | 600000000 | 419000000 | 1280000000 | 224000000 | 30000000 | 541000000 | 1550000 | 1030000 | 1940000

## Slide 26: Summary Dose and Health Effects
Over 95 percent of the collective effective dose within 50 miles, as well as over 95 percent of total latent fatalities within 50 miles, is associated with the combination of the late-phase exposures represented by the CHRONC cohort and the early-phase exposures to the non-evacuating individuals beyond the 20-mile evacuation zone.
Individual latent fatality risk for population within 10 miles is dominated by late-phase exposure for all release categories.
Early phase individual latent fatality risk for population within 10 miles is limited by protective actions.
Risks for late-evacuating cohorts are higher than weighted-average early phase risk.
Overall latent fatality risk arises from low-dose exposures.
Early fatalities in this analysis appear to arise only under the unlikely combination of all the following conditions:
  Occurrence of a bypass event (ISLOCA or SGTR cases) with a relatively large and fast release
  Occurrence of adverse meteorological conditions (primarily, stable, low wind speed conditions)
  Wind blowing in the direction of a populated sector very close to the site
  Delayed or slow evacuation of the populations toward which the winds are blowing

## Slide 27: Summary Land Contamination, Affected Population, and Economic Consequences
Magnitude of affected area and affected population depends on magnitude of source term and the effect of interest
Early-phase protective actions are largely confined to the area within 50 miles of the site
The size of the affected population drops as a function of the time since the accident
Most of the affected population in the late (recovery) phase is due to those requiring a relatively limited level of decontamination (no more than a decontamination factor [DF] of 3)
Total economic costs are generally dominated by population-dependent costs such as intermediate phase relocation and long-term recovery costs
Different affected population sizes and cost components exhibit a different sensitivity to total release magnitude, with early phase results being the least sensitive and late phase results being most sensitive
Majority of the economic impacts will occur within 50 miles for the types of source terms considered here

## Slide 28
QUESTIONS?

## Slide 29: Bibliography
NRC 2022a, “U.S. NRC Level 3 Probabilistic Risk Assessment (PRA) Project, Volume 2: Background, Site and Plant Description, and Approach” (ML22067A232)
NRC 2022b, “U.S. NRC Level 3 Probabilistic Risk Assessment (PRA) Project, Volume 3x: Overview of Reactor, At-Power, Level 1, 2, and 3 PRAs for Internal Events and Internal Floods” (ML22067A210)
NRC 2022c, “U.S. NRC Level 3 Probabilistic Risk Assessment (PRA) Project, Volume 3a, Part 1: Reactor, At-Power, Level 1 PRA for Internal Events, Part 1 – Main Report” (ML22067A211)
NRC 2022d, “U.S. NRC Level 3 Probabilistic Risk Assessment (PRA) Project, Volume 3a, Part 2: Reactor, At-Power, Level 1 PRA for Internal Events, Part 1 – Appendices” (ML22067A212)
NRC 2022e, “U.S. NRC Level 3 Probabilistic Risk Assessment (PRA) Project, Volume 3b: Reactor, At-Power, Level 1 PRA for Internal Flooding” (ML22067A213)
NRC 2022f, “U.S. NRC Level 3 Probabilistic Risk Assessment (PRA) Project, Volume 3c: Reactor, At-Power, Level 2 PRA for Internal Events and Floods” (ML22067A214)
NRC 2022g, “U.S. NRC Level 3 Probabilistic Risk Assessment (PRA) Project, Volume 3d: Reactor, At-Power, Level 3 PRA for Internal Events and Floods” (ML22067A215)
Sandia National Laboratories (SNL), 2019. State-of-the-Art Reactor Consequence Analyses (SOARCA) Project: Sequoyah Integrated Deterministic and Uncertainty Analyses (NUREG/CR-7245). Albuquerque, NM: Sandia National Laboratories, October 2019 (ML19296B786)