## Slide 1: Scoping Analysis of MACCS Modeling Improvements for the Study of Protective Action Recommendations (PARs)
A.J. Nosek, PhD
US Nuclear Regulatory Commission (NRC)
Notes: I’m a MACCS user since roughly 2007.

## Slide 2: Outline
Purpose and Objective
Background: Original PAR Study
Methodology
MACCS Version Comparison
Full Comparison
Sensitivity Analyses
Conclusions

## Slide 3: Purpose and Objective
U.S. NRC directed Sandia National Labs to conduct this analysis (SAND2022-3706).
  Sandia authors: Mariah Smith, Fotini Walton, Jennifer Leute, Joshua Dise
  NRC technical leads: AJ Nosek, Todd Smith, and Jonathan Barr
  NRC project manager: Salman Haq
Objective: Determine whether model and input parameter updates using the MACCS code result in changes when compared to the methodology of the original PAR study (NUREG/CR-6953).
Originally this work was intended to be a first step in determining whether a new PAR study was warranted.
This work has become an indication of how MACCS modeling has evolved, and it has become a case study that has helped identify important factors in consequence analysis.

## Slide 4: Background: Original PAR Study
The original PAR study (NUREG/CR-6953) contained many MACCS analyses that reflected various protective action strategies that radiological emergency response plans could implement.
The protective action strategies that were identified and evaluated include:
  Different types of evacuation (e.g., radial, lateral, staged)
  Sheltering in typical housing
  Sheltering in preferential shelters that offer greater shielding
  Various combinations of both sheltering and evacuation
The study evaluated strategies primarily on their ability to reduce potential health effects.

## Slide 5: Background: Original PAR Study, Vol. 1
Volume 1 of the original PAR study supports the following protective action strategies when appropriately selected for the incident:
  Immediate evacuation;
  Shelter-in-place;
  Staged evacuation;
  Preferential sheltering for special needs individuals;
  Delayed evacuation, until traffic controls are in place;
  Early closure of schools, parks, beaches, and government facilities at the Site Area Emergency;
  Consideration of early protective actions within the 3.2-km (2-mile) radius surrounding the plant at Site Area Emergency; and
  Early notification of the general population within the 10-mile EPZ to prepare for evacuation.
Preferential sheltering affords better shielding than normal residence but deemed unfeasible and not significantly more protective than evacuation.
Lateral evacuation can be an effective evacuation strategy when meteorologic conditions are such that wind direction does not change.

## Slide 6: Background: Original PAR Study, Vol. 3
Volume 3 provides a technical basis for decision criteria that can be used by licensees and offsite response organizations to enhance protective action strategy for nuclear power plant accidents that progress rapidly.
The results show that for a rapidly progressing accident, shelter-in-place is more protective when evacuation cannot be accomplished within predetermined timeframes.
  For the 0 to 2-mile area around a nuclear power plant: Evacuation is more protective when the evacuation time estimate (ETE) is less than 2 hours.
  For the 2 to 5-mile area: Evacuation is more protective when the ETE is less than 3 hours.
  For the 5 to 10-mile area: Shelter-in-place would likely be the initial protective action to allow a staged evacuation to proceed. If evacuation is the initial protective action for this area, it is more protective than shelter-in-place when the ETE is less than 3.2 hours.

## Slide 7: Methodology
This study (SAND2022-3706) selected one of the MACCS calculations from the original PAR study (NUREG/CR-6953, Vol. 3) known as “Scenario A.”
The new analysis then applied more recent inputs and methods to evaluate how these changes may impact results.
This was done in three steps:
  The first step was a MACCS version comparison: “Scenario A” (v.2.4) was rerun using MACCS v4.1, with no other updates.
  The second step was a full comparison: “Scenario A” (v2.4) was compared to a new analysis that applied a full set of new MACCS inputs and methods.
  The final step was a set of one-way sensitivity analyses using “Scenario A” (v4.1) as the base case.

## Slide 8: MACCS Version Comparison
Compared to version 2.4, MACCS version 4.1 provides many additional modeling capabilities, but the original models remain largely intact.
“Scenario A” using MACCS v4.1 was run with two weather models: “Non-uniform bin sampling” and “stratified random sampling.”
Results show strong agreement between the two versions of MACCS. The small differences are likely from the random sampling of different weather sequences.
 | MACCS Version 2.4.0.1 | MACCS Version 4.1.0.2 | Version 4.1.0.2
Radial Distance (mi) | Non-Uniform Bin Sampling | Non-Uniform Bin Sampling | Stratified Random Sampling
Latent Cancer Fatalities (mean weather results) |  |  | 
0-2 mi | 3.05E+01 | 3.17E+01 | 3.34E+01
2-5 mi | 2.10E+02 | 2.07E+02 | 2.24E+02
5-10 mi | 1.46E+02 | 1.57E+02 | 1.53E+02
Early Fatalities (mean weather results) |  |  | 
0-2 mi | 2.25E-01 | 7.96E-01 | 3.60E-01
2-5 mi | 7.68E-02 | 4.95E-01 | 1.61E-01
5-10 mi | 4.25E-05 | 5.58E-05 | 1.90E-04

## Slide 9: Full Comparison: Summary Inputs
Scenario A, a representative calculation from the original PAR study, Vol. 3 | Scoping analysis, using updated input/methodology
Report publication: 2010 MACCS v2.4.0.1 | Report publication: 2022 MACCS v4.1.0.2
Site: High population density SecPop site file created using 2000 population data and 2002 economic data 16 compass sectors | Site: High population density SecPop site file created using 2010 population data and 2007 economic data 64 compass sectors
Source term: Source term “A” (i.e., original PAR source term) | Source terms: Source term “A” (i.e., original PAR source term) SOARCA Surry STSBO Rlz 37 SOARCA Sequoyah STSBO Rlz 554
Shielding and exposure values: NUREG-1150, Peach Bottom | Shielding and exposure values: from various sources
Emergency Response: Circular evacuation (10-miles) 1 mph evacuation speed 0-2 miles: Immediate evacuation 2-5 miles: Shelter-in-place (SIP) then evacuate 5-10 miles: SIP then evacuate at 8 hours | Emergency Response: Evacuation cohorts and speeds based on Evacuation Time Estimates (ETEs) and subject matter experts Cohort-dependent evacuation modeling: Mixture of circular evacuation, keyhole evacuation, and no evacuation
Dose coefficients: Federal Guidance Report 13 (FGR-13) | Dose coefficients: FGR-13 (with minor updates)
Notes: As a second step, the selected MACCS analysis from the original PAR Study was compared to a new analysis that applied a full set of new MACCS inputs and methods.

## Slide 10: Full Comparison: Source Term Inputs
Cumulative release for the original PAR study source term and the two SOARCA source terms
The current scoping analysis includes:
  A source term from the original PAR study (Source Term “A”, Vol. 3)
  Two additional source terms from a more recent research project known as “State-of-the-Art Reactor Consequence Analyses (SOARCA)”.
All source terms represent rapidly progressing accidents.
The three source terms provide a range of release magnitudes.
Original PAR Source Term | SOARCA Surry STSBO Rlz 37 | SOARCA Sequoyah STSBO Rlz 554
Release starts <1 hour after initiation Modeled release period of ~21 hours ~60% of Iodine released from inventory | Release starts ~2 hours and 45 minutes after initiation Modeled release period of ~48 hours ~0.11% of Iodine released from inventory | Release starts ~ 3 hours after initiation Modeled release period of ~72 hours ~5.1% of Iodine released from inventory

## Slide 11: Full Comparison: Shielding Inputs
 | Activities | Cloudshine protection factor | Inhalation protection factor | Breathing rate () | Skin protection factor | Groundshine protection factor
Original PAR Study | Evacuation | 1.00 | 0.98 | 2.66E-04 | 0.98 | 0.50
 | Normal | 0.75 | 0.41 | 2.66E-04 | 0.41 | 0.33
 | Sheltering | 0.60 | 0.33 | 2.66E-04 | 0.33 | 0.20
Current Scoping Analysis | Evacuation | 1.00 | 0.98 | 2.66E-04 | 0.98 | 0.40
 | Normal | 0.68 | 0.46 | 2.66E-04 | 0.46 | 0.20
 | Sheltering | 0.60 | 0.25 | 2.66E-04 | 0.33 | 0.10
 | Activities | Cloudshine protection factor | Inhalation protection factor |  | Skin protection factor | Groundshine protection factor
Original PAR Study | Evacuation | 1.00 | 0.98 | 2.66E-04 | 0.98 | 0.50
 | Normal | 0.75 | 0.41 | 2.66E-04 | 0.41 | 0.33
 | Sheltering | 0.60 | 0.33 | 2.66E-04 | 0.33 | 0.20
Current Scoping Analysis | Evacuation | 1.00 | 0.98 | 2.66E-04 | 0.98 | 0.40
 | Normal | 0.68 | 0.46 | 2.66E-04 | 0.46 | 0.20
 | Sheltering | 0.60 | 0.25 | 2.66E-04 | 0.33 | 0.10
For the original PAR study, the shielding and exposure parameters were taken directly from NUREG-1150 for Peach Bottom.
For the current scoping analysis:
  The cloudshine and skin protection factors were taken from the SOARCA Surry Integrated Analysis Study
  The groundshine protection factors were taken from the Task 5 Letter Report: MACCS Uncertainty Analysis of EARLY Exposure Results
  The inhalation protection factors were taken from EPA’s Evacuation Risks: An Evaluation (EPA-520/6-74-002) study

## Slide 12: A Primer on Evacuation Models
Circular Evacuation
An evacuation region that is a 360-degree circle around the site.
Keyhole Evacuation
An evacuation region that has an inner circular area (red) and an outer downwind area (yellow).
As wind shift is forecasted to occur, the outer area expands to include the new downwind areas (green).
Allows for more targeted evacuation that focuses on areas of higher risk first.
Illustration of a Keyhole Evacuation Model

## Slide 13: Full Comparison: Emergency Response Inputs (1/2)
Scenario A | Evacuation Model | Population Distribution (0-10 miles) | 0-2 Miles |  |  | 2-5 Miles |  |  | 5-10 Miles |  |  | Evacuation Speed (mph)
Scenario A | Evacuation Model | Population Distribution (0-10 miles) | Delay to Shelter (hr) | Delay to Evac (hr) | Depart (hr) | Delay to Shelter (hr) | Delay to Evac (hr) | Depart (hr) | Delay to Shelter (hr) | Delay to Evac (hr) | Depart (hr) | Evacuation Speed (mph)
Cohort 1 | Circular | .909 | 0.5 | 0 | 0.5 | 0.5 | 0 | 0.5 | 0.5 | 8.0 | 8.5 | 1
Cohort 2 | Circular | .909 | 0.5 | 0 | 0.5 | 0.5 | 0.5 | 1.0 | 0.5 | 8.0 | 8.5 | 1
Cohort 3 | Circular | .909 | 0.5 | 0 | 0.5 | 0.5 | 1.0 | 1.5 | 0.5 | 8.0 | 8.5 | 1
Cohort 4 | Circular | .909 | 0.5 | 0 | 0.5 | 0.5 | 1.5 | 2.0 | 0.5 | 8.0 | 8.5 | 1
Cohort 5 | Circular | .909 | 0.5 | 0 | 0.5 | 0.5 | 2.0 | 2.5 | 0.5 | 8.0 | 8.5 | 1
Cohort 6 | Circular | .909 | 0.5 | 0 | 0.5 | 0.5 | 2.5 | 3.0 | 0.5 | 8.0 | 8.5 | 1
Cohort 7 | Circular | .909 | 0.5 | 0 | 0.5 | 0.5 | 3.0 | 3.5 | 0.5 | 8.0 | 8.5 | 1
Cohort 8 | Circular | .909 | 0.5 | 0 | 0.5 | 0.5 | 3.5 | 4.0 | 0.5 | 8.0 | 8.5 | 1
Cohort 9 | Circular | .909 | 0.5 | 0 | 0.5 | 0.5 | 4.0 | 4.5 | 0.5 | 8.0 | 8.5 | 1
Cohort 10 | Circular | .909 | 0.5 | 0 | 0.5 | 0.5 | 4.5 | 5.0 | 0.5 | 8.0 | 8.5 | 1
Cohort 11 | Circular | .909 | 0.5 | 0 | 0.5 | 0.5 | 5.0 | 5.5 | 0.5 | 8.0 | 8.5 | 1
Scenario “A” of the Original PAR Study

## Slide 14: Full Comparison: Emergency Response Inputs (1/2)
 | Description | Evacuation Model | Population Distribution (0-10 miles) | Notification Alarm (hr) | Delay to Shelter (hr) | Delay to Evacuation (hr) | Evacuation Start (hr) | Initial Evacuation Speed (mph) | Middle Evacuation Speed (mph)
Cohort 1 | Early Public | Circular | 0.055 | 1.50 | 0.25 | 0.25 | 2.00 | 20.0 | 10.0
Cohort 2 | Middle Public | Keyhole | 0.22 | 1.50 | 1.50 | 1.00 | 4.00 | 15.0 | 10.0
Cohort 3 | Late Public | Keyhole | 0.22 | 1.50 | 3.00 | 1.50 | 6.00 | 15.0 | 10.0
Cohort 4 | Tail Public | Keyhole | 0.1 | 1.50 | 6.50 | 1.50 | 9.50 | 20.0 | 20.0
Cohort 5 | Schools | Circular | 0.25 | 1.00 | 0.25 | 3.25 | 4.50 | 10.0 | 10.0
Cohort 6 | Special Facilities | Keyhole | 0.15 | 1.00 | 0.25 | 8.25 | 9.50 | 15.0 | 15.0
Cohort 7 | Shadow Public (10-20 mi) | Circular | 0 | 1.50 | 1.50 | 1.00 | 4.00 | 15.0 | 10.0
Cohort 8 | Non-Evacuating Public | No Evacuation | 0.005 | 1.50 | N/A | N/A | N/A | N/A | N/A
Current Scoping Analysis

## Slide 15: Results of Full Comparison
Results show a notable decrease in latent cancer fatalities using the PAR source term of about a factor of 2.
Significant decrease in latent cancer fatalities using the smaller source terms
Significant decrease in early fatalities using the PAR source term.
No early fatalities using smaller source terms.
While the PAR source term certainly displaces more individuals in total, it displaces slightly fewer individuals in our 0–10-mile region of interest.
Radial Distance (mi) | Original PAR Version 2.4.0.1 | Version 4.1.0.2 with Updates |  | 
 |  | PAR Source Term | SOARCA Surry STSBO Rlz 37 | SOARCA Sequoyah STSBO Rlz 554
Latent cancer fatalities (mean weather results) |  |  |  | 
0-2 | 3.35E+02 | 1.92E+02 | 2.06E+00 | 4.94E+01
2-5 | 1.67E+03 | 5.99E+02 | 3.10E+00 | 5.49E+01
5-10 | 1.61E+03 | 9.76E+02 | 2.65E+00 | 5.77E+01
0-10 | N/A | 1.77E+03 | 7.82E+00 | 1.62E+02
0-50 | N/A | 2.81E+04 | 5.17E+02 | 9.48E+03
Early fatalities (mean weather results) |  |  |  | 
0-2 | 2.48E+00 | 7.19E-02 | 0.00E+00 | 0.00E+00
2-5 | 1.70E+00 | 5.40E-03 | 0.00E+00 | 0.00E+00
5-10 | 4.67E-04 | 1.18E-06 | 0.00E+00 | 0.00E+00
0-10 | N/A | 7.72E-02 | 0.00E+00 | 0.00E+00
0-50 | N/A | 7.72E-02 | 0.00E+00 | 0.00E+00
Displaced individuals (mean weather results) |  |  |  | 
0-10 | N/A | 254,237 | 264,303 | 266,866

## Slide 16: Scoping Analysis Results: Peak Dose Comparison
Results show significant difference in peak dose among the source terms
“Peak dose” represents the spatial element with the highest dose in a radial interval.
Peak dose is closely related to centerline dose; however, centerline dose is not applicable for multiple plume segments.

## Slide 17: Scoping Analysis Results: Comparison of Source Terms
Radial Distance (mi) | Version 4.1.0.2 with Updates |  | 
 | PAR Source Term | SOARCA Surry STSBO Rlz 37 | SOARCA Sequoyah STSBO Rlz 554
0-2 | 2.41E+05 | 3.83E+03 | 6.09E+04
2-5 | 7.77E+05 | 5.75E+03 | 8.93E+04
5-10 | 1.33E+06 | 4.90E+03 | 1.07E+05
0-10 | 2.34E+06 | 1.45E+04 | 2.57E+05
0-50 | 4.76E+07 | 9.55E+05 | 1.71E+07
Radial Distance (mi) | Version 4.1.0.2 with Updates |  | 
 | PAR Source Term | SOARCA Surry STSBO Rlz 37 | SOARCA Sequoyah STSBO Rlz 554
0-10 | 2.89E-07 | 0.00E+00 | 0.00E+00
Radial Distance (mi) | Version 4.1.0.2 with Updates |  | 
 | PAR Source Term | SOARCA Surry STSBO Rlz 37 | SOARCA Sequoyah STSBO Rlz 554
0-2 | 1.42E-02 | 1.56E-04 | 3.19E-03
2-5 | 9.01E-03 | 4.79E-05 | 6.71E-04
5-10 | 5.00E-03 | 1.40E-05 | 2.51E-04
0-10 | 6.43E-03 | 2.92E-05 | 4.98E-04
Mean population-weighted individual cancer fatality risk comparison
Mean population dose (person-rem) comparison
99th percentile population-weighted individual risk of an early fatality comparison
Additional results comparing the source terms show the same trends

## Slide 18: Sensitivity Analyses
Other than for the source term input, the full comparison does not explain which updates in the current scoping analysis are responsible for the differences in the results.
As such, the study conducted several one-way sensitivity analyses.
Sensitivity analyses:
  Circular vs. keyhole evacuation
  Updated shielding inputs
  Compass sector resolution
All the sensitivity analyses use MACCS v4.1.0.2 and start with “Scenario A” of the original PAR study Vol. 3.

## Slide 19: Sensitivity Analysis: Circular vs Keyhole Evacuation (1/2)
Displaced Individuals During the Early Phase (All Cohorts)
Circular evacuation displaces entire 0–10-mile area.
Keyhole evacuation displaces almost entire 0–10-mile area. Why?
  Source terms release for tens of hours.
  Wind shift is more likely during long release durations.
  Therefore, long release durations expand the keyhole evacuation area.
When the keyhole evacuation expands to half of the sectors, the model assumes decision-makers evacuate the full area.
Radial Distance (mi) | PAR Source Term | SOARCA Surry STSBO Rlz 37 | SOARCA Sequoyah STSBO Rlz 554
Circular Evacuation (mean weather results) |  |  | 
0-10 | 254,100 | 253,900 | 254,300
Keyhole Evacuation (mean weather results) |  |  | 
0-10 | 232,100 | 249,600 | 253,800

## Slide 20: Sensitivity Analysis: Circular vs Keyhole Evacuation (1/2)
 | PAR Source Term |  | SOARCA Surry STSBO Rlz 37 |  | SOARCA Sequoyah STSBO Rlz 554 | 
 | Early Fatality | Latent Cancer Fatality | Early Fatality | Latent Cancer Fatality | Early Fatality | Latent Cancer Fatality
Circular Evacuation Model (mean weather results) |  |  |  |  |  | 
Cohort 1 | 1.29E+00 | 3.96E+02 | 0.00E+00 | 1.18E-01 | 0.00E+00 | 1.38E+02
Cohort 4 | 2.88E+00 | 3.85E+02 | 0.00E+00 | 1.29E-01 | 0.00E+00 | 1.47E+02
Cohort 7 | 1.15E+00 | 3.07E+02 | 0.00E+00 | 1.45E-01 | 0.00E+00 | 1.59E+02
Cohort 10 | 7.99E-01 | 2.90E+02 | 0.00E+00 | 1.70E-01 | 0.00E+00 | 1.74E+02
Keyhole Evacuation Model (mean weather results) |  |  |  |  |  | 
Cohort 1 | 1.29E+00 | 3.96E+02 | 0.00E+00 | 1.29E-01 | 0.00E+00 | 1.39E+02
Cohort 4 | 2.88E+00 | 3.85E+02 | 0.00E+00 | 1.31E-01 | 0.00E+00 | 1.47E+02
Cohort 7 | 1.15E+00 | 3.07E+02 | 0.00E+00 | 1.48E-01 | 0.00E+00 | 1.59E+02
Cohort 10 | 7.99E-01 | 2.90E+02 | 0.00E+00 | 1.73E-01 | 0.00E+00 | 1.75E+02
Health Effects of Various Cohorts in 0-10 Mile Area
Results show little difference in health effects between circular and keyhole evacuation model
Since the keyhole model displaces almost as many people as the circular evacuation, this is expected.

## Slide 21: Sensitivity Analysis: Updated Shielding Inputs
 | Original Shielding Values | Updated Shielding Values
Latent Cancer Fatalities (mean weather results) | Latent Cancer Fatality (mean weather results) | 
Cohort 1 | 3.96E+02 | 3.78E+02
Cohort 4 | 3.85E+02 | 3.65E+02
Cohort 7 | 3.07E+02 | 2.82E+02
Cohort 10 | 2.90E+02 | 2.63E+02
Early Fatalities (mean weather results) | Early Fatality (mean weather results) | Early Fatality
Cohort 1 | 1.29E+00 | 1.25E+00
Cohort 4 | 2.88E+00 | 2.81E+00
Cohort 7 | 1.15E+00 | 1.11E+00
Cohort 10 | 7.99E-01 | 7.74E-01
Health Effects of Various Cohorts in 0-10 Mile Area
Results show little difference in health effects between the original and updated shielding values
The updated shielding values did not change significantly from the original PAR study.
In general, shielding inputs are still expected to be important.

## Slide 22: Sensitivity Analysis: Compass Sector Resolution
 | 16 Compass Sectors | 64 Compass Sectors
Latent Cancer Fatalities (mean weather results) | Latent Cancer Fatality | 
Cohort 1 | 4.05E+02 | 2.98E+02
Cohort 4 | 3.94E+02 | 2.92E+02
Cohort 7 | 3.21E+02 | 2.41E+02
Cohort 10 | 3.05E+02 | 2.31E+02
Early Fatalities (mean weather results) | Early Fatality | 
Cohort 1 | 1.48E+00 | 1.00E+00
Cohort 4 | 3.14E+00 | 2.30E+00
Cohort 7 | 1.25E+00 | 8.47E-01
Cohort 10 | 9.37E-01 | 6.12E-01
Health Effects of Various Cohorts in 0-10 Mile Area
A compass sector sensitivity requires updated external files.
Both cases use:
  A site file based on 2010 population data and 2007 economic data.
  A meteorological file assuming 16 wind directions.
Results show a notable difference in health effects.
  The use of smaller spatial elements increases precision.
  The use of a 64-sector site file more accurately represents the spatial population distribution.

## Slide 23: Conclusions (1/2)
The current scoping analysis results in fewer health consequences than the original PAR study, indicating that the use of updated best practice modeling assumptions and capabilities are important.
The choice of source term had the largest impact on the health consequences.
The compass sector resolution update showed a significant difference.
The use of the keyhole evacuation model may affect the number of displaced individuals, depending on the release duration and wind persistence.

## Slide 24: Conclusions (2/2)
The shielding values in the PAR study and this analysis are not significantly different and did not significantly change the results.
Minimizing the potential harm from social disruption may also be important in determining which protective action strategies are best.
This analysis considered the number of displaced individuals as a measure of social disruption. This measure can be used to inform guidance to help ensure that protective actions provide more benefit than harm.
Notes: The original PAR study recommended protective actions strategies that minimize radiogenic health consequences.
This may be particularly true for source terms that produce relatively few radiogenic health effects.