## Slide 1: Pilot Research: Effectiveness of application of HVAC systems while sheltering-in-place
Nazila Tehrani, Ph.D. , Reactor Systems Engineer
U.S. Nuclear Regulatory Commission
Nazila.Tehrani @nrc.gov
September 20, 2022

## Slide 2: Disclaimer
The information and views expressed in the presentation are those of the authors and are not necessarily those of the NRC. Neither the U.S. Government nor any agency thereof, nor any of their employees, make any warranty, expressed or implied, or assumes any legal liability or responsibility for any third party’s use.

## Slide 3: Regulatory Purpose
Protective actions should provide more benefit than harm
NRC regulations require licensees to develop a range of protective actions, consistent with Federal guidance
Evacuation has historically been viewed as the default action
New evidence suggests that sheltering-in-place may be more beneficial than indicated by earlier studies

## Slide 4: Motivation for SIP Research
Provide insight into the use of heating, ventilation, and air conditioning (HVAC) while sheltering-in-place in response to a radiological release
Performed literature review to examine positive or negative health effects in populations sheltering-in-place in response to various emergencies, including nuclear power plant accidents

## Slide 5
Literature
Review
Effectiveness of sheltering from radiation exposures
Effectiveness
of HVAC for
shelter-in-place
Ventilation
Indoor particle penetration/ deposition
Literature Survey Categories

## Slide 6: Ventilation
Removes/dilutes pollutants concentration/Reduces high indoor temperatures
Several laboratory/field experiments performed to find optimum ventilation rates
Positive/negative effects of ventilation on human health explored
  office-type working
  residential buildings
  industrial environment
HVAC designs proposed to improve indoor air quality (IAQ)

## Slide 7: Ventilation using HVAC/Filtration
Filtration reduces particle exposures
Filter efficiency depends on particle size/type
Models produce data on particle size distributions
HVAC system can remove Ozone
  Residential 22%
  Commercial buildings 95%
HVAC associated with sick building syndrome (SBS) symptoms
  poor maintenance/hygiene
  lack of moisture control
  lack of control of HVAC materials and loaded filters
  pollutant emissions from HVAC
    duct liner
    duct connector
    duct sealant

## Slide 8: Effectiveness of HVAC for shelter-in-place
Sheltering-in-place is an option vs. evacuation in radiological release events
HVAC system with high efficiency filter reduce dose from radionuclides
A model developed to screen particle removal using high efficiency particle arresting (HEPA) air cleaners in residential buildings by changing
  number of stand-alone air cleaners
  air exchange rate
  volumetric flow rate through HVAC
  particle removal efficiency in HVAC filter
Larger particle size decreases HEPA HVAC effectiveness due to deposition on indoor surfaces instead of removal by HVAC filters

## Slide 9: Transient/Steady-State Conditions Model
(Ward et al. 2005)

## Slide 10: Ward (2005) Model Results
HVAC effectiveness depends on
  HVAC filter type
  HVAC operation
  Air exchange rate
  Particle size
  Duration of contamination release
90% particle absorption when three HVAC used vs. no HVAC

## Slide 11: Effectiveness Of Sheltering For Radiation Exposures
Sheltering in place (SIP) protects against radiation exposures
Reduction factor of radiation is the ratio of indoor to outdoor cumulative radioactivity doses
The indoor concentration depends on
  air exchange rate
  deposition rate
  penetration factor
Hirouchi (2017) calculated the reduction factor for (SIP) in Japanese dwellings
Hirouchi (2021) developed the data for deposition rate & penetration factor for I2 in Japanese dwellings for sheltering effectiveness

## Slide 12: Hirouchi (2021) Experiments
‘house experiment’ in Japanese dwellings
‘laboratory experiment’ inside a chamber using various
  Climate factors
  Temperature
  Humidity
  Air exchange rate
I2 assessed via laboratory experiments due to toxicity
parameters converted using a correlation factor to values associated to a house

## Slide 13: Laboratory Experiment
OPS is an optical particle sizer, GPD is a gas to particle device, GED is a gas exchange device, and MSAG is a metal standard aerosol generator. (Hirouchi, 2021)

## Slide 14: Hirouchi (2021) model
Hirouchi (2021) model simulate indoor setting to compute
  air exchange rate between indoor/outdoor environments
  penetration factor
  indoor deposition rate
  CI indoor concentration (m−3)
  CO outdoor concentration (m−3)
  P penetration factor (dimensionless, P ⩽ 1)
  λe air exchange rate (h−1)
  λd indoor deposition rate (h−1)
  λ decay constant (h−1)

## Slide 15: I2 Model/Experiment
Hirouchi, (2021) supplied data for particles and I2
Indoor deposition rate for a house room was
  independent of air exchange rate
  smaller than other researchers
    level of furnishings
    surface materials
Penetration factor
  associated with the air exchange rate
  consistent with those provided in literature
Effectiveness of sheltering-in-place
  higher when concentration of I2 is higher
  deposition rate of I2 is larger vs. particles (0.3–1 μm)
  penetration factor of I2 is smaller than particles (0.3–1 μm)

## Slide 16: Indoor particle penetration/ deposition
Pollutants enter a building through
  Infiltration
  Natural ventilation
  HVAC systems
Thatcher T. L., (2003)
Performed particle measurements in two houses
Determined correlation of particle
  Penetration
  Deposition
Measured particle loss rate
Estimated particle reduction using ventilation with HEPA-filtered air
Measured particle concentration

## Slide 17: Thatcher (2003) Model
SS conditions
  constant outdoor concentration
  steady infiltration rate
Reality
  time difference in Co and λv
  steady-state solution incorrect
  CI indoor particle concentration at time t (# cm-3)
  t time (h)
  Co outdoor particle concentration at time t (# cm-3)
  P penetration factor
  λv air exchange rate(h-1)
  β deposition loss rate (h-1)
  G formation of particles indoors (# cm-3 h-1)
  S particle generation through gas-particle conversion (# cm-3 h-1)
  F particle formation from chemical reaction (# cm-3 h-1)
  K particle size change through coagulation (# cm-3 h-1)
  H particle size change from hygroscopic growth (# cm-3 h-1).
  Thatcher T. L., (2003) K, H, or F have no effect on indoor particle concentrations

## Slide 18: Thatcher (2003) Results
Thatcher (2003) experiments data and model fit are illustrated
  measured/modeled indoor particle concentrations
  several optical particle diameter ranges
  downward sloping deposition stage
  upward sloping rebound stage
Deposition/penetration losses
  significant factors
  impact indoor particle concentrations
  impact exposures
  activate at the same time
Thatcher (2003) developed
  method for calculating
    size-resolved penetration factors
    deposition loss rates in full-scale homes

## Slide 19: Next Steps: Some questions to consider
Are current shelter models and simulation methods adequate to capture the dynamics of airborne radiological particulates?
  particle size distribution
  dynamic models of infiltration, filtration, deposition, indoor resuspension
Does research from various locations apply to U.S. homes?
Is there additional experimental work that needs to be performed?
Would the benefit of HVAC use outweigh the risk of non-use?

## Slide 20: References
Chen Chun, Zhao Bin, (2010), Review of relationship between indoor and outdoor particles: I/O ratio, infiltration factor and penetration factor.
Hirouchi J, Takahara S, Komagamine H, Watanabe M and Munakata M (2017) Factors affecting the effectiveness of sheltering in reducing internal exposure Asian Symp. Risk Assessment and Management.
Hirouchi Jun (2021), Penetration Factor And Indoor Deposition Rate Of Elementary And Particulate Iodine In A Japanese House For Assessing The Effectiveness Of Sheltering For Radiation Exposures.
Thatcher T L, Lunden M M, Revzan K L, Sextro R G and Brown N J (2003) A concentration rebound method for measuring particle penetration and deposition in the indoor environment Aerosol Sci. Technol. 37 275–88.
Ward M., Siegel J A, Corsi, R. L., (April 2005), The effectiveness of standalone air cleaners for shelter-in-place, Indoor Air, 15(2), pp. 127-134.

## Slide 21: Acronyms
AEERL Air and Energy Engineering Research Laboratory
ACH Air changes per hour
AMAD Activity median aerodynamic diameter
ASHRAE American Society of Heating, Refrigerating and Air-Conditioning Engineers
ASF Airborne sheltering factor
BWA Biological warfare agents
CFD Computational fluid dynamics
DRF Dose Reduction Factor
ELA Effective leakage area
GED Gas exchange device
GPD Gas to particle device
HEPA High efficiency particle arresting
HVAC Heating, ventilation, and air conditioning
IAQ Indoor air quality
FSEC Florida Solar Energy Center
Ls-1 Liter per second
LS Large structure
MERV Minimum efficiency reporting value
mm w.g. Millimeter of water gauge
MSAG Metal standard aerosol generator
NRC U.S. Nuclear Regulatory Commission
OPS Optical particle sizer
PAG Protective action guide
PAQ Perceived air quality
PFT Perfluorocarbon tracers
PM Particulate Matter
PNC Particle number concentration
PNSD Particle number size distribution
RES Nuclear Regulatory Research
RHS Right hand side
S/V surface-to-volume
SBS Sick building syndrome
SIP Shelter in place
SS Small structure
VOC Volatile organic compounds
WB Whole body