## Slide 1: Independent Verification of MACCS Functions
Osvaldo Pensado
opensado@swri.org
Center for Nuclear Waste Regulatory Analyses (CNWRA®)
Southwest Research Institute® (SwRI®)
Keith Compton, Salman Haq, AJ Nosek
US Nuclear Regulatory Commission (NRC)

## Slide 2: Acknowledgments
Project sponsored by the US Nuclear Regulatory Commission (NRC)
  Office of Nuclear Regulatory Research
  Division of Systems Analysis
  Accident Analysis Branch
This presentation describes work performed by the Southwest Research Institute (SwRI®) for the NRC under Contract No. 31310018D0002
This project is an independent product of the SwRI and it does not necessarily reflect the views of the NRC. The NRC staff views expressed herein are preliminary as part of an ongoing MACCS testing project
Pablo Bueno (SwRI) contributed with CFD simulations

## Slide 3: Testing approach and focus
Independent testing from software developers
Examination of extreme and limiting cases with closed form solutions
Simple system: one plume segment, constant windspeed, one cohort, no decay chains, one long-lived isotope, uniform population density
Continuation of work initiated in 2020
  MACCS Verification Report ML22026A461
Testing focus
  Plume meander model updates in MACCS Version 4.1
  Evacuation algorithm
  Gaussian plume dispersion model comparison to computational fluid dynamics (CFD)
Notes: MACCS Verification Report
ADAMS Accession Number ML22026A461
https://www.nrc.gov/docs/ML2202/ML22026A461.pdf

## Slide 4: MACCS defines concentrations on arcs of the grid
Air concentration on the line is mapped to the arc
Arc half-length is limited to 2.15 in MACCS
Run is stopped if the arc A-C exceeds 180° at 1000 m (stability class A)
  The stop condition is not consistently enforced when plume meander is enabled
Source

## Slide 5: Plume meander
MACCS applies empirical corrections to the lateral Gaussian dispersion coefficient to approximate the effect of plume meander
https://doi.org/10.1007/s10546-020-00547-4
Notes: Image source:
Concentration Fluctuations from Localized Atmospheric Releases (d-nb.info)
https://doi.org/10.1007/s10546-020-00547-4

## Slide 6: Ramsdell and Fosmire plume meander model
The broad plume run stop is not triggered when Gaussian dispersion coefficients, are computed using power law functions
Be careful combining the Ramsdell and Fosmire plume meander model with power law functions for
YSCALE
180°
360°

## Slide 7: Ramsdell and Fosmire plume meander model
MACCS assumes the last sectors (0° and 180°) accumulate the Gaussian tail concentrations, to enforce mass conservation
Notes: The high concentrations in the last sectors are non-intuitive. Higher doses could be produced by evacuating away from the plume centerline

## Slide 8: Regulatory Guide 1.145 meander model
The broad-plume run stop is always triggered when is computed with a power law function even when the plume spread is less than 180°
The meander factor for stability class A is 1, but the broad-plume run stop is triggered nonetheless
MACCS 4.1 does not allow combining RG 1.145 meander model with power law functions for

## Slide 9: Evacuation algorithm
Plume
Cohort

## Slide 10: Case 1: evacuation starts at plume arrival
Reasonable agreement between benchmarks (solid) and MACCS outputs (symbols)
Differences were expected due to approximated equations used in the benchmarks
Evacuation speed (m/s)
Evacuation speed (m/s)
Windspeed = 2 m/s
Symbols: MACCS outputs
Solid: independent computations
Symbols: MACCS outputs
Solid: independent computations
Windspeed = 2 m/s
End of evacuation zone
End of evacuation zone

## Slide 11: Case 1: evacuation starts at plume arrival, resuspension dose
MACCS assumes resuspension dose for evacuating cohort to be zero while plume is passing
  Non-zero doses are computed only when the evacuation speed is negligibly small (<0.008 m/s in the example)
Be careful using the resuspension dose pathway when evacuation is enabled
  MACCS mostly outputs zero, which is not informative
Symbols: MACCS outputs
Solid: independent computations
Evacuation speed (m/s)

## Slide 12: Case 2: evacuation triggered by an alarm
Evacuation speed = windspeed = 2 m/s
The evacuation alarm triggered at time 0 in the runs. The plume release was delayed
Sectors other than the sector closest to the source should avoid exposure
  Why is the dose non-zero?
The sector closest to the source (first sector, 100 m in length) should avoid exposure for plume delays > 50 seconds
  After 50 seconds the cohort fully evacuates the first sector
  Why is the dose non-zero in the first sector up to 900 s of plume delay?
Plume delay (s)
End of evacuation zone

## Slide 13: Gaussian plume modeling and CFD
Objective: explore consistency between Gaussian plume modeling and contaminant dispersion in air using computational fluid dynamics (CFD)

## Slide 14: Gaussian plume modeling
Gaussian functions solve the advective dispersive mass balance equation under steady-state
  No gravity and no settling
  Dispersivity
  Constand windspeed
  The plume does not disperse along the windspeed direction
Gaussian dispersion coefficients, , are empirically defined (e.g., based on work by Pasquill, Gifford, and Turner)
Ground deposition is modeled with additional assumptions and empirical concepts (e.g., deposition velocity)
Stability class
Stability class

## Slide 15: CFD Model
Ansys CFX software
Domain: 1005 m × 300 m × 800 m
Constant windspeed (2 m/s)
Atmospheric pressure at the outlet face
Source located on the ground
Contaminant of same density than air (to avoid settlement)
Steady-state solution
Two cases
  Laminar flow
  High turbulence at the inlet face

## Slide 16: CFD dispersion eventually plateaus
Gaussian plume model predicts more dispersion than the CFD model
Concentrations in the CFD model eventually plateau
  The centerline steady-state concentration becomes a constant (the plume moves undispersed from than point on)

## Slide 17: Observations
The extent of lateral dispersion in CFD is less than in Gaussian plume models
Dispersion in CFD is dependent on geometry and turbulence
  In flat geometries, turbulence dissipates
Gaussian plume model
Laminar case
High turbulence case

## Slide 18: General Observations
Broad-plume run stop is not consistently implemented in MACCS 4.1 when plume meander is enabled
Resuspension dose for evacuation cases is practically assumed to be zero in MACCS 4.1
Dose results for evacuation triggered by an alarm are difficult to explain
  Possible indication of implementation errors in MACCS 4.1
CFD in general predicts less lateral dispersion than Gaussian plume dispersion models
  Dispersion in CFD is dependent on the domain geometry
  Gaussian dispersion coefficients, , do not directly or “naturally” emerge from CFD model parameters