## Slide 1: Anticipated Impacts of Nuclear Accidents
A.J. Nosek, PhD
2022 International MACCS User Group
September 21, 2022

## Slide 2: Disclaimer
The information and views expressed in the presentation are those of the authors and are not necessarily those of the NRC. Neither the U.S. Government nor any agency thereof, nor any of their employees, make any warranty, expressed or implied, or assumes any legal liability or responsibility for any third party’s use.

## Slide 3: Who Am I
15 years experience at the Nuclear Regulatory Commission (NRC) with a focus on nuclear accident consequence analysis
  Consequence analyst for the NRC cost-benefit analysis on the Expedited Transfer of Spent Fuel (COMSECY-13-0030)
  Consequence analyst for various research projects (e.g., State-of-the-Art Reactor Consequence Analyses, NUREG-1935; Spent Fuel Pool Scoping Study, NUREG-2161)
  Dose analyst responding to the Fukushima Daiichi nuclear disaster through the NRC Incident Response Center
  Author of the theory manual for the MACCS severe accident consequence analysis code
  I help direct the development for the MACCS code
BS and MS in Nuclear Engineering (UW-Madison)
PhD in Decision Science and Operations Research, Industrial and Systems Engineering (UW-Madison)
  Dissertation titled, “Fukushima-informed Recovery and Cost Assessment: A Proposed Approach to Estimating the Cost of Nuclear Disasters”

## Slide 4: Outline
Introduction
Property Damage (Market Impact)
Economic Disruptions (Market Impact)
Nuclear Plant Damages (Market Impact)
Expenditures (Market Impact)
Environmental Damage (Non-Market Impact)
Burden of Societal Disruptions (Non-Market Impact)
Health Effects (Non-Market Impact)
A Practitioner’s Thoughts

## Slide 5: Introduction
Accounting for a comprehensive set of nuclear accident impacts is important for regulatory decision-making.
Nuclear accidents, particularly those with widespread contamination, have numerous adverse impacts.
Goal of presentation: categorize and present the broad range of adverse impacts resulting from nuclear accidents.
Notes: The goal of this presentation is to provide an overview of the impacts of a nuclear accident
The likelihood of an accident is very low, but the consequences can be very high.
To understand the value of nuclear safety, you have to understand what the consequences are.
Nuclear accidents cause a lot of different kinds of public consequences.
Nuclear accidents are very rare. They are not well-characterized with historical data.
Consequences that are not valued because they are overlooked or challenging to measure can undervalue the benefits of nuclear safety.
MACCS does not value or even measure all consequences of a nuclear disaster.
It is important for analysts to be diligent in evaluating different public harms and err on the side of inclusion where possible

## Slide 6: Introduction
Breakdown of Market and Non-Market Impacts of a Nuclear Accident
Market | Non-Market
Property damage (physical, contamination, interdiction, stigma) | Environmental damage (radiation-induced, disaster-related)
Economic disruptions (Losses to businesses, consumers, workers, and supply chains) | Burden of societal disruptions (related to stigma and evacuation / displacement)
Nuclear Plant (property damage and economic disruption) | Health effects (radiation-induced, disaster-related)
Expenditures (e.g., emergency response activities, relocation, medical services, decontamination-related activities, compensation and litigation system) | 
Notes: Market impacts here means impacts that can be valued with market data. Market impacts include disruptions to economic activity, but aren’t necessarily economic disruptions
Offsite contamination from a nuclear accident introduces many additional adverse impacts.

## Slide 7: Property Damage (Market Impact; 1/2)
Real estate
  Impacted by land interdiction, contamination, and stigma
  Impacted by local market conditions
    Business closures lead to loss of local employment opportunities, goods, and services
    Loss of local functional services (e.g., utilities, health care, schools)
Agriculture
  Crop losses impacted by food interdiction
Other tangible losses due to contamination
Nuclear plant damage
Notes: A nuclear accident does not cause direct physical damage to real estate.

## Slide 8: Property Damage (Market Impact; 2/2)
Two major offsite areas: interdicted and unrestricted areas
  Land interdiction makes property unusable
  Interdiction prevents upkeep, causing faster depreciation
  Interdiction can increase the perception that an area is hazardous
  Interdicted areas may have little to no salvage value
Notes: Interdicted areas are those with mandatory habitation restrictions,
Unrestricted areas can be lightly contaminated or may have a stigma due to proximity, and therefore people may practice avoidance.
Studies see market losses of real estate in unrestricted areas, but other studies see these values recover. Stark contrast to interdicted areas.
Interdicted areas are based on dose levels, but interdiction is typically performed along jurisdictional lines and may consider road access, utility access, and other local characteristics.
Interdicted areas are the most affected, as they are not only likely to be more contaminated, but they are also (at least temporarily) unusable and unmaintained.
In MACCS v3.10, property damage is based on how unmaintained structures may depreciate over time. Market conditions after a nuclear accident are not considered. As such, MACCS does not account for property losses outside the interdicted area. In interdicted areas, MACCS does not consider any immediate losses apart from the one-time loss for crops that become contaminated during the nuclear accident.

## Slide 9: Economic Disruptions (Market Impact; 1/2)
Economic activity requires:
  businesses that profit from operations
  workers that earn wages and benefits
  suppliers (and others) that sell their commodities to the businesses
  customers that purchase the goods or services
Economic disruptions can occur when restrictions disrupt one of these activities
Notes:   Capital in restricted areas is not usable
  Areas where customers work, workers live, or suppliers operate are restricted
Standard welfare analysis tends to focus on consumer and producer surplus.
MACCS: Two methods

## Slide 10: Economic Disruptions (Market Impact; 2/2)
Breakdown of Economic Value
Quantity
Business Revenue
Economic Value (i.e., the amount that consumers are willing to pay)
Consumer Surplus
Producer Surplus
Production Costs (i.e., labor, supply)
Notes:   Capital in restricted areas is not usable
  Areas where customers work, workers live, or suppliers operate are restricted
Standard welfare analysis tends to focus on consumer and producer surplus.
MACCS: Two methods

## Slide 11: Nuclear Plant Damages (Market Impact)
An accident causes both property damage and economic disruption
  Physical damage and contamination may lead to unusable property
  While the plant is not operating, there is a replacement energy cost to meet the electricity demand the plant would normally produce.
Nature of Accident | Property Loss | Economic Disruption
Minor damage (i.e., no permanent shutdown) | Restoration cost | Replacement energy (short period)
Permanent shutdown | Increased decommissioning cost Decreased salvage value | Replacement energy (long period)
Widespread nuclear plant shutdowns | Increased decommissioning cost Decreased salvage value | Replacement energy for affected nuclear plants
Notes: The utility experiences an opportunity cost while the plant is not operating.
  Physical damage to systems, structures, and components from exceedance of allowable temperatures and pressures
  Contamination may lead to unusable property

## Slide 12: Expenditures: Decontamination-Related Activities (1/2)
Widespread Decontamination Campaign
  Decontamination
  Waste storage
  Waste transportation
  Waste disposal
  Other support activities (e.g., community outreach, the development of plans and guidelines, research and development, worker training and acquisition, contract management and work verification)
Notes: Cleanup in Fukushima is the largest public works project in the history of Japan. Our models show a gap in being able to predict these costs that is not explained by Japan’s aggressive cleanup policies.

## Slide 13: Expenditures: Decontamination-Related Activities (2/2)
In addition to decontamination waste, other sources of contaminated waste include:
  Trash collection, agricultural, sewage / wastewater, deteriorating buildings, household belongings, disaster debris
Uncertain policies and level of preparedness will affect timeliness and costs
  Extent of decontamination
  Acceptable cleanup level
  Necessity of interim storage
  Final waste disposal site
  Decontamination pilot program
Notes: Cleanup in Fukushima is the largest public works project in the history of Japan. Our models show a gap in being able to predict these costs that is not explained by Japan’s aggressive cleanup policies.

## Slide 14: Expenditures: Relocation Expenses
Displaced individuals
  Food
  Transportation
  Temporary housing
  Moving costs
  Household goods
  Comparable replacement dwelling
  Ancillary housing costs (e.g., closing costs, mortgage interest, rental / down payment assistance)
Displaced businesses
  Operating expenses during a transitional period
  Temporary place of business
  Employee training
  Office supplies
Notes: If any areas exceed the relocation criteria, people and businesses may be displaced for years and may need to resettle elsewhere.
MACCS accounts for relocation costs using per capita input values in each phase of the accident.
Displaced individuals in the U.S. under the Uniform Relocation Assistance and Real Property Acquisition Act of 1970 are eligible for a comparable replacement dwelling.
A comparable replacement dwelling is commonly more expensive than the fair market value of the original property and may include a maximum payment of $22.5 thousand to cover the difference.
The Act also provides compensation for increased mortgage interest costs, rental assistance, down payment assistance, and incidental expenses such as closing costs.

## Slide 15: Expenditures: Medical Costs
Medical care for the sick and elderly
  Short-term care during evacuation and at shelters.
  Long-term living assistance for those separated from their support networks due to the evacuation.
Medical care for general population
  Care for displaced individuals with degraded physical or mental conditions.
  Periodic medical screenings for radiation-induced health effects, and care and treatment should they arise.
Notes: MACCS does not explicitly model medical costs.

## Slide 16: Other Expenditures
Emergency Response Activities
  Unified command and other field offices
  Emergency operations centers (Federal, state, and local)
  Offsite response organizations
Compensation and Litigation System
  Court and attorney fees
  Administration of claims
Notes: Emergency Response Activities:
The cost of operations is primarily for items like staffing and fuel. Emergency operations (e.g., facilitating an evacuation) are short-term and likely incur minor costs compared to costs for decontamination and compensation which may incur costs for years.
MACCS: Typical analyses assume the cost of emergency operations are relatively small and do not consider them, although could be accounted for in the relocation costs.
Compensation and Litigation System
Litigation costs include court and attorney fees related to legal disputes, but do not include settlements or awarded damages.
Costs related to administering a compensation program requires staffing for processing claims
These do not include the actual compensation to victims. Settlements and compensation amounts are benefit transfers and are already accounted for within property losses, income losses, or other types of impacts.

## Slide 17: Environmental Damage (Non-Market Impact)
Short-term radiation effects
  High doses can kill plants and animals (e.g., Chernobyl’s “red forest”).
Long-term radiation effects
  Studies observe negative effects on abundance, distribution, and life history of certain plants and animals (e.g., insects, birds).
  Mammals have flourished in exclusion areas without humans.
Physical damage
  No direct physical destruction of environment.
  Heavy decontamination (e.g., stripping topsoil, felling trees) is harmful in areas it is used.
  Light decontamination (e.g., grass cutting, washing, sweeping) is more widely used and has minimal impact.
Notes: Møller & Mousseau (2006).
When minimizing environmental harms was important to residents (e.g., family farms), Fukushima cleanup workers coordinated with residents to choose less invasive decontamination methods (JMOE, 2015, pg. 79). The heaviest types of decontamination methods tend to take considerably more effort and produce more waste which then must be managed.

## Slide 18: Burden of Societal Disruptions (Non-Market Impact)
Displacement of large populations creates significant personal and social disruptions
Types of impacts:
  Psychological distress (increased post-traumatic stress disorder and other disorders)
  Behavior and lifestyle changes (increased sleep issues, diabetes, dyslipidemia, overweight, and substance abuse)
  Loss of livelihood (loss of homes, jobs, lifestyle)
  Dysfunction in families and communities (conflicts regarding risk perception, compensation, and stigma)
  Diminished standard of living (worse living conditions, severe health care issues, and social isolation have been major causes of death among elderly)
Notes: lost control of their lives; lose their sense of purpose.
Standard of living: support network of elderly;
Standard of living: especially for Chernobyl.

## Slide 19: Health Effects (Non-Market Impact)
Disaster-related health effects
Radiation-induced health effects
  Stochastic effects (e.g., cancer)
  Deterministic effects (e.g., radiation sickness)
Notes: Disaster-related:
The Fukushima Prefecture Government has tallied 2,286 “disaster-related deaths” not directly caused by the earthquake or tsunami (JRA, 2019b). This toll accounts for most of the 3,739 disaster-related deaths in Japan, even though Fukushima Prefecture accounts for just 10% of the 15,899 deaths directly caused by the earthquake and tsunami (National Police Agency of Japan [JNPA], 2020).
MACCS does not estimate deaths related to displacement or the economic value of these deaths. Displacement-related deaths could be monetized in a similar way to radiation-induced deaths; however, this is not traditionally considered in cost assessments.
Radiation-induced:

## Slide 20: A Practitioner’s Thoughts
A nuclear accident with widespread contamination has many types of societal consequences
  Property damage
  Economic disruptions
  Nuclear plant damages
  Expenditures
    Emergency response activities
    Relocation expenses
    Medical costs
    Decontamination-related activities
    Compensation and litigation system
  Environmental damage
  Burden of societal disruptions
  Health effects
The information and views expressed in the presentation are those of the authors and are not necessarily those of the NRC. Neither the U.S. Government nor any agency thereof, nor any of their employees, make any warranty, expressed or implied, or assumes any legal liability or responsibility for any third party’s use
Notes: My thoughts about each
Property damage: Very important. Current methods don’t capture real estate losses well.
Economic Disruptions: Important, but somewhat limited by economic resiliency. New models capture well.
Nuclear plant damages: Fukushima accident shows this may be the biggest cost. Decommissioning $100 billion. Also, only 10 of Japan’s 54 reactors are back in operation.
Decontamination: Important. It’s possible that it’s more expensive than we anticipate. Also need to better quantify impacts of policy uncertainties on costs.
Burden of Societal Disruptions: Important. Cost analyses have not previously recognized this impact
Radiation-induced Health effects: Less important than traditionally thought. Models predict significant efforts to limit doses