## Slide 1
Tritium Dispersion and Exposure in the Near-field during a Nuclear Facility Demolition
Aneesh John & Sreeyuth Lal
September 2023
2023 International MACCS User Group (IMUG) Meeting and User Workshop
Notes: Thank you very much XYZ. As introduced, my name is Aneesh John, and I am part of the Thermalhydraulics and Safety Analysis Branch at CNL, working under Dr. David Wang. Today, I will present on some of the nearfield atmospheric dispersion research being conducted using Computation Fluid Dynamics at CNL.

## Slide 2: Background
Tritium dispersion
Tritium dispersion
Dispersion models often intended for local (e.g., ADDAM, MACCS) [1], or regional/global scales (e.g., HYSPLIT, WSPEEDI)
Nearfield concentrations are strongly affected by obstruction [2]
Building wake effects are captured by empirical factors in dispersion codes
CFD complements others in the nearfield
  Develop higher fidelity nearfield dispersion and deposition correlations
  CFD-informed data can be used to complement other systems’ nearfield dose assessments
CFD simulation of an explosive radiological dispersal device [4]
Gaussian atmospheric dispersion model [3]
Notes: Downwind distances ranging from 500 m to 30 km
Harper et al. (1995) document the expert elicitation that provides a technical basis for defining the plume lateral and vertical dispersion for a range of stability conditions, a range of surface roughness corresponding to several land-use categories, and downwind distances ranging from 500 m to 30 km.
MACCS assume building wakes complex geometry effect using simplification factor
MACCS does not directly model building wake effects. Instead, if there is building wake, it is up to the user to specify the initial plume width (SIGYINIT) and height (SIGZINIT) of the gaussian plume segments that are emitted from building wakes.
Radionuclide concentrations can increase several orders of magnitude due to nearfield obstruction
The maximum concentration of the radioactive material increased by 7 times compared to the concentration when the terrain and building effects were not considered.. [Jeong et al. 2014, "Terrain and building effects on the transport of radioactive material at a nuclear site"]
Simple models for deposition can be updated with CFD informed data for complex geometies
For small scales, CFD can provide spatially varying distribution of the radionuclide;
-complement MACCS efficiency for larger scales
-CFD can be used to develop efficient nearfield correlation for MACCS

## Slide 3: Tritium Emissions During Building Decommissioning
Tritium dispersion
During long-term operation of nuclear facilities, tritium can infiltrate into the concrete matrix of the structure.
Upon demolition, a fraction can be desorbed and released as HTO vapor, which presents an alternative transport and inhalation pathway (vs concrete demolition dust) when considering open-air demolition
Near field CFD assessments of dispersion aids in evaluating potential worker dose
Former Chemical Engineering and System Materials Building (B250) at Chalk River Laboratories
Notes: Radon exposure is a common issue and one of the leading causes of cancer around the world. The regulatory limits of safe concentration are below 200 Bq/m3
In many residential homes, the key pathway to radon exposure is through ingress of soil-laden radon into house through concrete slabs in buildings
A promising strategy to mitigate this issue is through a sub-slab depressurization where radon below the concrete slab is dispersed to the atmosphere through an above roofline or above ground line discharge
The above roofline is the standard practise which limits of the re-entrainment of radon-laden air back into the residential area. But during winter climates, this method can lead to icing and blockages.
On the other hand, above ground level dischange avoids these issues; but is presents the possibility of re-entrainment and exposure of individuals to discharged radon.

## Slide 4
Radon dispersion (past work)
Notes: This photo may be changed out for an alternate. Use a low transparency black & white.

## Slide 5: Domain Setup
6Lb
Lb
5Hmax
20Hmax
= Building angle
Vector
wind direction
Lb, max footprint of buildings
Total height = 6Hmax
Emitter
Neighbor
Domain setup
Computational grid
Positive building angles = release on upwind side
Zero building angle = wind parallel to gap
Negative building angles = release on downwind side
Notes: To investigate whether the ground level discharge was feasible, a CFD model was used to study the phenomenon.
The geometry was setup so that key parameters including the angle of the wind direction relative to the buildings could be modelled. The lateral extents of the domain was sized so that the boundary would have limited impact of the flow near the houses.
A small exhaust was placed at center of the canyon facing side of building 1 (shown by the yellow dot).
The building angle relative to the wind could be parametrically varied. An angle of 0 degrees is when the canyon opening was aligned with the vent flow; +90 degrees is when the wind direction is aligned to the vent flow, -90 degrees is when the wind direction opposes the vent flow.
A structured mesh was used with a refinement region located at the building, as shown on the right.

## Slide 6: Boundary Conditions & Calculation Models
Log-law velocity & temperature profiles, measurements at Chalk River Labs
Velocity, temperature and turbulence profiles following Monin-Obukhov theory
  friction velocity, 𝑢∗,
  roughness length, 𝑧_𝑜,
  ground temperature, 𝑇_𝑜,
  Monin-Obukhov length, 𝐿
Steady RANS with - tubluence
Boussinesq model for buoyancy
Emissions modeled using passive scalar transport equation, released as 1 a.c.u. (“arbitrary concentration unit”)
Notes: The atmospheric boundary layer was modelled following the Monin-Obukhov similarity theory. This approach required estimates of key parameters including friction velocity, roughness height, ground temperature and Monin-Obukhov length; these parameters are estimate for the CRL site from measurements at Perch Lake meteorological station.
The RANS equations were solved with realizable k-epsilon turbulence model
In this study, a passive scalar advection diffusion equation was used to model the dispersion of the radon; assuming that the particles are sparsely dispersed from the vent.
The passive scale represents the dilution factor of the radon stream, with a value of 1 at the vent.

## Slide 7: CFD Sensitivity Study – Overview
Explore the parameters that have the most important influence on concentration outside the emitting + neighbouring building
Wind direction influences ability for trap radon between buildings
Wind speed influences how much radon accumulates in vicinity vs dispersing away
Ventilation rate influences impingement on neighbour overall release rate
Stability influences vertical dispersion and has an important cross-correlation with wind speed
Size of buildings affects building canyon & cavity flow dynamics
Seasonality affects buoyant plume rise of exhaust gas
U1
U2
U1
U2
v1
v2
(**largest overall influence**)
Notes: The sensitivity of the dispersion to a number of different variables were explored. These include the wind direction, wind speed, ventilation rate, seasonality, stability and the size of the building.
Upon performing this study, it was discovered that the wind angle had the greatest impact on the dispersion behavior. Therefore, each of the variables were compared at a full range of building angles.
Altogether, these tests span over 300 simulations, which shows you just how large an undertaking this project was.

## Slide 8: Sensitivity to Atmospheric Stability & Season
winter-stable conditions (-12°C, MO: +26 m)
summer-stable conditions (16°C, MO: +13 m)
winter-unstable conditions (-7°C, MO: -89 m)
summer-unstable conditions (23°C, MO: -41 m)
Building 1 surface-avg. concentrations
Building 2 surface-avg. concentrations
(winter)
(winter)
winter
summer
stable
unstable
Notes: For example, atmospheric stability had a key effect on the dispersion behaviour.
As shown by the figures to the left, during stable conditions, there was less overall dispersion of the radionuclides.
Moving to the right, towards unstable conditions, the plume expands and disperses as it propagates downstream. Particularly, the summer stable cases show the greatest dispersion footprint.
The winter cases present the largest rise in the plume. During winter stable conditions, the radon stream rises significantly due to buoyant forces from the large difference in temperature between the indoor and outdoor air. In contrast, in the summer cases, the rise was minimum and summer stable cases present the highest ground level concentrations within the canyon.
Within any season and atmospheric state, the wind direction also affects the exhaust dilution, and the relationship is presented using curves such as those on the right. In this example we look at the building 1 on the top graph and building 2 on the bottom, and consider the surface facing the exhaust, the solid lines, and the surfaces away from the exhaust, dashed lines. In the example for winter cases, the stable, neutral and unstable states were compared using blue, green and red curves.
The effect of the wind direction is prominent, and some relationships can easily be seen.
For instance, for building 1 non-exhaust facing surfaces, dilution factors are highest at -90 degrees, where the wind blows the vented air against building 1 and immersing it to a larger portion of the radon laden air.
On the other hand, for building 2, dilution factors are highest at +90 where the wind blows the exhaust toward it.
Also, if we look at the building 2, on the bottom right, there is an order of magnitude drop in the dilution factor at an angle of 0 degrees as the radon-laden air is fully purged from the canyon when the canyon opening is aligned with the wind direction.
These are some of the simpler relationship we can see off-hand. However, even for this simple configuration, complex dispersion relationship exist.

## Slide 9: Method for Probabilistic Exposure Assessment
Developed method for assessing overall annual exposure, , based on:
Triple joint frequency distribution of (i) prevailing wind direction, (ii) wind speed categories, and (iii) atmospheric stability categories
Receptor residence time fraction, , indoors & outdoors
Infiltration factor, , along exhaust-facing () and non-exhaust-facing () surfaces
Used characteristic CRL meteorology to illustrate method
normalized exposure:
avg. outdoor concentration:
avg. indoor concentration:
Notes: Luke, Vlad and Kim were also involved with developing a method for assessing the normalized annual average exposures to radon gas near the residence from AGL discharge.
This method makes use of the triple joint frequency of the (i) prevailing wind direction, (ii) wind speed categories, and (iii) atmospheric stability categories. [A graphical representation of the joint frequencies is shown to the right.] [angular sector]
This is shown graphically on the figure to the right. Bins of stability state (stable, neutral, unstable) and wind speed (calm , reg, windy) are stacked for each wind direction in each 15⁰ increments.
Here, the total normalized exposure is the sum of the indoor exposure and the outdoor exposure. Each a product of the concentration and the residence time of the receptor at the setting.
An example is shown to the right. The outdoor exposure comprises the weighted sum of the atmospheric dilution factor by each of the triple joint frequency categories.
On the other hand, the average indoor concentration comprises the radon laden air infiltrating the house from the vented and non-vented walls, and the background concentration from direct infiltration from the soil.

## Slide 10
Tritium dispersion (ongoing work)
Notes: This photo may be changed out for an alternate. Use a low transparency black & white.

## Slide 11: Computational Setup
CNL site geometry and terrain from aerial scans
Source building surrounded by occupied buildings in the near vicinity
Lateral extents of domain according to Blocken [4]
CFD model of buildings and terrain
Hmax = 25 m
Source building
Source building
Steady RANS using segregated form
Realizable k-e two layer turbulence model
Boussinesq assumption for buoyancy
Passive scalar model for tritium
Numerical Method
N
Notes: Luke, Vlad and Kim were also involved with developing a method for assessing the normalized annual average exposures to radon gas near the residence from AGL discharge.
This method makes use of the triple joint frequency of the (i) prevailing wind direction, (ii) wind speed categories, and (iii) atmospheric stability categories. [A graphical representation of the joint frequencies is shown to the right.] [angular sector]
This is shown graphically on the figure to the right. Bins of stability state (stable, neutral, unstable) and wind speed (calm , reg, windy) are stacked for each wind direction in each 15⁰ increments.
Here, the total normalized exposure is the sum of the indoor exposure and the outdoor exposure. Each a product of the concentration and the residence time of the receptor at the setting.
An example is shown to the right. The outdoor exposure comprises the weighted sum of the atmospheric dilution factor by each of the triple joint frequency categories.
On the other hand, the average indoor concentration comprises the radon laden air infiltrating the house from the vented and non-vented walls, and the background concentration from direct infiltration from the soil.

## Slide 12: Meteorological Analysis
Meteorological data from onsite building
Joint frequency analysis of atmospheric stability and wind speed
Most frequent winds (neutral & windy) used for first analysis
Stability category | Wind speed category |  | 
Stability Class | Calm | Regular | Windy
Unstable | 0.20% | 4.95% | 2.61%
Neutral | 15.50% | 24.45% | 30.29%
Stable | 17.67% | 3.99% | 0.34%
Wind inlet profiles
Temperature inlet profiles
Notes: Luke, Vlad and Kim were also involved with developing a method for assessing the normalized annual average exposures to radon gas near the residence from AGL discharge.
This method makes use of the triple joint frequency of the (i) prevailing wind direction, (ii) wind speed categories, and (iii) atmospheric stability categories. [A graphical representation of the joint frequencies is shown to the right.] [angular sector]
This is shown graphically on the figure to the right. Bins of stability state (stable, neutral, unstable) and wind speed (calm , reg, windy) are stacked for each wind direction in each 15⁰ increments.
Here, the total normalized exposure is the sum of the indoor exposure and the outdoor exposure. Each a product of the concentration and the residence time of the receptor at the setting.
An example is shown to the right. The outdoor exposure comprises the weighted sum of the atmospheric dilution factor by each of the triple joint frequency categories.
On the other hand, the average indoor concentration comprises the radon laden air infiltrating the house from the vented and non-vented walls, and the background concentration from direct infiltration from the soil.

## Slide 13: Results - Wind speed
Wind velocity along streamwise center plane of source building
Wind
Wind
Notes: Luke, Vlad and Kim were also involved with developing a method for assessing the normalized annual average exposures to radon gas near the residence from AGL discharge.
This method makes use of the triple joint frequency of the (i) prevailing wind direction, (ii) wind speed categories, and (iii) atmospheric stability categories. [A graphical representation of the joint frequencies is shown to the right.] [angular sector]
This is shown graphically on the figure to the right. Bins of stability state (stable, neutral, unstable) and wind speed (calm , reg, windy) are stacked for each wind direction in each 15⁰ increments.
Here, the total normalized exposure is the sum of the indoor exposure and the outdoor exposure. Each a product of the concentration and the residence time of the receptor at the setting.
An example is shown to the right. The outdoor exposure comprises the weighted sum of the atmospheric dilution factor by each of the triple joint frequency categories.
On the other hand, the average indoor concentration comprises the radon laden air infiltrating the house from the vented and non-vented walls, and the background concentration from direct infiltration from the soil.

## Slide 14: Results - Turbulent kinetic energy
Turbulent kinetic energy along streamwise center plane of source building
Wind
Wind
Notes: Luke, Vlad and Kim were also involved with developing a method for assessing the normalized annual average exposures to radon gas near the residence from AGL discharge.
This method makes use of the triple joint frequency of the (i) prevailing wind direction, (ii) wind speed categories, and (iii) atmospheric stability categories. [A graphical representation of the joint frequencies is shown to the right.] [angular sector]
This is shown graphically on the figure to the right. Bins of stability state (stable, neutral, unstable) and wind speed (calm , reg, windy) are stacked for each wind direction in each 15⁰ increments.
Here, the total normalized exposure is the sum of the indoor exposure and the outdoor exposure. Each a product of the concentration and the residence time of the receptor at the setting.
An example is shown to the right. The outdoor exposure comprises the weighted sum of the atmospheric dilution factor by each of the triple joint frequency categories.
On the other hand, the average indoor concentration comprises the radon laden air infiltrating the house from the vented and non-vented walls, and the background concentration from direct infiltration from the soil.

## Slide 15: Results - Tritium Dispersion
Nearfield dispersion of tritium which is modeled as a passive scalar
N
Transport of tritium towards northeast due to hill-induced winds
Notes: Luke, Vlad and Kim were also involved with developing a method for assessing the normalized annual average exposures to radon gas near the residence from AGL discharge.
This method makes use of the triple joint frequency of the (i) prevailing wind direction, (ii) wind speed categories, and (iii) atmospheric stability categories. [A graphical representation of the joint frequencies is shown to the right.] [angular sector]
This is shown graphically on the figure to the right. Bins of stability state (stable, neutral, unstable) and wind speed (calm , reg, windy) are stacked for each wind direction in each 15⁰ increments.
Here, the total normalized exposure is the sum of the indoor exposure and the outdoor exposure. Each a product of the concentration and the residence time of the receptor at the setting.
An example is shown to the right. The outdoor exposure comprises the weighted sum of the atmospheric dilution factor by each of the triple joint frequency categories.
On the other hand, the average indoor concentration comprises the radon laden air infiltrating the house from the vented and non-vented walls, and the background concentration from direct infiltration from the soil.

## Slide 16: Results - Tritium Dispersion
Streamlines showing the impact of the hill on tritium dispersion downstream of it
N
Source building
Hill
Wind
Notes: Luke, Vlad and Kim were also involved with developing a method for assessing the normalized annual average exposures to radon gas near the residence from AGL discharge.
This method makes use of the triple joint frequency of the (i) prevailing wind direction, (ii) wind speed categories, and (iii) atmospheric stability categories. [A graphical representation of the joint frequencies is shown to the right.] [angular sector]
This is shown graphically on the figure to the right. Bins of stability state (stable, neutral, unstable) and wind speed (calm , reg, windy) are stacked for each wind direction in each 15⁰ increments.
Here, the total normalized exposure is the sum of the indoor exposure and the outdoor exposure. Each a product of the concentration and the residence time of the receptor at the setting.
An example is shown to the right. The outdoor exposure comprises the weighted sum of the atmospheric dilution factor by each of the triple joint frequency categories.
On the other hand, the average indoor concentration comprises the radon laden air infiltrating the house from the vented and non-vented walls, and the background concentration from direct infiltration from the soil.

## Slide 17: Results - Dilution factor
Dilution factor (DF) at 1 m above ground
Elevation view of site
0 °
60 °
30 °
-60 °
-30 °
Wind
DF
N
High dilution factors in the NE quadrant
Notes: Luke, Vlad and Kim were also involved with developing a method for assessing the normalized annual average exposures to radon gas near the residence from AGL discharge.
This method makes use of the triple joint frequency of the (i) prevailing wind direction, (ii) wind speed categories, and (iii) atmospheric stability categories. [A graphical representation of the joint frequencies is shown to the right.] [angular sector]
This is shown graphically on the figure to the right. Bins of stability state (stable, neutral, unstable) and wind speed (calm , reg, windy) are stacked for each wind direction in each 15⁰ increments.
Here, the total normalized exposure is the sum of the indoor exposure and the outdoor exposure. Each a product of the concentration and the residence time of the receptor at the setting.
An example is shown to the right. The outdoor exposure comprises the weighted sum of the atmospheric dilution factor by each of the triple joint frequency categories.
On the other hand, the average indoor concentration comprises the radon laden air infiltrating the house from the vented and non-vented walls, and the background concentration from direct infiltration from the soil.

## Slide 18: Conclusions
Lessons from a previous radon dispersion study applied to tritium dispersion study
From generic homes to a real site with uneven terrain  higher complexity
Effect of hill on near-field dispersion observed
Outlook
Complete test matrix for the joint frequency of wind speeds and atmospheric stability
Identify high dilution factor areas and dependence on key parameters
Use simulation results to inform demolition protocols
Notes: Luke, Vlad and Kim were also involved with developing a method for assessing the normalized annual average exposures to radon gas near the residence from AGL discharge.
This method makes use of the triple joint frequency of the (i) prevailing wind direction, (ii) wind speed categories, and (iii) atmospheric stability categories. [A graphical representation of the joint frequencies is shown to the right.] [angular sector]
This is shown graphically on the figure to the right. Bins of stability state (stable, neutral, unstable) and wind speed (calm , reg, windy) are stacked for each wind direction in each 15⁰ increments.
Here, the total normalized exposure is the sum of the indoor exposure and the outdoor exposure. Each a product of the concentration and the residence time of the receptor at the setting.
An example is shown to the right. The outdoor exposure comprises the weighted sum of the atmospheric dilution factor by each of the triple joint frequency categories.
On the other hand, the average indoor concentration comprises the radon laden air infiltrating the house from the vented and non-vented walls, and the background concentration from direct infiltration from the soil.

## Slide 19: References
[1] A. J. Nosek and N. Bixler, “MACCS Theory Manual,” Sandia Report SAND2021-11535, 2021. Accessed: Feb. 10, 2023. [Online]. Available: https://maccs.sandia.gov/docs/MACCS_factsheets/MACCS%20Theory%20Manual%20Final_SAND2021-11535_Jan.pdf
[2] H. Jeong, M. Park, H. Jeong, W. Hwang, E. Kim, and M. Han, “Terrain and building effects on the transport of radioactive material at a nuclear site,” Annals of Nuclear Energy, vol. 68, pp. 157–162, Jun. 2014, doi: https://doi.org/10.1016/j.anucene.2014.01.004.
[3] Snoun, Hosni, et al. “A Comprehensive Review of Gaussian Atmospheric Dispersion Models: Current Usage and Future Perspectives.” Euro-Mediterranean Journal for Environmental Integration, 28 Mar. 2023, https://doi.org/10.1007/s41207-023-00354-6.
‌[4] Kaminski, Michael D., et al. “Wide-Area Decontamination in an Urban Environment after Radiological Dispersion: A Review and Perspectives.” Journal of Hazardous Materials, vol. 305, Mar. 2016, pp. 67–86, https://doi.org/10.1016/j.jhazmat.2015.11.014.
[5] Lebel, Luke, et al. “Dispersion Simulations of Radon Discharges between Neighboring Buildings and Their Sensitivity to Meteorology, Discharge Rate, and Building Geometry.” Health Physics, vol. 122, no. 3, 29 Dec. 2021, pp. 383–401, https://doi.org/10.1097/hp.0000000000001510. Accessed 8 Feb. 2023.
[6] Lebel, Luke, et al. “Method for Assessing Radon Re-Entrainment Risks from above Ground Level Discharges from Sub-Slab Depressurization Systems.” Building and Environment, vol. 215, May 2022, p. 108942, https://doi.org/10.1016/j.buildenv.2022.108942. Accessed 26 Oct. 2022.
Notes: Luke, Vlad and Kim were also involved with developing a method for assessing the normalized annual average exposures to radon gas near the residence from AGL discharge.
This method makes use of the triple joint frequency of the (i) prevailing wind direction, (ii) wind speed categories, and (iii) atmospheric stability categories. [A graphical representation of the joint frequencies is shown to the right.] [angular sector]
This is shown graphically on the figure to the right. Bins of stability state (stable, neutral, unstable) and wind speed (calm , reg, windy) are stacked for each wind direction in each 15⁰ increments.
Here, the total normalized exposure is the sum of the indoor exposure and the outdoor exposure. Each a product of the concentration and the residence time of the receptor at the setting.
An example is shown to the right. The outdoor exposure comprises the weighted sum of the atmospheric dilution factor by each of the triple joint frequency categories.
On the other hand, the average indoor concentration comprises the radon laden air infiltrating the house from the vented and non-vented walls, and the background concentration from direct infiltration from the soil.

## Slide 20
Thank you
Contact information:
Aneesh.John@cnl.ca
Sreeyuth.Lal@cnl.ca