## Slide 1
UFOTRI: Application for accidental tritium releases and new developments
W. Raskob
Karlsruhe Institute of Technology (KIT) - retired

## Slide 2: Introduction to the Topic
Background and introduction
Assessment model UFOTRI
Example results from assessments for DEMO
  Accident sequence
  Screening calculations for unit releases
Further developments
Summary and conclusions

## Slide 3: Why special tritium model/UFOTRI
Main difference is the very dynamic behaviour of tritium which is comparable to cycling of water vapour in the environment – transfer rates in the order of minutes/hours compared to days and weeks for other radionuclides
  Due to the dynamic behaviour, environmental conditions play a dominant role in the transfer of tritium in the environment – process modelling for foodchain has to be part of the dispersion model
  Reemission to atmosphere from vegetation and soil
  Transfer into organic matter – only this fraction is stable in the foodchain
  Conversion of tritiated gas (HT) into tritiated water (HTO)
UFOTRI was selected as reference assessment code for ITER

## Slide 4: UFOTRI

## Slide 5: Sub-model short term (hourly time step)
Transport and dispersion in the atmosphere
  Primary plume by Gaussian trajectory model
  Secondary plume by an instantaneous area source model
Exchange atmosphere - plant - soil
  Deposition and reemission is expressed via resistance functions dependent on the prevailing meteorological conditions (for both tritium and water vapour)
Transport in soil
  Water and tritium movement depends on the matrix forces
Cycling through the foodchain
Photosynthesis rate (for OBT formation) depends on plant development stage, photosynthetic active radiation (PAR), leaf area index (LAI), leaf temperature (air temperature) and opening of stomata

## Slide 6: Limitations
Not many experimental data on animals is/was available
Limitation to most important food products, ignoring e.g. fruits
Reemission from soil/plants in particular in case of rain is modelled in a simplified manor
OBT formation model cannot reproduce early build-up of OBT after exposure – processes not fully understood; however, the OBT at harvest is quite OK
OBT formation at night – not many experimental data
Deposition via snowfall not considered

## Slide 7: Sub-model long term
Compartment model for calculating the longer term behaviour of tritium in the foodchain
  Transfer rates are means, valid for the vegetation period and derived from equilibrium conditions
  HTO and OBT are treated separately

## Slide 8: Current assessments for DEMO
Deterministic unit releases
Probabilistic unit releases for Cadarache, one year of meteorological data, 144 representative cases with probability of occurrence
Accident scenarios

## Slide 9: Deterministic and probabilistic calculations (1g of HT/HTO)
Deterministic conditions
  One release duration of 1 hour
  Different weather conditions representing moderate worst case conditions
  Three release heights from 10 to 150m
Probabilistic conditions
  Two different release durations of 1 and 30 hours
  Three release heights from 10 to 150m

## Slide 10: HTO: General findings
The maximum effective dose is highest for the probabilistic case (95% percentile, 10m, one hour), demonstrating the importance of the environmental conditions also after the end of the release
The maximum early dose of the most severe deterministic cases is very close to the early dose of the probabilistic one-hour release (95% percentile, 10m, one hour)
The 150m case without building wake shows lowest doses – even if unrealistic with the given building

## Slide 11: HT-HTO: General findings
The effective dose for HT releases is significantly higher than the early dose
Probabilistic results (95% percentile) are comparable or even higher compared to the deterministic ones
The difference between HT and HTO for the early dose is high
The difference between HT and HTO for the ED is less than a factor of 10 – mainly as result from reemission of HTO that is converted from deposited HT

## Slide 12: Scenario: Event of the loss of vacuum (LOVA)
LOVA in the VV occurs at a port seal of the closure plate in an equatorial port plug
  A small leak of 1.0E-3 m² (CaseI)
  A large break size of 1.0E-2 m² (CaseII, CaseIII)
  Air in one PC ingresses into the VV via the broken penetration
  Venting systems trap tritium (99% efficiency) and dust (99.9%)

## Slide 13: Dose at several distances (mSv)
Dose assessments due to the consequences of accidental tritium release assessed with UFOTRI, and W-dust with COSYMA
Historic weather conditions from Cadarache (ITER) in 1991 are applied for a probabilistic assessment
The early dose (7 days) exceeds 1 mSv up to several km from the release point, and it is dominated by tritium
The ED near to the release is higher than 10 mSv, and drops below 1 mSv only after 10 km
Contribution to the ED is similar for dust and tritium (higher)

## Slide 14: New developments
In a new task, the special functionalities of the tritium model UFOTRI will be integrated into JRODOS
There are two main rationales for this work
First, the atmospheric dispersion model of UFOTRI is a simple Gaussian type model that is no longer state of the art
Second, UFOTRI has limited applicability and support is difficult, whereas JRODOS has a broader community and support possibilities

## Slide 15: Near-range ADM models
Several models for atmospheric dispersion and deposition in the near range:
  Gauß-"puff"-models ATSTEP (KIT, no longer in) and RIMPUFF (DTU, Denmark)
  For complex terrain: Particle model DIPCOT (Demokritos, Greece)
  For powerful servers: Lagrange Particle Model LASAT (Janicke, Germany)

## Slide 16: Key features of RODOS/JRODOS Real-time On-line Decision Support system
Multi-user operation in national/regional emergency centres for off-site nuclear emergency management
Provision of information for decision-making
  on local / national / regional / European scales,
  in the early and later phases of an accident,
  for all relevant emergency actions and countermeasures.
Wide IT applicability - at present Microsoft Windows and Linux

## Slide 17: JRODOS: Tasks, input data, output
Environmental Contamination of Air, Ground, and Food, Potential Doses
Areas, Organ Doses, People affected by Countermeasures, Health Effects, Effort, Costs
Ranked List of Feasible Strategies of Long-Term Counter-measures (MAVT)
Meteorological and Release Data
Radiological Monitoring Data

## Slide 18: JRODOS EMERGENCY chain models
Accident Release of 52 hours
Dose rate calculation, Early countermeasure simulation, Health effects and costs

## Slide 19: Specialised functionalities of JRODOS
Dirty bomb
Wildfire
Tornadoes
Source term reconstruction
Continuous mode
Recurrent job launcher
Ensemble generator
Evaluation tool
Nuclear explosion
Statistical tool

## Slide 20: JRODOS will contain probabilistic functions
When tritium is part of JRODOS, we can follow the methodology applied by Germany (JRODOS) and Sweden (ARGOS) that performed assessments for new planning zones for countermeasures following Fukushima accident
In Germany, calculations were performed for 365 days, 3 sites and 3 source terms
80% percentile for maximum distance from NPP was taken as representative distance for the planning zone

## Slide 21: How to integrate

## Slide 22: Summary and Perspectives
As tritium behaves special, a specialised simulation model was developed about 30 years ago
UFOTRI was selected as reference assessment model for ITER and is now also used for DEMO
It can be coupled to COSYMA for assessing releases of tritium and activation products
Its main limitation were the Gaussian dispersion model and limited maintenance capabilities
Integration into the JRODOS system with state of the art dispersion models (e.g. particle models) more than 40 counties using the tool will overcome these limitations
A first version should be ready by 2025

## Slide 23
Thank you for your attention!
https://resy5.iket.kit.edu
Wolfgang Raskob – former Head - retired
JRODOS Team
Tel.: +49 721 608-22480
Wolfgang.raskob@partner.kit.edu
Karlsruhe Institute for Technology (KIT)
Institute for Thermal Energy Technology and Safety (ITES)
Hermann-von-Helmholtz Platz 1 76344 Eggenstein-Leopoldshafen, GERMANY
Notes: Thank your very much for your attention.