## Slide 1
The Use of Meteorological Fields Nudged with Local Observations for Dispersion Modeling
And
Recent HYSPLIT Updates
Fong (Fantine) Ngan1,2 (Fantine.Ngan@noaa.gov), Mark Cohen1, Christopher P. Loughner1,
Sonny Zinn1, Temple R. Lee3,4, Edward Dumas3,5, Travis J. Schuyler3,4, Michael Buban3,4,
Bruce Baker3, Joseph Maloney6, David Hotz6, Nebila Lichiheb3,5, Alice Crawford1,
Tianfeng Chai1, HyunCheol Kim1,2, Miguel Cahuich1,2, Bavand Sadeghi1,2
1 NOAA Air Resources Laboratory, College Park, MD
2 Cooperative Institute for Satellite Earth System Studies, University of Maryland, College Park, MD
3 NOAA/Air Resources Laboratory, Atmospheric Turbulence and Diffusion Division, Oak Ridge, Tennessee
4 Cooperative Institute for Severe and High-Impact Weather Research and Operations, Norman, Oklahoma
5 Oak Ridge Associated Universities, Oak Ridge, Tennessee
6 National Weather Service, Morristown, Tennessee
2023 International MACCS Users Group (IMUG) Meeting
September 11 – 14, 2021 (Virtual)

## Slide 2
2
Developed by NOAA’s Air Resources Laboratory (ARL), a transport and dispersion model for a variety of atmospheric research and emergency response applications.
Trajectories and Dispersion
Forward and Backward
3-D Dispersion (generally > ~1 km):
  “Particles” (i.e., computational points)
  Puffs (top-hat or Gaussian)
  Eulerian grid
Dry and Wet deposition
Chemical and Radiological Transformations
Ways to run HYSPLIT:
  Run online (READY)
  Download – run via Graphical User Interface
  Download – run via command line and scripts
  Windows, Mac, Linux
Users:
  Emergency response & science at NOAA
  Emergency response & science at other agencies
  Scientific community: e.g., Stein et al. 2015 ~ 4600 citations as of September 2023
Lagrangian (plume-based) modeling framework
Stein et al. 2015

## Slide 3
Atmospheric Transport and Dispersion: Overview

## Slide 4
Introduction
4
One of the sources of uncertainty in dispersion modeling is the accuracy of the meteorological input used to drive the model. The observational data may enhance both numerical weather prediction and atmospheric transport and dispersion models.
NOAA’s ARL operates:
Small Uncrewed Aircraft Systems (sUAS) at Oliver Springs Airport (OSI), in Oliver Springs, Tennessee
A meteorological monitoring site on the rooftop of the U.S. Department of Commerce Herbert C. Hoover Building (HCHB) in Washington D.C.
The goal of this study is to assimilate local measurements in WRF to improve meteorological fields that are used to drive HYSPLIT simulations and access its impacts on the transport and mixing of pollutants.

## Slide 5
An sUAS was deployed up to 800 m above ground level at the Oliver Springs Airport, Tennessee to obtain meteorological measurements.
Providing a unique observing system capable for the vertical profiles of meteorological conditions within PBL
Using the data in dispersion modeling may be beneficial for improving plume prediction due to inaccuracies in simulated wind velocities in numerical weather prediction models.
Small Uncrewed Aircraft Systems (sUAS)
5
Picture of the Meteomatics Meteodrone
(https://vlab.noaa.gov/web/suas/home)
sUAS profiles (temperature and wind) were used in HYSPLIT dispersion modeling.
1) Extracting the sUAS profile and writing to HYSPLIT format for the use of dispersion simulations.
2) Using converted drone data (available for a small area) and outer nest datasets (such as HRRR or other NWP products in HYSPLIT format) for driving HYSPLIT.
3) Incorporating sUAS data in WRF simulations through observational nudging. The nudged WRF data can be used to run dispersion simulations.
(Ngan et al., 2023; https://doi.org/10.1175/JAMC-D-22-0182.1)

## Slide 6
Test period – August 20, 2020
Obs nudging successfully adjusted the predicted wind and temperature toward the data taken by the sUAS.
Larger wind speed and more southerly (1100 UTC) components of wind direction were simulated in the nudged WRF run.
In the late-morning hours (1300 UTC), smaller differences between the non-nudged and nudged wind directions than earlier that morning.
Eight sUAS profiles
during 1104 - 1437 UTC
Wind speed and direction profiles at 11 UTC and 1300 UTC

## Slide 7
7
Spatial plots of HYSPLIT runs of continuous pollutant release 2 hours after initiation
HYSPLIT runs use five different meteorological datasets.
Using sUAS signle profile, the model plume hits the boundary of the data domain. No meteorological data beyond the boundary for HYSPLIT to continue the simulation.
The run with sUAS-HRRR pollutants may build up in the area of the inner domain boundary due to the inconsistency of winds between two datasets.
Using sUAS-nudged WRF, the model plume moves westward and then later curved northward when it is further away from the source location.
HYSPLIT simulations
- August 20, 2020
- Starting at 1130 UTC
- Unit emission (g/hr)
- 3 hrs continuous release
- Release height at 10 m
- Conc grid 0.01 x 0.01 deg (~1 km)
and 0-100 m height
- Unit g/m3

## Slide 8
8
Dec 15, eight sUAS profiles, starting 1303 UTC
Dec 16, eight sUAS profiles, starting 1306 UTC
Test period – Dec 15-16, 2021
The automated ingestion of sUAS profiles was added to READY for incorporating the sUAS measurements to generate WRF meteorological fields to drive HYSPLIT simulations in a quasi-operational end-to-end system.
The change of wind direction with height was better simulated in the nudged WRF simulation than in the non-nudged WRF and HRRR.

## Slide 9
Spatial plots of HYSPLIT runs on Dec 15 at 14 UTC (2 hours after initiation)
Non-nudged run had stagnant conditions, causing the plume to stay close to the release location.
The impact of using observational nudging was more noticeable on Dec 15 as a high pressure system was present over the eastern US.

## Slide 10
Spatial plots of HYSPLIT runs on Dec 16 at 14 UTC (2 hours after initiation)
On Dec 16, a relatively strong influence of the synoptic scale winds was present as a result of a cold front approaching. Thus, the influence of sUAS data nudging on the WRF simulation was small.

## Slide 11
As a result of the adjustment of wind and temperature toward the sUAS measurements, other meteorological variables such as vertical velocity, friction velocity, and mixing height are indirectly changed.
Cross section of vertical velocity and horizontal wind barbs

## Slide 12
Profiles of vertical velocity variance from HYSPLIT
Using the nudged WRF meteorological data, HYSPLIT may compute different stability and mixing parameters than the non-nudged data.
On Dec 15, nudged WRF had a larger vertical velocity variance and positive vertical velocity, that resulted in mixing particles more efficiently to higher altitudes.
On Dec 16, weak vertical velocity variance near the surface. Nudged WRF had a stronger vertical velocity variance and a slightly stronger downward vertical velocity, that resulted in keeping the plume under 200 m.

## Slide 13
Tower measurements at HCHB (Washington DC)
The Herbert C. Hoover Building (HCHB) station is located at the central point within the National Capital Region:
standard meteorological data
characteristics of atmospheric turbulence
Two towers – north tower (primary; used in this study)
south tower (secondary)
Location: 38.894 latitude and -77.033 longitude
On the rooftop of the U.S. DOC Herbert C. Hoover Building
Installed in 2003
Building height – approximately 25 m above ground level
Tower height – 10 m
The meteorological variables were measured at high temporal frequency (10 Hz), then reported as 15 min average.
A meteorological tower (north) on the rooftop of the U.S. Department of Commerce Herbert C. Hoover Building (HCHB)

## Slide 14
Time series comparison with HCHB tower measurements
The observational nudging successfully adjusted the wind speed and direction toward the HCHB measurements.
The nudged WRF data had better agreement with the observations than the non-nudged WRF on July 7th.
Relative accurate wind predictions in the non-nudged run were simulated on July 9th.

## Slide 15
Time series comparison with HCHB tower measurements
The nighttime temperature cold bias was corrected in the nudged simulation.
Higher PBL heights were predicted when using the HCHB measurements in the WRF simulation.

## Slide 16
Time series comparison with surface wind measurements at Reagan National Airport (DCA)
Note: DCA is located about 5.5 km south of the HCHB station and it is not included in the nudging simulation.
On July 7th, the surface wind prediction had better agreement with observations at DCA.
A weaker wind speed was simulated, especially the west of HCHB in the nudged case.
3rd model layer
Difference of wind speed
(non-nudged – nudged)
July 7, 2017
06 UTC

## Slide 17
Note: The x-axis corresponds to the A-B line shown on the map and the y-axis is WRF layer height in m AGL.
The black dot indicates the HCHB location and the HYSPLIT plume release location.
Cross-section of temperature and vertical velocity
A higher temperature was simulated near HCHB and lower part of the PBL.
Nudged WRF produced a more significant upward vertical velocity above the HCHB station.

## Slide 18
18
Spatial plots of HYSPLIT runs of continuous pollutant release 2 hours after initiation
Non-nudged plume moved further west and stayed closer to the surface.
Nudged plume moved much slowly due to a weaker wind speed produced by the HCHB data nudging.
Particles were mixed to higher altitudes due to stronger vertical velocity simulated in the nudged WRF.
HYSPLIT simulations
- July 7, 2017
- Starting at 0400 UTC
- Unit emission (g/hr)
- 3 hrs continuous release
- Release height at 10 m
- Conc grid 0.01 x 0.01 deg
and 0-100 m height
- Unit g/m3
Note: Top row is horizontal plots of tracer concentration (g m-3) and bottom row is vertical distribution of particles with color-coded dots for different altitudes (m AGL).

## Slide 19
19
Spatial plots of HYSPLIT runs of continuous pollutant release 2 hours after initiation
Note: Top row is horizontal plots of tracer concentration (g m-3) and bottom row is vertical distribution of particles with color-coded dots for different altitudes (m AGL).
Similar plume movement were simulated by non-nudged and nudged WRF.
Nudged run had a higher concentration and narrower plume due to a weaker wind.
Most particles stayed below 100 m.
HYSPLIT simulations
- July 9, 2017
- Starting at 0400 UTC
- Unit emission (g/hr)
- 3 hrs continuous release
- Release height at 10 m
- Conc grid 0.01 x 0.01 deg
and 0-100 m height
- Unit g/m3

## Slide 20
Summary
Local meteorological observations were utilized in the WRF meteorological model through observational nudging to improve temperature and wind predictions.
The observational nudging of observational data not only adjusts the prediction of state variables, such as mean wind and temperature, but also alters the conditions in the lower part of the PBL that further impact the simulated mixing used in dispersion simulations.
Using a single sUAS profile only provides a small area of data for running HYSPLIT simulation.
Using converted sUAS data with an NWP product may produce artificially high or low concentrations near the data domain boundary due to inconsistencies of winds in two datasets.
Incorporating sUAS profiles into WRF simulations improves wind prediction. The use of nudged WRF data has positive impacts on HYSPLIT modeling.
To enhance the HYSPLIT simulations on READY, we added an automated sUAS data ingestion to the system so that dispersion simulations can be driven by the meteorological data converted directly from the observations or the nudged files with sUAS data.
Observational nudging successfully adjusted the wind speed and direction toward the tower measurements at the HCHB site, especially during nighttime and in the early morning hours. The nighttime temperature cold bias was corrected in the nudged simulation, which resulted in higher PBL height at night.
The non-nudged and nudged meteorological inputs produced significantly different dispersion results. In addition to different patterns of plume movement, simulated particles in the run using nudged WRF are mixed to a higher altitude, while the non-nudged metrological fields kept particles near the surface.
20

## Slide 21: HYSPLIT Recent Updates (selected examples)
STILT dispersion schemes
  (2020) –numerous additional physics options from the HYSPLIT-based Stochastic Time-Inverted Lagrangian Transport Model were incorporated, involving vertical interpolation and Lagrangian time scale, mixed-layer convection and turbulence, and other dispersion algorithms
  (Loughner et al. 2021; doi.org/10.1175/JAMC-D-20-0158.1)
Random numbers – turbulence treatments
  (2019) – Options in turbulent velocity initialization (VINIT)
  (2020) – Options for random number generation (KRAND)
Buoyancy-driven plume-rise algorithms
  Existing: Briggs (based on point source observations)
  (2020) – New for wildfires: Sofiev scheme
  (2023) – New for wildfires: Freitas scheme
Dust emissions
  (2023) – Upcoming: FENGSHA algorithm
Nuclear simulations
  (2016-17) – simulate radionuclide daughter products
Deposition
  (2017) – time interpolation for deposition
Weather balloons trajectory functionality
  (2018) – to forecast weather balloon landing locations
Advection
  (2023) – improved interpolation of trajectories near the poles
  (2023) – improved divergence calculation
New HYSPLIT physics
More functionality for polar concentration grids
  (2018) - Now works with puffs as well as particles
HYSPTEST program
  (2019) - Tests inputs and configs to diagnose common errors
Center-of-Mass Trajectory option
  (2020) - Center-of-Mass trajectories (CMTFN)
Python post-processing graphics programs
  (2020) – including new map backgrounds, zooming features
SVG graphics outputs – as an alternative to postscript
  (2021) – avoids Ghostscript / Ghostview compatibility issues
Density estimation via Gaussian Mixture Models
  (2020) Crawford, A: The Use of Gaussian Mixture Models with Atmospheric Lagrangian Particle Dispersion Models for Density Estimation and Feature Identification. Atmosphere 11:1369. doi:10.3390/atmos11121369
Additional meteorological data conversion programs
  (2017-21) – e.g., ECMWF, ERA5, MERRA, CESM, AER
Higher resolution land cover, roughness length, and terrain datasets
  (2020) – 0.1o and 0.5o datasets added to supplement 1o dataset
Diagnostics
  (2022-2023) – unit-tests added for improved diagnostics
New HYSPLIT features
Notes: Here is a summary of some of the more important updates to the HYSPLIT model since the last Review in 2016, divided between model physics and model features.
I won’t go through all of these, but we will be happy to answer any questions.
A few of the physics highlights that I’d like to mention include:
  Incorporation of range of STILT turbulence, convection, and dispersion schemes into HYSPLIT
  Additional improvements in treatments of turbulence,
  and improvements in the treatment of plume-rise and nuclear phenomena
A few of the new model features that I’d like to mention include:
  A new center-of-mass trajectory option, that calculates a trajectory from a plume that has been transported and dispersed
  New graphics systems and capabilities, based on Python and now SVG graphics
  New meteorological model output conversion programs, to convert these outputs to HYSPLIT input format
  And higher resolution landcover, roughness length and terrain boundary files for the model simulations.

## Slide 22: HYSPLIT-based Emissions Inverse Modeling System (HEIMS)
Fire emissions (HEIMS-f) is designed to assimilate wildfire emissions based on the GOES Aerosol/Smoke Product (GASP) and HYSPLIT dispersion simulations.
(Kim et al. 2020; doi.org/10.5194/acp-20-10259-2020)
Volcanic emissions (HEIMS-v) is developed to estimate volcanic emissions based on aerosol (e.g. MODIS AODs) and/or gaseous properties (e.g. TROPOMI SO2). A case study has been conducted using the Nishinoshima (Japan) volcano eruptions that happened in August 2020.
Nuclear Power Plant (NPP) emissions (HEIMS-n)
Fukushima NPP incident
Comparison between the observed Cs-137 concentrations from SPM (Suspended Particulate Matter) monitors during the incident and the reconstruction of Cs-137 concentrations from HIEMS-n system.
Kori NPP in Korea
Using HIEMS-n to estimate emission from Kori KPP during May 15-16, 2022 and compare the result with PSEUDO observations.

## Slide 23: Gaussian Mixture Model (GMM) with HYSPLIT
The use of GMM with HYSPLIT:
Significantly reduce the number of particles needed in a simulation.
User defined concentration grid no longer needed as input
Output may be stored in a compact format consisting of the mean, weight and covariance matrix of each Guassian.
GMM may be useful in other tasks
(Crawford, 2020; doi:10.3390/atmos11121369)
CAPTEX tracer experiment
The GMM is much less affected by the choice of particle number.
GMM performed as well as simulations using 50,000 or 250,000 particles and original method. Performance did not exhibit much dependence on number of Gaussians, concentration grid, averaging method etc.
2008 Eruption of Kasatochi
Using a smaller number of particles results in spurious higher values in the mass loading due to the shot noise. The density reconstruction with the GMM reproduces the values of the reference run extremely well.
p = 500,000
p = 53,000
p = 26,000
CONTROL
Original Method
GMM (n=50)
Mass loading values too high

## Slide 24: Application – Chemical Accidents
Forecast downwind concentrations of toxic chemical
NWS Weather Forecast Offices (WFO’s) run HYSPLIT on demand (~3500 runs per year).
Sophisticated emissions estimates with NOS OR&R Cameo/Aloha model
NEW: Probabilistic forecasts. Ensembles using high resolution ensemble forecast (HREF) to drive HYSPLIT
Concentrations of three of the members
Contours at one concentration level for all 10 members
Screenshot from a HYSPLIT simulation using 10 members of HREF for hypothetical release. Demonstrating situation in which there is large uncertainty in wind field.
Train derailment in Ohio February 2023

## Slide 25: Thank you
Any questions?