## Slide 1: Revisiting Tritium in Accident Consequence Codes: One Analyst’s Perspectives
Kevin R. O’Kula
Nuclear Safety Consultant
IMUG 2023 – Session 2
12 September 2023

## Slide 2: Outline of Presentation*
Earlier Work in Incorporating Tritium Model in an Accident Consequence Analysis Code
Categories of Tritium ACA Applications
Atmospheric Release of Tritium – Similarities & Differences to General Purpose (non-tritium)
  Modularization Schematic of Release
Key Considerations
Probabilistic: Best Estimate – Acute and Long-Term Phases
  Modularization
  Protocols
Deterministic: Conservative Analyses – Acute Phase
Code Options
Important Prerequisites
Summary and Recommendations
Supporting Bibliography
* This talk represents the views and perspectives of the presenter alone and should not be interpreted as those of any of the presenter’s past/current employers, or other organization in which the presenter participates or has membership.

## Slide 3: Earlier Work in Incorporation of Tritium in ACA Codes
Piet et al. and Brereton (1980s) led modification of CRAC code to develop versions of FUSCRAC
  Primarily fusion design applications
Accounted for coolant, structural, and other activation products from fusion system source term along with tritium
  Fixed tritium deposition velocity
  Food compartment model
Example of application: PSA for SRS reactor
  MACCS 1.5.11 used for fission products and water ingestion H-3
  MACCS accounted for inhalation & skin absorption pathways
  FUSCRAC3 for food pathway tritium
  Metric example: PSA (1992) indicated mean population dose due to 3H < 7% total mean population dose
WASH-1400
(1975)
CRAC
(Sandia, 1975)
FUSCRAC3
(INL,1988)
FUSECRAC
(MIT, 1982)
FUSCRAC2
CRAC2
(Sandia, 1983)

## Slide 4: Emergent Interest & Categories of Tritium Accident Consequence Analysis (ACA) Code Applications
Current: Advanced reactor accident analysis involving fuel, coolant, structure, and other sources of activation products
Deterministic/Conservative:
  Reactor Safety Analysis Reports (SARs) and Nonreactor Documented Safety Analyses (DSAs) for Department of Energy (DOE) facilities
  Design studies and dose evaluation
  Typically examines Acute Phase (~first few days, plume passage) only
Probabilistic/Best Estimate:
  Safety Goal evaluation for tritium facilities
  Probabilistic Safety Assessments (PSA)
  Design studies and dose evaluation
  Typically examines Acute and Long-Term (~ several years) phase
Environmental Impact Statements or Environmental Assessments
  Existing Deterministic and Probabilistic studies

## Slide 5
Accidental tritium release from nuclear installation breach or stack
HTO Uptake by vegetation root system
HTO diffusion and transport into soil layers
Mixing layer height
HTO reemission from soil to the atmosphere
HTO re-emission from vegetation
Plant ingestion
Animal/milk ingestion
Inhalation/Skin absorption
HT/HTO deposition with conversion of HT to HTO in soil
HTO uptake by vegetation from atmosphere
HTO conversion into OBT
Atmospheric transport and dilution
Precipitation
Wet Deposition of HTO
Nuclear Installation
Atmospheric Release of Tritium: Similarities and Differences
Similarities to other radionuclides:
  Source term characteristics
  Atmospheric dispersion
  Time frames of interest (acute & long-term)
Differences:
  Interaction with biosphere
  Subsequent secondary, area sources
Recognize major transfer processes in the biospheric environment (soil, plant and animal) after release
Ref. 3: KfK 4605
( ) Based on Raskob, Description of the New Version 4.0 of the Tritium Model UFOTRI Including User Guide, KfK 5194 (1993)
Notes: HTO (and HT) dry deposition with subsequent conversion of HT to HTO in the soil
HTO uptake from the atmosphere by vegetation
Re-emission of HTO from the soil and vegetation
HTO uptake by the root system of vegetation
HTO diffusion and transport into soil layers; and
HTO conversion into OBT in vegetation; and
Wet deposition of HTO due to precipitation

## Slide 6: Key Considerations for Contemporary Applications
What type of source term does the ACA need to address?
  Tritium water vapor (HTO), Tritium gas (HT), Special Tritium Compounds (STCs), Others
  Fission and/or activation product radionuclides
  Both
Are there region of transport and dose conversion factor (DCF) data available for the tritium species?
  HTO, HT
  OBT
  STCs
  Others
Is the analysis for an Deterministic or Probabilistic application?
What phases of the accident release environment are analyzed and area/zone of interest?
  Acute
  Long-term
  Both
What site-specificity and regional data/characteristics are available?
  Generic
  Site/Regional

## Slide 7: Modularization of Tritium Release: Acute and Late Phases
1. Source Term
2. Dispersion Model and Site Meteorological Data
3. Site Grid and Region of Transport Model
A. Software Quality Assurance and Site V&V
B. Sensitivity & Uncertainty Analysis
10. Late Phase Radiological Consequence
Output
5. Acute Phase Radiological Consequence
Output
4. Inhalation and Skin Absorption Dosimetry Model
9. Ingestion Dosimetry Model
6. Plume/Terrain Interaction: Deposition and Reemission Model
Probabilistic – Acute Phase
Probabilistic – Late Phases
8. Late Phase Countermeasures
3.a Acute Phase Countermeasures
7.Agricultural Model and Regional Data
7.Agricultural Model and Regional Data
Conceptual Schematic of Analysis: Accidental atmospheric release of tritium over acute (left side) + long-term (right-side) phases
Undergirding inputs and assumptions for Probabilistic Application:
  Generic
  Site-Specific
  Combination of both
Supplement with
  A: Satisfactory SQA and V&V and
  B: Capability to perform Sensitivity and Uncertainty Analysis

## Slide 8: Tritium ACA Code Data Requirements
Tritium-specific data preparation presents resource challenges relative to non-tritium source term analysis
Specificities include
  Species
  Site characteristics
  Climate/meteorological
  Regional agriculture practices
  Regional diet
Table (=>) based on Raskob, Description of the New Version 4.0 of the Tritium Model UFOTRI Including User Guide, KfK 5194 (1993)

## Slide 9: Probabilistic Safety Analysis Protocols - 1
Site-Neutral or Generic Protocol
  Acute (Plume Passage): Conservative inputs to maximize consequence metrics; Site-specific meteorology but minimize surface roughness length (zo)
  Long-term Phase: Inputs to maximize food ingestion doses (temperate climate, agricultural productivity and traditional food basket)
Site-/Regional-Specific Protocol
  Acute (Plume Passage): Best estimate inputs for realistic consequence metrics; Site-specific meteorology and zo
  Long-term Phase: Best estimate of food ingestion doses (regional climate, agricultural productivity, and local food basket)
  Sample regions: such as temperate, arid north, arid south

## Slide 10: Probabilistic Safety Analysis Protocols - 2
Standardize input templates for anticipated types of advanced reactor sites
Borrow from DOE STD-3009-2014 (Section 3.2.4.2))
  Generic Site (Option 2)
  Site/Regional-Specific (Option 3)

## Slide 11: Transport, biokinetic and DCF considerations
Deposition and Re-emission/Resuspension
  Well-studied for HTO and HT
  Scarce to no data for other species suggest consideration of experimental studies for dry and wet deposition
Biokinetic behavior
  Organically Bound Tritium (mainly ingestion pathway)*
  Aerosols and particulates (F/M/S)
  ICRP and NRC models
DCF data
  Older: FGR 11 (ICRP 30) and ICRP-68 / -72
  ICRP 119 (Public and Occupational)
  ICRP 134 (Occupational)
  DOE‐STD‐1129‐2015 provides recommendations for special cases
__________________________
* Inhalation/skin absorption can arise from release of tritiated oils

## Slide 12: Tritium dose conversion factor (DCF) example – Public
ICRP 119 3H DCFs
Follows ICRP 60 guidance
Others include ICRP 71 and 72

## Slide 13: Tritium DCFs - Occupational
ICRP 134 3H DCFs
Others include ICRP 68 and ICRP 30

## Slide 14: Conceptual Schematic of Modules for Deterministic ACA Application
Consider acute phase and evaluate dose to maximally exposed individual (MEI)
Food ingestion pathway is omitted
Required modules:
1 through 6, and 1 through 5 for conservative dose estimate
  Eliminate wet and dry deposition
  Maximize high-DCF tritium species in source term (e.g., HTO)
  Treat all 3H species as neutrally-buoyant, inert gas (i.e., no interaction with terrain, vegetation, or soil)
Apply either generic or site-specific inputs and assumptions
1. Source Term
2. Dispersion Model and Site Meteorological Data
3. Site Grid and Region of Transport Model
A. Software Quality Assurance and Site V&V
B. Sensitivity & Uncertainty Analysis
5. Acute Phase Radiological Consequence
Output
4. Inhalation and Skin Absorption Dosimetry Model
6. Plume/Terrain Interaction: Deposition and Reemission Model
Deterministic – Acute Phase

## Slide 15: Computer Code Options – One Analyst’s Opinion
*See Bunz et al. (1997) for an example with UFOTRI and COSYMA for the SEAFP project. See Taylor and Raskob (2007) for an example with UFOTRI and COSYMA for ITER site/region.
Row | Analysis Mode | Mixed (M) Tritium Only (T) | Acute (A) + Long-Term (LT) | Food Pathway | Code Options
1 | Probabilistic | T | A + LT | Yes | UFOTRI 4.0 (or successor)
2 | Probabilistic | M | A + LT | Yes | UFOTRI 4.0 (or successor) MACCS 4.2 (or successor)
3 | Deterministic | T | A + LT | Yes | UFOTRI 4.0 (or successor)
4 | Deterministic | M | A + LT | Yes | UFOTRI 4.0 (or successor)* MACCS 4.2 (or successor)
5 | Deterministic | T | A | No | UFOTRI 4.0 (or successor) MACCS 4.2 (or successor)
6 | Deterministic | M | A | No | MACCS 4.2 (or successor)
Notes: European Safety and Environmental Assessment of Fusion Power (SEAFP)

## Slide 16: SQA and Sensitivity and Uncertainty Analysis
Recommend comprehensive review of tritium ACA code’s quality assurance before application
  Example references: DOE Order 414.1D, ANSI/ASME NQA-1-2008
Address validation and verification of the software
  Deterministic software V&V: IAEA No. SSG-2 (Rev. 1), Deterministic Safety Analysis for Nuclear Power Plants
  BIOMOVs code intercomparison reports
  Individual organization and industry V&V guides
Use code amenable to sensitivity and/or uncertainty analysis (UA)
  Latin Hypercube Sampling example: Dan Galeriu et al., Uncertainty and Sensitivity Analysis for the Environmental Tritium Code UFOTRI,” Fusion Technology, 28, pp. 853-858 (October 1995)
  Goossens, L. H. J. et al. (1998), Probabilistic Accident Consequence Uncertainty Analysis, Uncertainty Assessment for Internal Dosimetry, Vol. 1 & 2
  Brown, J. et al. (1999), “Probabilistic Accident Consequence Uncertainty Analysis, Food Chain Uncertainty Assessment.”
  SOARCA or Level 3 PRA - See NRC ADAMS for documentation
Notes: Goossens, L. H. J. et al., Probabilistic Accident Consequence Uncertainty Analysis, Uncertainty Assessment for Internal Dosimetry, Vol. 1 & 2, NUREG/CR-6571, EUR16773, SAND98-0119, USNRC, Washington, DC, 1998
Brown, J. et al., “Probabilistic Accident Consequence Uncertainty Analysis, Food Chain Uncertainty Assessment,” Vol. 1 & 2, NUREG/CR-6523, EUR 16771, SAND97-0335, USNRC, Washington, DC, 1999

## Slide 17: Summary
Probabilistic analysis documentation: (PRA or risk-informed decision-making applications)
  Best-estimate, consequence estimates for acute + long-term phase of 3H release
  Consider developing generic or regional/site-specific protocols
  Inhalation, skin absorption, and ingestion dose pathways to receptors
Deterministic safety analysis documentation: (SARs and DSAs)
  Conservative consequence estimates for acute phase of 3H release (some applications may not require long-term phase)
  Treat HTO, HT, and other compounds as non-interacting gas
  Maximize consequence-dominant source term
  Inhalation and skin absorption dose pathways to MEI receptor
Base ACA code choice on application and desired level of conservatism

## Slide 18: Recommendations
Expand existing dry and wet deposition experimental data for lesser-known tritium compounds (e.g., tritides, STCs or other 3H compounds) and for new siting regions where existing data are limited.
Establish PRA tritium-specific modeling protocols for generic and site-specific analyses.
Interim measure: Use UFOTRI and MACCS in concert to quantify consequences for tritium and non-tritium radionuclides, respectively, in accident analysis for mixed source term.
Address Software Quality Assurance practices applied to the code of choice before implementation.

## Slide 19: Thank you for your attention! Questions? - Comments?
Kevin O’Kula, Ph.D.
Contact Information
kokula52@gmail.com;
+1.706.726.0488 (m)

## Slide 20: Supporting Bibliography - 1
American Society of Mechanical Engineers (ASME), NQA-1-2008 with the NQA-1a-2009 addenda, Quality Assurance Requirements for Nuclear Facility Applications.
American Society of Mechanical Engineers (ASME)/American Nuclear Society (ANS) Standard ASME/ANS RA-S-1.4-2021, “Probabilistic Risk Assessment Standard for Advanced Non-Light Water Reactor Nuclear Power Plants,” ASME, New York, NY, ANS, La Grange Park, IL, (2021).
Andrews, N.C., Higgins, M., Taconi, A. and Leute, J., Preliminary Radioisotope Screening for Off-site Consequence Assessment of Advanced Non-LWR Systems, Sandia National Laboratories Report, SAND2021-11703, September 2021.
Barry, P.J. Ed., Tech. Report No. 8, BIOMOVS II Steering Committee, Stockholm, Sweden (1997).
Brereton, S.J. and Piet, S.J., “Modifications to FUSCRAC2 in Creating FUSCRAC3,” Idaho National Engineering Laboratory, (1988).
Brereton, S.J., et al., “Offsite Dose Calculations for Hypothetical Fusion Facility,” IAEA Workshop on Fusion Reactor Safety, Jackson, Wyoming, April 1989.
Brown, J. et al., “Probabilistic Accident Consequence Uncertainty Analysis, Food Chain Uncertainty Assessment,” Vol. 1 & 2, NUREG/CR-6523, EUR 16771, SAND97-0335, USNRC, Washington, DC, 1999.
Bunz, H., Forty, C.B.A., Freudenstein, K.F., Raskob, W., and Cook, I., “SEAP Modeling of Accident Sequences, Source Terms, and Public Doses,” Journal of Fusion Energy, 16, (3), pp. 269-276 (1997).
Clavier, K.A., and Clayton, D.J., Reviewing MACCS Capabilities for Assessing Tritium Releases to the Environment, Sandia National Laboratories Report, SAND2022-12016, September 2022.
Galeriu, D., Davis, P., Chouhan, S., and Raskob, W., “Uncertainty and Sensitivity Analysis for the Environmental Tritium Code UFOTRI,” Fusion Technology, 28, pp. 853-858 (October 1995).
Goossens, L. H. J. et al., Probabilistic Accident Consequence Uncertainty Analysis, Uncertainty Assessment for Internal Dosimetry, Vol. 1 & 2, NUREG/CR-6571, EUR16773, SAND98-0119, USNRC, Washington, DC, 1998
Gulden, W., and Raskob, W., “Accidental Tritium Doses Based on Realistic Modelling,” Fourth Topical Meeting on Tritium Technology in Fission, Fusion, and Isotopic Applications. Albuquerque, NM, September 29-October 4, 1991. Fusion Technology, 21, pp. 536-543 (March 1992).
International Atomic Energy Agency (IAEA), IAEA-TECDOC-1738, Transfer of tritium in the environment after accidental releases from nuclear facilities: Report of working group Environmental Modelling for Radiation Safety (EMRAS II) Programme. Vienna, Austria (2014).
International Atomic Energy Agency (IAEA), IAEA No. SSG-2 (Rev. 1), Deterministic Safety Analysis for Nuclear Power Plants, Vienna, Austria (2014).

## Slide 21: Supporting Bibliography - 2
International Commission on Radiological Protection (ICRP). (See Partial Bibliography – 3)
Kim, S.B., Baglan, N., and Davis, P.A., “Current understanding of organically bound tritium(OBT) in the environment,” Journal of Environmental Radioactivity, 126, pp. 83-91 (2013).
O’Kula, K.R., and Thoman, D.C., “Modeling Atmospheric Releases of Tritium from Nuclear Installations,” ANS Embedded Topical Meeting on the Safety and Technology of Nuclear Hydrogen Production, Control and Management, June 24-28, 2007, pp. 189-197 (Boston, MA).
Piet, S.J., et al., “FUSCRAC: Modifications of CRAC for Fusion Applications,” PFC/RR-82-20, M.I.T. Plasma Fusion Center, (June 1982).
Raskob, W., UFOTRI: Program for Assessing the Off-Site Consequences from Accidental Tritium Releases. KfK 4605, Karlsruhe, Germany (July 1990).
Raskob, W., Description of the New Version 4.0 of the Tritium Model UFOTRI Including User Guide. KfK 5194, Karlsruhe, Germany (August 1993).
Raskob, W., 1991. “Modelling of Tritium Behaviour in the Environment,” Fourth Topical Meeting on Tritium Technology in Fission, Fusion, and Isotopic Applications. Albuquerque, NM, September 29-October 4, 1991. Fusion Technology, 21, pp. 636-644 (March 1992).
Taylor, N.P., and Raskob, W., Updated Accident Consequence Analysis for ITER at Cadarache,” Fusion Science and Technology, 52, pp. 359-366 (October 2007).
U.S. Department of Energy (DOE). DOE Order 414.1D, Chg 2 (LtdChg), 9-15-2020.
U.S. Department of Energy. DOE-STD-3009-2014, Preparation of Nonreactor Nuclear Facility Documented Safety Analysis, November 2014.
U.S. Department of Energy. DOE‐STD‐1129‐2015, Tritium Handling and Safe Storage, 2015.
U.S. Nuclear Regulatory Commission Regulatory Guide 1.247 (For Trial Use), Acceptability of Probabilistic Risk Assessment Results for Non-Light-Water Reactor Risk-Informed Activities, (2022).
NUREG-1935, “State-of-the-Art Reactor Consequence Analyses (SOARCA) Report,” U.S. Nuclear Regulatory Commission, Washington, DC, November 2012.
U.S. Code of Federal Regulations, 51 FR 30028, “Safety Goals for the Operation of Nuclear Power Plants,” U.S. Nuclear Regulatory Commission, Washington, DC, August 1986.

## Slide 22: Supporting Bibliography – 3 (ICRP)
ICRP 26, “Recommendations of the International Commission on Radiological Protection,” Annuals of the ICRP, Ann. ICRP 1 (3), International Commission on Radiological Protection (1977).
ICRP 30 Part 1, “Limits for intakes of radionuclides by workers. ICRP Publication 30 (Part 1). Ann. ICRP 2(3/4), (1979).
ICRP 30 Part 2, “Limits for intakes of radionuclides by workers. ICRP Publication 30
(Part 2). Ann. ICRP 4(3/4), (1980).
ICRP 30 Part 3, “Limits for intakes of radionuclides by workers. ICRP Publication 30
(Part 3). Ann. ICRP 6(2/3), (1981).
ICRP 30 Part 4, “Limits for intakes of radionuclides by workers. ICRP Publication 30
(Part 4). Ann. ICRP 19(4), (1988).
ICRP 60, “1990 Recommendations of the International Commission on Radiological Protection,” Annuals of the ICRP, Ann. ICRP 21 (1-3), International Commission on Radiological Protection (1991)
ICRP 68, “Dose Coefficients for Intakes of Radionuclides by Workers,” Annuals of the ICRP, Ann. ICRP 24 (4), International Commission on Radiological Protection (1995).
ICRP 71, “Age-dependent Doses to Members of the Public from Intake of Radionuclides - Part 4 Inhalation Dose Coefficients,” Annuals of the ICRP, International Commission on Radiological Protection (1995)
ICRP 72, “Age-dependent Doses to the Members of the Public from Intake of Radionuclides: Part 5 Compilation of Ingestion and Inhalation Coefficients,” Annuals of the ICRP, Ann. ICRP 26 (1), P 072 errata in SG 03 JAICRP 32(1-2), International Commission on Radiological Protection (1995).
ICRP 103, “The 2007 Recommendations of the International Commission on Radiological Protection,” Annuals of the ICRP, Ann. ICRP 37 (2-4), International Commission on Radiological Protection (2007).
ICRP 119, “Compendium of Dose Coefficients based on ICRP Publication 60,” Annuals of the ICRP, Ann. ICRP 41 Supplement 1, International Commission on Radiological Protection (2012).
International Commission on Radiological Protection (ICRP). Occupational intakes of radionuclides: Part 2. ICRP Publication 134. Ann. ICRP 45(3/4), 1–352, (2016).