## Slide 1: MACCS Conference
Atmospheric Dispersion and Deposition of Radionuclides in the Vicinity of a Nuclear Power Plant in South Africa
September 2023, MS Teams
Mbulelo Dondolo, Iyabo Usman, Henriette van Graan, Adriaan Joubert, Ian Korir

## Slide 2
Contents
Motivation
Methodology
Results and Discussion
Conclusion and Recommendation

## Slide 3: Motivation
The work outlines how the transport and dispersion model of MACCS – the ATMOS module, can be developed in South Africa to performed in the level 3 PRA analysis to analyze the off-site radiological consequences analysis of a potential accident releases of radioactive materials in the vicinity of the NPP.
This will be done to aid the regulator to use MACCS to perform independent verification of the currently employed Level 3 code by the KNPS.

## Slide 4: Problem Description
The responses of the containment due to severe accident were grouped into eight release categories in the KNPS as described in the level 3 PSA report. The different release categories are designated RC-1 through to RC-8.
The release category that was selected for the simulation was RC-3, which is described as follows: “The containment remains unisolated, resulting in a continuous radioactive release into the external environment. Containment spray function is irrelevant in by-pass accidents, but Containment spray is impaired in CI failure accidents resulting in an unfiltered release.”
This scenario was modelled with the aim of developing the MACCS model using KNPS data.

## Slide 5: Scope
The present work focused only on the ATMOS module of MACCS, which is based on estimating atmospheric transport and dispersion capabilities of the off-site consequences of a severe accident in the KNPS resulting in major release of radioactivity to the environment.
Results on other modules of MACCS will be published separately as part of the ongoing project.

## Slide 6: WinMACCS Overview

## Slide 7: ATMOS
The dispersion and deposition of radioactive nuclides in the ATOMS module of MACCS can be performed by combining the following sets of data as shown by the relationship in the figure.
The analysis combines data sets of weather, source term and other specific atmospheric dispersion parameters to complete the calculations.
Scope of the ATMOS module

## Slide 8: Source Term Data
Atmospheric transport modeling for MACCS requires data that define the characteristics of a release, including radionuclide inventory data, plume timing and release fractions, plume release path information, and other plume segment definitions
The source term is the first major input to Level 3 analysis, and it defines the radioactive effluents that are released from a facility, in this case during accident scenarios.
The first step of the source term analysis is to group fission products based on their physical and chemical properties.
The fuel inventory at accident initiation (e.g., reactor scram) of those radioactive nuclides important for the calculation of offsite consequences.
The code also requires several plume segment characteristics that define the release.
These include the atmospheric release fraction, the heat content, the initial release and duration, and the initial release height and initial dispersion for each plume segment.
The code also requires the distribution of aerosol sizes of the released inventory.

## Slide 9: Meteorological Data
Traditionally, Probabilistic Consequence Analysis (PCA) codes require at minimum input data with hourly information on the wind direction, wind speed, stability category, rainfall rate, and mixing layer, for an entire year
To calculate the dispersion and transfer of radioactive isotopes in the environment the meteorological conditions had to be defined.
The Gaussian plume model is generally used in such a way as to allow changes in atmospheric stability, wind speed, wind direction and precipitation for each successive hour of travel time.
Meteorology data is fundamental for the dispersion of pollutants because it is the primary factor determining the diluting effect of the atmosphere. Therefore, it is important that meteorology is carefully considered when modeling the atmospheric transport and dispersion (ATD) of radiation release.

## Slide 10: Dispersion Parameters Data (Gaussian Plume model)
The Gaussian plume equations depend on the wind speed, atmospheric stability class, the effect of surface roughness, release height, and the height of the mixing layer
The Gaussian plume model uses two spatially dependent dispersion parameters, sigma-y and sigma-z, to estimate the atmospheric dispersion. These parameters can be specified in two ways in MACCS: as power-law functions or with lookup tables
The Gaussian plume equations that MACCS is using has the following form:
𝜒(𝑥,𝑦,𝑧) = air concentration (Bq∙s/m3)
𝑄 = activity (Bq) entering the spatial element,
u = wind speed (m/s)
h = height of the plume (m),
𝜎𝑦(𝑥)= horizontal dispersion variable (m),
𝜎𝑧(𝑥)= vertical dispersion parameter (m)
The dispersion parameters σy and σz in the Gaussian plume equations are important values that determine how quickly the plume disperses as it travels downwind.

## Slide 11: Dispersion Parameters Data
Plume Rise
In the Gaussian Plume Model (GPM) formula for the concentration, the effective height for emission is an important parameter for ground level concentrations. Due to the initial kinetic energy of the released plume and its thermal energy when the plume temperature is above ambient air temperature, there will be an increase in the emission height of the plume, this increase is known as the plume rise Δh. The effective source H is then given by:
H = hs + Δh
Gaussian air dispersion
In order to predict ground level concentration of pollutants, the plume rise should be taken into consideration.
Figure shows a simplified representation of a Gaussian Plume model, representing contaminants released from a stack.

## Slide 12: Methodology
Default inputs from the LNT sample input file distributed with the MACCS code were used, with modifications to simulate a simple case with one radionuclide, Cs-137.
The parameters were defined according to MACCS best practices (Theory Manual and User Guide).
The parameters (source term, meteorological data and dispersion parameters) were obtained, calculated, and analysed according to the research objective in the following structure:
  1. Atmos description
  2. Spatial grit
  3. Radionuclides
  4. Deposition
  5. Dispersion
  6. Plume Release Information
  Weather

## Slide 13: Methodology
The data of all these parameters was gathered from the KNPS documentations and was processed and implemented to the MACCS inputs through the WinMACCS interface as follows:
Data Fields
Usage in MACCS
Atmos Description
… has been provided in the problem description statement sub-section
… continuous radioactive release into the external environment
Spatial Grid
the distances provided in the sample were used in the simulation
Radionuclides
The radionuclide inventories were similar to those used in the MACCS LNT
samples.
Deposition Parameters
Both the wet and dry deposition parameters used in the simulations
were those provided in the MACCS sample.
Dispersion Parameters
For this simulations, the MACCS power law option was used to define the
Gaussian dispersion coefficients as functions of the position
Plume Release
Information
The plume delay time, plume hight, as well as the plume duration were
extracted from the collected documentation on Level 3 PRA report
Weather Data
The weather file that was used by KNPS was structured different from the
format required by MACCS specification. To create a weather file that is
readable by MACCS, one had to restructure the notepad weather file using MS
Excel then it was accepted by MACCS.

## Slide 14: Methodology
The concentration of an air pollutant at a given place is a function of a number of variables, including the emission rate, the distance of the receptor from the source and the atmospheric conditions
Table 1: ATMOS Output information (User Guide)

## Slide 15: Results and Discussion
Centerline ground-level 𝜒/Q is the ratio of air concentration (𝜒) to source strength (Q), averaged over the interval’s length (s/m3), not accounting for radioactive decay or deposition (s/m3).
This behaviour can be expected since the radiation is diffusing from a region of high concentration to a region of low concentration.
This is in agreement with previously observed trends, and it also conforms to the corresponding equation

## Slide 16: Results and Discussion
Adjusted source strength of the plume upon entering each radial interval after adjustment for losses in the previous intervals due to radioactive decay and wet and dry deposition (Bq).
When material decays or is deposited onto the ground during transport, the effective source strength for downwind distances is reduced.
This is treated in MACCS through the definition of an adjusted source strength, Qa, which is reduced by deposition and radioactive decay that occur over plume trajectory up to the current location.

## Slide 17: Results and Discussion
The effective crosswind dimensions of a plume segment are increased by lateral variation of the plume about its center-line trajectory.
Vertical expansion of a plume is enhanced by larger values of surface roughness and constrained by the ground and by the temperature structure of the atmosphere (location of inversion layers).

## Slide 18: Comparison with Test Samples
The Center-line Ground-level /Q for the KNPS compared well against the test samples as seen in the figure

## Slide 19: Comparison with Test Samples
Both the plume crosswind dispersion parameters for the KNPS and test sample showed similar trends.
Though results for the two graphs are not completely aligned, but they both increase with increasing distance from the radiation source
The vertical dispersion parameters for the KNPS was consistent with the test sample, with an exponential increase

## Slide 20: Summary
Testing focused on verifying equations and algorithms of the MACCS code, as described in the MACCS Theory Manual.
The main verification strategy adopted in this project was to compare the KNPS against the sample results.
Other similar studies were conducted in this field and they observed similar behaviours of χ/Q and other parameters as observed in this report.
It was verified that MACCS outputs using KNPS data satisfied those relationships predicted in the theory.
It was then observed that the parameters compares well with the sample results for all the parameters, with minor differences.
The assessment in this report was done to test whether the ATMOS module for MACCS was well replicated to aid the use by the regulator for assessment.
This was confirmed by the good agreement of the KNPS plant parameters against the test sample results.

## Slide 21: Conclusions and Recommendations
Concluding Remarks
This study was performed to develop an approach that can be followed to replicate the MACCS code in South Africa to aid the nuclear regulator to perform assessment of a level 3 PRA analysis.
The results obtained were verified against the completed testing sample models that were obtained with the WinMACCS code, and they all compared well with such a model. Therefore, the dispersion model of the KNPS has been developed in WinMACCS, and the results were verified
Recommendation
The weather file from the station at the KNPS has a different formatting, i.e., the columns are arranged in a different order than that of WinMACCS.
It would be of good practice to develop a script that can re-order the columns in the KNPS weather file to align with that of the WinMACCS code and to add some of the outstanding columns. This will maintain the integrity of the weather file.

## Slide 22: References
[1] IAEA, “Safety Assessment for Facilities and Activities, No. GSR Part 4,” Internation Atomic Energy Agency, Vienna, 2016.
[2] D. M. Osborn, “Seamless Level 2/Level 3 Probabilistic Risk Assessment Using Dynamic Event Tree Analysis,” Graduate Program in Nuclear Engineering The Ohio State University, Ohio, 2013.
[3] J. Leute, F. Walton and R. Mitchell, “MACCS (MELCOR Accident Consequence Code System) User Guide – Version 4.0,” Sandia National Laboratories, Albuquerque, New Mexico 87185, 2021.
[4] A. J. Nosek and N. Bixler, “MACCS Theory Manual,” Sandia National Laboratories, Washington, DC, 2021.
[5] A. Nosek, “Theory of Consequence Analysis Using MACCS, Part 1-3,” in MACCS Workshop 2021, US Nuclear Regulatory Commission, 2021.
[6] Y. Combrink, S. Ghoorum and L. Perryman, “The Koeberg Level 3 PSA Study, PSA-R-T16-01 Revision 17,” Eskom, Cape Town, 2015.
[7] A. Caldell, “Addressing Off-site Consequence Criteria Using Level 3 Probabilistic Safety Assessment,” Department of Nuclear Power Safety KTH Royal Institute of Technology , Stockholm, Sweden, 2012.
[8] NEA, “NEA/CSNI/R(2018)1: Status of Practice for Level 3 Probabilistic Safety Assessments,” NUCLEAR ENERGY AGENCY, Issy-les-Moulineaux, 2018.
[9] USNRC, “U.S. NRC Level 3 Probabilistic Risk Assessment (PRA) Project: Volume 3d: Reactor, At-Power, Level 3 PRA for Internal Events and Floods,” United State National Regulatory Commission, Washington, DC, 2022.
[10] IAEA-TECDOC-1914, “Case Study on Assessment of Radiological Environmental Impact from Potential Exposure,” INTERNATIONAL ATOMIC ENERGY AGENCY, VIENNA, 2020.
[11] J. Bluett, N. Gimson, G. Fisher, C. Heydenrych, T. Freeman and J. Godfrey, “Good Practice Guide for Atmospheric Dispersion Modelling,” Air Quality Technical Report 27 , New Zealand , 2004 .
[12] N. Bixler, J. Jones, D. Osborn and S. Weber, “ NUREG/CR-7009: MACCS Best Practices as Applied in the State-of-the-Art Reactor Consequence Analyses (SOARCA) Project,” U.S. Nuclear Regulatory Commission, United States, 2014.
[13] A. Nosek and N. Bixler, “SANDIA REPORT: "MACCS Theory Manual",” Sandia National Laboratories, Washington, DC 20555, 2021.
[14] M. Embaby, A. Mayhoub, K. Essa and S. Etman, “Maximum ground level concentration of air pollutant,” Mathematics and Theoretical Physics Department , Nuclear Research Center, Egypt, 2001.
[15] A. Caldwell, “Addressing Off-site Consequence Criteria Using Level 3 Probabilistic Safety Assessment,” Department of Nuclear Power Safety KTH Royal Institute of Technology, Stockholm, Sweden, 2012.
[16] T. Dinoko, “MODELING OF THE DISPERSION OF RADIONUCLIDES AROUND A Nuclear Power Station,” Department of Physics, University of the Western Cape. , Western Cape. , 2009.
[17] A. Abdel-Rahman, “On the dispersion models and atmospheric dispersion,” Int. J. Global Warming, vol. 3, no. 3, pp. 257-273, 2011.

## Slide 23: Thank you