## Slide 1: Resuspension Factors for Emergency Phase Modeling – Recommended Values and Progress in Field Experiments
2023 International MACCS User Group (IMUG)/MACCS Workshop
Michael D. Kaminski
Strategic Security Sciences, Argonne National Laboratory
Nico Daiyega
Ph.D Student
Department of Physics
University of Illinois
Matthew Magnuson
Center for Environmental Solutions and Emergency Response, Office of Research and Development, U.S. Environmental Protection Agency.

## Slide 2: Motivation
Outdoor plume and dispersion models that
describe particle resuspension lack the
experimental data needed to accurately
estimate the dose hazard for radioactive
contamination that is:
  Freshly deposited (emergency phase),
  Deposited on paved surfaces, and
  Disturbed by vehicle and pedestrian movement (emergency response, emergency phase critical infrastructure mitigation, evacuation)
Opportunity to critically evaluate prior resuspension studies to:
  Summarize data on vehicle and pedestrian movement
  Recommend resuspension factors for specific vehicle and pedestrian movement scenarios to be used in existing models (TURBO FRMAC, RESRAD, QUIC)
  Identify gaps and experimental/theoretical opportunities to improve our understanding of resuspension (improve models)

## Slide 3: Anspaugh et al.
Nuclear detonation studies in desert - Anspaugh (1975) and Maxwell and Anspaugh (2011):
“To avoid the effects of confounding factors, data collection should be taken under calm, isolated conditions. Anthropological mechanical disturbances, including the induced turbulence from the walking of a passer-by, have been known to produce resuspension levels of 10−10 to 10−2 (Langham 1971).”
Marshall (2018) stated that by weighting the long-term data, where there is less spread, the dose estimates will be better until the short-term resuspension phenomena can be further developed.
  resuspension phenomena is likely dominated by processes that move the rad particles into the soil profile as a sink
Anspaugh, L. R., Ji H. Shinn, and Paul L. Phelps. “Resuspension and redistribution of plutonium in soils.” No. UCRL-76419; CONF-740550-5. California Univ., Livermore (USA). Lawrence Livermore Lab., 1975.
AN IMPROVED MODEL FOR PREDICTION OF RESUSPENSION, Reed M. Maxwell* and Lynn R. Anspaugh, Health Phys. 101(6):722–730; 2011
Anspaugh, L. R., Shinn, J. H., & Wilson, D. W. (1974). Evaluation of the resuspension pathway toward protective guidelines for soil contamination with radioactivity (No. UCRL--75250). California Univ..
K(t)=
K(t)=

## Slide 4: Resuspension Factor analysis
Very few studies of resuspension
factors related to vehicles and
fresh contamination on paved
surfaces
  Sehmel (1970’s)
  Nicholson (1989)
  Nicholson & Branson (1989)
Wind tunnel by Loosmore
Emission factors (related to resuspension
factor) published
  Describe resuspension of dust from roadways
  From traffic emission studies
  Used for air quality studies
  Many studies published around the world
Pedestrian traffic
  Fewer studies outdoor and/or pavement or related proxies
  Nearly exclusive to indoor hazards
Diagram of Sehmel’s experimental setup.
Sehmel, G. A. (1973). Particle resuspension from an asphalt road caused by car and truck traffic. Atmospheric Environment (1967), 7(3), 291-309.
Loosmore, G. A. (2003). Evaluation and development of models for resuspension of aerosols at short times after deposition. Atmospheric environment, 37(5), 639-647.

## Slide 5
Fraction of particles resuspended from the road per vehicle pass
Vehicle speed in MPH
Sehmel, G. A. "Particle resuspension from an asphalt road caused by car and truck traffic." Atmospheric Environment (1967) 7.3 (1973): 291-309.
Sehmel Experiments (1972)

## Slide 6
Nicholson Experiments (1989)
Percent Remaining (%)
Percent Remaining (%)
Percent Remaining (%)
Percent Remaining (%)
Nicholson, K. W., et al. "The effects of vehicle activity on particle resuspension." Journal of Aerosol Science 20.8 (1989): 1425-1428.
4.5 µm
15 µm
9.5 µm
20 µm
56 km/h
48 km/h
40 km/h
32 km/h

## Slide 7: Emission Factors (US EPA AP-42 method)
Emission factors
  US EPA measures dust emissions from roadways
  Data developed clean air standards and calculated risk associated with working on contaminated sites
  Produced progressively more sophisticated empirical equations for particulate emission factors, E,
    relate the quantity of pollutants emitted to a unit of activity of the source.
  This provides an estimate of area-wide emissions or emission for a specific facility.
  Emission factors are exhaust and non-exhaust emissions
    Independent of vehicle speed and rely more on the weight of the vehicle, # of vehicles passing, LDV-HDV, climate…
  E values match closely with RESRAD data at m-1
  Preliminary Remediation Goals for Radionuclide Contaminants at Superfund Sites (PRG & SPRG)
*Beddows, David CS, and Roy M. Harrison. "PM10 and PM2. 5 emission factors for non-exhaust particles from road vehicles: Dependence upon vehicle mass and implications for battery electric vehicles." Atmospheric Environment 244 (2021): 117886.
*Timmers, V.R.J.H., Achten, P.A.J., 2016. Non-exhaust PM emissions from electric vehicles, Atmos. Environ., 134, 10-16. Corrigendum to “Non-exhaust PM emissions
from electric vehicles,”. Atmos. Environ. 147, 492.
*Timmers, V.R.G.H., Achten, P.A.G., 2018. Chapter 12 - non-exhaust PM emissions from battery electric vehicles. In: Non-Exhaust Emissions- an Urban Air Quality Problem for Public Health; Impact and Mitigation Measures. Academic Press, pp. 261–287.
E = particulate emission factor (g/VKT)
sL = road surface silt loading (g/m2)
kp = particle size multiplier for particle size range and unit of interest
W = average weight (tons) of the vehicles traveling the road

## Slide 8
Authors | Roadway | Vehicle movement | Particle sizes (μm) | Particle type (density [g/cm3]) | Dust load (g/m2) | Sample area (m2) | frem, fsus, E, Λ | Notes | Reported or calculated Sf [m-1]
Mork [1970] | NR | Vehicle passing through contaminated path for 1 hr. | NR | Plutonium contamination (NR) | NR | NR | 4.5x10-5-to 6.5x10-7 s-1 |  | CBD
Sehmel [1972] | Dry asphalt | Passenger and 0.75 ton truck passing through and alongside contaminated path | 2 µm and 5 µm | Phosphorescent zinc sulfide (4.1) | NR | 93m2 | 4.8x10-5-to 6.7x10-3 | Larger size vehicle and faster speeds increase Sf. | 1x10-3-4x10-3
 |  |  |  |  | NR | 93m2 | 4.8x10-6-to 6.7x10-3 | After a deposition is left on the ground for 4-5 days | 2x10-4 to 2x10-5
 |  |  |  |  | NR | 93m2 | 5.5x10-6-to 2.6x10-5 | Deposits left for up to 30 days | 2x10-6
Nicholson et al. [1989, 1990] | Metalled road | First vehicle pass at 64 km/h | 4.5-20 | ~1 g cm-3 | NR | 0.25m2 | 80-20% remaining | Larger size vehicle and faster speeds increase Sf. | 0.33 to 0.54
 |  | As speed increased from 5mph to 40mph |  |  | NR | 0.25m2 | 90- 30% remaining | Sf is highest after the first pass. Afterward, frem drops significantly from 10% to 60%. After 4 passes frem cannot be determined within the large uncertainties Vehicles were driven over the particles up to 12 times. | 2×10-4 to 1×10-2
Rock-salt resuspension [1990] | Urban roads | Rock-salt particles, Na+, and Cl- | NR | Rock-salt particles | NR | NR | Given in resuspension factor | Sf based on the application of rock-salt. Does not account for salt removed from road. | 1x10-7 to 4x10-7
Beddows and Harrison [2021] | Urban roads | Gasoline, diesel, and battery operated vehicles included | PM10 | Road dust (NR) | 0.0003-to 0.0082 | NR | 3.4x10-7-to 6.4x10-6 | Using AP-42 method. | 3.7x10-7
 |  |  | PM2.5 | Road dust (NR) | 0.0003-to 0.0082 | NR | 2.3x10-7-to 4.5x10-6 | Using AP-42 method. | 1.5x10-6
Timmers and Achten [ref] | Urban roads | Gasoline, diesel, and battery operated vehicles included | PM10 | Road dust (NR) | 0.0003-to 0.0082 | NR | 4.2x10-7-to 5.2x10-7 | Using AP-42 method. | 4.2x10-7
 |  |  | PM2.5 | Road dust (NR) | 0.0003-to 0.0082 | NR | 1.0x10-6-to 1.3x10-6 | Using AP-42 method. | 1x10-6

## Slide 9: Pedestrian Resuspension Rates
1 brief! study outdoors
4 studies on radioactive particles
1 study from Fukushima
Indoor air quality studies prevail
Argonne Below-Ground-Model
*Hession, H., Byrne, M., Cleary, S., Andersson, K. G., and Roed, J. (2006). Measurement of contaminant removal from skin using a portable fluorescence scanning system. Journal of Environmental Radioactivity, 85, 196-204.
*Liljegren, J. C., and D. F. Brown. Argonne Below Ground Model Part II: Population Dynamics, Exposure, and Fomite Transport. No. ANL/DIS-14/13. Argonne National Lab.(ANL), Argonne, IL (United States), 2014.
*McDonagh, A., and Byrne, M. A. (2014b). The influence of human physical activity and contaminated clothing type on particle resuspension. Journal of Environmental Radioactivity, 127, 119-126.

## Slide 10
Authors | Flooring | Disturbance | Particle sizes (μm) | Particle type (density [g/cm3]) | Dust load (g/m2) | Sample area (m2) | Resuspension fraction or rate | Chamber/ sampling air volume (m3) | Reported or calculate Sf (m-1)
Brunskill [1964] | Granolithic concrete in a laboratory changing room | Multiple workers moving about the room | NR | NR: Alpha activity | 0.2-0.5 dpm/cm2 | 20.5x11.5 ft | - | 20.5x11.5x10 ft | 3x10-3-10-4
Glauberman et al. [1964] | Painted concrete | Person moving dolly with oscillating fans on | NR | NR: alpha activity in plutonium facility | 5-50 kdpm per 100cm2 | 160 ft2 | - | 160x16 ft3 | 4x10-3-1.5x10-2
Glauberman et al. [1964] | Concrete | Person moving dolly with oscillating fans on | NR | NR: alpha activity in uranium facility | 5-50 kdpm per 100cm2 | 160 ft2 | - | 160x50 ft3 | 1.9x10-4-4.6x10-4
Jones and Pond [1964] | Linoleum and PVC flooring | Persons walking up to 200 steps/min | 90% of particles <10 μm | Plutonium nitrate or oxide (NR) | 6.5-18 μCi/m2 | 15.7 | - | 15.7 x 3.15 m3 | 2x10-5-10-4
Glen [2020] | Concrete pavers in experimental room | Four persons marching for <2 min | 10 | CeO2 (7.65) |  | 18x18 inch | - | 103 (@5 L/min) | 1.6x10-6 (@ 1 day); 6x10-6 @8 days
Glen [2020] | Pond liner in experimental room | Four persons marching for <2 min | 1 | CeO2 (7.65) |  | 18x18 inch | - | 103 (@5 L/min) | 3.4x10-4 @ 16h
Buttner [2020] | Vinyl tile in experimental room | Walking for 1 min | 1.8–3.5 | P. chrysogenum spores (~1) | 106 CFU/m2 | 16 | 0.00004 | 35.2 (sampled each minute) | 1.8x10-5
Karlsson [1996] | Unspecified flooring in experimental room | 1 person working at a large table for 1-h | 6x4 | Pollen (1) | 2.6x107 /m2 | 8.75 | 2x105/m3 |  | 7.7x10-3
Hambreaaus [1978] | Vinyl floor in hospital | 4 persons walking for 30 min |  | Staphylococcus aureus (1) | 3.4x104 CFU/m2 | 35 | 89.2 CFU/m3 | H=3.2m | 3.5 x10-3 (mean of 7-10 trials)
Shaughnessy | Vinyl tile in school and experimental room chamber | 10 min of walking (~105 steps/min) with the ceiling fans set on low | 0.8-1.5 | School dust | 18 | 3.721 | 9.5x10-3 min-1 | 7.92 (for 10 min) | 4.5x10-2
Lai [2017] | Tile in experimental room | One person “40 steps/minute for 1.5 min” | 0.9-9 | Ultrafine test dust | 8 |  | 6x10-4 (0.9 μm); 6x10-2 (9 μm) | 0.125 | 1.2x10-3 (0.9 μm); 1.2x10-1 (9 μm)

## Slide 11: Recommended resuspension factors Sf for specific conditions for vehicle and pedestrian traffic. “Fresh” refers to contamination that has not experienced any prior pedestrian or vehicle disturbance
Condition # | Disturbance type | Condition for Use | Recommended Resuspension Factor (m-1) | Mean value (m-1) | Associated time t (d) and multiplication factor M for Eqn. 15
1 | Vehicle | Fresh contamination from 0-4 days | 2.7x10-3-4.5x10-3 | 3.2x10-3 | t=1, M=110-430
2 | Vehicle | After many vehicle passes* | 1x10-4-4x10-4 | 3.2x10-4 | t=1, M=11-43
3 | Vehicle | Fresh contamination 4-30 days† | 2x10-5-2x10-4 | 9.8x10-5 | t=4, M=2.6-26
4 | Vehicle | Fresh contamination >30 days | 1x10-7-1x10-6 | 5x10-7 | t>30, M=1
5 | Pedestrian | Fresh contamination (no time limit) with continuous human activity | 5x10-4 | NA | t=1, M=50
* Applies a factor of 10-1 to condition #1 data, as explained in text.
†For lack of data, we recommend these values from days 4-30.

## Slide 12: Stay times calculated by RESRAD-RDD for 137Cs (left panel) and 241Am (right panel) contamination and its sensitivity to the resuspension factor
Highest maximum dose for an emergency

## Slide 13: Stay times calculated by RESRAD-RDD for 137Cs (left panel) and 241Am (right panel) contamination and its sensitivity to the resuspension factor
Occupational dose limits

## Slide 14: Stay times calculated by RESRAD-RDD for 137Cs (left panel) and 241Am (right panel) contamination and its sensitivity to the resuspension factor
Maximum dose to the public

## Slide 15: Next steps
Critical review paper in review at Health Physics on resuspension factors and rates induced by vehicle and pedestrian traffic
  Analyzed literature sources
  Summarize, recommend, and justify best values for specific scenarios
  Identify uncertainties and gaps
Laboratory and field experiments
  Sensor benchmarking
  Laboratory and field scale experimental design
  Field scale experiments

## Slide 16: Acknowledgments
The U.S. Environmental Protection Agency, through its Office of Research and Development, partially funded and collaborated in the research described here under Interagency Agreement 92380201 with Argonne National Laboratory. The research in this presentation was partially funded by the U.S. Department of Homeland Security (DHS) Science and Technology Directorate (S&T) under an interagency agreement with the U.S EPA under IAA 70RSAT21KPM00048. Any opinions contained herein are those of the author and do not necessarily reflect those of DHS S&T. This document was reviewed in accordance with EPA policy prior to publication. Note that approval for publication does not signify that the contents necessarily reflect the views of the Agency. Mention of trade names or commercial products does not constitute endorsement or recommendation for use of a specific product.
The submitted presentation has been created by UChicago Argonne, LLC, Operator of Argonne National Laboratory (“Argonne”). Argonne, a U.S. Department of Energy Office of Science laboratory, is operated under Contract No. DE-AC02-06CH11357. The U.S. Government retains for itself, and others acting on its behalf, a paid-up nonexclusive, irrevocable worldwide license in said article to reproduce, prepare derivative works, distribute copies to the public, and perform publicly and display publicly, by or on behalf of the Government.
All images courtesy of Shutterstock or personal archives unless stated otherwise.