## Slide 1: RASCAL Radiological Assessment System for Consequence Analysis
Jeff Kowalczik, CHP
Emergency Response Coordinator
Office of Nuclear Security & Incident Response
US Nuclear Regulatory Commission

## Slide 2: USNRC Incident Response Program
Established after TMI
Mission Areas
  Oversight of licensee actions and recommendations
  Support State/Local government with technical information
  Support larger Federal response efforts

## Slide 3: Radiological System for Consequence AnaLysis (RASCAL)
Used by NRC Incident Response Program
  Independent dose and consequence projections during radiological incidents and emergencies
Fast-running code that estimates doses for potential or ongoing releases from:
  nuclear power plants (light-water reactors),
  spent fuel storage pools and casks,
  fuel cycle facilities, and
  radioactive material handling facilities
Also estimates deposition, field measurements, and intermediate phase doses

## Slide 4: RASCAL / MACCS
 | MACCS | RASCAL
Inputs | Hundreds | <20
Input time | Hours to Days | <10 min
Run time | Minutes to Days | <5 min
Source Term | External Input | Included (Simplistic)
ATD Models | Y | Y
Weather | Sampled Historic Obs | Live Weather
Dose Calculations | Y | Y
Protective Actions | Credited | Not Credited
Health Effects | Y | N
Economic Effects | Y | N

## Slide 5: How RASCAL works
RASCAL creates an atmospheric source term, processes weather data, and calculates doses
Wind
Generation of Source Material
Plume
Dose/Concentration
Atmospheric Source Term

## Slide 6: RASCAL Defines Atmospheric Source Term
Models or measurements determine radionuclides available for release
  Unit-specific data for NPPs, spent fuel, and fuel facilities
  Models/measurements based on accident scenario studies
Source material may be filtered, reduced, or decayed
  Filtering and release height; NPP unit-specific pathways
Wind
Generation of Source Material
Plume
Dose/Concentration
Atmospheric Source Term

## Slide 7: Source Term
Source term models calculate material that can be released
Pick the best model; may have multiple options
Available choices depend on Event Type
Nuclear Power Plant
Spent Fuel
Fuel Cycle
Other Materials
Notes: Here is where we select which model RASCAL will use to calculate how much material can be released
We will need to pick the best model based on the information we have, and there may be multiple options
Remember we told you that these models depend on which event type was selected

## Slide 8: Nuclear Power Plant
RASCAL has 9 nuclear power plant source term options:
4 based on reactor condition models
5 based on nuclide measurements

## Slide 9: Spent Fuel
For Spent Fuel, RASCAL has 3 source term options
Includes both pool and dry storage
Sites are collocated with NPPs

## Slide 10: Fuel Cycle
RASCAL can model certain events from fuel fabrication facilities
UF6 release – special plume model with chemical HF hazard
Criticality – plume model for activation but includes prompt shine

## Slide 11: Other Materials Locations
RASCAL also has 3 “other” materials options
Useful for modeling transportation accidents, lab accidents, etc.
All models still focus on atmospheric releases
  Liquid releases (like spills and leaks) are not modeled in RASCAL

## Slide 12: Source Term Details
Each model requires additional details like timing or measurements
For example, in the LOCA model:
  Time of reactor shutdown
    Starts the decay of all nuclides in the core (they’re in equilibrium before)
  Time core was uncovered
    When NUREG-1465 models start, starting with 30 min of gap activity, then fuel melt
  Is the core recovered?
    Additional material stops being generated after the core becomes recovered
Notes: Rx SD @ 10
Uncover @ 13
Recover at 17

## Slide 13: Release Pathway
RASCAL needs information on how generated material is released to the atmosphere
  Pathway
  Height
    Wind speeds change with height
  Reduction
    Amount of material reduced by decay, holdup, filter, sprays
  Timing
    Release rates, start and stop
Notes: Describe how each

## Slide 14: Release Pathway Details
Release Height
  10m is minimum height allowed (ground release)
Select leak rate type
  Percent Volume / Time (e.g., 3%/hour)
  Containment pressure / Hole Size (e.g., 30 psi/2 cm2)
Define release timeline
  Used for leak rate and additional conditions
  Need to review/set initial conditions, then can add rows as needed
Notes: Explain the event table at the bottom
Add row
Event type dropdown
Event setting choices – may see additional screen to make selection

## Slide 15: RASCAL Defines Atmospheric Source Term
Atmospheric Source Term
  May be single nuclide or complex core damage
  Isotopic activity over time (15 min)
Wind
Generation of Source Material
Plume
Dose/Concentration
Atmospheric Source Term

## Slide 16: Atmospheric Source Term is Moved using ATD Models
Atmospheric Transport and Dispersion Models
  Transport material based on weather conditions
  Track material to where it falls/washes on ground
  Accounts for dry/wet processes and particle size
Wind
Generation of Source Material
Plume
Dose/Concentration
Atmospheric Source Term

## Slide 17: A straight-line Gaussian plume model on a polar grid is used to model distances close to the release point

## Slide 18: A puff model on a Cartesian grid is used to model at longer distances

## Slide 19: A sequence of discrete puffs is used to model the plume
Puff centers move with the wind.
Puffs grow larger as time passes.
Each puff represents 15 minutes of release.

## Slide 20: Final Calculations Provide Doses and Concentrations
Dose calculation accounts for multiple pathways
  External (Groundshine + cloudshine)
  Internal (Inhalation + ingestion)
Results includes other display/calculation options
Wind
Generation of Source Material
Plume
Dose/Concentration
Atmospheric Source Term
Notes: Tee up the walkthrough

## Slide 21: RASCAL Outputs

## Slide 22: Questions?

## Slide 23: Response Roles
Licensee/Operator
  Maintain safe operations of the facility in accordance with emergency plans
  Includes event classifications, notifications, dose assessment, and recommendations
State/Local government
  Make Protective Action Decisions (PADs)
  Protect public through public information, warning, evacuations/sheltering, etc.