## Slide 1: MACCS Consequence Analysis Demonstration Calculations
International MACCS User Group
September 2023
AJ Nosek, PhD
Reactor Systems Engineer
Accident Analysis Branch, Office of Nuclear Regulatory Research
U.S. Nuclear Regulatory Commission
Notes: MACCS is commonly used to analyze LWR designs. It is not nearly as often used to model non-LWR designs, but it can.

## Slide 2: Purpose
The purpose of this project was to:
  Assess the capabilities of the MACCS code to analyze a selected conceptual advanced reactor design under a postulated accident scenario.
  Identify potential gaps that may exist in conducting such an analysis, both technical and practical.
  Exercise new models (e.g., nearfield models) and new settings (i.e., inventory and source term) in the MACCS code for the selected advanced reactor design.
The project continued similar code readiness work using SCALE and MELCOR:
  Oak Ridge National Lab (ORNL) developed a SCALE model to compute the radionuclide core inventory of the Idaho National Lab (INL) Design A conceptual reactor design.
  Sandia National Labs (SNL) developed a MELCOR model to simulate postulated accidents of the INL Design A conceptual reactor design.

## Slide 3: Project Approach
All MACCS analyses used the following inputs:
  An example inventory from a demonstration SCALE model (ORNL/TM 2021/2021)
  An example source term and reactor building dimensions from a MELCOR demonstration model (SAND2022-2745)
  Weather and regional characteristics from an existing (Sequoyah Nuclear Plant) site
  Other general settings defined in the MACCS parameter guidance report (NUREG/CR-7270)

## Slide 4: Project Approach
The main analysis used the following settings:
  A radionuclide list for consequence analysis from SAND2022-12018 based on example inventory from the demonstration SCALE model
  The Regulatory Guide 1.145 full model for nearfield transport
Sensitivity analyses evaluated the following characteristics:
  Radionuclide lists for consequence analysis
  Dose exposure periods
  Nearfield models
  Release timings
Notes: since advanced reactors have unique characteristics that can affect the isotopic makeup of the reactor cores and releases, it may be important to reconsider the radionuclides included in advanced reactor consequence analysis.

## Slide 5: Project Approach
The project used MACCS v4.1.
All reported doses are projected doses in the ambient environment.
The MACCS calculations sample from a range of weather conditions as input. The mean, 5th quantile, and 95th quantile MACCS outputs represent the distribution of results due to weather uncertainty.

## Slide 6: Example Accident Scenario Description
To demonstrate code capabilities, the MELCOR team selected accident conditions for the MELCOR INL Design A model.
This effort produced an example accident progression and source term for a transient overpower (TOP) accident scenario.
The MACCS calculations use the example atmospheric release from the MELCOR demonstration project as input
The MACCS demonstration calculations do not reflect realistic radiological consequences outside of the conditions assumed in the MELCOR analysis.
INL Design A reactor vessel cross-section (from figure 3-1 of SAND2022-2745)

## Slide 7: Source Term*
Two release pathways from building at 5.15 m and 9.15 m (16.9 ft and 64 ft).
Release begins in less than 1 hour.
Relatively small amount of release before MELCOR cutoff time of 24 hours.
Project divided plume into 28, 1-hour segments.
*Note: Consequence results are shown to illustrate code capabilities only. Actual consequences would be based on design, site, and scenario-specific factors.

## Slide 8: Example of Main Analysis Results*
*Note: Consequence results are shown to illustrate code capabilities only. Actual consequences would be based on design, site, and scenario-specific factors.
Distance
Dose
Conceptual Regulatory Criteria
Notes: MACCS is capable of producing dose vs distance calculations. This can help inform decisions about EPZ sizing for new and advanced reactors.
Since the weather at the time of an accident is not predictable, MACCS supports various sampling options to run a representative set of simulations to evaluate weather variability.

## Slide 9: Sensitivity Analysis of Radionuclides
Co-58 | Y-90 | Ru-103 | Te-132 | Ba-137m | Nd-147
Co-60 | Y-91m | Ru-105 | I-131 | Ba-139 | Np-239
Kr-85 | Y-91 | Ru-106 | I-132 | Ba-140 | Pu-238
Kr-85m | Y-92 | Rh-103m | I-133 | La-140 | Pu-239
Kr-87 | Y-93 | Rh-105 | I-134 | La-141 | Pu-240
Kr-88 | Zr-95 | Rh-106 | I-135 | La-142 | Pu-241
Rb-86 | Zr-97 | Te-127 | Xe-133 | Ce-141 | Am-241
Rb-88 | Nb-95 | Te-127m | Xe-135 | Ce-143 | Cm-242
Sr-89 | Nb-97 | Te-129 | Xe-135m | Ce-144 | Cm-244
Sr-90 | Nb-97m | Te-129m | Cs-134 | Pr-143 | Sb-127
Sr-91 | Mo-99 | Te-131 | Cs-136 | Pr-144 | Sb-129
Sr-92 | Tc-99m | Te-131m | Cs-137 | Pr-144m | 
MACCS guidance recommends using a subset of radionuclides from the LWR core for analysis
Ag-111 | Ge-77 | Pm-149 | Sn-121
As-77 | Nb-95m | Pm-151 | Sn-123
Cd-115 | Nd-149 | Pr-145 | Sn-125
Cd-115m | Pd-109 | Sb-125 | Sn-127
Eu-154 | Pm-147 | Sm-151 | Te-125m
Eu-155 | Pm-148 | Sm-153 | U-234
Eu-156 | Pm-148m | Sm-156 | U-237
In-115m | In-115 | Th-230 | Ra-226 | Rn-222
Recommended Radionuclide List for LWR Applications (from NUREG/CR‑7270, Table 2-2)
Additional Radionuclides from draft
SAND2022-12018, Table 4-2
Additional Daughter Radionuclides
That list was expanded to include additional radionuclides from the conceptual HPR core

## Slide 10: Sensitivity Analysis of Radionuclides*
A sensitivity using the updated radionuclide list shows little change in the results.
The ratio of the peak doses from the new radionuclide list compared to the LWR list shows minimal increase in consequence.
Note: this did not evaluate radionuclides important to ingestion consequences, which is based on a separate list
*Note: Consequence results are shown to illustrate code capabilities only. Actual consequences would be based on design, site, and scenario-specific factors.

## Slide 11: Sensitivity Analysis of Dose Exposure Period*
The analyzed exposure periods begin at the start of the accident. Release begins quickly at less than 1 hour.
Longer exposure periods cause greater doses.
At 2 hours, only a fraction of the release has occurred, and no plume segments have travelled beyond 5 km (3.1 mi).
*Note: Consequence results are shown to illustrate code capabilities only. Actual consequences would be based on design, site, and scenario-specific factors.
Notes: this slide shows the capability of MACCS to model the effect of time-dependent releases. MACCS can address the effect of reactor designs with a higher likelihood of delayed and/or prolonged releases.

## Slide 12: Sensitivity Analysis of Dose Exposure Period*
Exposures during plume passage and exposures to short lived radionuclides occur only in the early phase of the accident.
Nevertheless, exposure to ground contamination over the long term is the dominant contributor to the overall lifetime dose projection
*Note: Consequence results are shown to illustrate code capabilities only. Actual consequences would be based on design, site, and scenario-specific factors.

## Slide 13: Sensitivity Analysis of Nearfield Modeling
Using the weather conditions of the Sequoyah Nuclear Plant, the project compared the following three MACCS nearfield modeling approaches:
  (1) Regulatory Guide (RG) 1.145 Partial Model (with Area Source)
  (2) RG 1.145 Full Model (with Point Source)
  (3) Ramsdell and Fosmire Model (with Point Source)
Both options 1 and 2 are based on the nearfield modeling approach described in RG 1.145.
  Option 1 is a partial implementation of RG 1.145. This model does not directly account for building wake. Instead, the project uses an area source based on the building size to model the building wake zone.
  Option 2 is a full implementation of RG 1.145. This modeling approach considers the effects of both building wake mixing and ambient plume meander.
Option 3 is based on the Ramsdell and Fosmire nearfield modeling approach used by ARCON96. (SAND2021-6924)
Options 2 and 3 are new models available in MACCS version 4.1

## Slide 14: Sensitivity Analysis of Nearfield Modeling*
The amount of plume spread in the different models notably impacts doses in the first 40 km (25 mi).
Because the Ramsdell and Fosmire Model has the most spread, it has the lowest peak doses of the three nearfield models.
The two RG 1.145 models have similar peak doses after roughly 1 km (0.62 mi), whereas the Ramsdell and Fosmire Model does not have the same peak doses until approximately 40 km (25 mi).
*Note: Consequence results are shown to illustrate code capabilities only. Actual consequences would be based on design and site-specific factors.

## Slide 15: Sensitivity Analysis of Nearfield Modeling*
There are 64 compass directions in the analysis. Direction 1 represents north, and ascending numbers represent a clockwise direction.
The double peak results are due to the meteorological conditions at the Sequoyah Nuclear Plant site, which has two dominant wind directions.
The RG 1.145 Full Model has the narrowest plume, and therefore it has the highest doses in the dominant wind directions.
The Ramsdell and Fosmire Model has more horizontal plume spread, creating a more uniform dose.
The Ramsdell and Fosmire Model shows a lower dose in all directions, likely because of vertical plume spread.
*Note: Consequence results are shown to illustrate code capabilities only. Actual consequences would be based on design, site, and scenario-specific factors.

## Slide 16: Sensitivity Analysis of Release Timing
MACCS assumes that reactor shutdown occurs at the beginning of an accident scenario. MACCS begins calculating decay and ingrowth at this time.
The TOP scenario is different in that shutdown does not immediately occur.
The reactor is postulated to operate for roughly an hour when the reactor power level steadily increases. This presents a few issues in computing offsite consequences:
  Since reactor shutdown does not immediately occur, the holdup time between reactor shutdown and the start of release is shorter than MACCS anticipates.
  The calculation of the core inventory assumes steady-state operation. If the reactor power level changes, it may not fully represent the new composition from the shift in fission rate before shutdown.
  Release can begin before reactor shutdown. MACCS is designed only to calculate decay and ingrowth from a core inventory given at a fixed time. It does not model production of fission and activation products during release.

## Slide 17: Sensitivity Analysis of Release Timing
A shift in the release timing impacts the dose. This sensitivity evaluates the dose over a 7-day exposure period.
The TOP release has a start time of 0.94 hours; a shift of -0.94 hours represents an immediate release.
Despite a shift by up to 4 days, the projected dose remained within about 6 percent.
Nearly half of this range (3 percent) can be attributed to a change in release timing of just 3 hours (i.e., from -0.94 to 2 hours).
Note: Consequence results are shown to illustrate code capabilities only. Actual consequences would be based on design and site-specific factors.

## Slide 18: Summary Results
The MELCOR analysis selected accident conditions during a TOP accident scenario that produced an example source term of the INL Design A conceptual design.
The sensitivity analysis of the nearfield models using the weather conditions of the Sequoyah Nuclear Plant site shows the following:
  The RG 1.145 Full Model has the highest peak dose.
  The Ramsdell and Fosmire Model has the most plume spread.
  The two RG 1.145 Models align quickly after 1 km.
  The Ramsdell and Fosmire Model may not align the RG 1.145 Models until 40 km (25 mi).
The other sensitivity analyses show the following:
  Exposure to ground contamination over the long term is the dominant contributor to the overall lifetime dose projection in this example.
  The use of an expanded subset of radionuclides in this example consequence analysis showed only a minimal increase in consequence.
  A shift in the release timing for this example source term has a small impact on the projected peak dose.

## Slide 19: Conclusions
The results of our evaluation confirm that, despite some limitations, analysts can use the flexibility of the MACCS code to analyze the offsite consequences of an advanced reactor design under a postulated accident scenario.
The evaluation exercise provided valuable practical experience in implementing new ORIGEN inventories and MELCOR source terms in MACCS.
As new source terms of new and advanced reactor designs become available, RES staff may assess whether further enhancements to the MACCS code are needed.
The project has identified several candidate future research activities:
  continue to demonstrate MACCS capabilities using as input the core radionuclide inventory and atmospheric release from the example SCALE and MELCOR demonstration calculations,
  continue the evaluation of radionuclides in non-LWR inventories important to dose and expanding these evaluations to include ingestion doses,
  develop a method to analyze or conservatively bound accidents with simultaneous release and fission, and
  develop methods to analyze or conservatively bound the impact of additional radionuclide chemical and physical forms and how they may transform in the environment.

## Slide 20: Questions?
A. Nosek, “MACCS Consequence Analysis Demonstration Calculations for an Example Heat Pipe Reactor Source Term,” U.S. Nuclear Regulatory Commission, March 2023, Agencywide Documents Access and Management System Accession No. ML23045A044
E. Walker, S.E. Skutnik, W.A. Wieselquist, A. Shaw, and F. Bostelmann, “SCALE Modeling of the Fast-Spectrum Heat Pipe Reactor,” ORNL/TM-2021/2021, Oak Ridge National Laboratory, Oak Ridge, Tennessee, 2021, ML22158A054.
K. Wagner, C. Faucett, R. Schmidt, and D. Luxat, “MELCOR Accident Progression and Source Term Demonstration Calculations for a Heat Pipe Reactor,” SAND2022-2745, Sandia National Laboratories, Albuquerque, New Mexico, March 2022, ML22144A188.
K.A. Clavier, D.J. Clayton, and C. Faucett, “Quantitative Assessment for Advanced Reactor Radioisotope Screening Utilizing a Heat Pipe Reactor Inventory,” SAND2022-12018, Sandia National Laboratories, Albuquerque, New Mexico, September 2022, ML22270A046.
Sandia National Laboratories, “Technical Bases for Consequence Analysis Using MACCS (MELCOR Accident Consequence Code System),” NUREG/CR-7270, U.S. Nuclear Regulatory Commission, Washington, DC, October 2022, ML22294A091.
D.J. Clayton, “Implementation of Additional Models into the MACCS Code for Nearfield Consequence Analysis,” SAND2021-6924, Sandia National Laboratories, Albuquerque, New Mexico, June 2021, ML21257A120.