## Slide 1: Independent Verification of MACCS Algorithms for Evacuation
Osvaldo Pensado
opensado@swri.org
Center for Nuclear Waste Regulatory Analyses (CNWRA®)
Southwest Research Institute® (SwRI®)
Keith Compton, Salman Haq, AJ Nosek
US Nuclear Regulatory Commission (NRC)

## Slide 2: Acknowledgments
Project sponsored by the US Nuclear Regulatory Commission (NRC)
  Office of Nuclear Regulatory Research
  Division of Systems Analysis
  Accident Analysis Branch
This presentation describes work performed by the Southwest Research Institute (SwRI®) for the NRC under Contract No. 31310018D0002
This project is an independent product of the SwRI and it does not necessarily reflect the views of the NRC. The NRC staff views expressed herein are preliminary as part of an ongoing MACCS testing project

## Slide 3: Testing approach and focus
Testing independent from software developers
Examination of extreme and limiting cases with closed form solutions
Simple systems: one plume segment, constant windspeed, one cohort, no decay chains, one long-lived isotope, uniform population density
MACCS Verification Report ML22026A461 is being updated
  Multiple tests were updated with MACCS Version 4.2
  MACCS Version 4.2 addressed issues identified in previous testing
The discussion on this presentation is focused on evacuation algorithms
Notes: MACCS Verification Report
ADAMS Accession Number ML22026A461
https://www.nrc.gov/docs/ML2202/ML22026A461.pdf

## Slide 4: MACCS treats the cohort as a point
Sector j
Sector j + 1
Sector j − 1
Sector j
Sector j + 1
Sector j − 1
People uniformly distributed in sector
Cohort is simplified in MACCS as a point

## Slide 5: Evacuation on plume arrival and on an alarm
Sector j
Sector j + 1
Sector j − 1
Sector j
Sector j + 1
Sector j − 1
This Photo by Unknown Author is licensed under CC BY-NC
Standing cohort: starts evacuating when plume arrives
Alarm triggers evacuation everywhere

## Slide 6: Plume and cohort overlap concept
Sector j
Sector j + 1
Sector j − 1
In this example, air and ground in sector j are assumed contaminated, and evacuees are assumed exposed while traveling in sector j, although the plume is behind
Overlap concept is not uniformly applied in all modeling cases in MACCS
  Exception: inhalation, cloudshine, and skin deposition under evacuation on plume arrival assume true physical overlap for exposure and non-zero doses
Air conservatively assumed contaminated everywhere above sector j
Ground conservatively assumed contaminated everywhere in sector j

## Slide 7: Exposure time
Exposure time = evacuees’ travel time through sector j
  Plume pathways under evacuation on plume arrival
Exposure time = evacuees’ departure time from j − plume arrival time to j
  Plume pathways under evacuation triggered by an alarm and groundshine
Sector j
Sector j + 1
Sector j − 1

## Slide 8: Resuspension model
Resuspension and groundshine should be mathematically identical, but they are treated differently in MACCS
MACCS assumes that dose is zero while plume is overhead
  What does it mean? How is this assumption practically implemented?
Sector j
Sector j + 1
Sector j − 1
Plume is not overhead
Non-zero resuspension dose
The ground concentration is zero until the back of the plume enters the sector
If the back of the plume enters sector j before the evacuees leave sector j, the resuspension dose is non-zero

## Slide 9: Resuspension model: exposure time
Exposure time in j = time cohort leaves j − back of plume arrival time to j
Exposure time in j = time some space above sector j is behind the plume while evacuees travel in j. What?
Sector j
Sector j + 1
Sector j − 1
Plume is not overhead
Non-zero resuspension dose

## Slide 10: Groundshine model: linear ground buildup
The ground concentration is assumed proportional to the fraction of the plume past the start of sector j: F = Lout/Lplume
Groundshine dose factors: exposure time and concentration buildup factor
Sector j
Sector j + 1
Sector j − 1
Lout
Lplume

## Slide 11: Doses are aggregated and assigned to the start sector
Evacuees starting evacuation in sector 𝑖 experience different doses as they travel in the sectors j
The j-doses are aggregated and assigned to the starting sector 𝑖
This reporting approach facilitates comparison of evacuation and no-evacuation scenarios, including population doses
Sector j
Sector j + 1
Sector 𝑖
The cumulative evacuation dose is assigned to the starting sector 𝑖

## Slide 12: Evacuation start on plume arrival, long-plume case
Evacuation at a sector initiates when the plume arrives
Windspeed = 2 m/s = plume speed
Plume duration = 1 day
Reasonable agreement between benchmarks (solid) and MACCS outputs (symbols)
Differences in the plots suggest that MACCS treats inhalation and cloudshine differently, although they should be mathematically identical
Evacuation speed (m/s)
Windspeed = 2 m/s
End of evacuation zone
Evacuation speed (m/s)
End of evacuation zone

## Slide 13: Evacuation start on plume arrival, long-plume case
An update in MACCS Version 4.2 caused an increase in the skin deposition dose by a factor of ~ 2
However, the factor 2 is missing in evacuation cases with evacuation speed = 0.1, 1, 2, 3, 10 m/s
  The MACCS Version 4.1 and 4.2 results are identical for these evacuation speeds
  Investigating issue with MACCS developers
Evacuation speed (m/s)
MACCS Version 4.1
Evacuation speed (m/s)
MACCS Version 4.2

## Slide 14: Evacuation start on plume arrival, long-plume case
Groundshine and resuspension pathways could be treated in similar manner
However, resuspension includes and assumption of zero-dose while plume is overhead
This assumption is too restrictive: non-zero doses only occur with very small evacuation speeds or very short plumes, which are cases of little interest
Zero dose because of assumption of zero dose while plume is overhead
Evacuation speed (m/s)
Evacuation speed (m/s)

## Slide 15: Evacuation start on plume arrival, long-plume case
Population dose (evac speed 10−6 m/s) < Population dose (no evacuation)
In this case, some mass is lost by the top-hat approximation used to model evacuation
Evacuation speed (m/s)
Population dose
Evacuation zone
1.5

## Slide 16: Evacuation start on plume arrival, short-plume case
For a short-plume case (1-minute plume), maximal doses occur when the time exposed to the plume is maximal; i.e., when evacuees travel at the same speed than the plume (1.66 m/s)
Evacuation speed (m/s)
Downwind distance (km)
Windspeed = 1.66 m/s
Plume duration = 60 seconds
Maximal dose
Inhalation
Evac speed = windspeed = 1.66 m/s

## Slide 17: Evacuation start on plume arrival, short-plume case
MACCS outputs non-zero resuspension doses when the plume is short (60 seconds in these runs)
Evacuation speed (m/s)
Windspeed = 1.66 m/s
Plume duration = 60 seconds
Evacuation speed (m/s)
Notes: The non-zero resuspension doses are non-intuitive, but they can be explained. For example, if the plume and the evacuees travel at the same speed, the plume is always overhead the evacuees. Why are the doses non-zero? Because the doses are non-zero whenever the back end of the plume enters the sector before the evacuees leave the sector. This occurs in long sectors, even if the evacuees overlap with the leading edge of the plume.

## Slide 18: Evacuation triggered by an alarm
Plume delay (s)
End of evacuation zone
Evacuation speed = windspeed = 2 m/s
The alarm triggered at time 0 in the runs. The plume release was delayed
Sectors other than the sector closest to the source should avoid exposure
  However, dose is not zero because of the MACCS plume-cohort overlap concept
The sector closest to the source (first sector, 100 m in length) should avoid exposure for plume delays > 50 seconds
  After 50 seconds the cohort fully evacuates the first sector
  However, the dose is non-zero up to 900 s of plume delay because of the conservative MACCS plume-cohort overlap concept
Plume delay (s)
Cloudshine model in MACCS is slightly different than the inhalation model

## Slide 19: Evacuation triggered by an alarm
Plume delay (s)
End of evacuation zone
Evacuation speed = windspeed = 2 m/s
Non-zero groundshine doses arise because the conservative MACCS plume-cohort overlap concept
Resuspension doses are zero because of the zero-dose while plume is overhead assumption
  This assumption is too restrictive
  Non-zero doses only arise in case of short plumes or very slow evacuation speed, which are cases of little interest
Plume delay (s)

## Slide 20: Conclusions
We designed equations to verify the MACCS outputs: lots of trial and error
The different MACCS models are asymmetrical (e.g., different assumptions applied to similar cases) sometimes making interpretation of results difficult
We recommend treating resuspension as mathematically identical to groundshine
  Eliminate assumption of zero-dose while plume is overhead
  Otherwise, non-zero resuspension doses arise only in cases of little interest: short plumes or very small evacuation speed
An anomaly in the skin deposition dose under evacuation in MACCS Version 4.2 was identified

## Slide 21: Backup Slides

## Slide 22: MACCS tracks concentrations on arcs of the grid
Air concentration on the line is mapped to the arc
Plume spread limited to an arc half-length ≤ 2.15
In case of evacuation, the plume spread is further constrained to an arc half-length ≤ 1.5 , referred to as top-hat approximation
Source

## Slide 23: Plume spread with and without evacuation
No evacuation case
Evacuation case
Evacuation zone
2.15
−2.15
1.5