## Slide 1: Comparison of Tritium DOSE Calculations FROM Selected Codes
Presented by: Mariah Smith (SNL)
In collaboration with: Kyle Clavier (SNL)* and Keith Compton (NRC)
SAND2023-08445C
2023 International MACCS User Group Meeting
*Currently on IPA assignment with the NRC
This research was sponsored by the US Nuclear Regulatory Commission under agreement number 31310020F0032

## Slide 2: Motivation and Scope
Motivation:
  MACCS capabilities for modeling doses from atmospheric releases of tritium in different chemical and physical forms such as particulates, tritium gas (HT), tritiated water vapor (HTO), or organically-bound tritium (OBT) are limited
  The benefit of implementing MACCS model enhancements to increase the fidelity of tritium dose calculations is unclear
  Work was identified as a need in the US Nuclear Regulatory Commissions Non-Light Water Reactors Vision and Strategy Volume 3 report (1)
Objectives:
  Evaluate the degree to which the capabilities of higher-fidelity tritium models impact dose assessment results
  Provide information to assist analysts in judging whether a postulated tritium release is likely to lead to significant doses
Approach:
  Conduct a model intercomparison study comparing results from MACCS to those generated using the tritium-specific dose assessment codes UFOTRI and ETMOD​
This work is a continuation of previous analyses documented in Clavier and Clayton, 2022 (2)​.
[1] U.S. Nuclear Regulatory Commission (NRC), 2020. NRC Non-Light Water Reactor (Non-LWR) Vision and Strategy, Volume 3- Computer Code Development Plans for Severe Accident Progression, Source Term and Consequence Analysis, Revision 1.
[2] K.A. Clavier and D.J. Clayton, 2022. Reviewing MACCS capabilities for assessing tritium releases to the environment (SAND2022-12016)

## Slide 3: ACCOUNTING for Tritium Phenomena In MACCs
Tritium releases are subject to atmospheric dispersion processes in a manner consistent with other types of contaminants. MACCS accounts for these atmospheric dispersion using Gaussian dispersion models. ​
During atmospheric transport, tritium gas (HT) can undergo conversion into tritiated water vapor (HTO). Although MACCS does not account for this process, this conversion is a very slow process.
Airborne tritium is subject to dry and wet deposition, which is accounted for in MACCS. However,
    MACCS deposition models have no detailed accounting for consideration of how factors such as humidity, tritium concentration gradients, solar insolation, plant resistance, etc.​, affect transport of tritium from the plume to soil and plants.
    MACCS does not account for uptake of tritiated water (HTO) from soil to plants.
Deposited tritium may be re-emitted to the atmosphere from plants and soil by evaporation (soil) and transpiration (plant). MACCS has only a simple resuspension model and does not include a dedicated reemission physics model.
MACCS does not account for oxidation of HT to HTO by soil microbes or conversion of HTO to organically bound tritium through biological processes in plants or animals.
Tritium-specific codes such as UFOTRI (1,2) and ETMOD (3,4) are available to address the physical and chemical phenomena not included in MACCS
[1] W. Raskob, 1990. UFOTRI: Program for Assessing the Off-Site Consequences from Accidental Tritium Releases (KfK 4605)
[2] W. Raskob and I. Hasemann, 1991. User guide for UFOTRI: A Program for Assessing the Off-Site Consequences from Accidental Tritium Releases. (KfK 4853)
[3] S.B. Russell and G. L. Ogram, 1988. Modelling elemental tritium deposition, conversion and reemission using Ontario Hydro’s tritium dispersion code. Fusion Technol., 14:2.
[4] G. L. Ogram, 1991. Improved ETMOD modules for HTO exchange, HT deposition, and vegetation HTO (CFFTPG-9188 / OHRD No. 91-191-K).
Notes: Process​

## Slide 4: Documented ACUTE tritium releases
Acute tritium releases from tritium production reactors have occurred* and may provide insight into the actual consequences of tritium releases
Documented in Murphy and Wortham 1991 (1)
Largest documented total activity released was 479,000 Ci of 99% tritium gas, corresponding to approximately 50 grams
The largest documented tritiated water vapor activity released was approximately 168,000 Ci (97.8% of 172,000 Ci), corresponding to 17.4 grams of tritium
Releases have been examined in benchmarking exercises (see subsequent slide)
* Releases occurred from tritium production reactors and do not represent releases that may occur from commercial nuclear power reactors
[1] C.E.Murphy Jr. and G. R. Wortham, 1991. An atmospheric tritium release database for model comparisons. (WSRC-TR-91-671). Rev. 1

## Slide 5: Previous MODEL COMPARISON EXERCISES
Model comparisons including tritium-specific models such as UFOTRI and ETMOD, as well as general purpose codes such as HOTSPOT and RSAC, were conducted as part of code evaluations for DOE analyses (1,2)
Nearly all models included are capable of estimating inhalation dose during plume passage
Major differences between codes related to capabilities for longer term transport and transformation processes
Assessments concluded that UFOTRI was the recommended model for tritium source terms, with HOTSPOT and MACCS also recommended for some applications
Scenario | Activity | Release Height | Release Duration | Other Assumptions | Models Compared* | Comparison
HTO Release, Low Energy Source Term[1] | 1.03E3 Ci of HTO | 60 m | 1 hour | Ambient outdoor temperature of 303K | ETMOD, HOTSPOT, MACCS2, RSAC, UFOTRI | Dose to receptor at various distances
Mixed HTO/HT Release, Medium-Energy Source Term[1] | 2.04E4 Ci of 50/50 HT/HTO | 20 m | 2 hours | 4 MW sensible heat | UFOTRI, ETMOD, MACCS2 | Dose to receptor at various distances
Environmental Model [1]** | 479, 000 Ci of 99/1 HT/HTO | 60 m | 4 minutes | 6.4-9.7 km/h winds, 90-100% cloud cover, neutral stability | UFOTRI compared to field measurements | Dose to receptor at various distances
HTO release [2] | 1000 Ci | Stack height | Unspecified | B/3.5, D/4.5, F/1.0 | MACCS2, UFOTRI | Doses to receptors at 100m, 640 m, 8 km
HTO fire release scenario [2] | 1000 Ci | Ground level | 20 min – 1 hour | Unspecified | MACCS2, UFOTRI | Doses vs. distance
* Models not listed include proprietary and/or research models not easily accessible ** Modeling case developed from release documented in Murphy and Wortham (1991)
[1] Evaluation of current computer models applied in the DOE complex for SAR analysis of radiological dispersion and consequences (U), 2003. Accident Phenomenology and Consequence (APAC) Methodology Evaluation Program Radiological Dispersion and Consequence Working Group (WSRC-TR-96-0126).
[2] A. Blanchard, K.R. O’Kula, and J. M. East, 1998. Selection of a tritium dose model: defensibility and reasonability for DOE authorization basis calculations (u). WSRC-MS-98-00016.

## Slide 6: Chosen State-of-Practice Models for Comparison
MACCS results were compared to results generated by UFOTRI and ETMOD
UFOTRI and ETMOD consider physical and chemical phenomena not included in MACCS
UFOTRI and ETMOD were chosen for code comparisons in this study based on
  Specific application to tritium​
  Relative portability and accessibility
  Previous mention in regulatory documentation or the scientific literature
Source: Raskob (1990)

## Slide 7: Baseline Scenario: Scenario definition
Activity Released | 5,000 Ci
Chemical Form​ | HTO​
Release Duration​ | 1-hr​
Weather​ | Constant, No Rain​
Mixing Layer Height​ | 1000 m​
Wind​ | 3 m/s​
Stability | D​
Air Temperature | 30°C
Solar Radiation | 600 W/m2
Building Dimensions | 40 m x 40 m x 40 m
Release Height | Ground level (0 m​)
Baseline scenario analogous to tritium release scenarios examined in previous model comparisons

## Slide 8: Baseline Scenario: Inputs
MACCS input parameters were selected according to NUREG/CR-7270, SAND2022-12166R​ unless otherwise noted
Input parameters for UFOTRI and ETMOD were selected according to defaults described in their respective user guides​
Parameter | MACCS | UFOTRI | ETMOD
Inhalation Dose Coefficients | HTO: 1.839E-11 Sv/Bq | HTO: 1.7E-11 Sv/Bq* HT: 1.7E-15 Sv/Bq OBT: 4.0E-11 Sv/Bq *Later adjusted by 50% to account for skin absorption | HTO: 2.00E-11 Sv/Bq HT: 2.4E-15 Sv/Bq OBT: 4.0E-11 Sv/Bq HTO skin absorption factor: 2
Wake Effects | Included | Included | Included
Surface Roughness | 0.03 m | Low plants, rural areas, Z < 10 cm to 1 m | 0.03 m
Dry Deposition Velocity | 0.003 m/s | 0.0005 m/s for HT-gas 0.005 m/s for HTO-vapour Resistance model flag selected | Unspecified (defaults were used)
Resuspension/ Reemission Parameters | Default short- and long- term resuspension factors | Default values Minimal duration of reemission process : 70 hours | Unspecified (defaults were used)
Breathing Rate | 2.66E-04 m3/s | 2.66E-04 m3/s | 2.66E-04 m3/s

## Slide 9: Baseline scenario: results
Notes: 1) ETMOD outputs do not differentiate between inhalation doses from plume and from reemission 2)The release magnitudes assumed in this analysis were developed for code assessment purposes only. Actual doses would be based on design and site-specific factors
Doses at 500 m from a postulated 5,000 Ci HTO release are compared
Inhalation dose results are broadly similar across models
Reemission appears to be a small(<10%) component of the total inhalation dose from the HTO release
Notes: Remove asterisk
Change number of sig figs

## Slide 10: Sensitivity Analyses
A release of 1,000 Ci was assumed for all sensitivity analysis scenarios with the remaining input assumptions being identical to those defined in the baseline scenario
Chemical speciation
  100% HTO
  75% HTO 25% HT
  50% HTO 50% HT
  25% HTO 75% HT
  100% HT
MACCS data files were modified to allow doses from mixed HTO and HT releases to be calculated in the same code execution
Investigating difference between 100% HTO and 100% HT releases for:
  Release height (ground-level versus elevated release)
  Receptor distance (distances <500m and >500m)
  Release conditions
    Nighttime release (15°C air temperature and no solar radiation)
    Extreme summer release (38°C air temperature and 1000 W/m2 solar radiation)

## Slide 11: 100% HTO Release Sensitivity Results
Doses at 500 m from a postulated 1,000 Ci HTO release are compared on a log scale
Inhalation dose results for HTO releases are broadly similar across models
Reemission appears to be a small (<10%) component of the total inhalation dose from the HTO release
Notes: 1) ETMOD outputs do not differentiate between inhalation doses from plume and from reemission 2)The release magnitudes assumed in this analysis were developed for code assessment purposes only. Actual doses would be based on design and site-specific factors
3) NT: Nighttime release, ES: Extreme summer release, 60m: Elevated release at 60 m

## Slide 12: Mixed HTO/HT Release Sensitivity Results
Doses at 500 m from a postulated 1,000 Ci HTO release are compared on a log scale
Additional sensitivities were not explored for the mixed HTO/HT releases
Inhalation dose results for the mixed HTO/HT releases explored are broadly similar across models
Reemission appears to be a small (<10%) component of the total inhalation dose from the mixed HTO/HT releases explored
Notes: 1) ETMOD outputs do not differentiate between inhalation doses from plume and from reemission 2)The release magnitudes assumed in this analysis were developed for code assessment purposes only. Actual doses would be based on design and site-specific factors
Notes: Mention speciation for variety of fraction, sensitivities were not explored here, each group is a code

## Slide 13: 100% HT Release Sensitivity Results
Doses at 500 m from a postulated 1,000 Ci HT release are compared on a log scale
Inhalation dose results for HT releases exhibit considerably more variability
MACCS results are substantially lower than UFOTRI or ETMOD results when MACCS is modified to use a dose coefficient consistent with HT
Reemission appears to be a large component of the total inhalation dose from the HT release
Notes: 1) ETMOD outputs do not differentiate between inhalation doses from plume and from reemission 2)The release magnitudes assumed in this analysis were developed for code assessment purposes only. Actual doses would be based on design and site-specific factors
3) NT: Nighttime release, ES: Extreme summer release, 60m: Elevated release at 60 m

## Slide 14: Receptor Distance Comparison
Note: The release magnitudes assumed in this analysis were developed for code assessment purposes only. Actual doses would be based on design and site-specific factors
Doses at various distances from postulated 1,000 Ci HTO and HT release are compared
Inhalation dose results for HTO releases are broadly similar across models
Inhalation dose results for HT releases exhibit considerably more variability
MACCS results are substantially lower than UFOTRI or ETMOD results when MACCS is modified to use a dose coefficient consistent with HT

## Slide 15: Dose-Distance Curves for INHALATION arising from A UNIT 1 CURIE Release
Curves representing dose from a unit release of 1 Ci at different distances generated using tritium-specific code UFOTRI
Includes curves representing alternate weather conditions such as stability class and wind speed (m/s)
Unit dose curves can provide insights regarding whether a postulated tritium release is likely to lead to significant doses

## Slide 16: Dose-Distance Curves for Ingestion arising from A UNIT 1 CURIE Release
Curves representing dose from a unit release of 1 Ci at different distances generated using tritium-specific code UFOTRI
Includes curves representing alternate weather conditions such as stability class and wind speed (m/s)
Results can provide insights regarding whether a postulated tritium release is likely to lead to significant doses

## Slide 17: SUMMARY: MODELING RELEASES OF HTO vs HT
Using typical input parameters, MACCS results for modeling inhalation doses of HTO releases compare reasonably well to UFOTRI and ETMOD.
Modeling HT releases in MACCS using the dose coefficients supplied in the MACCS DCF file may overestimate the inhalation dose by approximately 2 orders of magnitude relative to UFOTRI and ETMOD.
Modeling HT releases in MACCS using a dose coefficient representing HT may underestimate inhalation doses dose by approximately 2 orders of magnitude relative to UFOTRI and ETMOD

## Slide 18: Concluding observations
MACCS dose coefficients for tritium appear to be reasonably consistent with tritium in the HTO form
Inhalation doses from releases of tritium as organically-bound-tritium (OBT) were not evaluated
  It is expected that doses from OBT are more likely to arise from ingestion pathways (conversion of HT or HTO into OBT following deposition) rather than from releases of tritium as OBT.
  However, as described in O’Kula and Thoman 2007 (1), atmospheric releases of tritium as OBT may arise from source terms involving, for example, oil-based inventories
MACCS is not designed to model doses arising from ingestion following release and deposition of HTO, HT, or OBT.
Insights into the dose arising from ingestion may be evaluated using UFOTRI or ETMOD
[1] K. R. O’Kula and D. C. Thoman, 2007. Modeling Atmospheric Releases of Tritium from Nuclear Installations (WSRC-STI-2007-00027)