## Slide 1
Protective Action Recommendation Study using MACCS in NRA Japan
Regulatory Standard and Research Department,
Secretariat of Nuclear Regulation Authority (S/NRA/R)
Kodai Wadayama, Retsu Kojo

## Slide 2
Background and Objectives

## Slide 3: Past protective action recommendation study
Technical Basis for Protective Action Strategies (NUREG/CR-6953)
“Rapidly Progressing Severe Accident” is focused.
  General Emergency (GE) with rapid loss of ability of core cooling and loss of containment integrity.
The risk of early fatality and cancer fatality are used as indicators for the evaluation.
Insight:
  For the 0 to 2-mile area around a nuclear power plant: Evacuation is more protective when the evacuation time estimate (ETE) is less than 2 hours.
  For the 2 to 5-mile area: Evacuation is more protective when ETE is less than 3 hours.
Notes: A rapidly progressing severe accident is a This type of accident is determined for scenarios in which containment integrity can be determined as bypassed or immediately lost during a GE with core damage.
The estimated time to evacuate (ETE) of 90% residents is used to determine whether residents within a short distance should evacuate or remain indoors.

## Slide 4: Challenges in applying American research to Japan
There have been no similar studies specifically targeting Japanese sites.
While there are various conceivable scenarios where early core damage occurs, followed by loss of containment integrity, it's essential to determine which scenarios can be classified as "rapidly progressing accidents" that might necessitate temporary Sheltering In Place (SIP).
Investigating accident scenarios that have a beneficial effect on
temporary sheltering considering Japanese plants and sites, is valuable

## Slide 5: New mitigation system in Japanese plants
To mitigate risks of overpressure failure of containment vessel, Filtered Containment Venting System (FCVS) was introduced following the accident at the Fukushima Daiichi Nuclear Power Plant, supplementing the traditional hardened containment venting.
FCVS is designed to achieve a decontamination factor of approximately 1000 for aerosol.
However, FCVS does not eliminate noble gases.
  The impact of short-lived noble gases on effective dose becomes a concern, especially in early release.

## Slide 6: Protective Action Strategy in Japan
Emergency Classification:
  Based on the EAL, basically similar to the U.S.
Predefined Zones :
  Precautionary Action Zone (PAZ): 5 km radius ←Target in this study
  Urgent Protective action Zone (UPZ): 5-30 km radius
Protective Actions in PAZ:
  Evacuation is the top-priority protective action
  If evacuation isn't prioritized, then sheltering in place (SIP) is recommended.
Generic Criteria of IAEA:
  Effective dose 100 mSv for seven days is often referenced
It is fundamentally similar to the U.S., but there are some differences

## Slide 7: Research Activities in NRA Japan using MACCS
(1) Characterization of accident scenarios from the viewpoint of emergency preparedness
  Accident Progression Analysis (MELCOR)
  Consequence Analysis for Environment (MACCS)
(2) Characteristic analysis of risk considering protective actions
  Risk characteristic analysis considering protective actions (MACCS and OSCAAR)
Here, "Rapidly Progressing Severe Accident" scenario analyzed using MACCS is introduced.
Identify protective actions that can be effectively implemented based on status of plants in Japan.
Notes: Development of analytical models using MELCOR is carried out to analyze accident progression considering accident measures; such as FCVS, that are introduced in the new regulatory standards. Using those results, accident scenarios are characterized from the viewpoint of emergency preparedness.
Consequence analyses using MACCS are conducted for those accident scenarios in domestic environmental conditions. Based on analysis results, accident scenarios are to be grouped from the viewpoint of characteristic exposure doses, and classification of release categories considering effective protective actions corresponding to the plant conditions is carried out.
Appropriate combinations of protective actions are studied by confirming the effects on radiation doses for each scenario for each target of protective actions

## Slide 8: Objectives
differences from past studies in U.S. considering the unique situation in Japan
accident scenarios in which a major release starts within 5 hours of the scram and for which PAZ residents should temporarily shelter indoors.
Conduct sensitivity analysis on the duration of SIP for PAZ residents at representative plants in Japan to figure out;
Distinctive accident scenarios should be focused on
More effective protective action (off-site responses) should be discussed based on the plant's condition (on-site information) considering updated severe accident measures and procedures
Objectives:

## Slide 9
Materials and Methods

## Slide 10: MELCOR analysis condition
A representative PWR 3-loop plant and BWR5 were selected.
Analyses were conducted using MELCOR2.2.
Accident Scenario | Description
ISLOCA (PWR) | Radioactive materials are directly released into the environment, bypassing the containment vessel, due to a break in low-pressure system piping.
ISLOCA (BWR) | It is a similar scenario as the ISLOCA(PWR), but in a typical BWR. The release duration in this case is longer than that of ISLOCA (PWR).
ATWS (BWR): | The reactor fails to shut down after a small LOCA, leading to rapid accumulation of water vapor in the primary containment vessel(PCV) and subsequent overpressure failure of the PCV.
LBLOCA+PCV fail (BWR) | After a large-break LOCA(LBLOCA) occurs, there is failure to inject water into both the core and the PCV, resulting in early over-temperature failure of the PCV.
LBLOCA+FCVS (BWR) | After a LBLOCA, injection into the core/PCV fails, but containment failure is avoided, and the release occurs through FCVS.

## Slide 11: MACCS Analysis Condition
Accident Scenario | Description
Metrological Condition | Analysis was conducted by 8760 case for whole year and mean value was evaluated.
Evacuation model | Network evacuation model in a typical Japanese site
Shielding factor | Representative value in a typical Japanese site
Target residents | PAZ residents in a typical Japanese site
Calculation time | Seven days

## Slide 12: MACCS analysis condition
Accident progression
Accident initiation
General Emergency
Release
start
Release end
1500 s
Preparation (DLTSHL)
1 h
Evacuation
Start
Protective action
Notice for residents
(OALARM)
SIP initiation
Evacuation end
Evacuation Time
Fast Evacuation 1.75 h
Normal Evacuation 3.5 h
Slow Evacuation 7 h
Release Duration
Duration of SIP
(DLTEVA)
→Sensitivity Analysis
(0 ~24 h)
Protective actions: Switch to evacuation after initial indoor evacuation
Evacuation time: Normal evacuation time is referenced from the Japanese typical site
Focus: DLTEVA ≒ Duration of Shelter in Place (SIP)

## Slide 13: Key metric for the evaluation
The number of the population exceeding GC is assessed;
Number of the population exceeding the effective dose of 100 mSv
In prior research, evaluations were made regarding average Early Fatality Risk and Latent Fatality Risk in an entire population. However, in Japan, there is interest in whether the dose exceeds the IAEA’s Generic Criteria (GC) in an emergency.

## Slide 14
Result and Discussion

## Slide 15: MELCOR Analysis Result
Accident Scenario | Release start | Release duration
ISLOCA （PWR) | < 1 h | < 1 h
ISLOCA (BWR) | < 1 h | 5 h
ATWS (BWR) | 3.9 h | 2 h
LBLOCA+PCV fail (BWR) | 4.2 h | 24 h
LBLOCA+FCVS (BWR) | 3 h | 1 h
Major release began within 5 hours of accident initiation.
*Scenarios where the release starts within 5 hours were selected considering the effect of short-lived nuclides.

## Slide 16: Accident scenario grouping
Accident Scenario | Immediate Release | Delayed Release
Short release duration | Category1: ISLOCA (PWR) | Category2: LBLOCA+FCVS ATWS
Long release duration | Category3: ISLOCA (BWR) | Category4: LBLOCA+PCV fail
Accident Scenario | Release start | Release duration
ISLOCA（PWR) | < 1 h | < 1 h
ISLOCA(BWR) | < 1 h | 5 h
ATWS(BWR) | 3.9 h | 2 h
LBLOCA+PCV fail(BWR) | 4.2 h | 24 h
LBLOCA+FCVS(BWR) | 3 h | 1 h

## Slide 17: MACCS result (All scenarios)
The characteristics vary for each of the four categories mentioned earlier.
Various accident scenarios were analyzed
ISLOCA(PWR)
as Category 1
FCVS
as Category 2
ISLOCA(BWR)
as Category 3
ATWS as Category 2
LBLOCA+PCV fail
as Category 4

## Slide 18: Effect of release start (Category 1 vs 2)
ISLOCA (PWR): Temporarily SIP is effective.
ATWS,FCVS: Immediate evacuation is effective.
Analyzing the impact of different release timings
(Focusing on scenarios with short release duration)
ISLOCA(PWR)
ATWS
FCVS
Major plume release

## Slide 19: Effect of release duration (Category 1 vs 3)
ISLOCA (PWR) : Temporarily SIP is effective in the early phase.
ISLOCA (BWR) : Exposure during evacuation is observed due to continuous release.
ISLOCA(PWR)
ISLOCA(BWR)
Analyzing the impact of different release durations for immediate release
(Focusing on scenarios with early release start)
ISLOCA(PWR)
ISLOCA(BWR)

## Slide 20: Effect of release duration (Category 1 vs 3)
ISLOCA(PWR): Changing the evacuation speed does not alter the trend that temporary SIP reduces the number of people exceeding effective dose of 100 mSv.
ISLOCA(BWR): The number of people exceeding effective dose of 100 mSv during
the initial phase varies significantly depending on the evacuation speed.
Chart: DLTEVA (h)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 8 | 10 | 12 | 16 | 20 | 24 | 30 | 36 | 42 | 48 | 54 | 60 | 66 | 72 | 84 | 96 | 108 | 120 | 132 | 144 | 156
short evacuation | 0.12608 | 0.38312 | 0.41744 | 0.51635 | 0.47636 | 0.47012 | 0.52227 | 0.49128 | 0.5079 | 0.52592 | 0.5579 | 0.58459 | 0.60459 | 0.63016 | 0.653 | 0.67341 | 0.68868 | 0.70092 | 0.71163 | 0.72244 | 0.73248 | 0.75143 | 0 | 0 | 0 | 0 | 0 | 0
short evacuation | 0.85581 | 0.81861 | 0.71038 | 0.69274 | 0.6838 | 0.67577 | 0.66547 | 0.78845 | 0.87758 | 0.91446 | 1.0084 | 1.0721 | 1.0991 | 1.1183 | 1.1402 | 1.1594 | 1.1764 | 1.1911 | 1.2034 | 1.2146 | 1.2257 | 1.2458 | 1.2645 | 1.2818 | 1.2952 | 0 | 0 | 0
normal evacuation | 0.39192 | 0.49036 | 0.64854 | 0.61309 | 0.56001 | 0.57934 | 0.5835 | 0.51448 | 0.51785 | 0.53272 | 0.56381 | 0.58942 | 0.60857 | 0.63367 | 0.65651 | 0.67679 | 0.69104 | 0.70293 | 0.71363 | 0 | 0 | 0.75313 | 0 | 0 | 0.79257 | 0 | 0 | 0.8181
normal evasuation | 1 | 0.8776 | 0.79544 | 0.77436 | 0.76409 | 0.74669 | 0.72637 | 0.8926 | 0.96828 | 0.99668 | 1.098 | 1.1384 | 1.1114 | 1.1239 | 1.1457 | 1.164 | 1.1804 | 1.1943 | 1.2066 | 0 | 0 | 1.2489 | 0 | 0 | 1.2969 | 0 | 0 | 1.3287
long evacuation | 0.66477 | 0.70454 | 0.84542 | 0.71338 | 0.68703 | 0.70461 | 0.60561 | 0.53754 | 0.53624 | 0.54778 | 0.57734 | 0.59915 | 0.61651 | 0.64156 | 0.66447 | 0.68355 | 0.69549 | 0.707 | 0.71791 | 0.72829 | 0.73824 | 0.75689 | 0 | 0 | 0 | 0 | 0 | 0
long evacuation | 1.0676 | 0.90146 | 0.85475 | 0.8448 | 0.83543 | 0.82085 | 0.84541 | 1.0621 | 1.1014 | 1.0992 | 1.2092 | 1.223 | 1.1299 | 1.1376 | 1.1587 | 1.1739 | 1.1884 | 1.2017 | 1.2137 | 1.2248 | 1.2361 | 1.2557 | 1.2746 | 1.2886 | 1.3008 | 0 | 0 | 0
ISLOCA(PWR)
ISLOCA(BWR)
ISLOCA(PWR)
ISLOCA(BWR)

## Slide 21: Characteristics of each category
Scenario Category | Protective actions that reduce the number of population exceeding 100 mSv | Remarks
Category 1 | Temporary SIP | It is recommended to limit the duration of SIP to just a few hours.
Category 2 | Immediate evacuation | If preparation takes time, temporary SIP can also be effective.
Category 3 | Immediate evacuation | If evacuation takes time, temporary SIP can also be effective.
Category 4 | Immediate evacuation | Compared to other categories, there is a tendency for evacuation to be more effective than SIP.
Accident scenarios were categorized based on release timing and duration. Characteristics of each category were analyzed.

## Slide 22
Conclusion

## Slide 23: Conclusion
MACCS analyses were carried out focusing on the duration of SIP for PAZ residents at representative plants in Japan.
In this study, population exceeding 100 mSv is used as an evaluation indicator. The findings of this study are similar to those of the U.S. study.
  The overall trend that immediate evacuation becomes more effective as the evacuation time is shorter, is the same as the U.S. study.
In scenarios with short release duration and immediate release, alternatives to immediate evacuation can be considered if evacuation is estimated to be time-consuming.

## Slide 24: Limitations of the Case Study
Population distributions Results may vary for plants with special population distributions.
Meteorological conditions For example, the contribution of inhalation will be smaller, and that of groundshine will be larger with respect to cases of heavy rainfall. This will change the trend of the results, for example, and exposure will rise in case of a longer duration of SIP.
Building shielding factors Assumed a typical value in this case, but further analyses are needed assuming robust cases, etc.

## Slide 25: Model Uncertainty
The protective effect of sheltering in place can vary over the duration of SIP.
  MACCS uses a simple model as constant protection factors over time.
It is essential to evaluate the impact of the model on the results.
  JAEA has developed OSCAAR to simulate the effects of KI intake timing and the duration of sheltering or evacuation.

## Slide 26: Acknowledgements
We would like to extend our deepest gratitude to Mr. Mizuki Uono for taking primary responsibility for programming and for greatly assisting in the analysis of the results.
We would like to also extend our deepest gratitude to Dr. Chihiro Suzuki and Dr. Yutaka Abe for giving advice about our out results.

## Slide 27: Appendix

## Slide 28: Research Activities in NRA Japan using MACCS
(1) Characterization of accident scenarios from the viewpoint of emergency preparedness
  Accident Progression Analysis The Development of analytical models using MELCOR is carried out to analyze the accident progression considering accident countermeasures; such as FCVS, that are introduced in the new regulatory standards. These results are used to characterize accident scenarios from an emergency preparedness perspective.
  Consequence Analysis for the Environment Consequence analyses using MACCS are performed for those accident scenarios under Japanese environmental conditions. Based on analysis results, accident scenarios are to be grouped in terms of doses characteristics, and the release categories are classified considering effective protective actions based on the plant conditions.
(2) Characteristic analysis of risk considering protective actions
  Risk characteristic analysis considering protective actions (MACCS and OSCAAR) Appropriate combinations of protective actions are investigated by confirming the effects on radiation doses for each scenario for each target of protective actions
Identify protective actions that can be effectively implemented based on the status of plants in Japan. Here, "Rapidly Progressing Severe Accident" scenario analyzed using MACCS is introduced.

## Slide 29: Comparing the results under several evacuation time
Category 1: ISLOCA (PWR)
Chart: DLTEVA (h)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 8 | 10 | 12 | 16 | 20 | 24 | 30 | 36 | 42 | 48 | 54 | 60 | 66 | 72 | 84 | 96 | 108 | 120 | 132 | 144 | 156
long evacuation | 1.0676 | 0.90146 | 0.85475 | 0.8448 | 0.83543 | 0.82085 | 0.84541 | 1.0621 | 1.1014 | 1.0992 | 1.2092 | 1.223 | 1.1299 | 1.1376 | 1.1587 | 1.1739 | 1.1884 | 1.2017 | 1.2137 | 1.2248 | 1.2361 | 1.2557 | 1.2746 | 1.2886 | 1.3008 | 0 | 0 | 0
normal evacuation | 1 | 0.8776 | 0.79544 | 0.77436 | 0.76409 | 0.74669 | 0.72637 | 0.8926 | 0.96828 | 0.99668 | 1.098 | 1.1384 | 1.1114 | 1.1239 | 1.1457 | 1.164 | 1.1804 | 1.1943 | 1.2066 | 0 | 0 | 1.2489 | 0 | 0 | 1.2969 | 0 | 0 | 1.3287
short evacuation | 0.85581 | 0.81861 | 0.71038 | 0.69274 | 0.6838 | 0.67577 | 0.66547 | 0.78845 | 0.87758 | 0.91446 | 1.0084 | 1.0721 | 1.0991 | 1.1183 | 1.1402 | 1.1594 | 1.1764 | 1.1911 | 1.2034 | 1.2146 | 1.2257 | 1.2458 | 1.2645 | 1.2818 | 1.2952 | 0 | 0 | 0

## Slide 30: Comparing the results under several evacuation time
Category 2: ATWS
Chart: DLTEVA (h)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 8 | 10 | 12 | 16 | 20 | 24 | 30 | 36 | 42 | 48 | 54 | 60 | 66 | 72 | 84 | 96 | 108 | 120 | 132 | 144 | 156
long evacuation | 0.00070254 | 0.025299 | 0.16885 | 0.66014 | 0.92861 | 0.96171 | 1.0218 | 0.77179 | 0.66155 | 0.65179 | 0.77942 | 0.74362 | 0.74293 | 0.76664 | 0.78937 | 0.80939 | 0.82181 | 0.83325 | 0.84457 | 0.85516 | 0.86516 | 0.8835 | 0.90024 | 0.91164 | 0.9218 | 0 | 0 | 0
normal evacuation | 0 | 0 | 0.00073424 | 0.34027 | 0.69214 | 0.76053 | 0.84688 | 0.72131 | 0.63097 | 0.61313 | 0.67883 | 0.71288 | 0.72859 | 0.75423 | 0.77734 | 0.79759 | 0.81405 | 0.8267 | 0.83851 | 0 | 0 | 0.87747 | 0 | 0 | 0.91859 | 0 | 0 | 0.94571
short evacuation | 0 | 0 | 0 | 0.11648 | 0.46201 | 0.57614 | 0.631 | 0.65188 | 0.59752 | 0.59771 | 0.65285 | 0.70009 | 0.72253 | 0.74912 | 0.7726 | 0.793 | 0.81024 | 0.82355 | 0.83544 | 0.84621 | 0.85649 | 0.87476 | 0.8916 | 0.90594 | 0.91691 | 0 | 0 | 0

## Slide 31: Comparing the results under several evacuation time
Category 3: ISLOCA (BWR)
Chart: DLTEVA (h)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 8 | 10 | 12 | 16 | 20 | 24 | 30 | 36 | 42 | 48 | 54 | 60 | 66 | 72 | 84 | 96 | 108 | 120 | 132 | 144 | 156
long evacuation | 0.66477 | 0.70454 | 0.84542 | 0.71338 | 0.68703 | 0.70461 | 0.60561 | 0.53754 | 0.53624 | 0.54778 | 0.57734 | 0.59915 | 0.61651 | 0.64156 | 0.66447 | 0.68355 | 0.69549 | 0.707 | 0.71791 | 0.72829 | 0.73824 | 0.75689 | 0 | 0 | 0 | 0 | 0 | 0
normal evacuation | 0.39192 | 0.49036 | 0.64854 | 0.61309 | 0.56001 | 0.57934 | 0.5835 | 0.51448 | 0.51785 | 0.53272 | 0.56381 | 0.58942 | 0.60857 | 0.63367 | 0.65651 | 0.67679 | 0.69104 | 0.70293 | 0.71363 | 0 | 0 | 0.75313 | 0 | 0 | 0.79257 | 0 | 0 | 0.8181
short evacuation | 0.12608 | 0.38312 | 0.41744 | 0.51635 | 0.47636 | 0.47012 | 0.52227 | 0.49128 | 0.5079 | 0.52592 | 0.5579 | 0.58459 | 0.60459 | 0.63016 | 0.653 | 0.67341 | 0.68868 | 0.70092 | 0.71163 | 0.72244 | 0.73248 | 0.75143 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 32: Comparing the results under several evacuation time
Category 4: LBLOCA+PCV fail
Chart: DLTEVA (h)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 8 | 10 | 12 | 16 | 20 | 24 | 30 | 36 | 42 | 48 | 54 | 60 | 66 | 72 | 84 | 96 | 108 | 120 | 132 | 144 | 156
long evacuation | 0 | 0 | 0 | 0 | 0 | 0 | 3.7562e-05 | 0.0041753 | 0.03116 | 0.075008 | 0.13472 | 0.10831 | 0.10168 | 0.10206 | 0.10521 | 0.10807 | 0.11106 | 0.11385 | 0.11603 | 0.11802 | 0.11989 | 0.12304 | 0.12647 | 0.13004 | 0.13303 | 0.13524 | 0.13739 | 0.13983
normal evacuation | 0 | 0 | 0 | 0 | 0 | 0 | 1.7238e-05 | 0.00075506 | 0.0064953 | 0.022 | 0.065138 | 0.091273 | 0.099333 | 0.10173 | 0.10493 | 0.10774 | 0.11076 | 0.1136 | 0.11586 | 0.11784 | 0.11972 | 0.12288 | 0.12631 | 0.12988 | 0.13292 | 0.13512 | 0.1373 | 0.13971
short evacuation | 0 | 0 | 0 | 0 | 0 | 0 | 1.175e-05 | 0.00054429 | 0.0050435 | 0.016711 | 0.055126 | 0.08649 | 0.098284 | 0.10157 | 0.10485 | 0.10761 | 0.11061 | 0.11341 | 0.11577 | 0.11775 | 0.11962 | 0.12279 | 0.12622 | 0.12981 | 0.13285 | 0.13504 | 0.13725 | 0.13966

## Slide 33: MACCS Result (short evacuation time: 1.75h)
The peaks observed when the evacuation time is long become less noticeable.
Excluding ISLOCA, the quicker the evacuation, the fewer the number of people exceed 100mSv

## Slide 34: MACCS Result (normal evacuation time: 3.5h)
The trend is similar to that of a long evacuation.
However, the peaks observed in this case tend to be relatively flat

## Slide 35: MACCS Result (long evacuation time: 7 h)
ISLOCA(PWR): Temporarily SIP reduce population exceed 100 mSv
ATWS, ISLOCA(BWR): Better to evacuate, but if evacuation preparations take too long,
temporarily SIP can reduce the number of people exposed to over 100mSv by waiting out the plume

## Slide 36: ATWS release fraction
fig. 89 S2C-1放出割合
*Release fraction per hour
time after scram (h)
release fraction (-)

## Slide 37: ISLOCA (BWR) release fraction
fig. 92 V-1放出割合
*Release fraction per hour
time after scram (h)
release fraction (-)
*Release fraction from multiple release paths is shown

## Slide 38: ISLOCA(PWR) release fraction
fig. 93 ISLOCA Seq1放出割合
*Release fraction per hour
time after scram (h)
release fraction (-)

## Slide 39: LBLOCA+PCV fail release fraction
fig. 90 AE-1放出割合
*Release fraction per hour
time after scram (h)
release fraction (-)
*Release fraction from multiple release paths is shown

## Slide 40: LBLOCA+FCVS release fraction
fig. 91 AE-6fcfvs放出割合
*Release fraction per hour
time after scram (h)
release fraction (-)