## Slide 1
Risk assessment and Uncertainty Analysis of high-burnup ATF:
MELCOR & MACCS Modeling
Abe Whitmeyer
Kenneth Franzese
Prof. Ben Lindley

## Slide 2
NRC ZION model description
Initial MELCOR 2.0 model provided by NRC
ZION reactor
  Zion, Lake County, Illinois
  Operational 1973 - 1998
Core configuration
  Westinghouse 4-loop PWR
  2 x 3250 MWt units
LBLOCA scenario
  Pressurizer loop break, initiating trip
  LPSI re-activation at 27m
International MACCS User Groups Meeting - 9/13/23
U.S. Department of Energy Flickr photostream, HD.6B.335

## Slide 3
NRC ZION model parameters
International MACCS User Groups Meeting - 9/13/23
Reactor Parameter​ | Units | Value​
Net thermal capacity | MWt | 3250
Net electrical capacity​ | MWe | 1040​
Failure temperature for lower head penetration​ | K | 1273.15​
Heat transfer coefficient from debris to penetration structures​ | W/m2 K ​ | 500
Heat transfer coefficient from debris to lower head. ​ | W/m2 K ​ | 500
Hot leg temperature at steady state​ | K | 603.22​
Cold leg temperature at steady state​ | K | 566.10
Fuel & Materials |  | 
Fuel pin lattice configuration | - | 15x15
Number of fuel assemblies | - | 193
Fuel material | - | UO2
Clad material | - | Zr
Control material | - | B4C

## Slide 4
NRC ZION model scenario
International MACCS User Groups Meeting - 9/13/23
Control Volume​ | Description​
CV320​ | Lower Head​
CV340​ | Reactor Core​
CV350​ | Upper Plenum​
CV570​ | Loop Seal of the main pipe​
CV310​ | Downcomer​
CV330​ | Bypass​
CV500​ | Hot Leg of the main pipe​
CV580​ | Cold Leg of the Main Pipe​
Manual control
-200.0s Calculation begins
- 0.0s LBLOCA initiation
- 27.0s LPSI recovery
6h Calculation termination
MELCOR conditional
0.0s Reactor trip
? LPSI: injection ends, re- circulation mode begins
? Fuel melting, gap release

## Slide 5
FCA definition in MELCOR
15x15 → 17x17 fuel lattice
  Flow areas, component masses
Material properties
  Kanthal APMT & “Ironclad” C26M
  Thermophysical properties
  Molten material data
Oxidation behavior
  Parabolic rate equation
  Individual element specification
  Include temperature ranges for breakaway oxidation
International MACCS User Groups Meeting - 9/13/23
Growth of alumina layer on the surface of C26M and APMT exposed to air and steam at 1200°C for 4 h:
(a) & (b) APMT air & steam; (c) & (d) C26M air steam [1]

## Slide 6
MACCS Procedure
RN inventory initially calculated using SCALE for single assembly to core average burnup
Data transferred to MELCOR input with explicit RN definitions as well as specified in MACCS inventory file
Currently using 18 month burnup, with plans to investigate 24 month burnup with larger RN inventories
International MACCS User Groups Meeting - 9/13/23
Notes: MACCS (the Melcor Accident Consequence Code System) is used to calculate consequence probabilities for radionuclide release in a nuclear plant accident.
Inputs:
-Inventory of relevant radionuclides in the core at the time of the accident
-Release paths in MELCOR become plume segments in MACCS that are released at a set time and location for a set duration, with a calculated sensible heat and radionuclide content
-Weather data includes wind direction and magnitude as well as rainfall intensity. It should be characteristic of the given site
-Population data is constructed from census data and overlaid on a polar-coordinate grid surrounding the reactor that can extend up to 500 miles
-Land usage data for the region around the reactor is user-specified; it includes fractions of habitable land and farmland as well as the economic worth of the land, crops and buildings
-Users make assumptions about the short-term emergency response including delay to when officials are warned of the accident, delay to evacuation start, evacuation area, average evacuation speed and distance, and sheltering and relocation data; there are also long-term protective measures such as decontamination, relocation, and agricultural condemnation that are user-specified.
Outputs:
-MACCS models the movement of the release plumes
-MACCS estimates the short- and long-term radiation doses from cloudshine, groundshine, plume inhalation, inhalation of resuspended particles and ingestion of irradiated food
-MACCS estimates how those doses can be reduced by the aforementioned emergency response actions
-MACCS will also calculate how much those mitigation actions cost
-MACCS estimates how many people will be injured or die in the short term (<1 year), as well as the number of cancer fatalities and injuries throughout the lifetime of exposed individuals
MACCS users interact with the system through the WinMACCS interface (WinMACCS as in MACCS for windows). Users input files and select model settings through WinMACCS which are then carried out in MACCS.
WinMACCS also interacts with MACCS’ preprocessors: COMIDA2 “evaluates parameters affecting the food ingestion pathway;” PopMod alters the number of sectors in the MACCS site file (not to be confused with SecPop, which generates the site files); Combine Source handles the case of multiple release sources, combining them into a set of plume release segments. LHS (Latin Hypercube Sampling) is used when the user chooses to run a set of simulations to “evaluate uncertainty from input parameters represented by probability distributions to reflect degree of belief.”
MACCS is really three code systems in one. The ATMOS module handles the release and movement of the accident plume. The EARLY module deals with evacuation and short-term health consequences. CHRONC is for long-term health effects and mitigation actions.

## Slide 7
Inputs
Core inventory
Plume release information
Meteorological data
Population distribution
Land usage
Emergency response
International MACCS User Groups Meeting - 9/13/23
Outputs
Plume transport, dispersion and deposition
Radiation doses
Effect of mitigation actions
Mitigation action costs
Fatalities and injuries
MACCS Procedure
Notes: MACCS (the Melcor Accident Consequence Code System) is used to calculate consequence probabilities for radionuclide release in a nuclear plant accident.
Inputs:
-Inventory of relevant radionuclides in the core at the time of the accident
-Release paths in MELCOR become plume segments in MACCS that are released at a set time and location for a set duration, with a calculated sensible heat and radionuclide content
-Weather data includes wind direction and magnitude as well as rainfall intensity. It should be characteristic of the given site
-Population data is constructed from census data and overlaid on a polar-coordinate grid surrounding the reactor that can extend up to 500 miles
-Land usage data for the region around the reactor is user-specified; it includes fractions of habitable land and farmland as well as the economic worth of the land, crops and buildings
-Users make assumptions about the short-term emergency response including delay to when officials are warned of the accident, delay to evacuation start, evacuation area, average evacuation speed and distance, and sheltering and relocation data; there are also long-term protective measures such as decontamination, relocation, and agricultural condemnation that are user-specified.
Outputs:
-MACCS models the movement of the release plumes
-MACCS estimates the short- and long-term radiation doses from cloudshine, groundshine, plume inhalation, inhalation of resuspended particles and ingestion of irradiated food
-MACCS estimates how those doses can be reduced by the aforementioned emergency response actions
-MACCS will also calculate how much those mitigation actions cost
-MACCS estimates how many people will be injured or die in the short term (<1 year), as well as the number of cancer fatalities and injuries throughout the lifetime of exposed individuals
MACCS users interact with the system through the WinMACCS interface (WinMACCS as in MACCS for windows). Users input files and select model settings through WinMACCS which are then carried out in MACCS.
WinMACCS also interacts with MACCS’ preprocessors: COMIDA2 “evaluates parameters affecting the food ingestion pathway;” PopMod alters the number of sectors in the MACCS site file (not to be confused with SecPop, which generates the site files); Combine Source handles the case of multiple release sources, combining them into a set of plume release segments. LHS (Latin Hypercube Sampling) is used when the user chooses to run a set of simulations to “evaluate uncertainty from input parameters represented by probability distributions to reflect degree of belief.”
MACCS is really three code systems in one. The ATMOS module handles the release and movement of the accident plume. The EARLY module deals with evacuation and short-term health consequences. CHRONC is for long-term health effects and mitigation actions.

## Slide 8
Sensitivity Analysis
Sensitivities
Gap Fractions
  How much Cs and Xe released affect population dosages?
Oxidation parameters
  Parabolic rate equation coefficients
  Temperature ranges
International MACCS User Groups Meeting - 9/13/23
Post-test images of low-Cr FCA (top) and APMT FCA (bottom) in air and steam [3]

## Slide 9
Sensitivity Parameters
Input space runs from ±2 standard deviations
Monte Carlo used to generate 60 cases via RAVEN
Additional checks performed to verify completed set's parameters align with initial specifications
International MACCS User Groups Meeting - 9/13/23
Parameter​​ | Mean​​ | Standard Deviation ​​
Oxidation Start Temperature (K)​​ | 1323​​ | 33​​
Breakaway Oxidation Start Temperature (K)​​ | 1748​​ | 25​
Rod Burst Temperature (K)​​ | 1173​​ | 58.65​
CsI Gap Fraction​​ | .05​​ | .0125​​
Xe Gap Fraction​​ | .05​​ | .0125​​

## Slide 10
MELCOR: Fission Product Release
International MACCS User Groups Meeting - 9/13/23

## Slide 11
MELCOR: Average RN Released by Major Class
International MACCS User Groups Meeting - 9/13/23

## Slide 12
MACCS: Fatalities
International MACCS User Groups Meeting - 9/13/23

## Slide 13
MACCS: Peak Dose
International MACCS User Groups Meeting - 9/13/23

## Slide 15
References
International MACCS User Groups Meeting - 9/13/23
[1] | Rebak, R.B., Gupta, V.K. and Larsen, M., 2018. Oxidation characteristics of two FeCrAl alloys in air and steam from 800° C to 1300° C. Jom, 70(8), pp.1484-1492.
[2] | Gauntt, R.O., Cole, R.K., Erickson, C.M., Gido, R.G., Gasser, R.D., Rodriguez, S.B. and Young, M.F., 2000. MELCOR computer code manuals. Sandia National Laboratories, NUREG/CR, 6119.
[3] | Pint, Bruce A. "Performance of FeCrAl for accident-tolerant fuel cladding in high-temperature steam." Corrosion Reviews 35.3 (2017): 167-175.