## Slide 1: Using NCEP Data to Support Severe Accident Consequence Analysis at Locations without Onsite Meteorological Data
International MACCS User’s Group
September 11-14, 2023
Elena Yegorova1, Daniel Clayton2, Keith Compton1, Amy Sharp1
1US Nuclear Regulatory Commission, Washington, DC, USA
2Sandia National Laboratories, Albuquerque, NM, USA

## Slide 2: Background
HYSPLIT/MACCS Atmospheric Dispersion Model Technical Documentation and Benchmark Analysis – Published April, 2022
  The nuclear accident consequence analysis code MACCS has traditionally modeled dispersion during downwind transport using a Gaussian plume segment model.
  HYSPLIT/MACCS coupling has been implemented, with HYSPLIT as an alternative ATD option.
  MACCS uses the HYSPLIT-generated air concentration, and ground deposition values to calculate the same range of output quantities (dose, health effects, risks, etc.) that can be generated when using the MACCS Gaussian ATD model.
HYSPLIT/MACCS Atmospheric Dispersion Model Technical Documentation and Benchmark Analysis – Published April, 2022

## Slide 3: Background
Recent modifications to the MACCS modeling system have opened the possibility of using regional three-dimensional meteorological fields developed from the National Center for Environmental Prediction (NCEP) for severe accident consequence analysis.

## Slide 4: Future Focused Research
“Use of National Centers for Environmental Prediction (NCEP) Data to Support Severe Accident Consequence Analysis at Locations without Onsite Meteorological Data”:
  With the anticipated future deployment of advanced nuclear technologies, it becomes essential to assess the potential range of severe accident consequences for locations where onsite meteorological data is not currently available.
  The objective of this project is to assess the feasibility of applying NCEP reanalysis weather data at locations without meteorological tower data to perform consequence analysis.
  Understanding how the probabilistic consequences estimated using atmospheric reanalysis data compare to those using site meteorological tower data may lead to more flexibility in performing these calculations for future situations that require special techniques.
“Use of National Centers for Environmental Prediction (NCEP) Data to Support Severe Accident Consequence Analysis at Locations without Onsite Meteorological Data”

## Slide 5: Project Tasks
Compilation of a list of potential sources of publicly available hourly site meteorological data (environmental reports, National Weather Service (NWS) stations, etc.) and examine to determine if meteorological data are sufficient to develop a MACCS-formatted weather file.
Compilation of a list of numerical weather reanalysis products
Selection of case studies representative of various meteorological regimes.
Selection of a subset of publicly available hourly site meteorological datasets and development of MACCS weather files for those datasets.
Task 1
Task 2

## Slide 6: Project Tasks
Use the MACMETGEN utility to generate synthetic MACCS weather files for the same site/year combinations using selected observational datasets as determined in Task 2.
Run MACCS to generate complementary cumulative distribution functions for peak time-integrated, air concentration (Chi/Q) and area under a deposition isopleth at a range of distances (e.g., 100m, 500m, 1 km, 10 km, 50 km).
Compare the results from the observational data and the numerical reanalysis data to determine the potential error induced by using reanalysis data in place of in situ data.
Task 3
Task 4
Task 5

## Slide 7: Case Studies
Identifier | Description
A | Large river valley
B | Central midwestern plain
C | Alaska coastal site with orography
D | U.S. Gulf Coast with a potential for sea breezes

## Slide 8: Meteorological Observations
MACCS file format requirements:
  Meteorological data at one-hour intervals that include day, time, surface wind direction, wind speed, stability class, and precipitation rate, and mixing height (optional).
Meteorological Data Sources:
Federally Managed Weather Networks
  NWS – National Weather Service Network of Meteorological Towers – report temperature, humidity, wind speed and direction, atmospheric pressure, precipitation, solar radiation - https://www.weather.gov/
  ASOS/AWOS – Automated Surface/Weather Observing Systems at airports - Stations include sensors to measure wind speed and direction, dew point, air temperature, and station pressure. The vast majority also measure precipitation type and amount, visibility, and cloud height and thickness. https://www.ncei.noaa.gov/products/land-based-station/automated-surface-weather-observing-systems
Notes: Remote Automated Weather Stations (RAWS) are a network of automated weather stations run by the U.S. Forest Service (USFS) and Bureau of Land Management (BLM). They are used to monitor potential wildfire conditions.

## Slide 9: Meteorological Observations
RAWS – US Federal Interagency Remote Automatic Weather Stations https://weather.nifc.gov/ (~3,000 stations, used to monitor wildfire conditions, operated by US Forest Service and Bureau of Land Management) – report wind speed and direction, air temperature, precipitation, relative humidity, solar radiation and fuel moisture.
SNOTEL – Snow Telemetry Network- ~900 sites in remote mountainous sites. Monitor snowpack, precipitation, temperature, etc. https://www.nrcs.usda.gov/wps/portal/wcc/home/aboutUs/monitoringPrograms/automatedSnowMonitoring/
Notes: AWOS stations report weather information every minute and are operated by the Federal Aviation Administration (FAA)
ASOS stations are more advanced than AWOS stations and are typically operated by the National Weather Service (NWS)
Stations include sensors to measure wind speed and direction, dew point, air temperature, and station pressure. The vast majority also measure precipitation type and amount, visibility, and cloud height and thickness.

## Slide 10: What is Numerical Reanalysis?
Reanalysis is a scientific method that combines observations with a numerical model to create a record of how weather and climate have changed over time. Reanalysis data are a blend of observations and past short-range weather forecasts that are rerun with modern weather forecasting models.

## Slide 11: Numerical Reanalysis Datasets
North American Mesoscale Forecast System (NAM12)
  2010 – Present; 12 km resolution; CONUS, Alaska
  One of the National Centers For Environmental Prediction’s (NCEP) major models for producing weather forecasts. NAM generates multiple grids (or domains) of weather forecasts over the North American continent at various horizontal resolutions. Each grid contains data for dozens of weather parameters, including temperature, precipitation, lightning, and turbulent kinetic energy.

## Slide 12: Numerical Reanalysis Datasets
High-Resolution Rapid Refresh (HRRR)
  2019 – present; 3 km resolution; CONUS
  NOAA real-time 3-km resolution, hourly updated, cloud-resolving, convection-allowing atmospheric model, initialized by 3km grids with 3km radar assimilation. Radar data is assimilated in the HRRR every 15 min over a 1-h period adding further detail to that provided by the hourly data assimilation from the 13 km radar-enhanced Rapid Refresh Product.

## Slide 13: Numerical Reanalysis Datasets
Weather Research and Forecasting Reanalysis (WRF27)
1980 – present; 27 km resolution; CONUS
Created using the Weather Research and Forecasting (WRF) model (Skamarock et al., 2008), using the North American Regional Reanalysis (NARR) data set as initial conditions, and nudged by the observational data from the National Centers for Environmental Prediction (NCEP) Automated Data Processing (ADP) global surface data sets. Model output for each hour is converted to a 27-km Lambert conformal grid centered over North America (216 x 174 cells). Data at 34 sigma levels (vertical) are included for six variables: pressure, temperature, u, v, and w wind velocities, and relative humidity.
Notes: This meteorological data set can only capture complex meteorological behavior (e.g., land/sea breeze, valley flows, etc.) at length scales around 27 km or greater.

## Slide 14: MacMetGen Utility
The input reanalysis meteorological data used by MacMetGen are the same as those used by HYSPLIT (available at NOAA ARL ftp site).
The MACCS parameters define the period for the entries, number of sectors used in the discretization of wind direction, and method to determine stability class used to create the MACCS-formatted meteorological file.
Notes: MacMetGen - MACCS-formatted meteorological file generator. MacMetGen ensures consistency between the meteorological information used in HYSPLIT and MACCS.
MACCS uses a formatted meteorological file that contains data for wind speed, wind direction, stability class, and precipitation rate for each hour of a year at the release location. This is one of the inputs to MACCS shown in Figure 2-1 and Figure 2-5. Typically, this formatted meteorological file is generated from observational meteorological data at a site.
The MACCS parameters define the period for the entries, number of sectors used in the discretization of wind direction, and method to determine stability class used to create the MACCS-formatted meteorological file. The extracted wind speeds, precipitation rates, and stability classes in the MACCS-formatted meteorological file are then used in MACCS in the weather binning
algorithm with the weather bin sampling options. The calculated stability class is also used in MACCS to determine the plume rise for each plume segment.

## Slide 15: Summary
Understanding how the probabilistic consequences estimated using publicly available and synthetic data compare to those using site meteorological tower data may lead to more agility and flexibility in performing these calculations for future situations that requirement special techniques.
The time horizon for deploying small modular and micro-reactors varies with some projections starting in the next ten years. However, while the results of this study may be applied to analyses of specific new reactor designs, they may also inform severe accident analyses undertaken in the future related to generic requirements.

## Slide 16: Questions Contact: Elena.Yegorova@nrc.gov