## Slide 1: NRCDose3
Jon Napier, PhD
Health Physicist, CHP
PNNL-SA-204581

## Slide 2: Topics
NRCDose3 Overview
Overview of Features
XOQDOQ Modeling and Use/Screens
GASPAR Modeling and Use/Screens
LADTAP Modeling and Use/Screens
NRCDose3 Code Planning Discussions

## Slide 3: NRCDose3 Overview

## Slide 4: Purpose of Code
NRC Licensing Evaluation:
Exposure pathway dose modeling, primarily for reactors to demonstrate compliance with:
  10 CFR Part 20
  Appendix I to 10 CFR Part 50
  40 CFR Part 190
With expanded source term applicable to other fuel cycle facilities
Not suitable for short term releases; accident dose assessment

## Slide 5: NRC Guidance
NRC guidance on reactor effluent dose calculations is contained in:
  RG 1.109, Calculation of Annual Doses to Man from Routine Releases of Reactor Effluents for the Purpose of Evaluating Compliance with 10 CFR Part 50, Appendix I
  RG 1.111, Methods of Estimating Atmospheric Transport and Dispersion of Gaseous Effluents in Routine Releases from Light Water Cooled Reactors
  RG 1.113, Estimating Aquatic Dispersion of Effluents from Accidental and Routine Reactor Releases for the Purposes of Implementing Appendix I

## Slide 6: FORTRAN Codes

## Slide 7: XOQDOQ
Evaluation of transport, diffusion, and deposition of airborne radiological effluents
Routine releases
Intermittent releases
Non-emergency
Calculates atmospheric dispersion factors (χ/Q) and deposition factors (D/Q)
Predefined segmented distances by compass sectors out to 50 miles
User defined points of interest

## Slide 8: XOQDOQ
Straight-line trajectory Gaussian plume model. Considers:
  Dry deposition
  Radioactive decay
  Plume recirculation (stagnation)
Calculates effective plume height
  Physical release height
  Aerodynamic downwash
  Plume rise
  Terrain features

## Slide 9: GASPAR II
Estimates airborne effluent doses
  Routine
  Non-emergency
  Individuals or populations
Requires:
  Source term released (Ci/yr)
  Atmospheric dispersion (XOQDOQ)
  Demographics

## Slide 10: GASPAR II
Internal Exposure Pathways
  Inhalation (of plume)
  Ingestion of contaminated food
    leafy vegetables
    vegetables and grains
    meat
    milk
External Exposure Pathways
  Plume
  Ground Plane

## Slide 11: LADTAP II
Estimates liquid effluent doses
  Routine
  Non-emergency
  Individuals, populations or biota
Hydrologic model represents mixing in the effluent impoundment system and surface waters

## Slide 12: LADTAP II
Internal Exposure Pathways:
  Drinking water (freshwater site)
  Fish
  Invertebrates
  Aquatic plants
  Irrigated crops
External Exposure Pathways:
  Shoreline
  Boating
  Swimming

## Slide 13: GASPAR II and LADTAP II
ICRP-2 DCFs (1950s)
Four (4) Age Groups:
  Infant
  Child
  Teen
  Adults
Seven (7) Organs
  Total Body
  Bone
  Liver
  Thyroid
  Kidneys
  Lungs
  GI-LLI

## Slide 14: NRC and Industry End Uses
NRC licensing reviews
  Design Certification, Combined License, and Early Site Permit Applications
  License Amendment Requests
NRC health physics reactor inspections
  Independent assessment of potential doses from effluent releases
  Independent assessment of ODCM dose conversion factors and effluent dose calculations

## Slide 15: NRC and Industry End Uses
Calculate doses at locations of interest
Evaluate Land Use Census
  Public interest
Annual dose assessments
  Actual receiving water body flows and dilutions
  Meteorology with effluents for evaluated year
ODCM dose conversion factors

## Slide 16: Why Update to NRCDose3
Updates the NRCDose 2.3.20 (CCC-684) code
Significant increase in flexibility and functionality
Need for a licensing tool to support reactor application submittals
Provides an acceptable method for evaluating exposure pathway doses from reactor effluents
Improves efficiency in reactor licensing process, and NRC safety and environmental reviews

## Slide 17: Overview of Updates
Improved functionality
  Updated Windows interface
Option to select ICRP-2, ICRP-30, or ICRP-72 Dose Conversion Factors (DCFs)
  Age range
  Organs
Expanded license application ready reports
User-modifiable parameter values
  Bioaccumulation factors
  Consumption rates
  Usage factors
  Other parameters
Previous versions of NRCDose (and FORTRAN codes) did not allow for edits to parameters

## Slide 18: Updates – DCFs
Expanded ICRP-2 DCFs
ICRP-30 DCFs
ICRP-72 DCFs
Ingestion DCFs: Gastrointestinal Absorption Fractions (f1)
Inhalation DCFs: Lung Clearance Classes for Chemical Compounds
  ICRP-30: D/W/Y
  ICRP-72: F/M/S

## Slide 19: Updates – Biota Dose
Biota dose added to GASPAR and expanded in LADTAP
Biota dose calculated at all user defined special location (GASPAR)
Biota dose based on species mass, effective radius, primary food eaten (produce or meat) and consumption rate
LADTAP
  Algae
  Muskrat
  Racoon
  Duck
  Heron
  User defined
GASPAR
  Same as LADTAP plus
  Cow (herbivore)
  Fox (carnivore)
  User defined

## Slide 20: Documentation and Release
NRCDose3 Quick Start Guide
  How to install, run, and view output
DRAFT NUREG on NRCDose3 Code: User Guide and Technical Manual
  Technical basis
Distribution by NRC RAMP

## Slide 21: Overview of Features and Enhancements

## Slide 22: Installation and Operation
Double-click NRCDose3_v114_Setup.exe
Follow prompts
NRCDose3 will install in C:\directory (unless changed by the user)

## Slide 23: Installation and Operation

## Slide 24: File Structure
When a code is opened, it will be loaded with the last case file from the database
When first opened, an example case file will be pre-loaded
If a different case is desired, select File->Open LN3 File from the menu to load a saved case
Or “Open GN3 File” or “Open XN3 File” as applicable
When saving a case, it will be saved to the database as well as a case file (.xn3, .gn3, .ln3 file type, as applicable)

## Slide 25: Hard-Coded Parameters
Previous versions of codes had many hard-coded parameters that are now user-editable
Editing may be appropriate for site-specific conditions

## Slide 26: XOQDOQ Expanded Editable Parameters
Building wake constant
  Though not recommended without a sound technical bases
Essentially all other key modeling parameters (input values to the meteorological model) were already user defined or user controlled

## Slide 27: LADTAP Expanded Editable Parameters
Population age group fractions
Food and water consumption rates
Bioaccumulation and transfer factors
Various environmental exposure times and vegetable production and storage times

## Slide 28: GASPAR Expanded Editable Parameters
Population age group fractions
Human consumption and inhalation rates
Bioaccumulation factors
Various environmental times, vegetable production, and storage times
Meat and milk animal consumption rates

## Slide 29: Dose Conversion Factors
Expanded ICRP-2 DCFs from:
  RG 1.109, Revision 1, Calculation of Annual Doses to Man From Routine Releases of Reactor Effluents for the Purpose of Evaluating Compliance with 10 CFR Part 50, Appendix I (October 1977)
  NUREG-0172, Age Specific Radiation Dose Commitment Factors for One-Year Chronic Intake (November 1977)
  NUREG-0172, Errata (August 1983)
  NUREG/CR-2384, Age Specific Inhalation Radiation Dose Commitment Factors for Selected Radionuclides (August 1982)
  EMP-155, Review and Expansion of USNRC Regulatory Guide 1.109 Models for Computing Dose Conversion Factors (February 1983)

## Slide 30: DCFs
Some radionuclides in those sources were not included in LADTAP II/GASPAR II
NRCDose3 includes
  203 radionuclides
  ICRP-2 DCFs for ALL radionuclides
  ICRP-30 DCFs for ALL radionuclides
  ICRP-60/72 DCFs for ALL radionuclides

## Slide 31: Additional Radionuclides

## Slide 32: DCFs
NRCDose3 allows only one chemical form, inhalation class or ingestion class for each radionuclide
Multiple ingestion DCFs based on f1 value
Multiple inhalation DCFs based on inhalation class
  D/W/Y for ICRP-30
  F/M/S for ICRP-72
Nuclear power plant effluents are assumed to be oxides; other fuel cycle facilities may have different states

## Slide 33: Age and Organs
ICRP-30
  Adult Only
    Occupational DCFs
ICRP-72
  Adult
  15 year old
  10 year old
  5 year old
  1 year old
  Newborn
ICRP-30
  24 Organs, including remainder
ICRP-72
  27 Organs, including remainder
    Colon, ETA, skin(ext)

## Slide 34: XOQDOQ Modeling and Use

## Slide 35: XOQDOQ – Atmospheric Transport and Dispersion
Implements the straight-line Gaussian modeling of RG 1.111
Calculates ground-level concentrations
Accounts release points characteristics (height, plume rise)
Additional plume dispersion due to building wakes
Plume depletion via dry deposition and radioactive decay

## Slide 36: XOQDOQ – Atmospheric Transport and Dispersion
Annual average relative dispersion (χ/Q) and deposition (D/Q) values at user specified locations (MEI doses) and standard radial distances and segments (population doses) for routine releases
Intermittent releases (e.g., containment purge, waste gas tank)
Elevated, ground level, or mixed mode releases
Meteorological modeling considerations: building wake effects, plume depletion (dry deposition), and radioactive decay

## Slide 37: XOQDOQ – Atmospheric Transport and Dispersion
Wind direction in 16 compass directions (22.5 sectors), 14 wind speed classes, and 7 atmospheric stability classes (A-G)
Three different dispersion χ/Q values; one deposition D/Q value
  Undecayed, Undepleted χ/Q
  Decayed, Undepleted χ/Q (2.26-day half-life)
  Decayed, Depleted χ/Q (8-day half-life)
  Deposition D/Q (2.26-day and 8-day half-lives)
Output used as meteorological data input to GASPAR

## Slide 38: Basic Meteorology Dispersion – χ/Q

## Slide 39: Basic Meteorology Dispersion – χ/Q

## Slide 40: Gaussian Model – Sector Average
Dividing the area surrounding a point source into 16 segments gives 360°/16 = 22.5° per segment
For averaging condition (over time), the plume is assumed to meander, spreading uniformly over the 22.5° sector

## Slide 41: Starting and Running XOQDOQ
Double click “XOQDOQ”

## Slide 42: XOQDOQ – Atmospheric Transport and Dispersion
XOQDOQ Module Main Screen opens with case data that is saved in the database
Contains three main functional areas:
  toolbar and initial setup area,
  data input tabs
  code execution and reports

## Slide 43: XOQDOQ – File Management
New ─ New XOQDOQ case. Clears the databases.
Open XN3 File ─ open an existing “*.XN3” file previously created with NRCDose3
Open Legacy Input File ─ Opens Windows Explorer; navigate to “*.dat” file
  Uses a file created with the original XOQDOQ
  “Create input” not needed; select run XOQDOQ. Input screens and options cannot be used

## Slide 44: XOQDOQ – File Management
Save to Database ─ Choose this option to save current case to the database. When XOQDOQ is opened with “Current Project” selected, the information in the database, as last saved before exiting, initially populates all XOQDOQ screens and windows.
Save to XN3 File ─ Choose this option to save the completed case to a “*.XN3” file
Delete ─ Choose this option to open an explorer window that will allow the user to delete any previously saved “*.XN3” files

## Slide 45: XOQDOQ Main Screen – Options
Various options
  Purge calc (short term releases) printout compares sector spread to centerline values
  Printout plot of short-term X/Q values (not very useful)
  Open terrain recirculation: correction is applied uniformly to all directional sectors out to 10 km (NUREG/CR-2919, Figure 3.2)
  Use site-specific terrain recirc values (user input under Parameters)
  Desert sigma curves (specialized dispersion values developed for desert environment)

## Slide 46: XOQDOQ Options/Parameters

## Slide 47: XOQDOQ Main Screen - Parameters

## Slide 48: XOQDOQ Main Screen - Parameters

## Slide 49: Met Data Input
Calms
Met data: hours or % frequency
Height of measurement
Plant grade
Half-lives (do not change)
Inputting joint frequency distribution (JFDs)
  Line-by-line entering for each Stability Class

## Slide 50: Windspeed Input
Enter the “Number of velocity categories” (maximum 13), and then select “Max Wind Speeds…” to enter the maximum wind speed of each category

## Slide 51: Import Met Data
Met data (JFD) can be imported using 2 standard file formats
  MetQA: file format generated by an internal (NRC) application MetQA (Version 2.0), which represents the NRC staff’s implementation of NUREG-0917
  EXCEL: specific data array by wind direction, wind speed range, and atmospheric stability classes ranging, in sequence, from extremely unstable (Class A) thru extremely stable (Class G)

## Slide 52: Import Met Data – Example File Format

## Slide 53: XOQDOQ – Save, Create Input, Run
Save to save the dataset to any file name as being used.
Create Input to create the dataset in the format required by the FORTRAN code
View Input to view created input file
Run XOQDOQ

## Slide 54: View Input
Shows the input deck as used by the FORTRAN code
Follows the card format as described in NUREG/CR-2919

## Slide 55: Windspeed Input
A meteorological dataset suitable for import by GASPAR can be created
  Select Create Alternate X/Q and D/Q Input
Pop-up screen to select up to 5 locations
An input file will be created internal which may be referenced during the GASPAR run
Only applicable to XOQDOQ for single release point runs

## Slide 56: GASPAR Modeling and Use

## Slide 57: GASPAR
Performs dose assessments for gaseous radioactive effluents released into the atmosphere
Implements dose assessment methods described in RG 1.109
Calculates the radiation dose to individuals, population groups, and biota from:
  inhalation of contaminated air,
  direct exposure from contaminated ground, and
  consumption of contaminated foods
Basic calculation methods are described in NUREG/CR-4653

## Slide 58: GASPAR
Calculated doses support
  NEPA evaluations
  Compliance with the NRC public dose limits in 10 CFR Part 20
  EPA public dose limits in 40 CFR Part 190
  NRC ALARA design objectives and numerical guides in 10 CFR Part 50, Appendix I

## Slide 59: Starting and Running GASPAR
Double click “GASPAR”

## Slide 60: GASPAR Main Screen
Contains three main functional areas:
  the toolbar and initial setup area,
  data input tabs area and
  code execution and reports area
NOTE: GASPAR opens with the last saved database

## Slide 61: GASPAR Start-up
New ─ Select this option to begin a new GASPAR case. This will clear the database from any previously input information.
Open GN3 File ─ Select this option to access and open a “*.GN3” file that was previously created with NRCDose3.
Save to Database ─ Choose this option to save the current case to the database. When GASPAR starts, it loads the data that was last saved (typically from the last, previous run), populating all GASPAR screens and windows.
Save to GN3 File ─ Choose this option to save the completed case to a “*.GN3” file. This allows the file to be saved for later use, or for sharing with others.
Delete ─ Choose this option to open an explorer window that will allow the user to delete any previously saved “*.GN3” files.

## Slide 62: GASPAR Main Screen
Enter a Case Title
Select dose factors:
  ICRP-2 (Default)
  ICRP-30
  ICRP-72
Option for individual doses only
Printing cumulative or detailed reports
Printing dose factor library
PARTS calculations (dose conversion factors for site-specific modeling; used in ODCM)
NOTE: Changing DCFs will re-initialize the source term

## Slide 63: GASPAR Main Screen
Seven data input tabs:
  Options
  Source Term
  Pop/Prod Data
  Special Locations
  Dose Factors
  Pathway Factors
  Consumption Values

## Slide 64: GASPAR Options
Input site-specific for pathway modeling assumptions

## Slide 65: GASPAR - Biota
Modeling based on BNWL-1754 (same as LADTAP)
Six (6) biota types automatically included
  muskrat, racoon, duck, heron, cow, and fox
Option for user defined biota
  Food type (limited to either herbivore or carnivore)

## Slide 66: GASPAR – Source Term
Title
Source term multiplication
Add, delete or clear options
NOTE: Only a single source term may be used for each case

## Slide 67: GASPAR – Source Term
Select: Add Nuclide
  Pop-up menus with nuclide list
  Highlight desired nuclide; use ”control” key to select multiple nuclides
Selecting Add will add them to list
Delete Nuclide will delete selected nuclide
Clear will clear all nuclides in the source term

## Slide 68: GASPAR – ICRP-30 and ICRP-72 DCFs
ICRP-30 and ICRP-72 DCFs, select the applicable solubility (f1) or lung clearance type (F, M, S) for each radionuclide
NOTE: Only one solubility or inhalation class allowed per radionuclide

## Slide 69: GASPAR – Population/Production Data
Used for population dose calculations only
Dropdown menu for data type
  Population
  Milk
  Meat
  Vegetable
  Meteorology
Except for meteorology, 50 mile data may be entered rather than sector segmented data

## Slide 70: GASPAR – Population/Production Data
Applies for population, milk, meat, and vegetable production
Input population or production data by meteorological sector and distance (data typically found in applicant’s Safety Analysis Report or Environmental Report)

## Slide 71: GASPAR – Special Location Data
Select Add to add new location (will clear fields)
  Identified the location where individual doses will be calculated
Location data
  Name
  Distance/Direction (information use only)
Atmospheric dispersion factors
Detailed Reports
Save

## Slide 72: GASPAR – Dose Factors – Nuclide Data
Dropdown menu for displaying dose factors
  Inhalation
  Ingestion
  By age group
Values for the Dose Factors being used (mrem per pCi, inhaled or ingested)
  ICRP-2
  ICRP-30
  ICRP-72
NOTE: Dose factor data is not editable

## Slide 73: GASPAR – Dose Factors – Nuclide Data
Nuclide decay data
External dose factors
Absorbed Energies
  For biota calculations
  Effective radii
  Units (MeV/Bq s)
NOTE: Dose factor data is not editable

## Slide 74: GASPAR – Dose Factors Submersion
Submersion (semi-infinite plume) dose factors for noble gases
  (mrad or mrem per year per pCi/m3)
NOTE: GASPAR calculates airborne submersion dose only from noble gas

## Slide 75: GASPAR – Special Location Data
Default values included for various environmental pathway modeling parameters
Goat milk transfer factors
Hold-up and Transport Times
Physical parameters
Option to reset to default values

## Slide 76: GASPAR – Dose Factors Submersion
By element
  Feed-to-meat (cow, day/kg)
  Soil-to-vegetation
  Grass-to-milk (cow, day/liter)
Can be edited to address site-characteristic data
Tab to reset to Default values
Save – any changed

## Slide 77: GASPAR – Consumption Values
U.S. (country) population
  Artifact of FORTRAN code; required input but not used
Population fractions
Maximum and average individual consumption values; by age group
Get Defaults to reset
Save changes

## Slide 78: Running GASPAR – Outputs/Reports
Can be Saved and Run from any screen
  Save
  Create Input
  View Input
  Run GASPAR
  View Output
  FSAR Report
  Supplemental Report

## Slide 79: Running GASPAR – Input
Input follows the format of the “card deck” as described in NUREG/CR-4653
The datasets reflect modeling under the “Pathway factors” tab, such as transfer factors, exposure and transfer assumptions
The bottom section is the standard format for GASPAR input (individual doses only), containing the Selections inputs, source term, Special Location assumptions
If population doses performed, would also include the population, production and meteorological data

## Slide 80: Running GASPAR – Output
Basic assumptions used for calculations
Lists the Source Term
Followed by Doses
  Population (if performed)
  Individual by Special Locations
If selected “Print Dose Factor Library,” output will include all nuclides

## Slide 81: Running GASPAR – Output
Provides a summary report of assumptions and doses
Suitable for use in creating input for safety analyses and licensing support

## Slide 82: GASPAR – Supplemental Report
Provides additional information that may not be included in the GASPAR output or the FSAR Report

## Slide 83: LADTAP Modeling and Use

## Slide 84: LADTAP Dose Modeling
Routine liquid effluent releases – not for short-term accident
Modeling assumes annual average conditions
  Average dispersion in receiving water body
  Average radioactive effluents over time
RG 1.109, Calculation of Annual Doses to Man from Routine Releases of Reactor Effluents for the Purpose of Evaluating Compliance with 10 CFR Part 50, Appendix I, Rev. 1, October 1977

## Slide 85: LADTAP Dose Modeling
Exposure pathways to maximum exposed individual and to population:
  Potable water (downstream supply),
  Aquatic foods (fresh and saltwater water fish, invertebrate (crustacea and shellfish), and aquatic plants (seaweed)
  Shoreline deposits (build-up to mid-point of plant life (assumed 40-year life)
  Swimming and boating from direct exposure,
  Irrigated foods, and
  Non-human biota (7 surrogate species)

## Slide 86: LADTAP Dose Modeling
Models from RG 1.113:
  Plug-Flow Model - uniform, constant flow through pond; negligible evaporation
  Partially Mixed Model - applicable where blowdown and plant pumping significant
  Completely Mixed Model - estimates effluent concentration at midpoint of plant life
Refer to NUREG/CR-4013, Section 3.1.1 for more detail

## Slide 87: LADTAP Dose Modeling
Figure 3.2 from NUREG-4013, LADTAP II - Technical Reference and User Guide

## Slide 88: Starting and Running LADTAP
Double click “LADTAP”

## Slide 89: LADTAP Main Screen
LADTAP opens with data saved in the database
Contains three main functional areas:
  the toolbar and initial setup area,
  data input tabs area and
  code execution and reports area

## Slide 90: LADTAP Start-up
New ─ Select this option to begin a new LADTAP case. This will clear the database from any previously input information.
Open LN3 File ─ Select this option to access and open a “*.LN3” file that was previously created with NRCDose3.
Save to Database ─ Choose this option to save the current case to the database. When LADTAP starts, it loads the data that was last saved (typically from the last, previous run), populating all LADTAP screens and windows.
Save to LN3 File ─ Choose this option to save the completed case to a “*.LN3” file. This allows the file to be saved for later use, or for sharing with others.
Delete ─ Choose this option to open an explorer window that will allow the user to delete any previously saved “*.LN3” files.

## Slide 91: LADTAP Basic Information
Scenario Name
Source Term Identifier
Dose Factor Library
  ICRP-2 (Default)
  ICRP-30
  ICRP-72

## Slide 92: LADTAP Selections
Release/site information
Fresh or saltwater
Print dose factors
Dose contribution by nuclide
Modify Population Fractions
  (ICRP-2/ICRP-72)
    Adult (71%)
    Teen (11%)
    Child (18%)
  ICRP-30
    Adult (100%)

## Slide 93: LADTAP Reconcentration
Drop down menus for the three (3) models
  Alternatively, nuclide specific R-Factors can be assigned manually

## Slide 94: LADTAP Reconcentration Models
Plug-Flow Model
Partially Mixed Model
Completely Mixed Model

## Slide 95: LADTAP Source Term
Select: Add Nuclide
Pop-up menus with nuclide list
Highlight desired nuclide; use ”control” key to select multiple nuclides
  Select “Add” to add to list
“Delete Nuclide" will delete selected nuclide
“Clear” will clear all nuclides in the Source Term

## Slide 96: LADTAP Source Term
ICRP-30 and ICRP-72 DCFs
  For radionuclides with more than one solubility class, select the applicable one
  The same nuclide with more than one solubility class is not allowed

## Slide 97: ALARA Locations (Individual Doses)
Defines the exposure assumptions for individual dose calculations
Enter data
  Shore width factor defines the geometry for the shoreline exposure
  Dilution factors by pathway
  Transit time by pathways

## Slide 98: LADTAP Dilution Factor Calculation
Using the “Calc” options, a dilution factor will be calculated based on receiving water body parameters
  Based on RG 1.113
  For nontidal uniform flow and steady-state conditions, diffusive transport in the flow direction negligible compared with advective transport

## Slide 99: LADTAP Dilution Calculation
Surface Water Model ─ Select the appropriate hydrological model by clicking on either River or Lake model option
Surface Water Velocity ─ surface water velocity in units of feet per second (ft/s)
Surface Water Depth ─ surface water depth in units of ft
Downstream Distance ─ downstream distance in units of ft
Offshore Distance ─ offshore distance in units of ft
River Width/Lake Discharge Depth ─ either the river width or lake discharge depth depending on the model selected in units of ft

## Slide 100: Individual Age Group Exposure Assumptions
Drop down menu to select age group
  ICRP-2 DCFs: four age groups: Adult, Teen, Child, Infant
  ICRP-30 DCFs: Adult age group only
  ICRP-72 DCFs: Adult, 15-year, 10-year, 5-year, 1-year and newborn
Remember to Save before Exit

## Slide 101: Additional Locations (Individual Doses)
Add/remove additional locations of interest – by name
Define exposure assumptions
  Dilution
  Transit time
  Shore width factor
Ability to change exposure times and consumption rates

## Slide 102: LADTAP Population Doses: Fish and Shellfish
Select pathway from dropdown menu
Add location
Define harvest, dilution and transit time

## Slide 103: LADTAP Population Usages
From drop down, select:
  drinking water,
  shoreline,
  swimming or
  boating
Add location
For drinking water, define the population served or the supply rate
  For others, define person-hours annual usage
  Define dilution and transit time
  Add additional locations as needed

## Slide 104: LADTAP Population Usages
Add locations for calculating doses to biota
Add additional locations as needed
Define dilution and transit time
A “new” biota can be defined and added

## Slide 105: LADTAP Biota Doses
Select the “Add Biota Type” button
Enter the name and exposure assumptions for the new biota type.
Select the “Save” button
Up to five (5) new biota may be added

## Slide 106: LADTAP Irrigated Foods

## Slide 107: LADTAP Irrigated Foods
From dropdown menu select food type
Total production within 50 miles
Add irrigation rate
Option to change default consumption rates
For milk and meat, add non-contaminated water fractions
Save: adds Food type to list.

## Slide 108: LADTAP Irrigated Foods
ICRP-2
ICRP-72

## Slide 109: LADTAP Irrigated Foods, Farm Data
For each farm location:
  Dilution, Production and Transit Time
Save: adds food type to list
Add locations for selected farms for production
Option to change default consumption rates

## Slide 110: LADTAP Dose Factors

## Slide 111: LADTAP Dose Factors
Nuclide Data
  External TB and skin DFs from
  Ground Surface
  Water Submersion
  Absorbed Energies
  For biota calculations
  Effective radii
NOTE: Nuclide Data is non-editable

## Slide 112: LADTAP Pathway Factors

## Slide 113: LADTAP Bioaccumulation Factors
Bioaccumulation factors (fresh and saltwater):
  Fish
  Invertebrate
  Plants
Transfer factors:
  Soil-to-vegetables
  Grass-to-meat
  Grass-to-milk
NOTE: All bioaccumulation factors are editable for site-specific data

## Slide 114: Pathway Factors - Usage/Consumption
Consumption Rates
  Fish
  Invertebrate
  Plants
  Drinking water
  Shoreline
  Swimming
  Boating
Irrigated Food Consumption:
  Vegetables
  Leafy vegetables
  Milk
  Meat
  Transit and hold-up times
NOTE: All consumption rates are editable for site-specific data

## Slide 115: Running LADTAP – Viewing Outputs/Reports
Save
Create Input
View Input
Run LADTAP
View Output
FSAR Report
Supplemental Report

## Slide 116: Running LADTAP – Input
Input follows the format of the “card deck” as described in NUREG/CR-4013
The datasets at beginning reflect assumptions that could have been changed under the “Pathway factors” tab
The bottom section is standard LADTAP input:
  Selections inputs
  Source Term
  ALARA Location assumptions
  Fish/population/biota inputs
  irrigated foods

## Slide 117: Running LADTAP – Output

## Slide 118: Running LADTAP – FSAR
Provides a summary report of assumptions and doses
Suitable for use in creating input for safety analyses and licensing support

## Slide 119: LADTAP – Supplemental Report
Provides additional information that may not be included in the LADTAP output or the FSAR Report

## Slide 120: NRCDose Future Planning

## Slide 121: NRCDose3 Transition to PNNL
Retirement of Current Code Developer and pending retirement of Code knowledgeable expert.
Establishment of PNNL as knowledge center for NRCDose3 functions and intended uses.
Integration of NRCDose3 environmental calculations into SIERRA Code as part of the RAMP Code consolidation effort.

## Slide 122: NRCDose3 Integration into SIERRA
Short Term (next few months)
  Receive and review program files, documentation, and associated materials
Intermediate Term (<2 years)
  Continue as the knowledgeable experts on NRCDose3
  Complete code maintenance and updates as directed by the NRC
Long Term Integration into SIERRA (2+ years)
  Expected retirement of NRCDose3 (Transition to legacy code hosted by RSICC)
  Complete Integration of GASPAR II and LADTAP II into SIERRA
  Update Carbon and Tritium Models to address known issues

## Slide 123: SIERRA Integration Plan

## Slide 124: SIERRA Integration Plan

## Slide 125: Complete SIERRA Functionality