## Slide 1: Needlesticks and Implications for the Wound Dose Module in VARSKIN+v1.3
Bill Thomson , Holly Benderz
City Hospital , Birmingham , UK
Fortunately, uncommon!
But they do happen, and we need a dosimetry model
UK VARSKIN User group - Bill.Thomson@nhs.net

## Slide 2: Skin Dose Diagram
Sensitive Basal layer
Epidermis, average thickness 70µm
Vascular dermal layer
Staff - 500mSv annual limit
Notes: National Training Scheme for the Use of Radioiodine in Benign Thyroid Disease
2

## Slide 3: Needlestick?
Puncture wound through Basal layer
Activity deposited
Possibly 2 – 6mm depth
2mm used as worse case
(Other phrases are available!)
Not to Scale!
Notes: National Training Scheme for the Use of Radioiodine in Benign Thyroid Disease
3

## Slide 4: Scale Perspective
If drawn to scale ? -
2mm
70µm (diameter of
human hair!)
Basal layer
Skin Surface
Needlestick depth
Big distance from basal layer in radiation protection terms
Notes: National Training Scheme for the Use of Radioiodine in Benign Thyroid Disease
4

## Slide 5: VARSKIN+v1.3 Wound Dose Provides 2 Dose Components
Activity deposited uniformly
(line source)
Activity deposited at ‘needle tip’
(point source)
2mm
N.B. for alphas, range is ≈ 70 - 80 µm
No alphas at ‘needle tip’ will reach basal layer
Needle tract
Notes: National Training Scheme for the Use of Radioiodine in Benign Thyroid Disease
5

## Slide 6: VARSKIN+v1.3 Wound Dose and Alpha Emitters
The 107D database is not available in Wound Dose
Individual radionuclides of the decay scheme must be used
BUT need to be aware of the decay scheme
Example - Ra223
Notes: National Training Scheme for the Use of Radioiodine in Benign Thyroid Disease
6

## Slide 7: 223Ra daughters daughters in equilibrium with Ra223 – use 11.4d half-life CANNOT use calculated doses for the individual radionuclides
223Ra
219Rn
215Po
207Tl
207Pb
stable
211Po
211Bi
211Pb
0.28%
4s
11.4d
1.8ms
36min
2min
4.8min
0.5s
99.7%
100%
100%
100%
100%
100%
100%
Notes: National Training Scheme for the Use of Radioiodine in Benign Thyroid Disease
7

## Slide 8: VARSKIN+v1.3 Wound Dose and Alpha Emitters
Use the instantaneous dose-rates for each of the daughters (from ‘Dose Detail’)
Add these with percentage from the decay scheme
Gives the total instantaneous dose-rate for Ra223 + daughters
Integrate with an effective T½
[ physical T½ (11.4d) ; biological T½ for needlestick e.g. 6hrs ]
N.B. VARSKIN+v1.3 uses a tissue density of 1.1g/cc for alpha dose
Nuclear Medicine Communications. 45(3):159-168, March 2024
Notes: National Training Scheme for the Use of Radioiodine in Benign Thyroid Disease
8

## Slide 9: VARSKIN Models - Instantaneous Dose Rates mSv/h/kBq N.B. for 1cm2 averaging area - UK + Europe
mSv/h/kBq | Tc99m | F18 | 223Ra Incl. daughters
Point source (2mm deep) | 0.0013 | 0.011 | 0.25
Line Source (2mm length) | 0.04 | 0.49 | 1980
Ratio | x30 | x44 | x8050
2mm
Notes: National Training Scheme for the Use of Radioiodine in Benign Thyroid Disease
9

## Slide 10: Focus on Ra223
Some Combination of
% of line + % of point ?
e.g.
5% of line + 95% of point
Which Needlestick Model ?
line source?
Point source?
(some argue bleeding leaves this)
1980 mSv/h/kBq
0.25 mSv/h/kBq
100 mSv/h/kBq (x400)
Examine some factors which might influence the model
Notes: National Training Scheme for the Use of Radioiodine in Benign Thyroid Disease
10

## Slide 11: Impact of needle design on Activity Distribution?
Lance shape of needle is > 2mm!
‘Wipes’ along skin layers as punctures through tissue
activity is very likely distributed along the needle track.
2mm
70µm
Basal layer
Scale Perspective - Needle
Skin Surface
Notes: National Training Scheme for the Use of Radioiodine in Benign Thyroid Disease
11

## Slide 12: Doserate distribution with depth - 223Ra
0-150µm
Basal Layer Doserate/ µm-depth
>99.5% dose is from activity in 0 - 150µm depth!
SO, if activity is not uniform ?
Reduced activity in 0-150µm -
Smaller dose
BUT
Increased activity in 0-150µm - Larger dose
Which is it?
2mm
70µm
Basal layer
Skin Surface
Uniform activity along wound
Notes: National Training Scheme for the Use of Radioiodine in Benign Thyroid Disease
12

## Slide 13: Critical Question for dosimetry What is distribution of activity along the needletrack, particularly around the basal layer, 0-150µm ?
(Apologies! A UK quiz programme!)
Notes: National Training Scheme for the Use of Radioiodine in Benign Thyroid Disease
13

## Slide 14
Measure activity along needlestick wound?
(No volunteers!)
Use Agar gel - tissue mimic
insert needle into gel with fixed depths
using microtome mechanism, ‘immediately’ get thin slices through the needlestick (open razor)
Microtome accuracy 2um. However, overall mechanics allow about 50-100um
Slices are weighed for accurate thickness
Notes: National Training Scheme for the Use of Radioiodine in Benign Thyroid Disease
14

## Slide 15
~ 50% activity in
0 – 150µm
Activity %
Simulated Needlestick
0-150µm
2mm
70µm
Basal layer
Skin Surface
0 20 40 60 80 100
0% at ‘Needletip’
0% after ~800µm
Notes: National Training Scheme for the Use of Radioiodine in Benign Thyroid Disease
15

## Slide 16
=
Needlestick
Doserate
X
µm
0 -
500 -
1000 -
1500 -
Activity with depth
New Needlestick Dosimetry Model
Potentially, a radionuclide factor independent of needlestick depth?
(May need different factors for needle going through gloves)
Sum over depth
Ra223 doserate profile
with depth
Notes: National Training Scheme for the Use of Radioiodine in Benign Thyroid Disease
16

## Slide 17
=
Needlestick
Doserate
µm
0 -
500 -
1000 -
1500 -
Tc99m
Sum over depth
X
Doserate profile with depth
Tc99m
Notes: National Training Scheme for the Use of Radioiodine in Benign Thyroid Disease
17

## Slide 18
=
Needlestick
Doserate
Sum over depth
µm
0 -
500 -
1000 -
1500 -
F18
X
Doserate profile with depth
F18
Notes: National Training Scheme for the Use of Radioiodine in Benign Thyroid Disease
18

## Slide 19: Needlestick Dose – mSv/kBq (using a 6hr retention)
mSv/kBq | Tc99m | F18 | 223Ra + daughters
VARSKIN 2mm Line | 0.17 | 1 | 17,000
New model | 1.6 | 5.8 | 191,000
Ratio | x9.4 | x6 | x11
Notes: National Training Scheme for the Use of Radioiodine in Benign Thyroid Disease
19

## Slide 20: My New Model – Doses from Typical Needlestick Activities
Tc99m | F18 | 223Ra + daughters
1.6 mSv/kBq | 5.6 mSv/kBq | 191,000 mSv/kBq
Needlestick activity based on 0.1µl vol. |  | 
40 kBq | 15 kBq | 0.1 kBq
64 mSv | 84 mSv | 19 Sv
‘Never Event’ classification?
Cannot disprove any ‘washout’ from bleeding
Percutaneous absorption likely occurs – will reduce doses
N Banks et al ; IPEM Translation Open access Volumes 10–11, June 2024, ,
Not
Definitive!
BUT -
below 500mSv
Notes: National Training Scheme for the Use of Radioiodine in Benign Thyroid Disease
20

## Slide 21: Risks of 500mSv Needlestick?
99mTc , F18 etc. ; 2 to 5 Gy threshold for transient erythema
Alphas ; need to remove the weighting factor Wr of x20 (only for stochastic)
500mSv becomes 25 mGy for deterministic events
Erythema?
ICRP nos. 59 ; 92 ; 103 ; 147
M Charles :- Skin dose from Ra-226 contamination: Dose estimation & comments. November 2008 (sepa.org.uk)
No Erythema
Notes: National Training Scheme for the Use of Radioiodine in Benign Thyroid Disease
21

## Slide 22
Total skin area of body is approx. 20,000 cm2
Total Skin is included in effective dose, factor = 0.01
BUT - stochastic risk for skin is proportional to area
Only small skin area is irradiated , < 1 cm2
So, risk is reduced by 1 in 20,000
Calculated Risk for 500 mSv is < 10-7 ; or < 1 µSv effective dose
Risks are extremely low ( CONTROVERSIAL ? - no need to remove staff from work)
Stochastic?
Carcinogenic Risk of Hot-Particle Exposures M. Charles et.al .2003 J.Radiol.Prot. 23;5
M Charles :- Skin dose from Ra-226 contamination: Dose estimation & comments. November 2008 (sepa.org.uk)
Risks?
Extremely Low!
Risks of 500mSv Needlestick?
“Back of the Envelope” calculation
Notes: National Training Scheme for the Use of Radioiodine in Benign Thyroid Disease
22

## Slide 23
79 technologists’ responses
Anxiety
Stochastic
Alpha
Tc99m
Score 1 – no concerns , 10 - extremely concerned
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Frequency | 5 | 5 | 8 | 6 | 6 | 4 | 10 | 17 | 7 | 12
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Frequency | 2 | 1 | 3 | 3 | 5 | 4 | 6 | 12 | 11 | 32
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Frequency | 6 | 9 | 10 | 5 | 8 | 4 | 9 | 11 | 6 | 12
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Frequency | 2 | 4 | 2 | 4 | 4 | 5 | 10 | 9 | 5 | 34
500mSv skin dose?

## Slide 24
0-150µm
Dose
Dose is all within 0-150um
For a very high dose event ,
Potentially can remove that tissue.
Dermatology punch biopsy, 3mm diameter and <0.5mm deep will totally remove the dose !
2mm
70µm
Basal layer
Skin Surface
MUST be the individual’s decision, not ‘regulatory’.
Another Controversial Concept!
Notes: National Training Scheme for the Use of Radioiodine in Benign Thyroid Disease
24

## Slide 25
Conclusions
Needlestick activity seems weighted towards the 0-150µm depth,
increasing doses compared to uniform line model
Potentially, radionuclide dose factor independent of needlestick depth?
Staff awareness – particularly of very low risks (no need to remove from work?)
In very high dose cases, potential for the member of staff to consider dermatological removal? (their decision and consent!)
Specific Risk Assessments for dispensing/administration alpha emitters
Notes: National Training Scheme for the Use of Radioiodine in Benign Thyroid Disease
25

## Slide 26
Bill’s Needlestick Model
Hopefully Never Needed!
UK VARSKIN User group - Bill.Thomson@nhs.net

## Slide 27
=
Needlestick
Doserate
X
Sum over depth
µm
0 -
500 -
1000 -
1500 -
70µm
370µm
Finger pulp
Basal Layer depth
Notes: National Training Scheme for the Use of Radioiodine in Benign Thyroid Disease
27

## Slide 28
500mSv is essentially a deterministic limit
VARSKIN applies Wr of x20
ICRP do not recommend using this for deterministic purposes
Alpha doses Significance - Deterministic
Significant fraction of basal stem cells deeper than alpha threshold, so are ‘spared’ .
These cells can migrate following irradiation of upper basal cells
This significantly increases the threshold for deterministic events - 1kGy for erythema
“High skin doses calculated from alpha exposure to superficial layers of skin should not be compared directly with the skin dose limit”

## Slide 29
Stochastic risk for skin is proportional to area
Only small skin area irradiated , < 1 cm2
Total area of skin is approx. 20,000 cm2
So, risk is reduced by 1 in 20,000
Also, skin is included in effective dose calculations, factor = 0.01
Risk for 500 mSv is < 10-7 ; or < 1 µSv effective dose
Risks are extremely low ; - no need to remove staff from work
Stochastic?
Carcinogenic Risk of Hot-Particle Exposures M. Charles et.al .2003 J.Radiol.Prot. 23;5
M Charles :- Skin dose from Ra-226 contamination: Dose estimation & comments. November 2008 (sepa.org.uk)
Risks?
Extremely Low!
Risks of 500mSv Needlestick?
Notes: National Training Scheme for the Use of Radioiodine in Benign Thyroid Disease
29