## Slide 1: Comparison of VARSKIN+ EyeDose and new Eye Dose Calculators
RAMP 2024 Dosimetry Symposium
By: Jacques Dubeau
jdubeau@detec-rad.com

## Slide 2: Development of a “family” of codes
Activity determination (in contamination) & Skin dose software: Activity and Skin Dose Calculator (ASDC)
Eye-lens dose calculation based on published dose coefficients: Eye Lens Dose Calculator (ELDC)
Eye-lens dose calculator based on contact exposures (hot particles and liquids): Contaminated-Eye Dose Calculator
Development funded by CANDU Owners Group(COG). Collaborations between Canadian Nuclear Laboratories, DETEC and the Canadian Nuclear Safety Commission

## Slide 3: Common structure
INPUTS
(all SQLite databases)
Pre-calculated
Monte Carlo results or
published dose coefficients
Radiation emissions for
1252 radionuclides from
ICRP 107
=>>
GUI developed using AutoIT
Drop down menu
radionuclide selection
Specifying % or absolute
activity in mix for up to 18
radionuclides

## Slide 4
Activity and Skin Dose Calculator (ASDC)
Reference [Dubeau, 2023a]
Ludlum 44-9 GM pancake probe

## Slide 5
Eye-Lens Dose Calculator (ELDC)
Reference [Dubeau, 2023b]

## Slide 6
“Contaminated-Eye Dose Calculator” (CEDC)
Reference [Dubeau, 2023c] [Dubeau, 2024]

## Slide 7
Eye-Lens Dose Calculator (1)
Aims
Aims of the project:
Make use of published electron and photon dose conversion coefficients to calculate dosimetric quantities related to the lens of the eye.
Make accessible the large body of these quantities without risk of “confusion”.
Allow the comparison between operational and protection dose quantities.
Calculate dose quantities for single radionuclides or mixtures of radionuclides.

## Slide 8
Eye-Lens Dose Calculator (2) Dose quantities
Protection
(realistic eye model)
Operational
(3 mm depth in 20 x 20 cm
cylindrical phantom)
[Behrens, 2010, 2011, 2013, 2017]
[ICRP, 2010]
[Behrens, 2012] [Daures, 2009] [Ferrari, 2012] [Gualdrini, 2013] [Mariotti, 2011]
[ISO, 2019] [Vanhavere, 2012]
… and many others.

## Slide 9
A large array of available data
Variation of parameters for protection quantity:
Target: whole-lens or radio-sensitive part
Particle type: electron, photon
If photon: SCPE or non-SCPE
If photon: units of pSv cm2 or Sv/Gy (air kerma)
If photons: mono-energetic or X-ray spectra
Angles of incidence (left or right eye)
Variation of parameters for operational quantity:
Particle type: electron, photon
If photon: SCPE or non-SCPE
If photon: units of pSv cm2 or Sv/Gy (air kerma)
If photons: mono-energetic or X-ray spectra
Angles of incidence
Avoid mixing !!!

## Slide 10: Protection quantities
From Behrens and Dietze (2009) and used by ICRP 116

## Slide 11: Protection quantities
Coefficients from Compilation of conversion coefficients for the dose to the lens of the eye [Behrens, 2017]
Electrons, 2 tables
Positron, 2 tables
Photons, 8 Tables
Total available from Behrens: 43 tables (electrons (7), photons (29), positrons (7)) [Behrens, private communication, 2016]
ICRP 116 (2010) – aimed to be conservative
Photons: used data for “stylized” eye model (up to 2 MeV)[Behrens] and average male-female reference phantom values at higher energy.
Electrons:
  for AP direction, used “stylized” eye model [Behrens, 2010]
  for isotropic geometry used AP values up to 1 MeV
  for all other conditions, used values from reference phantoms

## Slide 12: Protection quantities
Some references:
Behrens R., Dietze G., Zankl M., 2010. Dose Conversion Coefficients for Electron Exposure of The Human Eye Lens (Corrigendum), Phys. Med. Biol., 55, 4069-4087.
Behrens R., Dietze G., 2011. Dose Conversion Coefficients for Photon Exposure of the Human Eye Lens, Phys. Med. Biol., 56, 415-437.
Behrens R., 2013. Dose Conversion Coefficients for Electron Exposure of the Human Eye Lens: Calculations Including a Whole Body Phantom, Radiat. Prot. Dosim., 155 (2), 224-235.
Behrens R., 2017, Compilation of Conversion Coefficients for the Dose to the Lens of the Eye, Rad. Prot. Dosim., 174 (3), 348-370.
ICRP, 2010. International Commission on Radiological Protection. Conversion Coefficients for Radiological Protection Quantities for External Radiation Exposures, ICRP Publication 116, Ann. ICRP 40 (2-5).
… apologies for omissions!

## Slide 13: Operational quantities
Definition:
Hp(3, α) : dose at 3 mm depth in a 20 x 20 right circular cylinder made of ICRU 4-element tissue.
Proposed by ORAMED collaboration (ORAMED: Optimization of radiation protection of medical staff, Vanhavere et al., 2012).
Figure from ORAMED Report [Vanhavere, 2012]

## Slide 14: Operational quantities
Some references:
Daures J., Gouriou J., Bordy J.-M., 2009. Conversion coefficients from air kerma to personal dose equivalent Hp(3) for eye-lens dosimetry, CEA-R-6235.
Mariotti F., Gualdrini G., Fantuzzi E., Ferrari P., Monteventi F., 2011. A New Proposal on the Operational Quantity Hp(3): Monte Carlo and Experimental Results, Rad. Prot. Dosim., 46, 375-380.
Vanhavere F. et al., 2012. ORAMED: Optimization of Radiation Protection of Medical Staff, EURADOS report 2012-02, ISSN 2226-8057, ISBN 978-943701-01-2, Braunschweig.
Ferrari P., Gualdrini G., 2012. Eye Lens Dosimetry: Hp(3), Fluence to Dose Conversion Coefficients for Electrons from 800 keV to 10 MeV Based on MCNPX Simulations, ENEA Technical Report.
Gualdrini G., Bordy J.-M., Daures F., Fantuzzi E., Ferrari P., Mariotti F., Vanhavere F., 2013. Air Kerma to Hp(3) Conversion Coefficients for Photons from 10 keV to 10 MeV Calculated in a Cylindrical Phantom, Rad. Prot Dosim., 154 (4), 517-521.
ISO, Radiological protection — X and gamma reference radiation for calibrating dosemeters and doserate meters and for determining their response as a function of photon energy — Part 3: Calibration of area and personal dosemeters and the measurement of their response as a function of energy and angle of incidence, ISO4037-3:2019.
Dubeau J., Sun J., 2020. Electron eye-lens dose operational coefficients, Rad. Port. Dosim., Vol. 188(3), pp. 372-377
Dubeau J., Sun J., Djeffal S., Ali F., 2024. Improving calculations of electron eye-lens operational dose coefficients using the Monte Carlo Codes PENELOPE and MCNP6.2, Health Phys., Vol. 126(5), pp. 339-345.
… apologies for omissions!

## Slide 15: Electron protection and operational quantities
Electron protection and operational dose coefficients at 0o

## Slide 16
Photon protection and operational dose coefficients at 0o,
per unit air kerma. Also available in pGy-cm2
Photon protection and operational quantities

## Slide 17
Eye-Lens Dose Calculator (ELDC)
Avoids mixing of
protection and
operational
coefficients
Gives reference and
description of coefficents
Alerts about incompatible
angle but will do calculation
after timeout.

## Slide 18
Eye-Lens Dose Calculator (ELDC)
If single energies are entered, ELDC will interpolate and give results
in same unit as original data.

## Slide 19
Eye-Lens Dose Calculator (ELDC)
Photon_protection.db, which includes 7 sets of data:
  Gy/Gy, maximum of the dose to the sensitive part of the left or right eye in the CPE approximation, Table A6 in [Behrens, 2017]
  Gy/Gy, maximum of the dose to the sensitive part of the left or right eye in the non-CPE approximation, Table A5 in [Behrens, 2017]
  Gy/Gy, maximum of the dose to the whole lens for the left or right eye in the CPE approximation, Table A11 in [Behrens, 2017]
  Gy/Gy, maximum of the dose to the whole lens for the left or right eye in the non-CPE approximation, Table A12 in [Behrens, 2017]
  Gy/Gy, dose to the eye lens, Table A.18 in ICRP74 [ICRP, 1996]
  pGy-cm2, dose to the sensitive part, Table B2 in [Behrens, 2011]
  pGy-cm2, dose to the whole lens, Table B2 in [Behrens, 2011]

## Slide 20
Eye-Lens Dose Calculator (ELDC)
Photon_operational.db, which includes 11 sets of data:
  Sv/Gy, non-CPE, Tables 21 to 21 in [Daures, 2009]
  Sv/Gy, coefficients given for various standard photon qualities, under CPE condition, from Table 3 of [Behrens, 2012]
  Sv/Gy, CPE condition, in an ICRU tissue slab phantom, from Table 1 in [Grosswendt, 1991]
  Sv/Gy, CPE condition, in PMMA slab phantom, from Table 2 in [Grosswendt, 1991]
  Sv/Gy, CPE condition, in a 20×20 cm ICRU tissue cylinder from Table 2.2 in [Vanhavere, 2012]
  Sv/Gy, CPE condition, in a 20×20 cm ICRU tissue cylinder from Table 2 in [Gualdrini, 2013]
  Sv/Gy, non-CPE condition, in a 20×20 cm ICRU tissue cylinder from Table 3 in [Gualdrini, 2013]
  pSv-cm2, non-CPE condition, in a 20×20 cm ICRU tissue cylinder, this work
  pSv-cm2, CPE condition, in a 20×20 cm ICRU tissue cylinder, this work
  pSv-cm2, non-CPE condition, in a 20×20 cm PMMA cylinder, this work
  pSv-cm2, non-CPE condition, in a 20×20 cm polycarbonate (LexanTM) cylinder, this work

## Slide 21
Eye-Lens Dose Calculator (ELDC)
Electron_protection.db, which includes 6 sets of data:
  pGy-cm2 for the thin radiosensitive part of the lens, Table A1 in [Behrens, 2010b]
  pGy-cm2 for the whole lens, Table A1 in [Behrens, 2010b]
  pGy-cm2 for the thin radiosensitive part of the lens, Table A1 in [Behrens, 2017]
  pGy-cm2 for the whole lens, Table A7 in [Behrens, 2017]
  pGy-cm2 for the whole lens, Table F.2 in ICRP 116 [ICRP, 2012]
  pGy-cm2 for the thin radiosensitive part of the lens and the whole lens, Table 5 in [Nogueira, 2011]. Note: This group contains calculated coefficients for different eye-lens depth, i.e., different cornea thickness values as found in the general population.
Electron_operational.db, which includes, includes 5 sets of data:
  pSv-cm2, at 3 mm depth in a 20×20 cm ICRU tissue cylinder, Table 1 and 2 in [Ferrari, 2012]
  pSv-cm2, at 3 mm depth in a 20×20 cm ICRU tissue cylinder, Table 1 and 2 in [Dubeau, 2020]
  pSv-cm2, at 3 mm depth in a 20×20 cm LexanTM cylinder, this work
  pSv-cm2, at 3 mm depth in a 20×20 cm PMMA cylinder, this work
  pSv-cm2, at 3mm depth in an ICRU tissue slab, Tables A.44 and A.46 in ICRP 74 [ICRP, 1996]

## Slide 22
Eye-Lens Dose Calculator (ELDC)

## Slide 23
Eye-Lens Dose Calculator (ELDC)
Fluence calculation:
1/distance2 for distance greater than 5 cm
Function calculated via Monte Carlo for 0.5 mm to 5 cm via parameter ε, where (for unit emission)
Fluence = ε/(4πd2)

## Slide 24
Eye-Lens Dose Calculator (ELDC)
Data saved as text file

## Slide 25
ELDC vs VARSKIN+, photons

## Slide 26
ELDC vs VARSKIN+, electrons

## Slide 27
Eye-Lens Dose Calculator (ELDC)
Activities 10 kBq

## Slide 28
Eye-Lens Dose Calculator (ELDC)
Activities 10 kBq

## Slide 29
“Contaminated-Eye Dose Calculator” (CEDC)

## Slide 30
“Contaminated-Eye Dose Calculator” (CEDC)
Natural extension of the work providing DRCF for 100 radionuclides (same as significant skin dose contaminants)
Dubeau J., Djeffal S., Sun J., Ali F., 2023c. Eye-lens dose rate conversion factors due to hot particles and surface contaminations on the cornea, J. Radiol. Prot., vol 42 (4).
ISO15382 states (2015):

## Slide 31
“Contaminated-Eye Dose Calculator” (CEDC)
Hot particle: 0, 10, 100 and 1000 μm dia.
Materials: void, plastic, Aluminum, Steel and UO2
Position: centered or off-centered
Surface contamination - thin

## Slide 32
“Contaminated-Eye Dose Calculator” (CEDC)
Photon DRCF Electron DRCF

## Slide 33
“Contaminated-Eye Dose Calculator” (CEDC)

## Slide 34
“Contaminated-Eye Dose Calculator” (CEDC)
Photon database DRCF (red line) versus VARSKIN+ 1.1 (points)
point particle on contact (set as 0.03 mm for V+ 1.1)
Differences 0 to 4%

## Slide 35
“Contaminated-Eye Dose Calculator” (CEDC)
Electron database DRCF (red line) versus VARSKIN+ 1.1 (points)
point particle on contact (set as 0.03 mm for V+ 1.1)
Differences 0 to 12%

## Slide 36
“Contaminated-Eye Dose Calculator” (CEDC)
Radionuclides in contact with center of cornea
point particle on contact (set as 0.03 mm for V+ 1.1)

## Slide 37: Conclusion
The Eye-Lens Dose Calculator (ELDC software) presents a convenient way for practitioners to access protection and operational eye-lens dose coefficients.
  Both compartments of the eye are considered
  Operational and protection quantities can be easily compared
  Agreement with VARSKIN limited by the intervening effect of air on electron radiation, which is neglected by the ELDC, and probable geometrical effects
Contaminated-Eye Dose Calculator provides dose rates for contact radioactive contaminants
  Both compartment of the eye are considered
  Non-zero mass particles considered in 3 geometries
  Very good agreement with VARSKIN+ for limited common geometries. Indicates that V+ can be used at short distances.

## Slide 38: References
Dubeau J., Sun J., Hakmana Witharana S.S., 2023a. A computer program for the determination of absolute activities in contaminations and skin doses, Rad. Prot. Dosim., Vol. 199 (7), pp. 660-669.
Dubeau J., Sun J., 2023b. A new software for the calculation of eye-lens dosimetry quantities based on dose rate coefficients, Health Physics J., Vol. 125, pp. 383-392.
Dubeau J., Djeffal S., Sun J., Ali F., 2023c. Eye-lens dose rate conversion factors due to hot particles and surface contaminations on the cornea, J. Radiol. Prot., vol 42 (4).
Dubeau J., Sun J., Djeffal S., Ali F., 2024. A software for the calculation of eye-lens dose due to contact exposure with radioactive contamination and hot particles, poster presentation at IRPA 2024, Orlando.