## Slide 1: MACCS Overview and Status
Nate Bixler, Sandia National Laboratories
Matt Humberstone and Jon Barr, US Nuclear Regulatory Commission
Presented at the 6th International MACCS Users Group Meeting, Sept. 10 - 11, 2014

## Slide 2: Outline
MELCOR Accident Consequence Code System (MACCS) overview
Improvements in the most recent versions
New models being developed
Improvements in preprocessor codes
Summary

## Slide 3: History of NRC Consequence Code Development
MACCS is the NRC tool used to evaluate the offsite consequences of hypothetical radioactive releases into the atmosphere
Evolved from codes going back to the 1970s
  Calculation of Reactor Accident Consequences (CRAC)
    Reactor Safety Study (WASH-1400)
  CRAC2
    1982 Siting Study
  MACCS v1.13.1
    NUREG-1150
  MACCS v2.4 – 3.8
    Security Studies
    Protective Action Recommendation Study
    State-of-the-Art Reactor Consequence Analyses (SOARCA)
    Spent Fuel Pool Consequence Study
    BWR Mark I and II Containment Venting Study
    Level-3 PRA

## Slide 4: MACCS Models and Capabilities
Models treat
  Atmospheric transport and deposition onto the ground
  Statistical effect of variability in weather
  Dose pathways for cloudshine, groundshine, inhalation, ingestion, and deposition onto skin
  Protective actions during emergency, intermediate, and long-term phases
Calculates offsite consequences
  Doses
  Health effects
  Economic costs
  Land contamination

## Slide 5: WinMACCS Interface
Graphical interface improves usability
  Organizes problem definition
  Provides visual cues
  Defines parameters and ranges
Automates evaluation of uncertainty
Incorporates post processing of output

## Slide 6: Status of WinMACCS/MACCS Development
WinMACCS/MACCS 3.7 released November 2012
WinMACCS/MACCS 3.9 released September 2014
WinMACCS/MACCS 3.10 is currently being developed
Development beyond version 3.10 is also ongoing

## Slide 7: Improvements In WinMACCS 3.9
Flexible capability to define the location of cohorts
Keyhole evacuation model
Tracking population movement
Resizable parameter input screens
Choice of units
Improvements in reporting options
Change-card paradigm for cohorts eliminated
  Auto-propagation of cohort values added to facilitate conversion
Upper limits increased
  Up to 150 chemical groups
  Up to 500 plume segments

## Slide 8: Defining Cohorts
Cohorts represent emergency response of distinct segments of the population
Each cohort follows a timeline of actions

## Slide 9: Added Flexibility in Defining Cohorts
The user can locate cohorts in regions anywhere within MACCS grid
  Feature was supported previously, but not user friendly
  Map layer can be used to facilitate cohort locations
E.g., regions might represent
  Emergency Planning Zone (EPZ)
  Shadow evacuation
  No evacuation
  Special facility

## Slide 10: Keyhole Evacuation Model
Keyhole consists of
  A central circular region
  An pie-shaped outer region
User defines initial dimensions of keyhole
Shift in wind direction causes pie-shaped region to expand
Model allows for foreknowledge of weather (forecasting)

## Slide 11: Tracking Population Movement
The timing of evacuating cohorts crossing boundaries can be evaluated to verify consistency with the Evacuation Time Estimate (ETE)
Overall timing of the entire population can also be evaluated
Fraction of Population Exiting EPZ for
SOARCA LTSBO Scenario

## Slide 12: Resizable Parameter Input Screens
Screens can usually be expanded to view all parameters at once

## Slide 13: Choice of Units
WinMACCS input units can be chosen for most dimensional parameters, e.g., time can be specified in seconds, minutes, hours, days, or years
MACCS output units can be chosen for activity, distance, area, and dose

## Slide 14: Reporting Options
Reports can be created, e.g., with just the most essential results

## Slide 15: Development of WinMACCS 3.10
Ability to calculate consequences from multiple reactor units and/or spent fuel pools
  Multiple accident initiation times
  Multiple fission product inventories
  Extended release durations
User-specified dose projection periods in emergency and intermediate phases
New output category to report number of people displaced during each phase

## Slide 16: Development Beyond 3.10
Dosimetry improvements – allow all organs and tissues in dose coefficient file to be used
Alternative economic model based on GDP losses
  Based on input-output economic model
  Uses modified REAcct code developed for DHS
Alternative atmospheric transport model (HYSPLIT) to evaluate special issues
  Gaussian puff model
  Lagrangian particle tracking model

## Slide 17: Typical WinMACCS Calculation Framework
MACCS
Input
Output
WinMACCS
MELMACCS
MELCOR
Plot File
LHS
User Input

## Slide 18: MACCS Preprocessors
MelMACCS
  Extracts and processes source-term data from MELCOR plot files
SecPop
  Evaluates census, land use, and economic data for a MACCS site file
COMIDA2
  Evaluates dose coefficients for the food pathway

## Slide 19: MelMACCS Status
MelMACCS 1.7.1 released in January 2011
MelMACCS 1.8.0 is currently being developed
  User-definable fission product inventories
  Support for spent fuel pool source terms

## Slide 20: SecPop Status
SecPop 4.2.0 released in October 2013
  Uses 2010 census data
  Allows 16, 32, 48, or 64 compass sectors
  Uses a smart algorithm for defining economic regions
  Supports alternative economic model development
  Supports Windows 7 operating system
SecPop 4.3.0 released in September 2014
  A bug related to the calculation of farm fraction was fixed
  The first three economic regions are automatically assigned as follows:
    Region 1 is the exclusion area – population and economic values are zero
    Region 2 – no land area
    Region 3 – no census blocks

## Slide 21: Summary
Recent MACCS, WinMACCS, and SecPop developments improve modeling fidelity and add user efficiency
  More flexible definition of cohorts
  Explicit modeling of keyhole evacuation
  Choice of units
  Output of population movement for verification against ETE data
  Updated population and economic data
Ongoing improvements address
  Requirements for NRC’s Level-3 PRA project
  Alternative models for atmospheric transport and economic analysis

## Slide 22: List of Acronyms
CRAC Calculation of Reactor Accident Consequences
DHS Department of Homeland Security
PRA Probabilistic Risk Assessment
REAcct Regional Economic Accounting tool
SECPOP Sector Population, Land Fraction, and Economic Estimation Program
SOARCA State-of-the-Art Reactor Consequence Analyses