## Slide 1: SOARCA Peach Bottom Uncertainty Analysis (UA) Tina Ghosh, PhD NRC/RES/DSA/AAB
IMUG Meeting
September 11, 2014

## Slide 2: Outline
Background on SOARCA
Goals and approach of uncertainty analysis (UA)
Selected MELCOR and MACCS parameters
Overall conclusions of UA
MACCS analysis: health consequence results and insights on most influential parameters
Relative contributions of aleatory (weather) uncertainty and epistemic uncertainty
Other content in the UA report

## Slide 3: Background -SOARCA
SOARCA was initiated to develop a body of knowledge on the realistic outcomes of severe reactor accidents
Plants examined in pilot study: Peach Bottom and Surry
Surry
Peach Bottom

## Slide 4: Background - Objectives of SOARCA
Develop a body of knowledge on the realistic outcomes of severe reactor accidents
  Update the quantification of offsite consequences found in the 1982 Siting Study (NUREG/CR-2239)
  Incorporate plant changes not reflected in earlier assessments
  Evaluate potential benefits of recent security-related improvements – 10 CFR 50.54(hh)
  Incorporate state-of-the-art modeling (MELCOR/MACCS)
  Enable NRC to communicate severe accident aspects of nuclear safety to diverse stakeholders

## Slide 5: Background – SOARCA Approach
Focus on important severe accident scenarios
Realistic assessments and detailed analyses
Integrated analyses
Incorporated recent physical experiments
Treatment of seismic impacts on evacuation
Range of health effects modeling

## Slide 6: SOARCA Process
Notes: SOARCA consisted of 4 elements: selecting which scenarios to analyze, determining what action the operators would take to mitigate each scenario, calculating how the accidents would progress with and without mitigation, and calculating public health consequences. This flow chart depicts the SOARCA process.
After the analysis was completed and documented, the study was reviewed by independent experts in risk assessment, accident progression, emergency preparedness, and consequence modeling.

## Slide 7: Scenarios Analyzed
Reactor Site | Accident Scenario | Description
Peach Bottom & Surry | Long-Term Station Blackout (LTSBO) | Seismic event; loss of ac power; batteries available initially
Peach Bottom & Surry | Short-Term Station Blackout (STSBO) | Seismic event; loss of ac power; batteries unavailable
Surry | STSBO with Thermally Induced Steam Generator Tube Rupture (TISGTR) | Variation of STSBO – a steam generator tube ruptures resulting in a pathway for radioactive material to potentially escape
Surry | Interfacing Systems Loss-of-Coolant Accident (ISLOCA) | Random failure of valves ruptures low-pressure system piping outside containment
Notes: For both Peach Bottom and Surry, we modeled station blackout scenarios that were caused by an earthquake. In these scenarios, the earthquake causes power failures that disable the plants’ motor-driven pumps. In some cases, power failures also disable systems for monitoring plant status, such as the system for measuring how much water is in the reactor. For Surry, we also modeled two scenarios in which radioactive material can escape through failed pipes and valves, bypassing the containment building.

## Slide 8: Background – SOARCA Reports
NUREG-1935, State-of-the-Art Reactor Consequence Analyses (SOARCA) Report
  Final published November 2012
NUREG/BR-0359, Modeling Potential Reactor Accident Consequences
  Rev. 1 published December 2012
NUREG/CR-7110, Vol. 1, SOARCA Project Peach Bottom Integrated Analysis
  Rev. 1 published May 2013
NUREG/CR-7110, Vol. 2, SOARCA Project Surry Integrated Analysis
  Rev. 1 published August 2013
Notes: Conference presentations on UA approach and parameter selection:
  PSAM 11/ESREL-2012 – June 2012
  IAEA Technical Meeting on Level 3 PSA – July 2012
  CSARP – September 2012 and September 2013
  ANS PSA special session – September 2013

## Slide 9: Goals of the Uncertainty Analysis
Develop insight into overall sensitivity of SOARCA results and conclusions to uncertainty in inputs
Identify most influential input parameters for releases and consequences
Demonstrate uncertainty analysis methodology

## Slide 10: Approach
Focus on epistemic (state-of-knowledge) uncertainty in parameter values
  Aleatory (random) uncertainty due to weather is handled in the same way as the SOARCA study
Peach Bottom, unmitigated, long-term station blackout scenario chosen
Scenario definition not changed after Fukushima
  Qualitative discussion included in introduction
Looking at uncertainty in key model inputs
  MELCOR parameters
  MACCS parameters

## Slide 11: Approach (continued)
Key uncertain input parameters were identified
Uncertainty in these parameters propagated in a two-step Monte Carlo process using Simple Random and Latin Hypercube (LHS) sampling
An epistemic sample set of 865 generated to complete a corresponding number of individual code runs (Monte Carlo “realizations”) to evaluate the influence of the uncertainty on the estimated outcome

## Slide 12: Approach (continued)
Tools used to analyze results include statistical regression-based methods as well as scatter plots and phenomenological investigation of individual realizations of interest
Guidance solicited from SOARCA peer reviewers and the Advisory Committee on Reactor Safeguards in choosing final approach, parameters and distributions

## Slide 13: SOARCA Uncertainty Analysis
Best estimate calculations include weather variability in the consequences
Probabilistic UA includes both the weather variability and the uncertainty in the epistemic input parameters
||H|| is the mean consequence for a specific accident sequence, e.g., latent cancer fatality risk

## Slide 14
Probabilistic Uncertainty analysis is an iterative process
Scenario Selection
current MELCOR model/software
current WinMACCS model/software
Inputs & Parameter Selection
informal expert elicitation from SMEs & Peer Review
Uncertainty Analysis
Framework
MELCOR Uncertainty Engine
MELCOR
MELMACCS
WinMACCS/LHS
Uncertainty Analysis
regression analyses
scatter plots
Single Realization phenomenological analysis
Stability Analysis
# realization stability
random seed stability
alt. modeling cases
Iterate
Range of validity
Stability of analysis
Alternative model scenarios
  SRV Stochastic
  SRV Thermal
  MSL Creep Rupture
Sensitivity Analysis
Address Bugs or Modeling Errors
Analysis Complete

## Slide 15: Process for Choosing Parameters and Distributions
Core team of staff from SNL and NRC with expertise in probability and statistics, uncertainty analysis, and MELCOR and MACCS modeling for SOARCA
Approach used informal expert elicitation
Focus on confirming that the parameter representations appropriately reflect key sources of uncertainty, are reasonable, and have a defensible technical basis
Attempt to obtain contribution from uncertainty across the spectrum of phenomena operative in the analyses

## Slide 16: Core Team Members
MELCOR and severe accident progression: SNL staff including Randy Gauntt, Kyle Ross, Doug Osborn, Don Kalinich, Mike Young, Jeff Cardoni, Andrew Goldmann; Mark Leonard (dycoda); Ed Fuller (NRC)
MACCS, consequence analysis and emergency response: SNL staff including Nate Bixler, Joe Jones, Doug Osborn
UA methodology: SNL staff including Patrick Mattie, Cedric Sallaberry, Jon Helton; Tina Ghosh (NRC)
Consultants for MACCS latent health effects modeling: Keith Eckerman (ORNL); Tony Huffert (NRC)

## Slide 17: MELCOR Uncertain Parameters
Sequence Issues
Battery duration
SRV stochastic failure rate
In-Vessel Accident Progression
SRV thermal seizure criteria,
  and open area fraction
Main steam line (MSL) creep rupture open area fraction
Zircaloy melt breakout temperature
Molten clad drainage rate
Fuel failure criterion
Debris radial relocation time constants (solid and liquid)
Ex-vessel Accident Progression
Debris lateral relocation time constants (solid and liquid)
Containment & building behavior
Drywell liner failure flow area
Drywell head flange leakage parameters
Hydrogen ignition criteria (where flammable)
Railroad doors open fraction
Fission Product release, transport, and deposition
Cesium and iodine chemical forms
Aerosol deposition parameter

## Slide 18
MACCS Uncertain Parameter Groups
Atmospheric Transport and Deposition
Wet deposition model linear coefficient
Dry deposition velocities
Dispersion parameters
Emergency planning and response
Shielding factors
Hotspot and normal relocation
Evacuation delay and speed
Health Effects
Early health effects
Latent health effects
    Groundshine dose coefficients
    Dose and dose rate effectiveness factors
    Inhalation dose coefficients
    Cancer mortality risk coefficients

## Slide 19: Overall UA Conclusions
Peach Bottom UA corroborates SOARCA study conclusions
  Public health consequences from severe nuclear accident scenarios modeled are smaller than previously calculated, and very small in absolute terms
  Delay in releases calculated provide more time for emergency response actions such as evacuating or sheltering; long-term phase dominates health effect risks because emergency response is faster than progression to release
  “Essentially zero” early fatality risk projected
Notes:   Comparison to Siting Study, NUREG/CR-2239
  The long-term dominates the overall health effect risk within the 10-mile emergency planning zone (EPZ) because the emergency response is faster than the onset of environmental release. More than half the time, the long-term is the larger contributor to overall health effect risk beyond the EPZ.

## Slide 20: Overall Conclusions (2)
A major determinant of source term magnitude and health consequences is whether the SRV sticks open before or after core damage, and compounding that, whether or not Main Steam Line (MSL) creep rupture occurs (leads to higher consequences)
    Health-effect risks vary sublinearly with source term because people are not allowed to return to their homes until dose is below habitability criterion
Analysis confirms known importance of some phenomena, and reveals some new phenomenological insights
The use of multiple techniques to post-process Monte Carlo results provides better explanatory power of which input parameters are most important to uncertainty in results

## Slide 21
MACCS Analysis: Public Health Consequence Results and Insights on Most Influential Parameters

## Slide 22: Conditional mean, individual latent cancer fatality (LCF) risk (per event) for combined results (865) with LNT model
 | 0-10 miles | 0-20 miles | 0-30 miles | 0-40 miles | 0-50 miles
5th percentile | 3x10-5 | 5x10-5 | 3x10-5 | 2x10-5 | 2x10-5
Median | 1x10-4 | 2x10-4 | 1x10-4 | 9x10-5 | 7x10-5
Mean | 2x10-4 | 3x10-4 | 2x10-4 | 1x10-4 | 1x10-4
95th percentile | 4x10-4 | 8x10-4 | 5x10-4 | 3x10-4 | 3x10-4
SOARCA UA Base Case | 9x10-5 | 8x10-5 | 6x10-5 | 4x10-5 | 3x10-5
Notes: 8.9, 7.6, 5.3, 3.3, 2.7

## Slide 23: Conditional mean, individual prompt-fatality risk (per event) for combined results (865)
 | 0 - 1.3 miles | 0 - 2.5 miles | 0 - 5 miles | 0 - 10 miles
Median and 75th percentile | 0 | 0 | 0 | 0
Mean | 5x10-7 | 9x10-8 | 1x10-8 | 5x10-9
95th percentile | 2x10-6 | 4x10-8 | ~0 | ~0

## Slide 24: Most Influential Parameters for Source Term Magnitude
The expected number of SRV cycles before failing to reclose (i.e., remain in the fully open position) (SRVLAM)
The chemical form of cesium (i.e., the amount of cesium as CsOH vs. Cs2MoO4) (CHEMFORM)
The size of the breach in the drywell liner resulting from core debris contacting and melting through the liner (FL904A)
The fractional open area of an SRV after it has failed to reseat because of overheating (SRVOAFRAC)
The time-at-temperature criterion specified for loss of “intact” fuel rod geometry (FFC – fuel failure criterion)
The temperature at which oxidized cladding mechanically fails (SC1131_2)
Whether railroad doors open, and fraction open (RRDOOR, RRIDFRAC)
Notes: Whether the stuck-open SRV occurs before or after the onset of core damage
Whether a MSL creep rupture occurs
Amount of cesium chemisorbed from CsOH onto the stainless steel of reactor pressure vessel (RPV) internals (initially unanticipated)
Whether core debris relocates from the RPV to the reactor cavity all at once or over an extended period of time
The degree of oxidation, primarily canister and fuel-cladding oxidation, occurring in-vessel
Whether a surge of water from the wetwell to the drywell floor occurs at drywell liner melt-through (unexpected)
Could not have gotten some of these insights with individual sensitivity analyses alone

## Slide 25: Most Influential Parameters for Individual LCF Risk
MACCS dry deposition velocity (VDEPOS)
MACCS residual cancer risk factor (CFRISK–Residual)
MELCOR SRV stochastic failure probability (SRVLAM)
MELCOR fuel failure criterion (FFC)
MELCOR drywell liner melt-through open area flow path (FL904A)
MACCS residual dose and dose-rate effectiveness factor (DDREFA–Residual)
Notes: The first three showed up as the most important consistently for all radial distances.
The next three showed some level of importance at all circular areas in at least one of the regression methods
Surprised some people that MELCOR parameters showed up as most important for LCF risk too
Benefit of doing integrated UA

## Slide 26: Most Influential Parameters for Individual Prompt Fatality Risk within 2 mile Circular Area
MACCS wet deposition parameter (CWASH1)
MELCOR SRV stochastic failure probability (SRVLAM)
MELCOR SRV open area fraction (SRVOAFRAC)
MELCOR DC station battery duration (BATTDUR)
MACCS early health effects threshold and beta (shape) factor for red bone marrow (EFFTHR-Red Marrow and EFFACB-Red Marrow)
MACCS linear, crosswind dispersion coefficient (CYSIGA)
Notes: Useful for model validation
Makes sense that Battery Duration shows up here because timing of release, tied directly to when battery fails, is important for prompt fatality risk (but not important for LCF risk in the LTSBO scenario)

## Slide 27
Relative Contributions of Aleatory (Weather) Uncertainty and Epistemic Uncertainty

## Slide 28: Aleatory (weather) Uncertainty Sensitivity Studies
Comparison of results using SOARCA sampling, versus using all available weather data in the year
  Miniscule difference
Comparison of effect of aleatory uncertainty versus epistemic uncertainty
  Epistemic uncertainty seems to bound the uncertainty stemming from weather, for the LNT model

## Slide 29
Weather sampling comparison of the conditional, mean, individual LCF risk (per event) using the LNT dose-response model
Distance | SOARCA UA Base Case | All Weather Trials | Difference (%)
10 | 9.0x10-5 | 8.9x10-5 | 0.8%
20 | 8.3x10-5 | 8.1x10-5 | 2.4%
30 | 5.8x10-5 | 5.7x10-5 | 1.7%
40 | 3.7x10-5 | 3.7x10-5 | 1.1%
50 | 3.0x10-5 | 3.0x10-5 | 1.3%

## Slide 30
Brief source term description for the single realizations selected from MELCOR analyses for the aleatory weather uncertainty analyses
Scenario | Integral Release Fractions by Chemical Group |  |  |  |  |  |  |  |  | Atmospheric Release Timing | 
 | Xe | Cs | Ba | I | Te | Ru | Mo | Ce | La | Start (hr) | End (hr)
SOARCA UA Base Case | 0.981 | 0.005 | 0.010 | 0.025 | 0.019 | 0 | 0 | 0 | 0 | 19.9 | 48
RLZ062 | 0.995 | 0.055 | 0.014 | 0.104 | 0.089 | 0 | 0.012 | 0 | 0 | 13.6 | 48
RLZ170 | 0.985 | 0.020 | 0.022 | 0.031 | 0.027 | 0 | 0 | 0.001 | 0 | 16.6 | 48

## Slide 31: CCDFs of conditional, mean, individual LCF risk (per event) within the 10‑mile circular area for aleatory weather uncertainty, the epistemic uncertainty analysis
— Base Case Weather
— Rlz062 Weather
— Rlz170 Weather
— Epistemic Uncertainty

## Slide 32: CCDFs of conditional, mean, individual LCF risk (per event) within the 50‑mile circular area for aleatory weather uncertainty, and the epistemic uncertainty analysis
— Base Case Weather
— Rlz062 Weather
— Rlz170 Weather
— Epistemic Uncertainty

## Slide 33: Relative Contributions of Different Sources of Uncertainties
Uncertainty in LCF risk stems from:
Epistemic uncertainty in source term analysis, from uncertain MELCOR parameters
Aleatory uncertainty due to unknowable weather conditions
Epistemic uncertainty in off-site consequence analysis, from uncertain MACCS parameters
Notes: The next two slides show the contribution first from source term alone, then a comparison of the epistemic uncertainty in off-site consequence modeling parameters alone (captured as the means from all the weather trials) vs. the epistemic uncertainty combined with the aleatory/weather uncertainty in the off-site consequence modeling.

## Slide 34: Conditional Mean, Individual LCF Risk (per Event) for 865 Source Terms and Fixed MACCS Inputs
Individual LCF Risk per Event
CCDF
Chart: 
Notes: Contribution to uncertainty in LCF risk from source terms alone (MELCOR analysis)

## Slide 35: Conditional Individual LCF Risk (per Event) CCDFs for Combined Aleatory and Epistemic Uncertainty and Epistemic Uncertainty with Aleatory Means
Individual LCF Risk
Chart: 
0-10 miles Epistemic & Aleatory | 0.01 | 0.05 | 0.1 | 0.15 | 0.2 | 0.25 | 0.3 | 0.35 | 0.4 | 0.45 | 0.5 | 0.55 | 0.6 | 0.65 | 0.7 | 0.75 | 0.8 | 0.85 | 0.9 | 0.95 | 0.99
0-20 miles Epistemic & Aleatory | 0.01 | 0.05 | 0.1 | 0.15 | 0.2 | 0.25 | 0.3 | 0.35 | 0.4 | 0.45 | 0.5 | 0.55 | 0.6 | 0.65 | 0.7 | 0.75 | 0.8 | 0.85 | 0.9 | 0.95 | 0.99
0-50 miles Epistemic & Aleatory | 0.01 | 0.05 | 0.1 | 0.15 | 0.2 | 0.25 | 0.3 | 0.35 | 0.4 | 0.45 | 0.5 | 0.55 | 0.6 | 0.65 | 0.7 | 0.75 | 0.8 | 0.85 | 0.9 | 0.95 | 0.99
CCDF

## Slide 36: Other Content in UA Report
Separate sensitivity analyses for lower-head penetration failures, operator action timing (manual depressurization), habitability criterion
Hydrogen generation insights
Fukushima comparison
Stability analysis for results, statistical convergence
Probabilistic analysis methodology
MELCOR version changes since best-estimate analysis was complete, and their effects
Peer review & ACRS comment resolution

## Slide 37: Status
April 2013 draft of NUREG/CR-7155, documenting the SOARCA Peach Bottom Uncertainty Analysis, publicly available in ADAMS
Currently addressing comments from NRC offices and the ACRS
Publication of the final NUREG/CR-7155 report planned in 2014
Notes: Conference presentations on UA approach and parameter selection:
  PSAM 11/ESREL-2012 – June 2012
  IAEA Technical Meeting on Level 3 PSA – July 2012
  CSARP – September 2012

## Slide 38
Questions and Comments

## Slide 39: Back-up slides

## Slide 40
MELCOR Analysis: Source Term Results and Insights on Most Influential Parameters

## Slide 41: SRV Stochastic Failures from Replicate 1 and Single Realizations chosen for analysis

## Slide 42: Fraction of the cesium core inventory released to the environment for all (865) results for the PB Unmitigated LTSBO
Notes: By contrast, the
1982 Siting Study SST1 case calculated an iodine release of 45 percent and a cesium release of
67 percent of the core inventory.
Starting at 1.5 hours

## Slide 43: Fraction of the iodine core inventory released to the environment for all (865) results for the PB Unmitigated LTSBO
Notes: SOARCA best estimate was on the order of 2-3% -- again, between median and 5th percentile of UA results

## Slide 44
 | Rank Regression |  |  | Quadratic |  |  | Recursive Partitioning |  |  | MARS |  | 
Final R2 --Variance explained | 0.61 |  |  | 0.64 |  |  | 0.90 |  |  | 0.66 |  | 
Input name | R2 inc. | R2 cont. | SRRC | Si | Ti | p-val | Si | Ti | p-val | Si | Ti | p-val
SRVLAM | 0.50 | 0.50 | -0.72 | 0.39 | 0.64 | 0.00 | 0.43 | 0.70 | 0.00 | 0.57 | 0.68 | 0.00
FL904A | 0.53 | 0.03 | 0.19 | 0.01 | 0.04 | 0.12 | 0.06 | 0.02 | 0.44 | 0.00 | 0.03 | 0.10
FFC | 0.55 | 0.02 | 0.19 | 0.04 | 0.05 | 0.31 | 0.02 | 0.10 | 0.00 | 0.01 | 0.08 | 0.00
RRDOOR | 0.58 | 0.03 | 0.33 | 0.02 | 0.10 | 0.00 | 0.02 | 0.03 | 0.19 | --- | --- | ---
SRVOAFRAC | 0.59 | 0.02 | -0.13 | 0.07 | 0.19 | 0.00 | 0.11 | 0.33 | 0.00 | 0.12 | 0.27 | 0.00
CHEMFORM | 0.60 | 0.01 | 0.09 | 0.00 | 0.08 | 0.38 | 0.01 | 0.18 | 0.00 | 0.02 | 0.00 | 0.87
SC1131_2 | 0.60 | 0.01 | -0.07 | 0.02 | 0.01 | 0.63 | 0.00 | 0.07 | 0.00 | 0.00 | 0.04 | 0.01
Regression analyses of fraction of cesium released over 48 hours
Notes: Notice the Ti values are quite high for some variables, and these interaction effects are not captured by standardized linear rank regression
Shows importance of SRVLAM coupled with SRVOAFRAC (to determine scenario), and in turn importance of CHEMFORM depending on scenario;

## Slide 45
Cumulative distribution function of fraction of cesium core inventory released to the environment after 48 hours based on all combined (i.e., 865) results, with 95% confidence interval over statistical measures

## Slide 46
SRV Seizure Versus MSL Rupture
Main Steam Line Rupture vents
Fission products to drywell
Release to environment via head
Flange failure or drywell liner melt through
SRV Seizure vents fission products
Into wetwell
Wetwell scrubbing prevents release
To the environment
MSL Rupture
SRV cycles long time
MSIV
SRV sticks open

## Slide 47: SRV Thermal Failures without MSL rupture from Replicate 1 and Single Realizations chosen for analysis

## Slide 48
SRV Thermal Failures with MSL creep rupture from Replicate 1 and Single Realizations chosen for analysis

## Slide 49
Cumulative distribution function of SRVOAFRAC with samples where MSL creep rupture indicated for Replicate 1