## Slide 1
World Meteorological Organization’s Evaluation of the Radionuclide Dispersion and Deposition from the Fukushima Daiichi Nuclear Power Plant Accident
Glenn Rolph
Dr. Ariel Stein
Roland Draxler
NOAA Air Resources Laboratory
September 21-22, 2015
International MACCS User’s Group Meeting
Bethesda, MD USA
Notes: This presentation is based on the research paper titled, “World Meteorological Organization’s model simulation of the radionuclide dispersion and deposition from the Fukushima Daiichi nuclear power plant accident” in the Journal of Environmental Radioactivity, 139 (2015), 172-184, doi:10.1016/j.jenvrad.2013.09.014.

## Slide 2
World Meteorological Organization (WMO)
Regional Specialized Meteorological Centers (RSMC)
After Chernobyl, the WMO, on request from the IAEA, established the current 8 RMSCs to provide dispersion model products to WMO member countries meteorological services and the IAEA in the event of a nuclear accident
In 1993, RSMC Washington was accepted as an RSMC by WMO and is operated by NOAA (National Centers for Environmental Prediction and the Air Resources Laboratory)
RSMC Washington operates jointly with RSMC Montreal to provide products to the Americas
NOAA’s HYSPLIT dispersion model is used by 3 RSMCs (Washington, Beijing, Melbourne)
Notes: RSMC Washington, jointly with RSMC Montreal, provides dispersion model products to the IAEA and WMO member countries in North, Central and South America in the event of a major nuclear accident. It was established in 1993 and operated jointly by NOAA’s National Centers for Environmental Prediction and the Air Resources Laboratory.

## Slide 3
In 2011, a WMO task team was established to assist the United Nations Scientific Committee on the Effects of Atomic Radiation (UNSCEAR) with the meteorological aspects of the accident
Task: how meteorological analyses and other observational data could improve atmospheric transport, dispersion and deposition calculations
Plan: best way to evaluate the suitability of the various meteorological analyses for the assessment was to actually use the meteorological data in Atmospheric Transport Dispersion and Deposition Models (ATDM)
Results: compare the model predictions against radiological monitoring data
WMO Task Team
http://dx.doi.org/10.1016/j.jenvrad.2013.09.014
Notes: The WMO Task Team was organized to assist UNSCEAR in providing the best meteorological analyses to use in the evaluation of the transport, dispersion, and deposition from the NPP accident. The Task Team decided that the best way to approach the question was use their individual dispersion and deposition models (ATDM) with the various meteorological data available and compare the model results against radiological monitoring data.

## Slide 4
NOAA - Roland Draxler (Lead), National Oceanic and Atmospheric Administration, College Park, MD, USA
WMO - Peter Chen, World Meteorological Organization, Geneva, Switzerland
UKMET - Matthew Hort, Met Office, Exeter, United Kingdom
CMC - Alain Malo, Canadian Meteorological Centre, Dorval, Canada
JMA - Kazuo Saito, Japan Meteorological Agency, Ibaraki, Japan
ZAMG - Gerhard Wotawa, Zentralanstalt für Meteorologie und Geodynamik, Vienna, Austria
Members of the WMO Task Team
Notes: The WMO Task Team members consisted of representatives from several of the WMO Regional Specialized Meteorological Centers, which are part of the WMO Emergency Response Activities program (http://www.wmo.int/pages/prog/www/DPFSERA/EmergencyResp.html). The Task Team was assisted in its work by individual contributors from each organization as well as the EC Joint Research Centre’s ENSEMBLE project (http://ensemble2.jrc.ec.europa.eu/public/) with respect to the analyses of the modeling results.

## Slide 5
CMC’s Global Environmental Multiscale (GEM) system
  6 hourly at 0.30 degrees
NOAA’s Global Data Assimilation System (GDAS)
  3 hourly at 0.50 degrees on hybrid sigma and pressure levels
The European Centre for Medium-Range Weather Forecasts (ECMWF)
  3 hourly at 0.125 and 0.20 degrees on hybrid sigma levels
UKMET’s operational global configuration of the Unified Model (MetUM)
  3 hourly at 0.23 x 0.35 degrees on height levels
  _____________________________________________________________________
JMA’s mesoscale analyses fields (MESO)
  3 hourly at 5 km resolution on hybrid height levels
JMA’s radar-rain gauge-analyzed precipitation (RAP) dataset
  Hourly accumulations every 30 minutes at 30 x 45 seconds resolution (~ 1 km)
Meteorological Analyses
GLOBAL
LOCAL
Notes: There were four global meteorological analyses data sets available to the Task Team: from the CMC, NOAA, ECMWF, and UKMET. The JMA provided two regional high-resolution analyses. The MESO analysis consisted of 3D fields of the key meteorological variables needed for dispersion deposition calculations and the RAP dataset provided radar- rain-gauge analyzed precipitation fields for use in the models. Not all of the ATDMs were able to use all of the meteorological data combinations. All of the ATDMs required substantial modification to use the JMA MESO analysis.

## Slide 6
NOAA’s HYSPLIT - the Hybrid Single-Particle Lagrangian Integrated Trajectory
CMC’s MLDP0 - Modèle Lagrangien de Dispersion de Particules d’ordre 0
JMA’s RATM - Regional Atmospheric Transport Model
UKMET’s NAME - Numerical Atmospheric-dispersion Modelling Environment
ZAMG’s FLEXPART - Lagrangian Particle Dispersion Model
Atmospheric Transport Dispersion and Deposition Models (ATDM)
Off-line Lagrangian Particle Models
Notes: All the ATDM’s available to the Task Team members were of a class of models called Lagrangian Particle Models (LPDMs). Individual pollutant particles or gases are followed in a computational framework that follows the position of the individual element by its mean motion from the wind fields and a turbulent component to represent the dispersion. These models are all run off-line, meaning that the meteorological fields need to be available as input to the ATDM.

## Slide 7
ATDM-Meteorology | CMC | NOAA | ECMWF | UKMET | JMA
CMC-MLDP0 | C |  |  |  | C
JMA-RATM |  |  |  |  | C,R
NOAA-HYSPLIT |  | C,R | C,R |  | C,R
UKMET-NAME |  |  | C | C | C,R
ZAMG-FLEXPART |  | C,R | C,R |  | 
Completed ATDM-Meteorology Simulations
C – completed simulations
R – RAP data replaced model precipitation
Limited use of other meteorological data sets by each dispersion model indicates the difficulty of incorporating external data into the dispersion models.
Notes: As noted earlier, not all of the ATDMs were able to use all of the meteorological data combinations. Shown in the table are the completed simulations (C) of each ATDM with respect to the input meteorological data analyses. The “R” signifies when the calculation was done with the same meteorological data but replacing the wet deposition precipitation scavenging calculation with the radar- rain-gauge analyzed precipitation.

## Slide 8
Each ATDM retained unique treatment of deposition (largest uncertainty), but otherwise were configured similarly.
Unit source (1 Bq/m3) release every 3-h from 11-31 March
Uniform from the ground to 100 m
168 simulations of duration of 72 h
601 by 401 grid cells
0.05 degrees resolution (about 5 km)
3-h averaged for air concentrations
  From the ground to 100 m
3-hour deposition accumulations
3 surrogate radionuclides
  gas with no wet or dry scavenging (noble gases)
  gas with a relatively large dry deposition velocity and wet removal (I-131)
  particle with wet removal and a small dry deposition velocity (Cs-137)
ATDM Configuration
Conc./deps. grid
JMA MESO grid
Notes: All the ATDMs were configured identically as much as possible in terms of the dispersion and deposition configuration such as release duration, height, concentration grid size and resolution. Each ATDM retained its unique treatment of wet and dry deposition, one of the largest uncertainties in these calculations and thereby providing for a range of possible solutions. However, each ATDM was also configured to represent at a minimum three different surrogate radionuclide species in terms of the deposition parameterization. These surrogate species results are post-processed with the appropriate emission rates and half-life to represent specific radionuclides.

## Slide 9
Computational Approach Transfer Coefficient Matrix (TCM)
Cj,k,m = ∑ Qi,m Dm TCMi,j,k,m
Q is the emission rate for release (i) and species (m)
D is the species (m) dependent radioactive decay factor
i represents the number of time varying releases
j represents the number of sampling periods
Concentration and deposition are available over k grid points
with each new release (i), there will be one less output period (j)
Computations are made with a unit emission
TCM is computed for each computational species (scavenging dependent)
The emission (Q) and decay (D) are applied in a post-processing step allowing for multiple emission scenarios
Notes: All the ATDM calculations were performed in such a manner to define the elements of a Transfer Coefficient Matrix (TCM). That is each 3-hour release period was treated as an independent computation with a 72 h particle duration. The period of 11-31 March required 168 simulations. Naturally for global scale calculations, the duration would need to be much longer. Computations were done using a unit release rate (1 per hour). In the post-processing step, the results from each simulation would be multiplied by the actual emission rate and decay factor for the radionuclide desired. The individual simulation results added together for each output time period. For instance, in the example shown the concentration and deposition is calculated 36 hours after the start of the first release, but only 33 hours after the start of the second release.

## Slide 10
Cs-137 Emission Rates Chino et al. (2011) modified by Terada et al. (2012)
Notes: The TCM approach easily permits the testing of multiple emission scenarios. However, determining the optimal emissions was not part of the Task Team effort. For the results shown in this presentation, we used the Cs-137 emissions originally derived by Chino et al. (2011) and later modified by Terada et al. (2012). The emission rates were tabulated into 168 values representing the hourly emission rate for each simulation valid over one 3 hour emission period.
Chino, M., H. Nakayama, H. Nagai, H. Terada, G. Katata, and H. Yamazawa, 2011, Preliminary Estimation of Release Amounts of 131I and 137Cs Accidentally Discharged from the Fukushima Daiichi Nuclear Power Plant into the Atmosphere, Journal of Nuclear Science and Technology, 48 (7), 1129–1134, doi:10.1080/18811248.2011.9711799.
Terada,H., G. Katata, M. Chino, and H. Nagai, 2012, Atmospheric discharge and dispersion of radionuclides during the Fukushima Dai-ichi Nuclear Power Plant accident. Part II: verification of the source term and analysis of regional-scale atmospheric dispersion, Journal of Environmental Radioactivity, 112, 141–154, doi:10.1016/j.jenvrad.2012.05.023.

## Slide 11
Website Interface
http://ready.arl.noaa.gov/READY_fdnppwmo.php
Web interface created to assist task team with interpretation
Permits selection of ATDM, emission rate, radionuclide, and measurement data
Creates maps and graphics of model results in common format
Notes: To assist the Task Team evaluation efforts, a web interface was designed to permit the selection of the ATDM, emission rate, radionuclide, and measurement data. The web interface output provides graphical results in a common format for all models, model performance statistics compared with measurement data, and various output options from native binary to NetCDF.

## Slide 12
Monitoring Data for ATDM Verification
- JAEA Tokai-mura
- Takasaki
Asahi Shimbun newspaper (11/21/2011)
Air monitoring sites:
Notes: Two measurement data sets were used in these evaluations. The first consisted of Cs-137 deposition measurements shown in the left panel, averaged together from aircraft monitoring and ground based sampling. The available deposition data did not have the same spatial coverage as the maps frequently reproduced in the media and elsewhere, an example is shown in the right panel. The available digital data did cover the high deposition Fukushima Prefecture and could more easily be used in quantitative verification. There were 543 grid points with data for model verification. The other data consisted of a time series of air concentration measurements at the Japan Atomic Energy Agency site at Tokai-mura located to the south of the Fukushima NPP. The Takasaki site was not used due to unresolved contamination issues.

## Slide 13
Model Results (Cs-137)
CMC-MESO
Deposition
Air Concentration
Modeled
Measured
Notes: There were 18 ATDM-meteorology combinations available for analysis. The Cs-137 total deposition and air concentration time series for four different models all using the JMA MESO analyses are shown in this and the next three slides. In terms of the deposition pattern, it is interesting that although using the same meteorological analysis, each model can produce quite different patterns, perhaps understandably at the further distances from the source, but this is true even in the close-in high-deposition region. The variability in the prediction is also evident in the air concentration time series. These results are shown to illustrate that model performance is not just dependent upon having the best meteorology to drive the calculations, but also depends upon the pre-processing and other transformations that are required for an ATDM to use meteorological data.

## Slide 14
Model Results (Cs-137)
UKMET-MESO
Deposition
Air Concentration
Modeled
Measured

## Slide 15
Model Results (Cs-137)
JMA-MESO
Deposition
Air Concentration
Modeled
Measured

## Slide 16
Model Results (Cs-137)
NOAA-MESO
Deposition
Air Concentration
Modeled
Measured
Notes: The NOAA ATDM result shows considerable granularity and had the worst quantitative performance of these four ATDMs when using the MESO data. This was not true when using other meteorological data.

## Slide 17
Model Results (Cs-137)
NOAA-ECMWF
Deposition
Air Concentration
Modeled
Measured
Notes: The NOAA ATDM result shows considerable granularity and had the worst quantitative performance of these four ATDMs when using the MESO data. This was not true when using other meteorological data.

## Slide 18
Ensemble Approach to Model Selection
Instead of looking at individual results, we could calculate an ensemble mean
However, ensemble mean may not provide better results if models are not truly independent (share modules, etc.)
Given observed variability, select a subset of models that provides non-redundant information, which should give better results than ensemble mean.
JRC ENSEMBLE (Galmarini and Solazzo) approach was used to calculate the minimum number of ensemble members to reproduce the observed variability in deposition by minimizing RMSE.
Conclusion: 5 models out of 18 minimizes RMSE (NOAA-GDAS, UKMET-MESO, UKMET-ECMWF, NOAA-ECMWF, and ZMAG-ECMWF)
These results (5 members) are case specific.
Notes: Rather than relying upon an individual ATDM-meteorology combination for assessment purposes, when multiple model results are available it is possible to create an ensemble mean. In this situation, because measurement data are available it is possible to select a subset of models for the ensemble that provides non-redundant information. An ensemble mean of all the models could provide poorer performance than a subset of models selected for their independence. The JRC ENSEMBLE (Galmarini and Solazzo) approach relies upon comparing the deviations of the individual model results from the mean model to the deviations of the models to the measurements through principal component analysis. See Potempski and Galmarini (2009) and Solazzo (2012) for a more detailed discussion. They found that 5 of the 18 ATDM-meteorology combinations could account for most of the variability in the measurements.

## Slide 19
Ensemble Options for the Cs-137 Deposition Evaluation
Minimum Set | Select (Ten Member) Set
NOAA-GDAS | NOAA-GDAS
UKMET-MESO | NOAA-ECMWF
UKMET-ECMWF | UKMET-MESO
NOAA-ECMWF | UKMET-ECMWF-RAP
ZAMG-ECMWF | ZAMG-GDAS
 | ZAMG-ECMWF-RAP
 | JMA-MESO
 | JMA-MESO-RAP
 | CMC-GEM
 | CMC-MESO
Notes: The five optimal model combinations are shown in the left column of the table. Note however that at the time of the analysis, only preliminary results for some of the models were available (JMA). Subsequent revised calculations (used in this presentation) showed better performance than the original calculation. The other column represents a compromise 10-member set (each ATDM with two different meteorological analyses). A compromise solution may be required because the minimum models set were optimized for a pre-determined performance metric (mean square error), a specific set of measurement data (deposition), and the particular ATDMs and meteorology combinations available for the evaluation.

## Slide 20
Cs-137 Deposition Evaluation
Center | Meteorology | CC | NMSE | FB | FMS | KSP | RANK
CMC | GEM | 0.75 | 6.16 | -0.32 | 100 | 19 | 3.22
CMC | MESO | 0.76 | 8.88 | -0.44 | 100 | 6 | 3.29
JMA | MESO | 0.71 | 4.81 | -0.04 | 100 | 10 | 3.37
JMA | MESO-R | 0.84 | 3.79 | 0.56 | 99 | 13 | 3.28
NOAA | ECMWF | 0.83 | 4.20 | -0.30 | 100 | 10 | 3.44
NOAA | ECMWF-R | 0.55 | 14.09 | -0.74 | 100 | 33 | 2.60
NOAA | GDAS | 0.87 | 2.59 | -0.08 | 100 | 6 | 3.65
NOAA | GDAS-R | 0.67 | 9.72 | -0.57 | 100 | 23 | 2.94
NOAA | MESO | 0.56 | 5.91 | 0.38 | 100 | 15 | 2.97
NOAA | MESO-R | 0.48 | 7.35 | 0.43 | 100 | 16 | 2.86
UKMET | UKMO | 0.46 | 8.14 | 0.24 | 100 | 30 | 2.80
UKMET | ECMWF | 0.80 | 2.87 | 0.11 | 100 | 25 | 3.34
UKMET | MESO | 0.76 | 3.86 | 0.04 | 100 | 11 | 3.45
UKMET | MESO-R | 0.66 | 4.86 | 0.03 | 100 | 9 | 3.33
ZAMG | GDAS | 0.67 | 12.69 | -0.59 | 100 | 10 | 3.05
ZAMG | GDAS-R | 0.66 | 18.32 | -0.84 | 100 | 20 | 2.82
ZAMG | ECMWF | 0.78 | 3.84 | -0.08 | 100 | 15 | 3.42
ZAMG | ECMWF-R | 0.83 | 2.55 | 0.13 | 100 | 6 | 3.56
Ensemble Mean | All | 0.85 | 3.27 | -0.04 | 100 | 13 | 3.57
Ensemble Mean | Select (10-member) | 0.89 | 2.65 | -0.04 | 100 | 15 | 3.62
Ensemble Mean | Minimum (5-member) | 0.89 | 2.48 | -0.05 | 100 | 17 | 3.60
1
2
3
4
Notes: A summary of all the performance metrics for deposition is shown. To avoid reliance upon a single metric, a Rank is computed, which is defined as the normalized sum of (CC, FB, FMS, KSP). The yellow highlight shows the best performance for each metric. In terms of NMSE, the best performance is the Ensemble-Minimum (the 5-member set), which was the evaluation metric in determining the 5-member set. In terms of overall performance (Rank and Correlation), the Ensemble-Select (the 10-member set), provides a level of performance very close to the optimized 5-member set. Another noteworthy result is that when comparing individual ATDM results using global data (GEM, GDAS, ECMWF) versus the MESO data, all models (except NOAA) improved (in Rank) when the MESO data are used. Also when using the RAP data for wet removal, results were inferior to the calculations using the meteorological model derived precipitation fields.

## Slide 21
Cs-137 Air Concentration Evaluation
Center | Meteorology | CC | NMSE | FB | FMS | KSP | RANK
CMC | GEM | 0.10 | 70.86 | -1.37 | 75.0 | 54 | 1.54
CMC | MESO | 0.26 | 15.24 | -0.09 | 82.5 | 34 | 2.51
JMA | MESO | 0.45 | 16.43 | -0.40 | 77.5 | 44 | 2.34
JMA | MESO-R | 0.11 | 156.29 | -1.68 | 62.5 | 69 | 1.10
NOAA | ECMWF | 0.32 | 62.96 | -1.34 | 62.5 | 61 | 1.45
NOAA | ECMWF-R | 0.32 | 64.29 | -1.35 | 62.5 | 61 | 1.44
NOAA | GDAS | 0.32 | 71.23 | -1.37 | 60.0 | 71 | 1.31
NOAA | GDAS-R | 0.32 | 72.67 | -1.38 | 60.0 | 68 | 1.34
NOAA | MESO | 0.18 | 128.54 | -1.63 | 62.5 | 68 | 1.16
NOAA | MESO-R | 0.18 | 127.89 | -1.63 | 60.0 | 69 | 1.13
UKMET | UKMO | 0.10 | 78.35 | -1.42 | 67.5 | 54 | 1.44
UKMET | ECMWF | 0.17 | 35.91 | -0.93 | 70.0 | 54 | 1.72
UKMET | MESO | 0.29 | 21.33 | -0.50 | 80.0 | 53 | 2.10
UKMET | MESO-R | 0.29 | 21.95 | -0.53 | 80.0 | 53 | 2.09
ZAMG | GDAS | 0.23 | 22.88 | -0.37 | 57.5 | 58 | 1.87
ZAMG | GDAS-R | 0.27 | 23.83 | -0.43 | 57.5 | 56 | 1.87
ZAMG | ECMWF | 0.21 | 27.93 | -0.54 | 52.5 | 61 | 1.69
ZAMG | ECMWF-R | 0.18 | 30.81 | -0.56 | 42.5 | 71 | 1.47
Ensemble Mean | All | 0.27 | 31.19 | -0.88 | 82.5 | 36 | 2.10
Ensemble Mean | Select (10-member) | 0.30 | 26.77 | -0.77 | 82.5 | 34 | 2.19
Ensemble Mean | Minimum (5-member) | 0.22 | 32.98 | -0.89 | 75.0 | 51 | 1.85
1
2
3
4
4
Notes: A performance summary for air concentration is shown. Note that in this case the best performance over most of the metrics comes from the CMC-MESO combination. The 10-member ensemble (Select) is a close 3rd, considering the Rank, FMS, and CC. Not surprisingly, the performance for air concentration is quite different from the deposition results shown on the previous slide.

## Slide 22
ENSEMBLE 5-member set
Deposition
Air Concentration
Modeled
Measured
Notes: The results for the 5- and 10-member sets are shown in this and the next slide. There are small differences in the deposition pattern and the air concentration time series. The primary difference is that the 10-member set captures the 2nd peak in the air concentration time series.

## Slide 23
ENSEMBLE 10-member set
Deposition
Air Concentration
Modeled
Measured
Notes: The results for the 10-member set is shown in this slide. There are small differences in the deposition pattern and the air concentration time series from the 5-member set. The primary difference is that the 10-member set captures the 2nd peak in the air concentration time series.

## Slide 24
The ATDM computational framework permits existing unit source calculations to be adjusted to reflect changes in source term without rerunning the ATDM
The individual ATDM results tended to improve when the MESO analysis was used instead of global analyses (especially evident for the air concentration results)
  Individual ATDM results were very sensitive to how the MESO analysis was incorporated into the model’s computational framework
The use of the RAP data as input to the models in place of the NWP precipitation fields resulted in a deterioration of ATDM results
  Model results overall very sensitive to scavenging parameterizations
Additional spatial analyses of the ATDM results showed that the ensemble model performance for deposition could be improved by selecting different subsets of members
For the same subset of models, their ensemble mean performance could be quite different between air concentration and deposition
  Results sensitive to lack of air concentration measurement data
Due to the variability of individual model results and sensitivity to the evaluation metric, it is difficult to make an a-priori decision about which model to use, suggesting that one solution is to use the ensemble mean of multiple models
Summary and Conclusions

## Slide 25: HYSPLIT modeling capabilities
Includes an automated method of sequentially using multiple meteorological model grids going from finer to coarser horizontal resolution.
Calculation of the dispersion rate from the vertical diffusivity profile, wind shear, and horizontal deformation of the wind field
Different kinds of Lagrangian representations of the transported air masses: 3D particles, Top Hat Puff, Gaussian Puff and combinations of the three. These mass representations can be transferred to an Embedded Global Eulerian Model (GEM) to maintain computational efficiency for long-range calculations.
In-line integration capability with the Weather Research and Forecast (WRF) meteorological model making use of higher frequency availability of meteorological variables.
Includes emissions estimates updates based on inverse modeling technique.
Incorporates tools for uncertainty estimation using dispersion ensembles.
Model applications include: Volcanic ash, dust, wild fire smoke, ozone photochemistry, mercury, allergens, viruses, tracer experiments and radionuclides.
Notes: Summary of NOAA HYSPLIT transport and dispersion model capabilities.

## Slide 26
Extra Slides

## Slide 27
Model Results (Cs-137)
NOAA-GDAS
Deposition
Air Concentration
Modeled
Measured
Notes: The NOAA ATDM result shows considerable granularity and had the worst quantitative performance of these four ATDMs when using the MESO data. This was not true when using other meteorological data.

## Slide 28
Model Results (Cs-137)
NOAA-WRFARW
Deposition
Air Concentration
Modeled
Measured
Notes: The NOAA ATDM result shows considerable granularity and had the worst quantitative performance of these four ATDMs when using the MESO data. This was not true when using other meteorological data.

## Slide 29
Cs-137; global sampling; HYSPLIT; GDAS ½ degree meteorology;
original and final deposition scheme
Original wet removal
Final wet removal
Notes: Scatter diagrams showing calculated Cs-137 air concentrations and measurements from the CTBTO’s global network, the U.S. EPA’s radiation monitoring network (RADNET), and from various European countries. The data shown on the left represent the original calculation of wet removal that uses an in-cloud scavenging ratio and below cloud scavenging coefficient (removal time-constant) , and on the right is the final method, where the in-cloud scavenging ratio method was replaced by scavenging coefficients for both in-cloud and below-cloud removal, the same approach as the UK NAME model. Note that the final method did not perform as well as the original for the local deposition over the Japanese mainland. The disparity between local and long-distance wet scavenging results is attributed to the inadequate spatial resolution in wind fields, precipitation, and the timing of the radionuclide releases.

## Slide 30
I-131; global sampling; HYSPLIT; GDAS ½ degree meteorology;
original and final deposition scheme
Original wet removal
Final wet removal
Notes: Scatter diagrams showing calculated I-131 air concentrations and measurements from the CTBTO’s global network, the U.S. EPA’s radiation monitoring network (RADNET), and from various European countries. The data shown on the left represent the original calculation of wet removal that uses an in-cloud scavenging ratio and below cloud scavenging coefficient (removal time-constant) , and on the right is the final method, where the in-cloud scavenging ratio method was replaced by scavenging coefficients for both in-cloud and below-cloud removal, the same approach as the UK NAME model.

## Slide 31
Cs-137 at Melbourne, Florida; HYSPLIT; GDAS ½ degree meteorology;
original and final deposition scheme
Original wet removal
Final wet removal
Notes: Time series showing calculated and measured Cs-137 air concentrations from Melbourne, Florida. The data shown on the left represent the original calculation using an in-cloud scavenging ratio, and on the right is the final method, where the scavenging ratio method was replaced by the scavenging coefficient approach (removal time-constant).

## Slide 32
Ensemble Approach to Model Selection
Project the observed anomalies onto the principal components (PCs) of the covariance matrix of the deviation of the models from the mean
The first (largest) eigenvalue accounts for more than twice the observed spatial variability
The mean model explains 9 times the observed deposition variability
There is a substantial amount of redundant variability
Identify which model results are meaningful with respect to the observed variability
Identify the subset of models that provides non-redundant information
Notes: Rather than relying upon an individual ATDM-meteorology combination for assessment purposes, when multiple model results are available it is possible to create an ensemble mean. In this situation, because measurement data are available it is possible to select a subset of models for the ensemble that provides non-redundant information. An ensemble mean of all the models could provide poorer performance than a subset of models selected for their independence. The JRC ENSEMBLE (Galmarini and Solazzo) approach relies upon comparing the deviations of the individual model results from the mean model to the deviations of the models to the measurements through principal component analysis. See Potempski and Galmarini (2009) and Solazzo (2012) for a more detailed discussion. They found that 5 of the 18 ATDM-meteorology combinations could account for most of the variability in the measurements.