## Slide 1: Some issues on MACCS application in dividing EPZ of NPPs of China
Department of Nuclear Emergency & Radiation Environment Monitoring
Nuclear and Radiation Safety Centre
Ministry of Environmental Protection, P. R. China
LI Bing, HOU Jie

## Slide 2: Contents
Emergency Planning Zones of NPPs in China
Method of Dividing Emergency Planning zone in Support of NPPs
  Accidents Considerations
  Safety Criteria
    Plume Exposure EPZ
    Ingestion Exposure EPZ
Some Issues on MACCS Application in Dividing EPZ of NPPs of China

## Slide 3
NPP | Overview | Plume exposure EPZ（Radius, km） |  | Ingestion EPZ（Radius, km）
 |  | Inner Zone | Outer Zone | 
Qinshan | 1 CNP300+4 CNP600+2 CNP1000+2 CANDU6 (All operating) | 5.25 | 7 | 30
Daya Bay | 4 M310 +2 CPR1000 (All operating) | 5 | 10 | 50
Hongyanhe | 2 CPR1000 (operating)+ 2 CPR1000 (constructing) | 5 | 10 | 50
Tianwan | 2 WWER-1000/B-428 (operating)+ 2 WWER-1000/B-428 (constructing) | 4 | 8 | 30
Ningde | 2 CPR1000 (operating)+ 2 CPR1000 (constructing) | 5 | 10 | 50
Fuqing | 2 M310 plus (operating)+ 2 M310 plus (constructing) +2 hualong-1 (planned) | 5 | 10 | 50
Yangjiang | 2 CPR1000 (operating)+ 4 CPR1000 (constructing) | 5 | 10 | 50
Changjiang | 2 CNP650(constructing)+ 2 CNP600 (planned) | 5 | 10 | 50
Haiyang | 2 AP1000 (operating)+ 4 AP1000 (planned) | 5 | 10 | 50
Fangchenggang | 2 CPR1000 (operating)+ 2 CPR1000 (constructing)+2 hualong-1 (planned) | 5 | 10 | 50
Taishan | 2 EPR (constructing) | 5 | 10 | 50
Sanmen | 2 AP1000 (constructing)+ 4 AP1000 (planned) | 5 | 10 | 50
Overview of China NPPs’ EPZ

## Slide 4: Method of Dividing Emergency Planning zone in Support of NPPs(GB/T 17680.1-2008)
  Accidents Considerations
    Both Design Basis Accidents and Severe Accidents should be considered in dividing EPZ
      Design Basis Accidents – DBA LOCA (RG 1.183)
      Severe Accidents – S3, PSA
    For such accidents of exceedingly low occurrence probability, do not need to be considered

## Slide 5: Method of Dividing Emergency Planning zone in Support of NPPs(GB/T 17680.1-2008)
Safety Criteria (with Reference to NUREG 0654)
  The size of the Plume Exposure EPZ was based primarily on the following considerations:
    projected doses from severe accident sequences which consequences are the worst , would not exceed dose levels at which intervention is expected to be undertaken under any circumstances according to GB 18871 outside the zone
    For the design basis accidents and most severe accident sequences, avertable doses of urgent protective actions would not exceed the generic optimized intervention values according to GB 18871 outside the zone

## Slide 8
The size of the Ingestion Exposure EPZ was based on the following considerations:
      For most severe accident sequences, contamination levels of foods and drinking water would not exceed the generic action levels for foodstuffs intervention values according to GB 18871 outside the zone

## Slide 10
For PWR NPPs, consider thermal power
  Plume Exposure EPZ : 7 km~10 km Radius of Inner Area 3 ~ 5 Km

## Slide 11
Application of WinMACCS
  Review to Ingestion EPZ of Nuclear Power Station
  Version: WinMACCS 3.7.0
  Source Term: S3(severe accidents)
  Module Used: General, ATMOS, EALAY, Dose Coefficients

## Slide 12
Site Specific Information
  Meteorological File
  8760h data from 31st July 2011 to 31st July 2012
  Inventory
  Radioactivity with 18 months of refueling
  Calculation Grids
  16 directions extend to 40kms with 26 circles
  Population
  Uniform, 400 per square kilometers
  Dispersion Stability
  Site Specific

## Slide 14
Source Term of S3

## Slide 15
Caculation results
  7 days effective dose with different distances under the probability of 50%, 90%, 95% and 99%
  At the distance of 5km, the exceeding probability of 50mSv is 6.37E-02

## Slide 16: Some Issues on MACCS Application in Dividing EPZ of NPPs of China
The effect of spatial grid to the calculation results.
  SPAEND value should be uniform or changed with distances.
Advanced use of RUNMODELS.
  The use of more number of simulation.
  during what kind of calculation, the software need simulations can be defined as larger than 1. If possible, the explicit example can be clarified.
The interface of WinMACCS to the MELCOR.
  For further analysis of exceeding probability based on source term calculation of MELCOR stems from software of MELMACCS.
  If there we can get further enhancement on MELCOR and WinMACCS calculation. It will helpful for analysis to different types of reactor for review.
SECPOP for site specific files.
  To get more information from site specific data, the use of SECPOP will be benefit more to the application.
  The share of SECPOP will be helpful for input of site specific information.
Flexible output of concentration of radioactivity
  Calculating the ingestion plume EPZ, the output of radionuclide activity concentrations in water and food is needed for comparing with generic action levels of national standard.
Dose conversion coefficients file
  During the calculation, the dose conversion coefficients file can be modified adapted to the users need since dose conversion coefficients in national standard may be different.

## Slide 17
Thanks For Your Attention