## Slide 1: Assessment of the MACCS Code Applicability for Nearfield Consequence Analysis
Dan Clayton, Nate Bixler
Sandia National Laboratories
Presented at 2020 Virtual International MACCS Users’ Group Meeting, August 31 to September 2, 2020

## Slide 2: Outline
Background
Introduction/Setup
Code Trends
Code Comparisons
Wrap up

## Slide 3: Background (1/3)
NRC continues preparing to review and regulate a new generation of diverse non-LWRs designs
Figure taken from SECY-20-0010, “Advanced Reactor Program Status”
Notes: The NRC along with its contractors including Sandia and many other national labs have been preparing to review and regulate a new generation of diverse non-LWR designs.
In late 2016, NRC published its strategy to ensure it’s ready to effectively and efficiently conduct its mission for these technologies and its has been releasing periodic updates ever since.
As you can see from this figure, there is significant diversity among the designs and within each type of design. Different coolants, materials, fuels, sizes, and other features including transportability for microreactors.
The blue shaded boxes indicate these six developers have formally notified NRC of their intent to begin regulatory interactions by providing a response to a Regulatory Issue Summary (RIS). These are in different stages of design development.
Oklo Power LLC submitted its combined license application for its Aurora compact, fast, heat pipe reactor design in March 2020.

## Slide 4: Background (2/3)
NRC has organized its non-LWR readiness efforts into six strategic areas:
  Staff development and knowledge management
  Analytical tools
  Regulatory framework
  Consensus codes and standards
  Resolution of policy issues
  communications
Under strategy 2, NRC developed code development plans in a series of volumes
Volume 3 identifies plans for MACCS/consequence analysis
Notes: NRC has organized its non-LWR readiness efforts into these six strategic areas.
Strategy 2 is concerned with the identification, evaluation, and preparation of the computer codes and tools that will be used to evaluate the non-LWR designs.
NRC developed a series of reports to identify computer codes and gaps for non-LWRs for systems analysis, fuel performance analysis, severe accident progression analysis, source term, and consequence analysis.
The current version of Volume 3 was published in January 2020 and includes MACCS, MELCOR, and SCALE.
Additional volumes are in progress for other areas.

## Slide 5: Background (3/3)
Technical issues related to MACCS/consequence analysis warranting investigation for non-LWRs include the following:
  Assess and improve MACCS near-field atmospheric transport and dispersion capabilities to better treat building wake effects in the near field
  Evaluation of radionuclides to include in MACCS for each non-LWR type
  Evaluation of non-LWR radionuclide properties (size, shape, and chemical form) and their impact on atmospheric transport and dosimetry
  Evaluation of tritium particularly for MSRs and its contribution to offsite consequences
Notes: In Volume 3, NRC identified technical issues that warranted evaluation and potential code development for consequence analysis.
In my presentation today, I’m going to be speaking about efforts to date on the first item related to near-field atmospheric transport.
The second item will evaluate which radionuclides to include in consequence analysis calculations for the different non-LWR types since these are different from the standard set of 69 radionuclides used in the SOARCA project for LWR analysis. The selection of radionuclides for consequence analysis should consider several factors including the core inventory, physical and chemical properties including the nature of radioactivity and volatility, atmospheric transport factors including deposition properties, and biological factors including uptake, biological half-life, and specific organ effects.
The third item concerns the potential differences in properties of the radionuclides that could be released into the environment from severe accidents at different non-LWR designs including their size, shape, and chemical form since these may impact atmospheric transport and dosimetry.
The fourth item is related to tritium modeling particularly for molten salt reactors because they can produce large quantities during normal operation and tritium diffuses rapidly through metals at elevated temperatures. The point of this item is to better account for the unique ways tritiated water interacts with the human body via inhalation, ingestion, and skin absorption.

## Slide 6: Introduction (1/2)
The adequacy of the MELCOR Accident Consequence Code System (MACCS) in the nearfield is discussed in a non-Light Water Reactor (LWR) vision and strategy report that discusses computer code readiness for non-LWR applications developed by the Nuclear Regulatory Commission (NRC)
MACCS currently includes a simple model for building wake effects. The MACCS2 User’s Guide suggests that this simple building wake model should not be used at distances closer than 500 m. This statement raises the first question of whether MACCS can reliably be used to assess nearfield doses, i.e., at distances less than 500 m

## Slide 7: Introduction (2/2)
MACCS is a highly flexible Gaussian model and the user can choose whether to model a variety of physical phenomena, including such things as building wake effects, plume buoyancy, and plume meander. Furthermore, the user has flexibility in choosing how to model the Gaussian dispersion parameters
So, a second question goes beyond the first question of whether MACCS can be used in the nearfield to the related question of how can MACCS be used to generate results that are bounding of other codes intended for nearfield analysis

## Slide 8: General Arrangement of Flow Zones Near a Sharp-edged Building
Meteorology and Atomic Energy, 1968

## Slide 9: Objective
An evaluation of modeling approaches (methods) to estimate nearfield air concentrations and depositions was performed where several candidate codes were ranked for comparison and potential incorporation into the MACCS code
In this report, it is assumed that the results from the selected codes are all adequate in the nearfield, which is reasonable because these codes are specifically intended to be used in the nearfield
Hence, by comparing the results of these codes to the results from MACCS, the adequacy of MACCS for assessing exposures in the nearfield can be evaluated, along with determining how MACCS can be used to generating bounding results

## Slide 10: Nearfield Code List
Four candidate codes were selected from the three main methods of atmospheric transport and dispersion (ATD) in the nearfield and evaluated
  CFD models – OpenFOAM
  Simplified wind-field models – QUIC
  Modified Gaussian models – AERMOD and ARCON96
Based on these rankings, QUIC, AERMOD, and ARCON96 and were selected for comparison with MACCS

## Slide 11: Test Cases
Two weather conditions
  4 m/s, neutrally-stable (D stability class) – typical condition
  2 m/s, stable (F stability class) – reduced dispersion condition
Three building configurations (HxWxL)
  20m x 100m x 20m (5:1 W:H) – extreme width to height ratio
  20m x 40m x 20m (2:1 W:H) – typical building size
  No building (point source) – evaluate differences for elevated releases with no building
Two power levels (heat content)
  0 MW – without buoyancy
  5 MW – with buoyancy

## Slide 12: Code Trends

## Slide 13: MACCS Results
Building and elevation effects greatly diminished at 800 m downwind
Building significantly increases dispersion at short distances
Dilution for stable conditions generally higher than the corresponding dilution for neutrally-stable conditions
Buoyant plumes that escape building wake produce significantly lower dilution values due to fast plume rise compared with dispersion

## Slide 14: ARCON96 Results
Minimal change due to inclusion of building or elevated release within 1 km
Dilution for stable conditions generally higher than the corresponding dilution for neutrally-stable conditions
No plume rise model implemented; buoyant cases were not modeled

## Slide 15: AERMOD Results
Building and elevation effects greatly diminished at 500 m downwind
Building significantly increases dispersion at short distances
Dilution for stable conditions generally higher than the corresponding dilution for neutrally-stable conditions
Minor differences due to buoyancy

## Slide 16: QUIC Results (1/2)
Building and elevation effects greatly diminished at 1 km downwind
Building significantly increases dispersion at short distances
Dilution for stable conditions generally higher than the corresponding dilution for neutrally-stable conditions
No straightforward way to implement buoyancy; buoyant cases were not modeled

## Slide 17: QUIC Results (2/2)
Horizontal and vertical slices for a 4 m/s, neutrally-stable weather condition with a non-buoyant, elevated release from a 20 m x 100 m x 20 m building (Case 01)

## Slide 18: Code Comparisons

## Slide 19: Comparison Results
At 50 m, order from highest to lowest dilution is ARCON96, AERMOD, QUIC, MACCS
Order changes with distance
  ARCON96 shifts from highest to lowest
  AERMOD shifts from 2nd highest to 2nd lowest
  Relative order between QUIC and MACCS is consistent

## Slide 20: Potential Modifications to MACCS Input
Specify a ground-level release, instead of a release at the height of the building
  ARCON96 model showed little dependence on elevation of release
  Wake-induced building downwash observed in QUIC output
  Regulatory Guide 1.145 discusses releases less than 2.5 times building height should be modeled as ground-level releases
Specify no buoyancy (plume trapped in building wake)
  AERMOD model showed little dependence on buoyancy
If additional conservatism needed or desired, model as a point source
  ARCON96 model showed little dependence on building size
  DOE approach used for collocated workers
  If point source too bounding, use an intermediate building wake size

## Slide 21: Updated Comparison Results
MACCS input modified to reflect a ground-level (1), non-buoyant (2) release (grey) bounds AERMOD and QUIC up to 1 km and ARCON96 from 200 m up to 1 km
MACCS input modified to reflect a ground-level (1), non-buoyant (2), point-source (3) release (light blue) bounds all three up to 1 km

## Slide 22: Wrap up

## Slide 23: Summary (1/3)
ARCON96, AERMOD, and QUIC selected for comparison with MACCS based on initial evaluation
Test cases developed to give a broad range of conditions, not to be exhaustive
  Two weather conditions
  Three building configurations
  Two buoyancy variations

## Slide 24: Summary (2/3)
MACCS calculations configured with point-source, ground-level, nonbuoyant plumes provide conservative nearfield results that bound the centerline, ground-level air concentrations from ARCON96, AERMOD, and QUIC .
MACCS calculations with ground-level, nonbuoyant plumes that include the effects of the building wake (area source) provide nearfield results that bound the results from AERMOD and QUIC and the results from ARCON96 at distances >200 m
If using a point-source is too conservative and it is desired to bound the results from all three codes, another alternative is to use area source parameters in MACCS that are less than the standard values, i.e., an area source intermediate between the standard recommendation and a point source.

## Slide 25: Summary (3/3)
MACCS can be used at distances significantly shorter than 500 m downwind (50 – 200 m) from a containment or reactor building
However, the MACCS user needs to select the MACCS input parameters appropriately to generate results that are adequately conservative for a specific application
A conservative nearfield result may be obtained using the following MACCS parameter choices:
  The parameterization of Eimutis and Konicek for the dispersion model.
  The plume meander model based on Regulatory Guide 1.145. This model is selected by setting the value of the MACCS parameter MNDMOD to NEW.
  The release modeled as a point-source, ground-level, nonbuoyant plume.
Additional information available from final technical report (Clayton D.J and N.E. Bixler, “Assessment of the MACCS Code Applicability for Nearfield Consequence Analysis” Sandia National Laboratories, Albuquerque, NM, February 2020, ADAMS Accession Number ML20059M032)