## Slide 1: Optional Economic Model in MACCS 4.0 - RDEIM
N. E. Bixler
Coauthors: A. V. Outkin, F. Walton
Sandia National Laboratories
Presented at 2020 Virtual International MACCS Users’ Group Meeting, August 31 to September 2, 2020

## Slide 2: Contents
Uses for economic modeling in MACCS
Purpose for GDP-based model (RDEIM)
Economic modeling in MACCS
  Original, cost-based model
  RDEIM model
  Model comparison
Current implementation of RDEIM (MACCS 4.0)
Verification and benchmarking
Summary

## Slide 3: Uses for MACCS Economic Model
Cost/benefit analyses used in regulation
National Environmental Policy Act (NEPA) analyses
  Cost-benefit analyses to support license renewal (SAMA)
  Cost-benefit analyses to support new licenses (SAMDA)
Regulatory analyses by NRC
MACCS used to estimate offsite costs
  Offsite property damage costs (total loss reported by MACCS)
  Public exposure costs ((population dose) x (cost per unit dose))
  Occupational exposure costs (included with public exposure costs)
Total averted cost risk also includes onsite costs
  Cleanup and decontamination costs
  Replacement power cost
Other uses
NRC research (e.g., Level 3 PRA study)
Notes: averted public exposure costs, averted offsite property damage costs, averted occupational exposure costs, and averted onsite costs which include both averted cleanup and decontamination costs and averted replacement power cost

## Slide 4: Purpose for RDEIM Model
Estimate effect of an accident on national GDP losses using state-of-practice macroeconomic model
Create a consistent model across geographic regions (limited to continental U.S.) and time periods
Provide an economic model that enables MACCS analysts flexibility but also simplicity (does not require an economist)
RDEIM (Regional Disruption Economic Impact Model) was created to serve these purposes

## Slide 5: Description of Original Economic Model
Costs are summed over three phases – emergency, intermediate, and long-term.
Cost equations and additional details are provided in SAND2020-5567.
Losses are reported in 8 categories:
  Emergency-phase evacuation and relocation (per diem)
  Intermediate-phase relocation (per diem)
  Long-term relocation (one time)
  Decontamination
            Restore habitability when cost-effective
            Performed separately for farmland and non-farmland
            Allows up to 3 levels of dose reduction, cost, and time to implement
            Accounts for characterization, local area cleanup, and waste management
  Loss of use (expected return on property investment)
  Depreciation (on improvements to property)
  Condemnation (entire value of property)
  Milk and crop disposal (annual farm income)
Losses do not account for indirect affects due to supply-chain disruption or lost income.

## Slide 6: Original Economic Model Logic
Decision to decontaminate is based on cost effectiveness:
The following logic is used at the beginning of the long-term phase to determine which action to perform for non-farmland

## Slide 7: Decision Process for Farmland (COMIDA2)
Farmland is immediately farmable when both first- and second-year food-ingestion limits are satisfied and farmland is habitable
Food-disposal costs are invoked when farmland is not immediately farmable
Farmland is never decontaminated because of farmability

## Slide 8: RDEIM Model Concepts
Like with the original cost-based model, habitability and farmability criteria define the disrupted region.
  When a grid element is not habitable, all industrial sectors are affected.
  When a grid element is habitable but not farmable, only farming is affected.
National recovery is faster than local recovery.
Losses are reported as real (as opposed to nominal) GDP losses discounted to the base year, currently 2011.
GDP losses account for
  Direct losses to industry within the disrupted region
  Indirect losses caused by loss of demand for commodity flows outside the disrupted region
  Induced losses from lost pay throughout the national economy

## Slide 9: RDEIM Is Based on Input-Output Theory
I-O theory is based on empirical tables of final demand, industry income, and interindustry transactions.
Among other uses, I-O models can capture the short-term effects of a regional disruption, e.g., a hurricane.
Classical I-O models do not account for long-term effects in which there is adaptation of the economy.
Parent of RDEIM, the Regional Economic Accounting Tool (REAcct), was designed to evaluate short-term economic losses.
RDEIM evolved from REAcct to better capture long-term economic losses based on recommendations by an external peer review panel of experts.
Direct losses are estimated according to the number of disrupted workers in each industry based on county-level employment data.
Indirect and induced losses are estimated by multiplying direct losses by Type I and Type II net total requirements multipliers from Bureau of Economic Analysis (BEA).
  Type I multipliers estimate direct plus indirect losses.
  Type II multipliers estimate direct, indirect, plus induced losses.

## Slide 10: Peer Review
Peer review panel consisted of three experts
Dr. Jeff Werling, University of Maryland
Mr. Neil Higgins, Public Health England
Dr. Haydar Kurban, Howard University
Significant recommendations included
Results should account for induced losses.
Capital losses for condemned property should be included.
Depreciation during periods of interdiction should be included.
National economy should recover faster than regional economy.
  National economy recovers linearly over period (default is 3 yr).
  Disruption of regional economy can last longer (default is 10 yr).
Double counting should be minimized by modifying multipliers to account for commodity flows within disrupted region.

## Slide 11: Economic Model Comparison
Most loss elements are the same for both models.
GDP losses replace expected return on investment in cost-based model
  RDEIM model reports both regional (direct) and national (total) losses.
  Cost-bases model only accounts for regional losses.
Disposal of contaminated crop and dairy products is not currently included in RDEIM model.
Inequality to determine cost effectiveness of decontamination is different.
Cost-Based Model | RDEIM Model
Evacuation/relocation costs | Evacuation/relocation costs
Long-term relocation costs | Long-term relocation costs
Decontamination cost | Decontamination cost
Depreciation on property improvements | Depreciation on property improvements
Value of condemned property | Value of condemned property
Expected return on investment | GDP losses (direct, indirect, and induced)
Disposal of crop and dairy products | 

## Slide 12: RDEIM Implementation
SecPop 4.3 creates site data required by RDEIM model.
RDEIM contains economic multipliers to estimate indirect and induced losses.
Input parameters have defaults that can be modified.
  Social discount rate (default is 0.03/yr)
  GDP annual growth rate (default is 0.033/yr)
  Year accident is assumed to occur (default is 2011)
  Maximum duration of regional disruption (default is 10 yr)
  Maximum duration of national disruption (default is 3 yr)
            National economy recovers linearly over this period
  Land value multiplier (affects decision to decontaminate or condemn) (default is 1.0)

## Slide 13: Illustration of Results
Total loss curve (orange) shows all losses at the national level.
  National economy recovers faster than regional economy
Direct loss curve (blue) shows regional losses (excluding induced losses).
Indirect losses have two components:
  Losses due to disruption of the supply chain outside the affected region
  Gains from economic adaptation outside the disrupted region
Induced losses are always positive and are distributed across economy.

## Slide 14: RDEIM Verification
Three cases were evaluated by comparing with REAcct (parent code of RDEIM) using default economic parameters.
Case 1: entire economy of the contiguous US is disrupted.
  RDEIM first-year direct loss is the same as REAcct result to three significant digits.
  Result is within 1% of BEA value.
Case 2: nearly all of a single county and a small fraction of a neighboring county are disrupted.
  RDEIM and REAcct results agree to three significant digits.
Case 3: a fraction of a single county is disrupted.
  Disruption boundaries were estimated approximately.
  Results agree within 5% of estimated value.

## Slide 15: Benchmark of RDEIM Model
Default economic parameter values were used.
Five US sites representing a range of non-farmland wealth were evaluated.
  Points near left of plot are more rural with lower population densities.
  Points near right of the plot are more urban with higher population densities.
Three source-term magnitudes were evaluated.
RDEIM model produces greater losses (up to 16%) than the original cost-based model.
  Difference between models is greater for larger source terms.
  Difference generally increases with wealth of region (population density).
  Larger losses are attributable in part to including losses outside disrupted region.
Chart: Percentile of Non-Farm Wealth
| 0.16 | 0.52 | 0.68 | 0.87 | 0.93
Small ST | 0.02 | 0.06 | 0 | 0.04 | 0.03
Medium ST | 0.05 | 0.15 | 0.13 | 0.15 | 0.14
Large ST | 0.07 | 0.14 | 0.12 | 0.16 | 0.12

## Slide 16: Summary
MACCS 4.0 includes an alternative economic model (RDEIM).
  Based on input-output theory
  Accounts for direct, indirect, and induced GDP losses
  Peer reviewed by panel of experts
            Panel recommended several changes, including accounting for faster national than regional economic recovery.
            Panel evaluated RDEIM model to be state of practice.
Major difference between the economic models is that GDP losses replace expected return on property investments.
RDEIM implementation was verified by comparing with REAcct.
A benchmark study was performed for five sites and three source terms.
  Results are remarkably similar for cost- and GDP-based models.
  Losses predicted by RDEIM are consistently larger (up to 16% for 5 sites).
  Differences generally increase with source-term magnitude and population density.

## Slide 17: List of Acronyms
BEA Bureau of Economic Analysis
GDP Gross Domestic Product
I-O Input-Output
MACCS MELCOR Accident Consequence Code System
NRC Nuclear Regulatory Commission
RDEIM Regional Disruption Economic Impact Model
REAcct Regional Economic Accounting Tool
SAMA Severe Accident Mitigation Alternative
SAMDA Severe Accident Mitigation Design Alternative
SOARCA State-of-the-Art Reactor Consequence Analysis
US United States