## Slide 1: Results of Benchmark Exercise with MACCS-HYSPLIT Atmospheric Transport and Dispersion Model Implementation
Dan Clayton1, Nate Bixler1, Keith Compton2
1Sandia National Laboratories
2U.S. Nuclear Regulatory Commission
Presented at 2020 Virtual International MACCS Users’ Group Meeting, August 31 to September 2, 2020

## Slide 2: Outline
Background
Integration of HYSPLIT atmospheric transport results into MACCS
Benchmark study
Benchmarking Results
Wrap-up
2

## Slide 3: Background

## Slide 4: Purpose for MACCS
Created by Sandia to support NRC research and regulatory requirements
  Origins go back to the mid-1970s
Typically used for prospective analyses, e.g.,
  Probabilistic risk assessments (NUREG-1150 and Level 3 PRA)
  Probabilistic consequence assessments (SOARCA)
  Cost/benefit analyses (commonly used for environmental analyses in licensing)
Very versatile with a large set of user inputs
  Intended to run rapidly for PRA applications
  Large set of weather trials (hundreds or thousands)
  Significant set of release categories (ten or twenty)
    A release category is a group of similar source terms that can be represented by one or a few source terms.
    Each source term can be complex, multi-isotope, and time-dependent.
4

## Slide 5: Challenges to Gaussian Plume Model
Use of Gaussian model questioned
  Adequacy at locations that experience lake or sea breezes
  Suitability for river valleys that strongly influence local winds
  Adequacy for areas with significant surface relief
  Distance to which a Gaussian plume model is reliable
Challenges motivated a detailed benchmark study (NUREG-6853, 2004)
  Four ATD models
    Lagrangian model (LODI)
    Two Gaussian puff models (RASCAL and RATCHET)
    Gaussian plume segment model (MACCS)
  Oklahoma ARM site using weather station data (ADAPT)
  Showed differences in the annual average exposure and deposition results were nearly within a factor of two out to 100 miles
  Did not address sea breezes, river valleys, or other terrain variations
5

## Slide 6: Integration of HYSPLIT Atmospheric Transport Results into MACCS

## Slide 7: MACCS Modules
ATMOS
  Source term definition
  Weather sampling algorithms
  Atmospheric transport, dispersion, and deposition
    Option for either HYSPLIT or Gaussian model
EARLY (1 to 40 days)
  Doses as modified by emergency-phase countermeasures such as sheltering, evacuation, relocation, and KI ingestion
  Multiple population cohorts
  Acute and latent health effects from early acute exposure
CHRONC (1 week to >50 years)
  Doses as modified by intermediate and recovery-phase protective actions such as relocation, interdiction, decontamination, and condemnation
  Latent health effects from chronic exposure to deposited materal
  Economic impact from early and late phase protective actions
7

## Slide 8: MACCS-HYSPLIT Coupling Process
8

## Slide 9: Benchmark Study

## Slide 10: Benchmark Purpose (1/2)
Serves as an initial analysis using the HYSPLIT/MACCS coupling
  Demonstrates the potential modeling results that can be obtained from using this new option
  Is a practical test of the implementation
  Provides information on the differences in the model data needs and computational resources needed to exercise the new capability
Serves as a further test of the hypothesis tested in (Molenkamp et al., 2004) that the results of a simple Gaussian plume segment model are sufficient for purposes of estimating expected values of consequence measures when averaged over a broad set of meteorological conditions
  Wider array of consequence measures
  Longer distances
  Multiple sites
  5th and 95th percentile results in addition to the mean
10

## Slide 11: Benchmark Purpose (2/2)
Informs decisions on when it may be appropriate to choose the Gaussian model versus the HYSPLIT model for specific applications
  With the introduction of the new capability, the logistical challenge of benchmarking the simple Gaussian plume segment model against a more advanced model going forward is considerably reduced
  Some applications may be substantially different from these benchmarking comparisons, and therefore this study does not attempt to draw general conclusions
  Users are encouraged to perform their own studies to determine which modeling approach best suits their needs in terms of model fidelity and computational expense
11

## Slide 12: Benchmark Cases
Source term
  #1 - NUREG-1150 historic (puff release followed by a longer duration tail)
  #2 - SOARCA Short-Term Station Blackout (more delayed and prolonged)
Five representative sites
  Site A - Large river valley
  Site B - Central midwestern plain
  Site C - Dry western region
  Site D - Atlantic coast with potential for sea breezes
  Site E - Southeast river valley influenced by Bermuda high
MACCS grid of 29 radial intervals (out to 1,000 mi) and 64 compass sectors
General evacuation scheme
  Modeled with multiple evacuating cohorts
Uniform weather bin sampling (40 samples per bin)
12

## Slide 13: Source Terms
Source Term #1 -NUREG-1150 historic (puff release followed by a longer duration tail, 2 plume segments)
Source Term #2 - SOARCA Short-Term Station Blackout (more delayed and prolonged, 42 plume segments)
13

## Slide 14: Meteorology
NAM 12-km meteorological database - 2008
14

## Slide 15: Benchmark Output Metrics
Mean, 95th and 5th percentiles
Atmospheric Model Outputs
  Peak (around the compass) normalized, time-integrated, ground-level, air concentration (c/Q, s/m3) as a function of distance from the site (Peak Air)
  Peak (around the compass) normalized ground concentration (D/Q, 1/m2) as a function of distance from the site (Peak Ground)
  Normalized land areas that exceed various levels of contamination (unitless) (Land Area)
Consequence Outputs
  Normalized peak ionizing radiation dose (unitless) as a function of distance (Peak Dose)
  Early fatality risk (unitless) within a circular area near the point of release (EF Risk)
  Normalized regional population doses (unitless) (Pop Dose)
  Latent cancer fatality risk (unitless) over region (LCF Risk)
  Normalized, regional economic loss (unitless) (Econ Loss)
15

## Slide 16: Benchmarking Results

## Slide 17: Computational Cost
HYSPLIT Preprocessing
  ~31,000 processor hours per site
  Total disk space = 500-600 GB per site
  Converted files = additional 200 GB per site
MACCS
  NUREG-1150 source term
    Run on one Windows processor
    Gaussian ADT model, ~2 processor minutes per site
    HYSPLIT ADT model, ~20 processor hours per site (600 times longer)
  SOARCA, Short-Term Station Blackout (STSBO)
    Run on one Windows processor
    Gaussian ADT model, ~30 processor minutes per site
    HYSPLIT ADT model, ~130 processor hours per site (260 times longer)
17

## Slide 18: Typical Benchmark Comparisons
Compare model results over distance
Mean values over all weather trials
5th and 95th percentiles over weather trials
Peak Quantities
Integrated Quantities
18
Site A, ST #1

## Slide 19: Near-Field, <50 km (<30 mi) Comparison
Ratio of mean HYSPLIT ADT model to mean Gaussian ATD model
  Shown as Average (Minimum | Maximum)
  >1 indicates HYSPLIT larger
  <1 indicates Gaussian larger
19
Notes: Looking at Peak Air & Ground, illustrates the differences between sites and between source terms.
Source term #1 shows higher results for HYSPLIT for peak dose, population dose, LCF risk, economic loss and EF risk.
Source term #2 generally higher results for HYSPLIT output.
The various outputs did not all increase uniformly. Some of the metrics increase more that peak air/ground (e.g. EF Risk).
Site C/ST #1 shows similar or lower peak air and ground, but an increase in consequences.

## Slide 20: Far-Field, >50 km (>30 mi) Comparison
Ratio of mean HYSPLIT ADT model to mean Gaussian ATD model
  Shown as Average (Minimum | Maximum)
  >1 indicates HYSPLIT larger
  <1 indicates Gaussian larger
20
Notes: Looking at Peak Air & Ground, illustrates the differences between sites and between source terms
Higher results for HYSPLIT for peak dose, population dose, LCF risk, economic loss and Land Area for both source terms
Some of the metrics increase more that peak air/ground (e.g. Site D/ST#2).

## Slide 21: Wrap-up

## Slide 22: Summary (1/3)
Integration of HYSPLIT results included in MACCS 4.0
  Supplements Gaussian plume segment model in MACCS with an alternative
Need to balance the need for higher fidelity models with associated higher computational costs
Benchmark analysis performed over wide set of metrics and distances
  Five sites
  Two source terms
22

## Slide 23: Summary (2/3)
The level of agreement between annual average results from the Gaussian and HYSPLIT ATD model results is similar to the results shown in NUREG/CR-6853 (Molenkamp et al., 2004), with a wider set of metrics and a longer distance range.
Many results obtained using the HYSPLIT model are larger on average than the results obtained using the Gaussian plume segment model
While there are changes in trends between the Gaussian and HYSPLIT ATD models between the near and far fields for some of the consequence metrics considered in this study, there is no clear distance at which the Gaussian model seems to systematically diverge from the HYSPLIT model
23

## Slide 24: Summary (3/3)
The ability to incorporate HYSPLIT model results in MACCS is a major improvement in the capabilities of MACCS simulations and provides a state-of-the-art alternative to use of the Gaussian plume segment model
24