## Slide 1: A Proposed Methodology for Estimating Decontamination Costs in MACCS 3.10
N. E. Bixler (Sandia National Labs)
Coauthor: A. J. Nosek (USNRC)
Tech. Monitor: K. Compton (USNRC)
Presented at 2020 Virtual International MACCS Users’ Group Meeting, August 31 to September 2, 2020

## Slide 2: Objectives
Develop a documented, traceable, and transparent methodology for the development of decontamination parameters for MACCS 3.10
Present overview of key elements of the proposed methodology
Illustrate proposed methodology using a mixture of
Documented data sources
Reasonable assumptions
Provide examples of resulting MACCS decontamination parameters by applying the proposed methodology

## Slide 3: MACCS Parameters Evaluated
Number of Decontamination Levels (LVLDEC)
Decontamination Factors (DSRFCT)
Non-Farmland Decontamination Cost (CDNFRM), per capita
Farmland Decontamination Cost (CDFRM), per hectare
Notes: Note that this methodology does not address the time needed to complete decontamination (which is the sum of the intermediate phase duration and the late phase duration), or the parameters needed to estimate the collective doses to decontamination workers.

## Slide 4: Development of Decontamination Levels (LVLDEC and DSRFCT)
Selected values based on BNL 2009
DFs of 1-4 can be achieved using mechanical methods such as sweeping and washing
DFs of 5-10 can be achieved by additional more aggressive methods such as high pressure washing, sand blasting, and selective surface replacement.
Currently Proposed Decontamination Levels:
Decontamination Level (DF) | Percentage of the Initial Dose Remaining After Decontamination | Total Dose Reduction Percentage
2 | 50% | 50%
4 | 25% | 75%
8 | 12.5% | 87.5%

## Slide 5: Overall Framework for Estimating Decontamination Costs
Total decontamination costs include:
  Cost for local decontamination activities ()
  Cost for waste characterization ()
  Cost for waste storage, transportation, and disposal ()

## Slide 6: Decontamination Cost Estimation
Estimation of decontamination costs should consider
  Types of surfaces (e.g., lawns, roads) requiring decontamination
  Decontamination method applied to a given surface (e.g. topsoil removal, pressure washing, etc.)
        Effectiveness
        Unit cost
        Unit waste generated
  The total amount of decontamination target surfaces to be decontaminated for each type of land use
  The fraction of land dedicated to each land use category
  The extent of decontamination in each land use category
  The population density of populated areas in each land use category

## Slide 7: Cost Estimation Decontamination Activities
Estimate decontamination costs as a weighted sum
Where:
 | Average fraction of area dedicated to land use (dimensionless)
 | Fraction of area dedicated to land use that is decontaminated (dimensionless)
 | Average decontamination surface area per land area dedicated to land use (square yards per acre)
 | Average unit cost to decontaminate surface area to achieve an overall decontamination level ($ per square yard)
 | Total area (acres)
 | Total population (people)
 | Total area (acres)
 | Total population (people)
Non-Farmland ($/person) | 
Farmland ($/ha) | 
Non-Farmland ($/person) | 
Farmland ($/ha) | 

## Slide 8: Cost Estimation Waste Management Activities
Estimate waste management costs as a weighted sum:
Where:
 | Total waste management cost for storage, transportation, and disposal ($ per cubic yard )
 | Average fraction of area dedicated to land use (dimensionless)
 | Fraction of area dedicated to land use that is decontaminated (dimensionless)
 | Average decontamination surface area per land area dedicated to land use (square yards per acre)
 | Average unit waste volume generated in decontaminate surface area to achieve an overall decontamination level (cubic yard per square yard)
 | Total area (acres)
 | Total population (people)
 | Total waste management cost for storage, transportation, and disposal ($ per cubic yard )
 | Total area (acres)
 | Total population (people)
Non-Farmland ($/person) | 
Farmland ($/ha) | 
Non-Farmland ($/person) | 
Farmland ($/ha) | 

## Slide 9: Selection of Decontamination Technologies
JAEA 2015 (Remediation of contaminated areas in the aftermath of the accident at the Fukushima Daiichi Nuclear Power station: Overview, analysis and lessons learned Part 1: A report on the “Decontamination Pilot Project" (Review No. 2014-051)) is the primary reference for decontamination methods and their associated costs, effectiveness, and waste generation rates
Multiple types of surfaces require decontamination
Each type of surface contributes a different amount to the dose received by an individual
Each type of surface has a different unit cost and decontamination effectiveness
Tables to follow show source of values used for and

## Slide 10: Examples of Residential Decontamination Methods (adapted from Appendix A of JAEA, 2015)
*Assumed conversion of 100 Yen per dollar
Reference | Type of Surface | Method | Unit cost* ($/SY unless otherwise noted) | Dose Reduction Factor | Solid waste volume (L/m2 unless otherwise noted) and type
Residential-1a | Residential Houses: tile roof, iron roof | Surface brushing and washing (iron roof) | 9.11 | 1.1 - 1.5 | almost none (sludge & solids)
Residential-2 | Residential Houses: gutter | Removal of debris and wiping | 3.35 $/lf | 1.4 - 10 | 1 m3 per house on average (litter, soil)
Residential-5 | Residential Land: garden | Thin-layer topsoil stripping | 4.93 | 1.1 - 10 | 20 – 40 (thickness of stripping 2-3 cm) (vegetation, soil)
Residential-8 | Residential Land: turf | Turf stripping | 12.54 | 5 | 20 - 50 (stripping 2-5cm) (turf)
Residential-12 | Concrete/asphalt surfaces: hard-packed floors, scarcement, flat roofs, stairs, terraced areas, car parks, pavements | Ultra-high-pressure water jet | 9.62 | 5 | ~3 (Concrete & asphalt)
Residential-14 | Concrete surfaces: concrete walls, scarcement | Brushing followed by high pressure water jet washing | 8.03 | 1.3 - 3.3 | almost none (sludge)
Residential-15 | Concrete surfaces: hard floors, scarcement, roof, stairs, balcony | High-pressure washing | 8.03 | 1.3 - 3.3 | almost none (sludge)

## Slide 11: Examples of Non-Residential Decontamination Methods (adapted from Appendix A of JAEA 2015)
*Assumed conversion of 100 Yen per dollar
Reference | Type of Surface | Method | Unit cost* ($/SY unless otherwise noted) | Dose Reduction Factor | Solid waste volume (L/m2 unless otherwise noted) and type
Public Infrastructure-1b | Asphalt roads | Road Sweeper (On-board road sweeper) | 0.17 | 1 - 2 | 1 - 1.5 (soil, road dust, vegetation)
Public Infrastructure-3 | Asphalt roads | Water-jet vehicle | 1.25 | 1 - 3 | few (sludge)
Public Infrastructure-8 | Asphalt roads | Asphalt removal by surface stripping machine | 3.26 | 22 | ~8 (stripping ~5mm) (Asphalt)
Forest-2 | Forested flat ground | Humus and thin-layer topsoil removal (stripping) | 7.44 | 1.3 - 5 | 20 - 90 (litter, humus, soil)
Forest-3 | Forested flat ground | Strimming | 1.34 | - | 5 - 10 (grasses, shrubs, litter)
Agricultural land-1 | Paddy fields, vegetable fields | Reversal tillage | 0.28 | 1.4 - 2.5 | -
Agricultural land-2 | Paddy fields, vegetable fields | Interchanging topsoil with subsoil | 2.59 | ~3 | -
Agricultural land-6 | Paddy fields, vegetable fields | Mowing | 0.59 | - | 9 -12 (vegetation)
Agricultural land-7 | Paddy fields, vegetable fields, fruit farm | Strimming | 0.84 | - | 9 - 12 (crops)

## Slide 12: Farmland Decontamination
Decontamination of farmland in MACCS does not affect contamination levels in crops produced on the land.
Preliminary work showed that methods involving farmland soil removal are cost-prohibitive in MACCS due to the cost of removing contaminated soil.
It is appropriate to consider only methods that are based on mixing or exchanging surface and subsoil, providing shielding.
Reversal Tillage and Interchanging Topsoil with Subsoil are therefore included in all three farmland decontamination levels.
Waste management costs are therefore zero for farmland.
High costs associated with soil interchange methods may be cost-ineffective due to relatively low typical farmland values.

## Slide 13: Non-Farmland Decontamination Methods Selected to achieve targeted dose reduction
Values are inferred from Appendix B of [Brown et al. 2007]. When the relative contribution between two surface types is unknown (e.g., interior walls and floors), each surface is assumed to contribute an equal amount. Information on the contribution to dose from roof gutters was not available in Appendix B of [Brown et al. 2007].
Decontamination Surface | DF=2 | DF=4 | DF=8 | Approximate Dose Contribution1 | 
 |  |  |  | dry | wet
Asphalt | Public infrastructure-1b, -3 | Public Infrastructure-1b, -8, seal coat | Public Infrastructure-1b, -8, seal coat | 4% | 7.5%
Concrete | Residential-14 | Residential-12 | Residential-12 | 4% | 7.5%
Roof area | Residential-1a | Residential-1a 50% of surface Remove & Replace 50% of surface | Remove & replace 100% of surface | 11% | 9%
Roof gutters2 | Residential-2 | Residential-2 | Residential-2 |  | 
Wall area - exterior | Residential-15 | Residential-15 50% of surface Remove & Replace 50% of surface | Remove & replace | 9% | 1%
Wall area - interior | Wash | Wash 50% Replace 50% | Remove & replace | 8% | 0%
Floor area | Scrub floors and shampoo carpets | Scrub floors and shampoo carpets 50%, Replace 50% | Remove & replace | 8% | 0%
Landscape - trees | Forest-2 | Forest-2 | Forest-2 with increased topsoil removal | 10% | 0.5%
Landscape - shrubs | Forest-2 | Forest-2 | Forest-2 with increased topsoil removal | 10% | 0.5%
Landscape - lawn | Residential-8, 3.5 cm, 67% of surface | Residential-8, 3.5 cm | Residential-8, 3.5 cm Residential-5, 3.5 cm | 32% | 74%

## Slide 14: Assumed Surface Areas Associated with Each Housing Intensity ()
Assumptions:
High Density Residential Areas: two two-story 10-unit structures on one acre, each unit consisting of 1000 ft2 of floor space
Medium Density Residential Areas: four single-level 2000-ft2 houses on one acre (one unit per quarter-acre).
Low Density Residential Areas: one single-level 2000-ft2 house on 2.68 acres
All land uses include assumptions for roads (asphalt) and driveways and sidewalks (concrete)
Remaining landscape (excluding the areas occupied by the house, concrete, and asphalt) is assumed to be 2/3 lawn, 1/6 trees, and 1/6 shrubs/bushes/plants.
Decontamination Surface Area (SY/acre) | High Intensity Urban Areas | Medium Intensity Urban Areas | Low Intensity Urban Areas
Asphalt | 1316 | 696 | 205
Concrete | 383 | 470 | 45
Roof area | 1111 | 1026 | 96
Roof gutters (lf/acre) | 560 | 400 | 37
Wall area - exterior | 1562 | 1005 | 94
Wall area - interior | 15967 | 3129 | 292
Floor area | 2222 | 889 | 83
Landscape - trees | 338 | 464 | 752
Landscape - shrubs | 338 | 464 | 752
Landscape - lawn | 1353 | 1857 | 3010

## Slide 15: Land Use () and Decontamination () Fractions
Assumptions:
All developed areas (urban, rural residential, and rural roads) are decontaminated.
For DF=4 and DF=8, strips of land adjacent to rural roadways are also decontaminated.
Land use fractions derived based on data from:
U.S. Census Bureau, "2013 National - Housing Unit Characteristics - All Housing Units"
U.S. Census Bureau, "American Community Survey 2013"
U.S. Department of Agriculture 2017, "Major Land Uses 2012"
D. P. Bigelow and A. Borchers 2017, "Major Uses of Land in the United States, 2012 (EIB-178)”
Notes: Note that the detailed derivation of these fractions is not included in this presentation because of length. However,

## Slide 16: Land Use and Decontamination Fractions
* Total sums to less than 100% because agricultural land is treated separately and decontamination of water bodies is not considered.
** Assumes decontamination of 2.68 acres per household
*** Assumes decontamination of a 20 m buffer area on each side of rural roads; assumes no decontamination for level 1
Land Use | High-Intensity Urban | Medium-Intensity Urban | Low-Intensity Urban | Low-Intensity Rural Residential | Rural Roads (Not Included with Housing) | Other (Treated as Forest)
Estimated Land-Use Fraction ()* | 0.069% | 1.6% | 2.0% | 5.6% | 1.2% | 69%
Fraction Decontaminated () | 100% | 100% | 100% | 71%** | 100% | 0 or 4.5%***
CONUS-averaged fraction decontaminated | 0.069% | 1.6% | 2.0% | 4.0% | 1.2% | 0 or 3.1%***
Land Use | High-Intensity Urban | Medium-Intensity Urban | Low-Intensity Urban | Low-Intensity Rural Residential | Rural Roads (Not Included with Housing) | Other (Treated as Forest)
 | 0.069% | 1.6% | 2.0% | 5.6% | 1.2% | 69%
 | 100% | 100% | 100% | 71%** | 100% | 0 or 4.5%***
CONUS-averaged fraction decontaminated | 0.069% | 1.6% | 2.0% | 4.0% | 1.2% | 0 or 3.1%***
Notes: Note that the detailed derivation of these fractions is not included in this presentation because of length. However, note that developed areas are a small fraction of land use in the United States.

## Slide 17: Waste Management Costs
Assumptions:
  Onsite temporary storage in soft-sided bags (Yasutaka and Naito, 2016)
  Waste is 61% debris and 39% soil (JMOE 2014)
  Transportation costs based on Feizollahi et al. (1995) assuming shipping 1000 miles using 20 ton flatbed trucks
  Low-level waste facility unit disposal costs assumed to be $250/CY for soil and $630/CY for debris (assumption, consistent with Carilli et al. 2009)
  Disposal costs assumed reduced by half to account for the potential for hazardous waste disposal facilities rather than low-level waste disposal facilities
Unit Costs ($/CY) | Temporary Storage | Transportation | Disposal | Total
Non-Farmland | $216 | $254 | $241 | $711

## Slide 18: Characterization Costs
Non-Farmland Characterization Assumptions:
  One sample is collected per household (per housing unit).
  The cost to collect a sample is $750 and the cost to analyze it is $900.
  The number is adjusted to a per acre basis accounting for land-use-specific population density.
  Resulting values range from $400 per acre for rural residential areas to $22,000 per acre for urban high density land use.
  On a per acre basis, the cost of waste characterization for Roads and Other land-use categories is assumed to be the same as for rural housing, but Other is adjusted lower to account for the small fraction that would be decontaminated (4.5%).
Farmland: $330/ha
  Assumes one sample is collected for every five hectares of farmland at a cost of $750 for acquisition and $900 for analysis.

## Slide 19: Summary of Potential Decontamination Costs
Non-Farmland decontamination costs averaged over all land usages within the CONUS
Farmland decontamination costs
 | Decontamination | Waste Generation | Waste Management | Waste Characterization | Total Cost to Decontaminate | 
 | $/acre | CY/acre | $/acre | $/acre | $/acre | $/person
Level 1 (DF 2) | $5,200 | 15 | $11,000 | $170 | $16,000 | $78,000
Level 2 (DF 4) | $11,000 | 38 | $27,000 | $170 | $38,000 | $180,000
Level 3 (DF 8) | $15,000 | 57 | $40,000 | $170 | $56,000 | $270,000
 | Decontamination | Waste Generation | Waste Management | Soil Characterization | Total Cost to Decontaminate
 | $/ha | CY/ha | $/ha | $/ha | $/ha
Level 1 (DF 2) | $3,349 | 0 | $0 | $330 | $3,679
Level 2 (DF 4) | $38,032 | 0 | $0 | $330 | $38,362
Level 3 (DF 8) | $38,032 | 0 | $0 | $330 | $38,362
Notes: Using the equations, data, and assumptions described previously results in the following results
Review of the results

## Slide 20: Observations
Majority of dose arises from land areas surrounding structures
  Mainly lawns, forest, asphalt, and concrete
  Especially so for wet deposition
Decontamination of land areas requiring vegetation, humus, and topsoil removal tend to generate large amounts of waste.
Per-capita decontamination costs are highest for low population density.
Some non-farmland decontamination costs are greater than CDNFRM parameter limit of $100,000/person in MACCS 3.10.
High non-farmland decontamination costs coupled with extended interdiction periods may result in increased condemnation.
High farmland decontamination costs may result in increased condemnation of farmland.

## Slide 21: Summary
A methodology has been developed by Sandia National Laboratories that provides a documented, traceable, and transparent method for estimating decontamination costs in MACCS.
Values have been estimated using unit cost, waste, and dose reduction data from Fukushima cleanup experience coupled with generic US-average land use statistics.

## Slide 22: Selected References
BNL 2009, "Decontamination Technologies Task 3. Urban Remediation and Response Project Prepared for New York City Department of Health and Mental Hygiene," Brookhaven National Laboratory, Upton, NY, 2009.
J. Brown, K. Mortimer, K. Andersson, T. Duranova, A. Mrskova, R. Hänninen, T. Ikäheimonen, G. Kirchner, V. Bertsch, F. Gallay and N. Reales, "Generic handbook for assisting in the management of contaminated inhabited areas in Europe following a radiological emergency: Part II - Compendium of Information on Countermeasure Options, Version 1.0 (EURANOS(CAT1)-TN(07)-02)," Health Protection Agency, Chilton, Didcot, UK, 2007.
T. Yasutaka and W. Naito, "Assessing cost and effectiveness of radiation decontamination in Fukushima Prefecture, Japan," Journal of Environmental Radioactivity, vol. 151, pp. 512-520, 2016
Japan Atomic Energy Agency, "Remediation of contaminated areas in the aftermath of the accident at the Fukushima Daiichi Nuclear Power station: Overview, analysis and lessons learned Part 1: A report on the “Decontamination Pilot Project" (Review No. 2014-051)," Fukushima Environmental Safety Center, Japan Atomic Energy Agency, Tokai-Mura, Japan, 2015.
U.S. Census Bureau, "2013 National - Housing Unit Characteristics - All Housing Units," 2013. [Online]. Available: https://www.census.gov/programs-surveys/ahs/data/interactive/ahstablecreator.html.
U.S. Census Bureau, "American Community Survey, 2013," 2013. [Online]. Available: https://www.census.gov/programs-surveys/acs.
U.S. Department of Agriculture, "Major Land Uses, 2012," 2017. [Online]. Available: https://www.ers.usda.gov/data-products/major-land-uses/major-land-uses/.
D. P. Bigelow and A. Borchers, "Major Uses of Land in the United States, 2012 (EIB-178)," U.S. Department of Agriculture, 2017.
Japan Ministry of the Environment, "Jokyo Dojou tou no Chuukan Chozou Shisetsu no An ni tsuite [Draft Plan of Interim Storage Facility for Removed Soil and Waste] (in Japanese)," Fukushima Headquarters for Interim Storage Facilities, 2014.
F. Feizollahi, D. Shropshire and D. Burton, "Waste Management Facilities Cost Information for Transportation of Radioactive and Hazardous Materials (INEL-95/0300)," Idaho National Engineering Laboratory, Idaho Falls, ID, 1995.
J. T. Carilli, S. K. Krenzien, R. G. Geisinger, S. J. Gordon and B. Quinn, "Overview of Nevada Test Site Radioactive and Mixed Waste Disposal Operations - 9117," in WM2009 Conference, Phoenix, AZ, 2009.