## Slide 1
Consideration of the evacuation model based on the radiation dose rate criteria
Regulatory Standard and Research Department,
Secretariat of Nuclear Regulation Authority
(S/NRA/R)
ICHIKAWA Ryohei
Aug. 31st - Sept. 2nd, 2020
2020 International MACCS User Group (IMUG) meeting
Notes: My name is ICHIKAWA Ryohei
I am in charge of Level 3 PRA research at NRA with Chihiro-san, who gave a presentation on the updates of the dose reduction factors yesterday.
The objective of this presentation is to introduce the new evacuation model of MACCS.

## Slide 2: Contents
Background and Purpose
Introduction of dose rate evacuation model
Analysis to confirm the new function
Conclusion
Notes: I have divided my presentation into 4 sections.
First, I would like to give you background and purpose about this consideration.
Secondly, I’m going to talk about introduction of dose rate evacuation model.
Thirdly, we will move on to analysis to confirm the new function.
Finally, I’ll conclude this presentation.

## Slide 3: Background and Purpose
Background
Level 3 probabilistic risk assessment (PRA) methodology for the assessment of risk based on site characteristics is being considered.
Population distribution data, agricultural/livestock product data and protective action data are required for the site-specific calculation.
  The protective action data include the start time of evacuation.
Purpose
The expansion of Level 3 PRA code (MACCS2-NRA*) to allow for measurable values, such as air radiation dose rate, to be taken into account at the start time of evacuation.
  3rd choice in addition to “ALARM” and “ARRIVAL”.
*MACCS2 code modified by NRA.
Notes: I want to begin by discussing background and purpose.
~
Level 3 PRA methodology for the assessment of risk based on “site characteristics” is being considered.
For the site-specific calculation, population distribution data, agricultural/livestock product data and protective action data are required.
For protection data, the protective action data include the start time of evacuation.
~
Although MACCS specifies the time required to start evacuation, we have extended MACCS2-NRA so that measurable values such as air radiation dose rate can be taken into account at the start time of evacuation.

## Slide 4
Basic concept of protective action
In the UPZ (approximately 5-30 km from nuclear facilities), after a declaration of general emergency has been issued, the evacuation of the area will be initiated after the indoor sheltering if necessary.
 |  | PAZ | UPZ
Before release | < few hours |  | 
After release | < few hours |  | 
 | < 1 day |  | 
 | < few days |  | 
 | < 1 week |  | 
PAZ (Precautionary Action Zone) and UPZ (Urgent Protective action planning Zone)
PAZ (5 km from nuclear facilities)
UPZ (30 km from nuclear facilities)
General Emergency
Sheltering
Emergency monitoring
Evacuation,
KI ingestion
OIL1
Evacuation
OIL2
Temporary relocation
Example of implementing protective action (slightly changed the layout from NRA nuclear emergency preparedness and response (EPR) guide)
Notes: In this slide, I’m going to talk about basic concept of protective action in Japan.
~
The figure on the left shows the range of PAZ, Precautionary Action Zone and UPZ, Urgent Protective action planning Zone.
Different protection measures are planned for each of these.
~
In the UPZ, after a declaration of general emergency has been issued, the evacuation of the area will be initiated after the indoor sheltering if necessary.
~
The figure on the right shows the flow of protective measures for PAZ and UPZ.
Evacuation based on the air dose rate that we considered is within the UPZ.
Both OIL1 and OIL2 are movements based on the dose rate criteria, but the criteria are different and the time range to be carried out is also different.

## Slide 5: Introduction of dose rate evacuation model
In the conventional MACCS2-NRA evacuation model, evacuation start time is set by input data based on the radionuclide released information.
Chart: Time
Check source term → Set evacuation time
Example) 5 hours after the end of maximum release
Evacuation start time
(Constant regardless of weather)
Manual input
Notes: In this part, I’d like to tell you about dose rate evacuation model.
~
In the conventional MACCS2-NRA evacuation model, evacuation start time is set by input data based on the radionuclide released information.
For example, we set up to evacuate 5 hours after the last release.
This is a manual setting by the analyst, and it is a calculation that the same evacuation time is set regardless of weather conditions.

## Slide 6: Introduction of dose rate evacuation model
In the conventional MACCS2-NRA evacuation model, evacuation start time is set by input data based on the radionuclide released information.
In the dose rate evacuation model, the start time of evacuation is based on the air radiation dose rate.
Chart: Time
Annual weather data
Chart: 
Chart: 
Chart: Time
Dose rate calculation → Comparison with criteria → Set evacuation time
Evacuation start time
(For each weather data)
Example) 5 hours after the criteria are exceeded
Calculation
Internal processing
Chart: Time
Check source term → Set evacuation time
Example) 5 hours after the end of maximum release
Evacuation start time
(Constant regardless of weather)
Manual input
Notes: On the other hand, in the dose rate evacuation model, the start time of evacuation is based on the air radiation dose rate.
This is an internal setting, and different evacuation times will be set according to weather conditions.
First, the variation of the dose rate is calculated for each weather condition and compared with the criteria to finally set the evacuation time.
The evacuation start time set in this way will differ depending on the weather conditions used in the calculation.

## Slide 7
Setting an evacuation start time based on multiple criteria
The EPR guide has several criteria for air dose rate, each with a different reference time for implementation of protective action.
The dose rate evacuation model sums the delay time of each criterion to each OIL timestamp, implementing the protective action that comes first.
Relationship between air dose rate, criterion values, and evacuation start time
Air dose rate
OIL2 timestamp
OIL1 timestamp
OIL2
(20 µSv h-1)
OIL1
(500 µSv h-1)
Relocation start time by OIL2 (within 1 week from confirmation)
Evacuation start time by OIL1 (within 1 day from confirmation)
Time
Increased dose rate due to contribution of plume and increased deposition during passage of plume
Notes: Next slide shows setting an evacuation start time based on multiple criteria.
~
The EPR guide has several criteria for air dose rate, each with a different reference time for implementation of protective action.
~
This figure shows relationship between air dose rate, criterion values, and evacuation start time.
When radioactive material is released, the dose rate increases due to the plume's contribution and the increased deposition during the plume's passage.
As the dose rate increases, each OIL criteria will be exceeded, and these exceeded time will be recorded as a time stamp for each criteria.
Since the time from the excess to the start of evacuation differs for each criteria, the earlier protective measures will be implemented.
~
That is, the dose rate evacuation model sums the delay time of each criterion to each OIL timestamp, implementing the protective action that comes first.

## Slide 8
Function for calculating the time to reach the criterion
The addition of calculation function for air dose rate
  In order to simulate the dose rate of the monitoring posts, dose conversion coefficients were prepared.
  The contribution of groundshine and cloudshine was taken into account.
Addition of a function to compare dose rate and the criteria
  A function to compare the dose rate with the criteria set by input was added.
MP
Groundshine
Cloudshine
Consider the doses of groundshine and cloudshine
Simulate the dose rate indicated by the monitoring post
Compare dose rate with criteria
Dose rate calculation and comparison with criteria
Notes: This slide shows the considerations taken into account in comparison to the criteria.
~
The first point is the addition of an air dose rate calculation function.
In order to simulate the dose rate of the monitoring posts, dose conversion coefficients were prepared.
This coefficients were estimated from the relationship between effective dose and air dose by energy.
And, the contribution of groundshine and cloudshine was taken into account.
~
The second point is addition of a function to compare dose rate and the criteria.
A function to compare the dose rate with the criteria set by input was added.

## Slide 9
Evacuation model processing flow
The process is based on the delay time from OALARM to sheltering (DLTSHL) and to evacuation (DLTEVA). Sheltering is the same as the conventional model.
In the dose rate evacuation model, the delay time for evacuation is set up by internal processing, considering the time to reach criterion, which is different for each weather sampling.
Processing of conventional evacuation model and dose rate evacuation model.
Conventional evacuation model
Accident
OALARM
DLTSHL
DLTEVA
OIL timestamp
DLTOIL
(DeLay Time OIL)
Evacuation
Set everything in the input file.
DLTEVA
Setting of evacuation delay time by internal processing.
OALARM
DLTSHL
Dose rate evacuation model
Notes: Evacuation model processing flow is shown.
~
The process is based on the delay time from OALARM to sheltering and to evacuation.
Sheltering is the same as the conventional model.
In the dose rate evacuation model, the delay time for evacuation is set up by internal processing, considering the time to reach criterion, which is different for each weather sampling.
~
In more detail, the conventional evacuation model sets protective measures along the upper line.
On the other hand, in the dose rate evacuation model, protective measures are set along the flow within the dashed line.
DLTEVA, which sets the evacuation delay time, is internally set using OALARM and DLTSHL, as well as the OIL timestamp and the delay time from OIL described in the previous slide.

## Slide 10: Analysis to confirm the new function
Analytical conditions
A trial analysis was conducted to confirm the function of the evacuation model in comparison with a conventional one.
*Japan Nuclear Energy Safety Organization, Level 2 PSA analysis for consideration of preventive protective measures range, 2012 (in Japanese)
 | Conventional model | Dose rate evacuation model
Accident | Overpressure failure due to loss of all ECCS in the case of medium LOCA in 3-loop PWR* (Leakage from the containment started at 20 minutes after the accident onset, large-scale release 72 hours later) | 
Protective action (PAZ) | Evacuation after the declaration of a general emergency | 
Protective action (UPZ) | After sheltering, evacuate 5 hours after the end of release | After sheltering, evacuate 5 hours after the confirmation of OIL1
Analysis period | 1 week | 
Other analytical conditions | Same conditions | 
Main analytical conditions of conventional model and dose rate evacuation model
Chart: Time [h]
Release rate cumulative value for each nuclide group
Maximum release
Notes: In this part of my presentation, I’d like to tell you about analysis to confirm the new function.
~
A trial analysis was conducted to confirm the function of the evacuation model in comparison with a conventional one.
~
This table shows analytical conditions.
Postulated accident is loss of coolant accident in 3-loop PWR.
There is a maximum release between 72 and 96 hours. After that, the release continues until 120 hour.
The only different calculation conditions between the Conventional model and the Dose rate evacuation model is the protective measure in UPZ.
In conventional model, the evacuation was set 5 hours after the release.
Therefore, under this analysis condition, evacuation will start after 125 hours.
On the other hand, the Dose rate evacuation model was set to start evacuation 5 hours after exceeding the OIL1 standard.

## Slide 11
Calculated result
A comparison of results between the conventional evacuation model and the dose rate evacuation model was conducted.
The differences in the calculated results were confirmed within the UPZ where the dose rate evacuation was set.
Analysis results using the conventional evacuation model (●) and radiation dose rate evacuation model (●) (- : Conditions for continuing normal activities)
Chart: Distance [km]
| 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6.3 | 8 | 10 | 13 | 20 | 30
感度3(6) | 6489.4795 | 4504.2222 | 3383.4154 | 2677.2487 | 2194.5558 | 1851.6967 | 1606.048 | 1422.7947 | 1264.6259 | 1054.5051 | 729.1323 | 511.7805 | 334.1166 | 161.3962 | 81.416
感度5(7) | 1 | 0.71977 | 0.55287 | 0.44656 | 0.37399 | 0.32132 | 0.27806 | 0.24559 | 473.1293 | 395.2498 | 275.2117 | 193.8562 | 127.0552 | 61.0409 | 30.3023
感度6(9) | 0.99889 | 0.71977 | 0.55287 | 0.44656 | 0.37307 | 0.32132 | 0.27806 | 0.24559 | 495.2381 | 488.5621 | 472.5063 | 434.238 | 359.1185 | 147.9465 | 40.8224
Within UPZ: Difference in effective dose
Within PAZ: No difference because evacuated due to the declaration of a general emergency
95%
Average
Notes: This slide shows a comparison of results between models.
~
The normalized value of the effective dose is plotted on the vertical axis against the distance on the horizontal axis.
The blue plot represents the conventional evacuation model and the red plot represents the dose rate evacuation model.
The black line is the result of continuing normal life without setting protective measures.
~
A slight difference in the calculation results was confirmed within the UPZ where the dose rate evacuation was set.
~
There was another interesting point.
Depending on the distance, the dose rate evacuation model showed higher doses than continuing a normal life.
It suggests that proper evacuation after exceeding OIL criteria may be important.
Although not shown in this presentation, I confirmed the calculation result that the exposure dose is reduced when the indoor evacuation period after OIL1 confirmation is extended.

## Slide 12
Analysis
The start times of evacuation within the UPZ were shown as a cumulative distribution function of the weather samplings used in the analysis.
For dose rate evacuation, three meteorological conditions were confirmed: (1) no evacuation (dose rate has not reached criteria), (2) the evacuation starts after the passage of the maximum radioactive plume, and (3) the evacuation starts during the passage.
Chart: Time [h]
Conventional evacuation model
(Evacuation start setting 5 hours after the end of release under all weather samplings)
Cumulative distribution function of evacuation start time (9.2-10.8km area from plant)
Notes: This slide shows a comparison of start time of evacuation between models.
~
The start times of evacuation within the UPZ were shown as a cumulative distribution function of the weather samplings used in the analysis.
First, in the conventional evacuation model, evacuation started 5 hours after the maximum release under all weather conditions.
Therefore, the CDF goes from 0 to 1 at 125 hours.

## Slide 13
Analysis
The start times of evacuation within the UPZ were shown as a cumulative distribution function of the weather samplings used in the analysis.
For dose rate evacuation, three meteorological conditions were confirmed: (1) no evacuation (dose rate has not reached criteria), (2) the evacuation starts after the passage of the maximum radioactive plume, and (3) the evacuation starts during the passage.
Chart: Time [h]
Conventional evacuation model
(Evacuation start setting 5 hours after the end of release under all weather samplings)
Dose rate evacuation model
(Different for each weather samplings)
Cumulative distribution function of evacuation start time (9.2-10.8km area from plant)
Notes: Next, in the Dose rate evacuation model, the evacuation start time differs depending on the weather.
Therefore, the CDF has a curve that gradually increases as time increases.
I will classify this. It can be said that three types of evacuation start times have been set.

## Slide 14
Analysis
The start times of evacuation within the UPZ were shown as a cumulative distribution function of the weather samplings used in the analysis.
For dose rate evacuation, three meteorological conditions were confirmed: (1) no evacuation (dose rate has not reached criteria), (2) the evacuation starts after the passage of the maximum radioactive plume, and (3) the evacuation starts during the passage.
Chart: Time [h]
Conventional evacuation model
(Evacuation start setting 5 hours after the end of release under all weather samplings)
Dose rate evacuation model
(Different for each weather samplings)
(1) No evacuation
Cumulative distribution function of evacuation start time (9.2-10.8km area from plant)
Notes: The first is the percentage that CDF did not reach 1.
This is the percentage of the weather conditions there was no evacuation.
That is, the dose rate did not reach the OIL1 criteria.

## Slide 15
Analysis
The start times of evacuation within the UPZ were shown as a cumulative distribution function of the weather samplings used in the analysis.
For dose rate evacuation, three meteorological conditions were confirmed: (1) no evacuation (dose rate has not reached criteria), (2) the evacuation starts after the passage of the maximum radioactive plume, and (3) the evacuation starts during the passage.
Chart: Time [h]
Conventional evacuation model
(Evacuation start setting 5 hours after the end of release under all weather samplings)
Dose rate evacuation model
(Different for each weather samplings)
(2) After passage of the maximum radioactive plume
(1) No evacuation
Cumulative distribution function of evacuation start time (9.2-10.8km area from plant)
Notes: The second is the rate at which evacuation begins after the maximum plume is released.
The last plume release continues during this time.
Although not shown in this presentation, the exposure dose during this evacuation stage was the highest of the three evacuation stages.

## Slide 16
Analysis
The start times of evacuation within the UPZ were shown as a cumulative distribution function of the weather samplings used in the analysis.
For dose rate evacuation, three meteorological conditions were confirmed: (1) no evacuation (dose rate has not reached criteria), (2) the evacuation starts after the passage of the maximum radioactive plume, and (3) the evacuation starts during the passage.
Chart: Time [h]
Conventional evacuation model
(Evacuation start setting 5 hours after the end of release under all weather samplings)
Dose rate evacuation model
(Different for each weather samplings)
(3) During passage of the maximum radioactive plume
(2) After passage of the maximum radioactive plume
(1) No evacuation
Cumulative distribution function of evacuation start time (9.2-10.8km area from plant)
Notes: The third is the rate at which evacuation is initiated during the emission of the maximum plume.
It shows that even with a limited release rate, the air dose rate is higher depending on the weather conditions.

## Slide 17: Conclusion
We are developing a Level 3 PRA methodology for risk assessment based on site characteristics.
Conclusion
A radiation dose rate evacuation model was introduced into the MACCS2-NRA.
The functional verification analysis revealed that the model can quantify the effect of different weather conditions on the start time of evacuation.
  The model enables us to evaluate the case of no evacuation, evacuation after the plume has passed, and evacuation while the plume is passing.
Notes: I conclude this presentation.
We are developing a Level 3 PRA methodology for risk assessment based on site characteristics.
A radiation dose rate evacuation model was introduced.
The functional verification analysis revealed that the model can quantify the effect of different weather conditions on the start time of evacuation.
The model enables us to evaluate the case of no evacuation, evacuation after the plume has passed, and evacuation while the plume is passing.