## Slide 1: Overview of MACCS Status and Development
J. E. Leute
Coauthors: N.E. Bixler, D. J. Clayton
Sandia National Laboratories
Presented at 2020 Virtual International MACCS Users’ Group Meeting, August 31 to September 2, 2020
Notes: Hello!
Intro
Thank you

## Slide 2: Contents
MACCS background
Version 3.11.2
Version 4.0
AniMACCS
Supporting documents
Auxiliary files
Summary
Notes: History - predecessor codes leading up to the MACCS we know today
Version 3.11.2 released in March of 2018 - recap
Version 4.0 – spend some time- released in June of this year – and the updates associated (greater capabilities with the introduction of HYSPLIT, and a new economic model).
New Animation tool! Allows users to animate results from MACCS. You can make videos and screenshots, over a map background. Greatly helps to visualize results. and demo during the workshop.
You can still register for the workshop. Watch Ahead videos.

## Slide 3: Purpose for MACCS
  Created by Sandia to support NRC research and regulatory applications
  Origins go back to the mid-1970s
Typically used for prospective analyses, e.g.,
  Probabilistic risk assessments (NUREG-1150 and NRC’s Level 3 PRA)
  Probabilistic consequence assessments (SOARCA)
  Cost/benefit analyses (required for environmental analyses in licensing)
Very versatile with a large set of user inputs
  Intended to run rapidly for PRA applications
  Large set of weather trials (hundreds or thousands)
  Significant set of source term categories (ten or twenty) plus additional sensitivity studies
Notes: Discuss the background…why was MACCS created.
WASH 1400: Reactor Safety study – which ____
Level 3 PRA – Assess the consequences (both biological and economic) of a potential release of radioactive material into the atmosphere for a whole range of accident scenarios.
More specific probabilistic safety assessments like SOARCA which focused on a select few severe accidents
Help influence design decisions – also can be used following realized accident scenarios to evaluate the addition of extra protections. (filtered vent).
Emphasize the rapidly portion:
How many user inputs (depending on how complicated your run – simple run (100-ish) to 1000s)
Weather trials (about a thousand, max of 8760 hrs/year)
Source terms categories? Normally around 10-20 something for typical PRA

## Slide 4: MACCS Lineage
  Calculation of Reactor Accident Consequences (CRAC) Code (1975)
  Developed for the Reactor Safety Study (WASH-1400)
CRAC2 (1982)
  Primarily used in 1982 siting study (NUREG/CR-2239)
  MACCS (MELCOR Accident Consequence Code System) (1990)
  Primarily used in NUREG-1150
  MACCS2 (1998)
  Developed to support DOE documented safety analyses of nuclear facilities
WinMACCS/MACCS (2011)
  Enhance user friendliness
  Reduce likelihood of user errors
  Enable routine examination of uncertainty
Notes: As mentioned on the previous slide.
  CRAC and Reactor Safety Study – first U.S. systematic attempt to search out large spectrum of accidents
  first to use quantitative techniques to estimate the following in an integrated manner:
    probabilities: 1/20,000 core melt per reactor per year
    source terms
    public consequences
    Nine PWR and five BWR release categories defined and frequencies quantified
  Assign probability distribution to key variables
    release magnitude
    weather conditions
    population
1982 Siting Study –
NUREG-1150 – First full PRA? Five assessed plants
Five principle steps of risk analysis:
  Accident (frequency) analysis
  Accident progression, containment loadings, and structural response analysis
  Radioactive material transport (source term) analysis
  Offsite consequence analysis
  Risk Integration - combines and analyzes the first four steps
MACCS2 - Improvements in dose conversion data base, decay chains, emergency response model, and food pathway model
WinMACCS – what we have today
Sampling for uncertainty analyses

## Slide 5: Phenomena Treated by MACCS
Representation of source term
Atmospheric transport and dispersion
  Statistical sampling of archived weather data
Wet and dry deposition
Exposure pathways to humans
  Inhalation
  Cloudshine
  Groundshine
  Resuspension
  Ingestion
Emergency actions
  Sheltering
  Evacuation
  KI ingestion
  Relocation
Long-term remedial actions
  Decontamination
  Temporary or permanent interdiction of property
  Crop disposal
Economic losses
  Evacuation and relocation per diem costs
  Long-term relocation cost
  Decontamination costs
  Loss of property use
  Depreciation during interdiction
  Property value for permanent interdiction
Notes: Source term – imported as a file from MELCOR or similar application, or input directly into MACCS itself by specifying the release characteristics. Magnitude and timing, to include buoyancy (heat), height, initial timining, release rate by radionuclide by chemical group, particle size distribution by chemical group…items like that to characterize your release.
Models Atmospheric transport and dispersion – weather is a key part of that – options for statistical sampling of your weather data
(120 hour, bin sampling)
Deposition – deposited on the ground, or washed out by interactions with clouds or rain.
Exposure pathways – and ultimately the biological impacts and resulting risks
Broken down into multiple time domains:
Emergency – sheltering, biological impacts and potential shielding effects
Evacuation – speed and timing of evacuation for example. You can also modify this for certain groups of people, or modify speeds (weather)
Potassium Iodine Ingestion –
Relocation
Long Term effects:
Impacts on the land – work associated with decontaminating land, possible interdition, and crop disposal
Economic Losses:
Mentioned biological impacts, but a key part of MACCS is also calculating economic impacts to have a full picture of the risk.

## Slide 6: MACCS Code Modules
ATMOS
  Calculates transient air and ground concentrations
EARLY
  Treats emergency phase (up to 40 days, usually one week)
  Models emergency response actions
  Estimates doses from exposure pathways
  Estimates health effects
CHRONC
  Treats intermediate phase (up to 30 years, usually one year)
  Treats long-term phase (up to >300 years, usually 50 years)
  Estimates long-term doses from exposure pathways
  Estimates health effects
  Calculates economic losses
Notes: Atmos:
Models atmospheric transport and dispersion. MACCS utilizes the Gaussian plume model, however with MACCS 4.0 you now have the option to use HYSPLIT (Lagrangian particle tracking).
Models the movement of your plume, accounts for weather effects, buoyancy, advection downwind, dispersion, turbulence, and deposition of particles from the plume. This ultimately informs the user on air and ground concentrations.
Early:
Also looking at your biological impacts
Time period up to 40 days (usually one week)
Doses from those exposure pathways we just talked about (inhalation, cloudshine, groundshine, resuspension) – resulting health effects. Early (acute) radiation effects.
Chronc:
Much longer time frame
Treats both the intermediate phase and long term phase (up to over 300, usually 50)
NO CLOUDSHINE OR INHALATION!
Long term exposure pathways – health effects – chronic effects like cancer
Economic losses (contamination, interdiction, loss of property value)
Emergency response actions – breaks your population into cohorts and assigns evacuation times
Acute symptoms, like early fatalities and injuries
CHRONC:
Long term effects-
Cancer
Economic effects

## Slide 7: Improvements in MACCS 3.11.2 (3/18)
Emergency response
  OALARM can be defined for each cohort.
Decontamination
  The limits on CDNFRM and CDFRM were increased to $1 M.
  The limits for decontamination and intermediate-phase durations are now 30 years.
Doses and health effects
  All organs listed in DCF file can be used to define health effects.
  The maximum number of early health effects increased to 10.
  The maximum number of cancer health effects increased to 40.
Usability
  MACCS now distributed as a 64-bit executable to eliminate memory errors.
  MACCS now allows scale factor for each radionuclide (analogous to CORSCA) to facilitate sensitivity analyses.
Notes: Discussed at last IMUG but just want to recap as many individuals and organizations are using this version of MACCS:
OALARM (Notification delay – in reference to accident initiation) defined for each cohort – used to be everyone
Upper bounds for contamination costs: CDNFRM and CDFRM – 100,000 to $1M
Organs listed – approx. 10 to 28 organs
Health effects before?
Cancer effects before?
1 to 30 YEARS
NUCSCA – SOARCA for simplified sensitivity analysis

## Slide 8: MACCS 4.0 Revolutionary Improvements
  Optional capability to perform high-fidelity atmospheric transport modeling with HYSPLIT
  User is responsible for downloading HYSPLIT (from NOAA) and supporting tools (special request to Sandia)
  Preprocessor steps needed prior to running WinMACCS and MACCS
  Significantly more computing requirements than the Gaussian model
  Optional state-of-practice, GDP-based model (RDEIM) to account for economic losses (database currently supports contiguous USA)
  Initially developed prior to 2015
  Peer review conducted in 2015 led to significant improvements
  Model was improved and benchmarked between 2015 and 2020
  Benchmark report published in May 2020
  Latest version of SecPop supports site data requirements
  Support for special files needed by animation tool, AniMACCS

## Slide 9: MACCS 4.0 Evolutionary Improvements
  Limits extended on a large set of input parameters
  Number of output requests for all output types (999)
  Number of plume segments using multi-source model (9999)
  Duration of food ingestion with COMIDA2 (50 yr)
  Convenience enhancements added for cyclical file management
  Network access
  Reordering capabilities
  Creates templates on all valid files
  Allows source term set per realization when running multi-source model
  Simplified method to eliminate quadratic parameters for the linear-quadratic dose-response model
  Qualifiers can be tab-separated in reports to facilitate importing into a spreadsheet
  Input parameters can be exported, including distribution definitions
  Results for each weather trial are used to define quantile results
  Unused correlations are supported
Notes: Question – smaller number of input requests before?
Unused correlations are now supported? 500 plume segments per source
Comida2 8/9 before?
Data repository – fairly large set threshold type models – reusing for multiple runs.
Cyclical files – network access and reordering capabilities
In previous versions, when running MACCS using the cyclical file feature, when a cyclical file fails validation, the process of creating the template files stops. The algorithm was changed to continue to validate the cyclical files and create templates on valid files even when one or more cyclical files fail validation. This feature allows the user to fix all the cyclical files in error before having to restart the process.
An option to choose a source term file set per realization was added when running the Multi Source model.
Eliminate – different form based on different options you select. WinMACCS. Don’t see parameters you don’t have to specify.
Tab separated – additional separation – all run together before – easier to import. Only Qualifiers/Identifiers. Allows you to sort or filter.
Weather – old method binned all results – lose actual value associated with result. Now you keep value, and bin after. You save a lot of information this way
Unused correlations – sampling correlations – but then you change model you couldn’t change you had to delete. Now it ignores.

## Slide 10: New Licensing Process
  MACCS 4.0 contains new licensing features
  Software is locked to a specific computer
  Licenses are for one-year duration
  Steps to activate license
  Run WinMACCS 4.0.0 Setup.exe (no installation key required)
  Open WinMACCS 4.0.0
            A popup screen briefly describes the licensing process
            Readme file provides more details on licensing process
  Run CreateLicenseRequestFile.exe in folder C:\Users\Public\WinMACCS to create license.request
  Send a copy of license.request to wg-maccs-entity@sandia.gov
  Once approved, Sandia sends MACCS_license.key to user
  License key is linked to WinMACCS
Notes: Product.key?
Order is switched

## Slide 11: Linking License Key
  File Specifications/License File is used to link MACCS_license.key
  WinMACCS provides the number of days left on license
  User should be proactive in updating license key

## Slide 12: AniMACCS Capabilities
  AniMACCS software expected to release in September 2020
  Included with MACCS 4.0
  Can be obtained for a $1000 fee with MACCS 3.X
  Allows MACCS single weather sequence runs to be animated
  Movement of plume segments for Gaussian model
  Instantaneous air concentrations (C, Bq/m3)
  Time-integrated air concentrations (, Bq-s/m3)
  Ground deposition (D, Bq/m2)
  Creates both animations and snapshots
Notes: For multiple weather trials it will animate the first one

## Slide 13: AniMACCS Features
  User can modify
  Map scale and center
  Contour colors and isopleth ranges
  Type of contour and choice of radionuclide
  Aspect ratio
  Animation speed for videos
  Interpolation time of plume movement animations
Notes: Map scale and center - Zoom in and zoom out
Contour colors and isopleths – legend
Choice of radionuclide
Aspect ratio
Animation speed -
Interpolation time -

## Slide 14: Animation of Plume Segments
Notes: Taken from sample problem?

## Slide 15: Animation of Ground Deposition (Gaussian)
Notes: Sample problem?
Ground Concentration
Cs-137
nCi/m2

## Slide 16: Animation of Ground Deposition (HYSPLIT)
Notes: Not a sample problem – but a animation for Fukushima using MACCS coupled with HYSPLIT
Also ground concentration, also Cs-137, map legend and units are different.
I think this is integrated?

## Slide 17: Major Supporting Documents
  MACCS User’s Guide and Reference Manual Draft Report (consistent with Version 3.10) (NUREG/CR-XXXX)
  4.0.0 Supplement to MACCS Users Guide and Reference Manual
  Assessment of the MACCS Code Applicability for Nearfield Consequence Analysis (SAND2020-2609)
  Economic Model for Estimation of GDP Losses in the MACCS Offsite Consequence Analysis Code (SAND2020-5567)
  Complete set of published SOARCA Reports (NUREG-1935 Parts 1&2, NUREG/CR-7110 Vol. 1&2 Rev. 1, NUREG/CR-7155, and NUREG/CR-7245)
  Technical Bases for Consequence Analyses Using MACCS (NUREG/CR-XXXX)
Notes: Question – technical bases document not in there?
Describe how to get to these
User Guide – very descriptive
SOARCA reports – good description of a consequence analysis – when starting a new project makes a good reference
Input Parameter Guidance? In Process.

## Slide 18: Auxiliary and Supporting Files
  Dose coefficient (DCF) files for LNT and non-LNT applications
  FGR-13 (based on FGR-13 using standard radiation weighting factors)
  FGR-13 Gray Equivalent (Rev. A) (based on FGR-13 using relative biological effectiveness (RBE) factors consistent with FGR-13 cancer induction modeling and with all SOARCA analyses)
  COMIDA2 files to go with each type of dose coefficient file
  Created with COMIDA2 2.0.0.2
  Exposure duration (LASTACUM) set to 50 years
  NRC and DOE sample problems
  Tutorials based on NRC sample problems
  Documents to support HYSPLIT applications

## Slide 19: Summary
MACCS performs prospective consequence analysis of potential atmospheric releases of nuclear materials
Major enhancements in Version 4.0 include
  Coupling with HYSPLIT to perform high-fidelity ATD modeling
  A state-of-practice model for economic losses resulting from a nuclear power plant accident (RDEIM)
  Ability to animate plume segments and air and ground concentrations
MACCS 4.0 comes with a large set of documents and auxiliary files

## Slide 20: List of Acronyms
ATD Atmospheric Transport and Dispersion
CRAC Calculation of Reactor Accident Consequences
DCF Dose Conversion Factor
DOE Department of Energy
FGR Federal Guidance Report
GDP Gross Domestic Product
HYSPLIT Hybrid Single Particle Lagrangian Integrated Trajectory
LNT Linear No-Threshold
MACCS MELCOR Accident Consequence Code System
NOAA National Oceanographic and Atmospheric Administration
NRC Nuclear Regulatory Commission
PRA Probabilistic Risk Assessment
RBE Relative Biological Effectiveness
RDEIM Regional Disruption Economic Impact Model
SOARCA State-of-the-Art Reactor Consequence Analyses