## Slide 1: PACE: recent developments
IMUG 2020
Tom.Charnock@phe.gov.uk

## Slide 2: PACE recent developments
Application to new REPPIR 2019
High spatial and temporal resolution population estimation, Pop247
European wide agricultural data-set update
Future developments
Public Health England:
We exist to protect and improve the nation’s health and wellbeing, and reduce health inequalities. PHE is an executive agency, sponsored by the Department of Health and Social Care.
https://www.gov.uk/government/organisations/public-health-england

## Slide 3: PACE
Probabilistic Accident Consequence Evaluation – Level 3 PSA
Implemented as an add-in to ArcGIS™ Geographic Information System, Windows 10
Incorporates the UK Meteorological Office, Lagrangian particle atmospheric dispersion model NAME
https://www.metoffice.gov.uk/research/approach/modelling-systems/dispersion-model
Endpoints:
Environmental radioactivity
Extent of protective actions: sheltering, evacuation, SI, relocation, clean-up and food restriction
Public doses with and without protective actions (cloud-shine, ground-shine, inhalation, skin/clothes deposition, resuspension and ingestion)
Health effects, stochastic and deterministic with and without protective actions
Economic consequences (Industry, agriculture, tourism, health care)
Hypothetical incident

## Slide 4: REPPIR 2019
Radiation (Emergency Preparedness and Public Information) Regulations 2019
https://www.hse.gov.uk/radiation/ionising/reppir.htm
A framework to ensure arrangements are in place to respond to an emergency onsite and offsite.
Changes:
Radiation emergency no longer defined by a specific dose to member of public (smaller operators encompassed)
Introduction of outline planning and outline planning zones (OPZs)
Local authority, instead of regulator, sets the detailed emergency planning zones (DEPZs).
Not just ‘reasonably foreseeable’, strengthens requirement to assess all radiation hazards
Introduces a proportionate and graded approach
Operators make hazard assessment and prepare a consequence report
Local authorities define DEPZs and OPZs, using report and in discussion with the operator
DEPZ about capabilities, what protective actions are necessary and how to put them into effect
OPZ about information/communication and marshalling resources. Less planning but some consideration of rare events.
Schedule 3, the consequence assessment must account for:
the range of potential source terms and weather conditions;
the different persons that may be exposed and the effective and equivalent doses they are likely to receive;
the pathways for exposure;
the distances in which urgent protective action may be warranted for the different source terms when assessed against the relevant Emergency Reference Level (ERL).
Notes: PACE designed for PSA, but now under REPPIR being used for emergency planning.

## Slide 5: REPPIR 2019, PHE Guidance
PHE published “REPPIR 2019 Consequence Assessment Methodology” (RCAM)
https://www.gov.uk/government/publications/radiation-consequence-assessment-methodology-for-reppir-2019
Practical guidance for applying PSA Level 3 codes (i.e. PACE or MACCS etc) to REPPIR 2019.
Following RCAM will fulfil REPPIR 2019 Schedule 3 requirements.
Suggests values or sources for all important inputs, e.g. locations factor, occupancy, shielding etc.
Defines outputs required for the consequence report, mean and 95th percentile:
Effective and thyroid dose by distance and pathway with no protective action:, 1, 3, 5, 10, 30, 50 km, 2 days,1 year
Distances of protective actions: evacuation, sheltering, stable iodine, restriction of milk and green vegetables
Residual doses for comparison against reference levels, 1 year and 1 km and other distances, with appropriate protective actions applied.
For each urgent protective action, number of people and areas of land impacted
For food restrictions, area of land and quantities of food.
Hypothetical facility and incident

## Slide 6: Pop247 – high temporal/spatial resolution population estimates
PACE currently assumes a static resident population
actually population moves around on daily, weekly and seasonal cycles
Pop247 methodology developed by University of Southampton
‘pulls’ people from ‘origins’ (residences/census) to ‘destinations’ (workplaces, education, shops, recreation etc) using age dependent occupancy profiles:
http://pop247.geodata.soton.ac.uk/
Notes: Another area we’ve been looking at is how we use population in PACE
The current version assume a static residential population. Unchanging regardless of time of day and day of year.
Obviously that is not the case. People move between locations on daily and weekly and seasonal cycles. For example, school age children attend schools during school hours in school terms on week days, but stay at home or go elsewhere on weekends and during school holidays. Information about school capacity, location, and opening hours is not secret or ambiguous, but it is dispersed among systems and documents and is rarely included in any systematic way in population estimation.
There are many other underutilized sources of information such as road usage, workplace occupancy, retail habits, public transport, and university time tables which could be used to inform the distribution of the population on a spatial and temporal basis. The University of Southampton has developed a flexible and robust methodology called Pop247 to systematically and consistently incorporate such information on a regional or national basis to enable estimates at a high temporal and spatial resolution of the numbers of people in different groups to be generated. The estimates are broken down into broad groups indicating whether people are at home, in transit or in some non-residential location such as school, workplace or shops, however the data does not track individuals
No people are created or omitted by the approach. The dataset is further resolved into population age groups (0-4, 5-9, 10-15, 16-17, 18-64, 65 and over) and into location categories: origin (i.e. at home), in travel (moving to or from a home location) or on-site (at location not home, e.g. school, work etc.).
Not about long term pop projections
Weather

## Slide 7: Pop247
England dataset made available to PHE
Open source data: 2011 census (residence, workplace, schools), NHS attendance figures, tourism, road network etc.
Gives age groups and ‘location’ (at home, in transit, ‘on-site’).
2am
2pm

## Slide 8: Pop247
 |  | Out of term |  | In Term | 
 |  | 2am | 2pm | 2am | 2pm
children | residence | 740 | 698 | 737 | 100
children | travelling | 0 | 5 | 0 | 20
children | OnSite | 3 | 617 | 3 | 1656
children | All | 743 | 1319 | 741 | 1776
adults | residence | 5224 | 2529 | 8082 | 4493
adults | travelling | 3 | 65 | 3 | 247
adults | OnSite | 421 | 15226 | 425 | 21737
adults | All | 5648 | 17819 | 8509 | 26477
AllAges | residence | 5964 | 3226 | 8819 | 4592
AllAges | travelling | 3 | 70 | 3 | 267
AllAges | OnSite | 424 | 15843 | 428 | 23394
AllAges | All | 6391 | 19139 | 9250 | 28253
Hypothetical transport incident

## Slide 9: Pop247
Challenges of applying Pop247 data to PACE:
Each met-sequence has a start time/date so can be matched with a Pop247 estimate.
Pop247 does not track individual people – difficult to generate individual doses, difficulty merging short term dose (location when plume passes) and long term (dominated by residence)
Behaviour will change during/after an incident – a starting point for a calculation but assumptions about subsequent behaviour have to be made
Assumptions might depend on; time/date, age, protective action status, distance from release
Prototype interface:

## Slide 10: Update of agriculture database
Current data set is old and only available for UK (EDINA)
Requirements:
European coverage
Repeatable/automated process for maintaining it
Quantify exports (regional level) and imports (national level)
Data sources:
FAOSTAT – Global coverage at a national scale (http://www.fao.org/faostat/en/#home )
EUROSTAT- European coverage, national down to NUTS2*, includes trade data, but data often missing/late
https://ec.europa.eu/eurostat/web/main/home
Hybrid approach combining FAOSTAT and
EUROSTAT plus CORINE land-use data
*NUTS regions are based, where possible,
on existing national administrative subdivisions
NUTS level2 has between 800k and 3m people.

## Slide 11: Agricultural update
1000kg per 4km2 per year

## Slide 12: Areas of future development
Preparing PACE for small modular reactors
radionuclides and physicochemical properties from novel reactor designs
PACE capabilities for urban areas
Multiple points of release
relative timing of releases
triggering of countermeasures
Evacuation routing
Sherwood (2017) “An investigation of the effectiveness of sheltering versus evacuation” (https://eu-neris.net/library/proceedings/155-proceedingsnerisworkshop2017pdf/file.html)
combined PACE with network analysis capabilities of ArcGIS
possible improvements: agent based modelling, traffic jams, Pop247, intelligent strategies
Hypothetical facilities and incidents

## Slide 13
Questions?