## Slide 1: SMR Emergency Planning Zone R&D at CNL
Luke Lebel, PhD (Luke.Lebel@cnl.ca); David Hummel, PhD; Lucian Ivan, PhD
2020 September 1
Notes: For best results, please send the large top image to the back layer. Choose “Arrange” then select “Send to Back”.

## Slide 2: Outline
SMR EPZ Overview
Dose consequences of postulated limiting accidents for SMRs
Fine resolution dispersion modeling (ongoing developments)

## Slide 3: Canadian Small Modular Reactor Landscape
Applications of SMRs in Canada
  On-grid applications
  Mining and large industry
  Remote communities
https://smrroadmap.ca
Recent advancements:
  12 SMR vendors engaged with CNSC for pre-licensing vendor design review
  Environmental assessment and License to Prepare Site evaluation underway for demonstration SMR at Chalk River
  Industry-led SMR Roadmap published in 2018
  Government SMR Action Plan in 2020 November

## Slide 4: IAEA Coordinated Research Project
“Development of Approaches, Methodologies and Criteria for Determining the Technical Basis for Emergency Planning Zone (EPZ) for Small Modular Reactor Deployment”
Objectives:
  Formulate criteria, e.g., novel safety systems, smaller source term, that require consideration
  Develop approaches for EPZ sizing and formulating EPR arrangements
  Provide a technical basis for use in future IAEA EPR technical guidance documentation relating to SMRs
CNL’s contributions:
  Study on dose consequences for SMR limiting accidents (scoping study)
  Information on iPWR and HTGR source term experiments at CNL
  Fine resolution dispersion and dose modeling

## Slide 5: SMR Limiting Accident – Scoping Study
Dispersion & dose consequence evaluations for hypothetical limiting accident source terms
  exploratory work, not intended to align with PSA or regulatory expectations
Considered four technologies, scaled to 30 MWth:
  High Temperature Gas-cooled Reactor (HTGR)
  Molten Salt Reactor (MSR)
  Lead-cooled Fast Reactor (LFR)
  Integral Pressurized Water-cooled Reactor (iPWR)
Publication: D. Hummel, S. Chouhan, L. Lebel, and A. Morreale, “Radiation Dose Consequences of Postulated Limiting Accidents in Small Modular Reactors to Inform Emergency Planning Zone Size Requirements”, Annals of Nuclear Energy, 137:107062 (2020) DOI:10.1016/j.anucene.2019.107062.

## Slide 6: Dispersion and Dose Assessment
Study employed ADDAM (Atmospheric Dispersion and Dose Analysis Method)
  Canadian “Industry Standard Toolset” code
  Based on Canadian standard N288.2-14
Gaussian plume model with stochastic sampling of meteorological data
  Figure of merit: 90th percentile cumulative adult whole body effective dose (P90 dose) at receptors over 3.5 days
Example meteorological data from Chalk River Laboratories
ADDAM sectors around release point

## Slide 7: SMR Source Term Assumptions
HTGR | iPWR | LFR | MSR
JAERI assessment of hypothetical HTTR accident
Loss of forced circulation with severe air ingress
Chart: Release Fraction
| La, Pr | Ce | Mo, Ru | Sb | Cs, Te | I | Xe, Kr
Series 1 | 0.001 | 0.003 | 0.028 | 0.012 | 0.15 | 0.15 | 0.3
Assumptions based on open-literature fractional releases from representative cases
Open MELCOR analysis of “natural circulation” SMR
Sustained station black out and draining of water pool
Quasi-equilibrium thermo-chemical assumption of various FPs in lead
Prompt-criticality event (multiple control rod bank ejection)
Maximum credible accident assessment for the MSRE
Primary circuit failure with ingress of air/water into molten salt
Chart: Release Fraction
| Ce, Zr | La, Pr | Te | Mo, Ru | Sb | Sr, Ba | Cs, Rb | I | Xe, Kr
Series 1 | 6.8e-05 | 0.068 | 0.11 | 0.00038 | 0.0044 | 0.00053 | 0.38 | 0.32 | 0.68
Chart: Release Fraction
| Po-like | Cs-like | Sr, Ba | I | Xe, Kr
Series 1 | 3e-07 | 4.9e-06 | 5.3e-13 | 3e-05 | 1
Chart: Release Fraction
| others | I | Xe, Kr
Series 1 | 7.99e-05 | 4e-05 | 1e-10
5.3x10-13
n/a
Notes: High Temperature Gas Reactor
  Block-type TRISO fuel, no containment
  Postulated Depressurized Loss-of-Forced Circulation (guillotine break) with failure to scram and severe air ingress
  Fractional radionuclide releases based on JAERI’s assessment of hypothetical accident of HTTR as well as INL reports
Molten Salt Reactor
  Liquid-fluoride fuel salt, graphite moderated
  Postulated primary circuit failure and ingress of air/water
  Fractional radionuclide releases from MSRE analysis of maximum credible accident
Lead-cooled Fast Reactor
  Uranium oxide fuel, integral steam generators
  Postulated prompt-critical reactivity insertion (multiple control rod bank ejection)
  Fractional radionuclide releases from quasi-equilibrium thermo-chemical models of various fission products in lead
Integral Pressurized Water-cooled Reactor
  Integral RPV within small Containment Vessel in water pool
  Postulated sustained station blackout and draining of water pool
  Fractional radionuclide releases from MELCOR analysis found in literature

## Slide 8: Maximum Distance at P90 Dose Level (1)
High Temperature Gas Reactor
Dose Results for 72 h Release Duration and 15 m Release Height
Dose Level | Distance
250 mSv | 1.92 km
100 mSv | 3.39 km
10 mSv | 10.7 km
1 mSv | 35.3 km
P90 dose by sector - HTGR
Integral Pressurized Water Reactor SMR
Dose Level | Distance
250 mSv | 2.33 km
100 mSv | 3.68 km
10 mSv | 12.4 km
1 mSv | >40 km
P90 dose by sector - iPWR

## Slide 9: Maximum Distance at P90 Dose Level (2)
Lead-Cooled Fast Reactor
Dose Results for 72 h Release Duration and 15 m Release Height
Dose Level | Distance
250 mSv | <0.1 km
100 mSv | <0.1 km
10 mSv | 0.53 km
1 mSv | 2.79 km
P90 dose by sector - LFR
Molten Salt Reactor
Dose Level | Distance
250 mSv | <0.1 km
100 mSv | <0.1 km
10 mSv | <0.1 km
1 mSv | 0.72 km
P90 dose by sector - MSR

## Slide 10: Informing EPZ Arrangements
First step in justifying smaller EPZ sizes for SMRs, compared to large plants
  Crediting inherently smaller radionuclide inventories
  Crediting chemical retentions for advanced technologies
Limiting accidents used for scoping
  Extremely low probability, high consequence accidents
  More detailed PSA-related analysis required for making final recommendation
Conclusions that smaller EPZ sizes can be justified also imply that more fine-resolution dispersion & dose modeling is needed

## Slide 11: Challenges of Fine Resolution Dispersion Modeling
vertical meandering
horizontal
spreading
Assumptions of Gaussian plume model less valid at close distances
Require more dynamic, time dependant, fine resolution dispersion model
  e.g., near-field puff model

## Slide 12: Fine Resolution Dispersion Modeling R&D at CNL
Near-field capabilities challenging for existing codes
On-going work on fine-resolution models
  modelling options for plume dispersion:
    Gaussian plume & puff models
    stochastic Lagrangian particle model
    polydisperse Gaussian-moment model (PGM)
  dynamic meteorology
  3D dose calculations
Compare new models against NRU (research reactor at Chalk River) 41Ar plume measurements
UAV measurements and concentration reconstruction of 41Ar plume

## Slide 13: Dynamic Meteorology and Dispersion Model Options
Integration with CALMET (U.S. EPA) for wind, temperature field and other properties (e.g., stability class)
  reconstruction based on field measurements
  account for complex terrain effects, overwater transport and other effects
Dispersion models implemented in an in-house parallelizable computational framework
Easy generation of arbitrary number of dose receptor networks
  2D and 3D, adaptive, stretched grids
Lagrangian particle simulation
CALMET wind field reconstruction

## Slide 14: Incorporating Near-Field Dose Calculations
Near-field effects especially important for cloud and ground shine calculations
  no simple dose conversion factor
Dose calculation techniques:
  9th-order Gaussian quadrature integration on continuous fields (plume & puff dispersion)
  dose summation on discrete solutions (Lagrangian and PGM)
  parallelization to mitigate computational cost
Dose calculation from Lagrangian model
Dose calculation from Gaussian plume model

## Slide 15: Application of Models to NRU 41Ar Plume Dispersion
Ongoing study (results not available yet)
Benchmarking versus Chalk River Lab monitoring network of NRU routine emissions
  22 ambient 𝛾-dose rate monitors
  NRU stack emission monitors (noble gases, iodine, particulates)
  meteorological measurement network
Study period: 2016 November 10 – December 7
Assessment of dose predictions and comparative study of different models
Chart: Stack Activity
Map of monitoring network around CRL
NRU stack 41Ar source term

## Slide 16
Thank you!
Questions?
Luke Lebel, PhD
Nuclear Safety Experiments Branch
Nuclear Engineering and Systems Analysis Division
Luke.Lebel@cnl.ca
www.cnl.ca