## Slide 1
Design of a novel decision-making tool for the analysis of sheltering-in place during a radiological emergency

## Slide 2
Background
Protective Action Guides (PAGs) are based on the premise that protective actions should do more good than harm.
Sheltering-in-place may be just as effective as evacuation in some cases.
No practical tools assess the benefit of shelters for the immediate time period following a release.
Design Challenge: Develop a tool to analyze the benefit of shelter-in-place vs. evacuation.

## Slide 3
Capability to import data from RASCAL dose projection software.​
Account for specific exposure pathways of cloudshine, groundshine, and inhalation. ​
Capability to import and read from various file formats including GIS shape txt files. ​
Provide time-integrated dose in 15-minute intervals up to 96 hours from t=0 (start of radiological release). ​
Compute time-dependent, material-specific, and energy dependent building protection factors based on radionuclide mix and shelter construction and type. ​
Apply protection factors to dose projection and provide time-dependent dose output. ​
Provide assessment of SIP effectiveness within 15 minutes. ​
Provide computation of evacuation dose for comparison to SIP. ​
Constraints

## Slide 4
RASCAL
RASCAL provides dose rate data for:
  Cloudshine
  Groundshine
  Inhalation

## Slide 5
RASCAL

## Slide 6: Dose Pathway - Inhalation
Equations derived from a mass balance air flow model of the shelter
Input is inhalation dose from RASCAL
Region specific air filtration parameters used
Model Validation
Benchmarked against data from Kulmala et al.
Kulmala
Design Team

## Slide 7: Building Protection Factors
Figure 1: Dose Curves Example
Building protection factors are typically applied as constants independent of radionuclide
In reality, shielding effectiveness will change over time and by pathway
Constant PF Energy-dependent PF

## Slide 8: Dose Pathway – Cloudshine/Groundshine
Modeled time- and energy-dependent protection factor equations for residential homes
  Energy weighted by isotopic importance
  Time dependent to account for short-lived isotope decay
  Sensitivity analysis performed to quantify uncertainty
One-Story Building Cloudshine Protection Factors
x = photon energy (MeV)
One Story Vinyl No Basement Groundshine Day 0 |  | 
Calculated Energy-Dependent PF = 0.532915 |  | 
Energy of Remainder (MeV) | Total PF | % diff
0.001* | 0.5050 | 5.37
0.01 | 0.5145 | 3.51
0.1 | 0.5240 | 1.68
1 | 0.5335 | 0.12
10* | 0.5526 | 3.62
Protection Factor Example
* These energies were considered for sensitivity analysis only.

## Slide 9: Evacuation Model
Evacuation time can be split into phases of mobilization and travel
Representative evacuation times can be based on EPZ resident population (NUREG/CR-7269)
Protection factors are dependent on the evacuation phase:
  Shelter PF is assumed during mobilization time
  Vehicle protection factor (PF = 0.9) assumed for travel time (NUREG/CR-7009)
EPZ Resident Population: | 
Small | <50,000
Medium | 50,000-200,000
Large | >200,000
Population: | Small |  | Medium |  | Large | 
Evacuation: | Early | Late | Early | Late | Early | Late
Mobilization Time [min]: | 30 | 120 | 60 | 180 | 60 | 180
Travel Time [min]: | 15 | 15 | 15 | 30 | 30 | 60

## Slide 10: PRISEM
Post Radiological Incident Shelter-in-place vs. Evacuation Model (PRISEM)
PRISEM expands our view of combined dose projection data and separates the information into actionable results

## Slide 11
PRISEM Interface

## Slide 12: Analysis
What are the important dose pathways?
Figure 1: Dose Curves Example

## Slide 13
Figure 1: Dose Curves Example
How much does residential construction matter?
Analysis

## Slide 14
Figure 1: Dose Curves Example
Where in the house should you shelter?
Should I operate the HVAC?
Analysis
Chart: 

## Slide 15
Figure 1: Dose Curves Example
What are other applications of PRISEM?
PRISEM provides insight into importance of penetration factors (active research area)
PRISEM can be used in planning to enhance implementation of protective actions
Analysis

## Slide 16
Evacuation cost estimated from federal cost estimates related to site-specific burden of: lodging, food, transportation, and lost income
Exposure cost per person-rem taken from approved federal estimates in NUREG-1530
Emergency planners can see how site-specific populations are affected by the cost of implementing protective actions
Cost of developing PRISEM for site-specific use ~ $1000
Use of SIP represents savings in hundreds of millions to the economy
Cost Savings
$400 million
Cost Savings
$250 million
19
Economic Analysis

## Slide 17
PRISEM is a novel tool that provides decision-makers vital information for implementing appropriate protective actions during a time-critical event
PRISEM is a cost-effective method to enhance public health and safety
PRISEM can be used for research and emergency planning
20
Conclusions

## Slide 18: Questions?
21

## Slide 19
Time-Dependent Protection Factor