## Slide 1: Update on Development of Technical Bases for Consequence Analyses using MACCS
K. Compton, A. Nosek (USNRC)
N. Bixler (SNL)
2020 International MACCS User’s Group

## Slide 2: Objective
Provide summary of ongoing work to develop a reference document on technical bases for consequence analyses using MACCS
Provide an overview of document scope, structure, content, and limitations
Provide selected highlights of material from ongoing work

## Slide 3: MACCS Applications
 | Individual Early / Latent Fatality Risk | Total Early / Latent Fatality Cases | Collective Dose | Offsite Property Damage | Land Contamination
Backfit Analyses | X |  | X |  | 
Regulatory Analyses | X |  | X | X | 
Environmental Assessment | X | X | X | X | X
Severe Accident Mitigation Alternatives |  |  | X | X | 
Other Analyses | As needed |  |  |  | 

## Slide 4: Motivation
Original MACCS user guide states that “It is the responsibility of each MACCS user to ensure the appropriateness of all data in the MACCS input files which they prepare.”
A comprehensive reference source is not available to assist users in evaluating the appropriateness of the data in their MACCS input files.

## Slide 5: Scope of Document
Describes approaches for developing a technical basis for 172 MACCS input parameters
Addresses all MACCS 3.10 parameters, data files, or modeling options that may be selected by the user
Includes citation to primary references, current databases, or recommended methodology wherever possible
Includes sources of information for developing parameter distributions for uncertainty analyses
MACCS may be used for a variety of applications, and the values used should be appropriate for the application. These values and recommendations are therefore not intended as “default” values.

## Slide 6: Report Organization
Radionuclide Release Characterization
Atmospheric Transport, Dispersion, and Deposition
Protective Action Parameters, Other Site Data, and Economic Factors
Dosimetry and Health Effects
Quantification
Appendices

## Slide 7: Radionuclide Release Characterization
Focuses on development of radiological source term using MELCOR but includes discussion of considerations when using other accident progression codes such as MAAP.
One-hour plume segments recommended to align with hourly meteorological data and allow use of RG 1.145 meander model.
Recommend inclusion of Sb-127 and Sb-129 and associated addition of Chemical Group 10.

## Slide 8: Atmospheric Transport, Dispersion, and Deposition
Generally (but not always) follows SOARCA approaches
May either sample all weather trials using METCOD=5 and NSMPLS=24 or use non-uniform bin sampling with ~1000 weather trials
Dispersion coefficient lookup table implementing Pasquill-Gifford curves based on Eimutis and Konicek (1972), coupled with RG 1.145 meander model, is recommended when uncertainty analyses are not required
Use of SOARCA power-law dispersion parameters from NUREG/CR-7245 are recommended when uncertainty analyses are to be performed
Use of boundary weather rainout to force plume depletion discouraged at distances closer than 500 miles

## Slide 9: Protective Action Parameters, Other Site Data, and Economic Factors
Includes consideration of:
  Methodology and considerations for development and adjustment of MACCS site file using SECPOP
  Considerations for development of site-specific shielding and exposure factors based on housing stock and activity patterns

## Slide 10: Early Phase Duration and Protective Actions
Includes consideration of:
  Development of evacuation cohorts from evacuation time estimate (ETE) information
  Development of evacuation delays and speeds from ETE information
  Development of evacuation routing models (e.g., radial, network, and keyhole)
  Development of early phase relocation times based on size of affected population
  Estimation of early phase costs from site-specific data sources (e.g., federal per-diem rates)

## Slide 11: Highlight: Early and Intermediate Phase Daily Costs
Early phase evacuation/relocation cost (EVACST)
  Lodging: Federal per diem lodging rates adjusted by household size
  Food: Federal per diem rates for meals and incidental expenses
  Transportation: based on IRS standard mileage rage and average distance of 50 miles and adjusted by household size
  Lost income: daily wages lost during temporary displacement based on either SSA average wage index coupled with Employment-Population Ratio or the per-capita GDP coupled with share of gross domestic product (GDP) that comes from labor.
Intermediate phase relocation cost (RELCST)
  Includes only lodging and lost income from EVACST; food and transportation not recommended for inclusion during intermediate phase

## Slide 12: Intermediate and Long-Term Protective Actions and Exposures
Subsections
  Intermediate and Long Term Phase Durations
  Dose Criteria for Relocation, Interdiction, and Decontamination
  Costs of Intermediate and Long Term Phase Relocation and Interdiction
  Decontamination Plan development
  Agricultural Countermeasures, Food Ingestion, and Water Ingestion
Includes consideration of
  Estimating intermediate and recovery phase durations based on size of affected population
  Estimation of relocation and interdiction costs from site-specific data sources (e.g., federal per-diem rates)
  Costs of decontamination based on decontamination level required

## Slide 13: Highlight: Recommended Phase Durations
Number of people subject to intermediate and long-term phase protective actions may be examined using the MACCS Type 14 output to inform selection of phase durations.
Intermediate Phase (DUR_INTPHAS)
  One-year intermediate phase is recommended for large releases.
  A one-year intermediate phase allows the analyst to directly use the first-year EPA criterion of 2 rem for intermediate phase and the second-year criterion of 500 mrem for long-term phase.
Long term phase (TIMDEC)
  One-year cleanup phase recommended for large releases
  Larger areas requiring a low DF coupled with MACCS limit that lower DFs be equal or less in duration than higher DFs
  Maximum value allowed in MACCS 3.10 for TIMDEC is one year.

## Slide 14: Highlight: Updated Cost and Decontamination Approach
For the parameters related to decontamination, current national and international practices, including the ongoing Fukushima activities, were investigated.
Decontamination costs were estimated for farmland and non-farmland regions.
Cost considerations for various decontamination factors include
  decontamination surface (asphalt, roofing, landscape, etc.)
  decontamination technology (soil removal, sandblasting, pressure washing, etc.)
  radioactivity sampling and waste characterization prior to clean up
  waste transportation, storage and disposal costs
A method for derivation of CDFRM and CDNFRM is described in appendices.

## Slide 15: Dosimetry and Health Effects
Includes a brief summary of methodology for developing dose coefficients.
Currently recommends use of cancer model based on the expert elicitations documented in NUREG/CR-6555 because the SOARCA dose coefficient file was not publicly available for MACCS 3.10.

## Slide 16: Quantification
The types of MACCS output measures typically used for different applications
Considerations for constructing output control statements
Examples:
  Type 8 Output for Population-Weighted Individual Risk
  Type 5 Output for Collective Dose
  Type 10 Output for Economic Costs
  Type 14 Output for Evacuated and Relocated Population Sizes

## Slide 17: Highlight: Input Parameter Application Guidance Appendix
 | Nomenclature Guidance | Documentation Expectations
Standard | Standard value that should not be changed without very good reason. | No additional documentation expected
Generic | Parameters that are generic values but could be changed by a user, depending on the analysis, including non-site specific parameters; generally good for the US, but if the data are available, the parameter may be made more site-specific. | User should verify applicability of input parameter with little additional documentation on technical basis expected or needed; usually review or consideration is sufficient to verify parameter applicability.
User-Defined | Parameters that should in almost all cases be evaluated by the user, including site-specific parameters. Examples are provided but these values may not be applicable to other analyses. | User should develop and document parameter value chosen for an application with a reasonable and defensible technical basis.

## Slide 18: Scope Limitations
Parameters based on MACCS Version 3.10; i.e., does not address MACCS parameters for some recent MACCS model enhancements (e.g., dosimetry model updates, updated parameter limits, alternative economic consequence model, alternative atmospheric transport and dispersion model, etc.)
Does not address MACCS parameters that are no longer commonly exercised or that are only retained for backward compatibility
Does not address food chain model parameters (either from original MACCS Food Chain Model or from MACCS2 COMIDA2 model)

## Slide 19: Conclusions
Objective is to develop a comprehensive, updated summary of the technical bases for the quantification and application of MACCS input parameters.
Because MACCS may be used for many different applications, the recommendations in the input parameter guidance report should be considered in context of the analysis being performed.
Report develops recommendations for 172 MACCS input parameters.
Draft document is undergoing internal review.

## Slide 20: References
E. C. Eimutis and M. G. Konicek, "Derivations of Continuous Functions for the Lateral and Vertical Atmospheric Dispersion Coefficients," Atmospheric Environment, pp. 6:859-863, 1972.
U.S. Nuclear Regulatory Commission, "Reactor Safety Study: Appendix VI (NUREG-75/014; WASH-1400)," U.S. Nuclear Regulatory Commission, Washington, DC, 1975.
W. G. Snell and R. W. Jubach, "Technical Basis for Regulatory Guide 1.145, Atmospheric Dispersion Models for Potential Accident Consequence Assessments at Nuclear Power Plants" (NUREG/CR-2260)," NUS Corporation, Rockville, MD, 1981.
J. L. Sprung, J. A. Rollstin, J. C. Helton and H.-N. Jow, "Evaluation of Severe Accident Risks: Volume 2, Rev. 1, Part 7: Quantification of Major Input Parameters, MACCS Input (NUREG/CR-4551)," U.S. Nuclear Regulatory Commission, Washington DC, 1990.
D. I. Chanin, J. Sprung, L. Ritchie and H.-N. Jow, "MELCOR Accident Consequence Code System (MACCS). Volume 1: Users Guide (NUREG/CR-4691)," Sandia National Laboratories, Albuquerque, NM, 1990.

## Slide 21: References
M. P. Little, F. T. Harper, C. R. Muirhead, S. C. Hora, L. Goossens, B. Kraan and R. M. Cooke, "Probabilistic Accident Consequence Uncertainty Analysis: Late Health Effects Uncertainty Assessment, Volumes 1 and 2 (NUREG/CR-6555)," Sandia National Laboratories, Albuquerque, NM, 1997.
D. I. Chanin and M. L. Young, "Code Manual for MACCS2: Volume 1, User’s Guide (NUREG/CR-6613)," Sandia National Laboratories, Albuquerque, NM, 1998.
N. Bixler, J. Jones, D. Osborn and S. Weber, "MACCS Best Practices as Applied in the State-of-the-Art Reactor Consequence Analyses (SOARCA) Project (NUREG/CR-7009)," Sandia National Laboratories, Albuquerque, NM, 2014.
Sandia National Laboratories, "State-of-the-Art Reactor Consequence Analyses Project: Sequoyah Integrated Deterministic and Uncertainty Analyses (NUREG/CR-7245)," U.S. Nuclear Regulatory Commission, Washington DC, 2019.