## Slide 1: MACCS-COMIDA2 Input Parameter Analysis Revisiting the MACCS Food-Chain Model
Osvaldo Pensado and Daniel Speaker
opensado@swri.org
Center for Nuclear Waste Regulatory Analyses (CNWRA®)
Southwest Research Institute® (SwRI®)
Keith Compton, Salman Haq
US Nuclear Regulatory Commission (NRC)

## Slide 2: Acknowledgments
Project sponsored by the US Nuclear Regulatory Commission (NRC)
  Office of Nuclear Regulatory Research
  Division of Systems Analysis
  Accident Analysis Branch
This presentation describes work performed by the CNWRA for the NRC under Contract No. 31310018D0002.
This project is an independent product of the CNWRA and it does not necessarily reflect the views of the NRC.
The NRC staff views expressed herein are preliminary as part of an ongoing research program.

## Slide 3: Food-Chain Model
COMIDA
  M.L. Abbott and A.S. Rood, Idaho National Laboratory, 1993
  Based on PATHWAY model by F. Whicker and T. Kirchner, 1987
  Outputs food concentrations and integrated concentrations
    Bq/kg and Bq-day/kg (per unit of fallout, Bq/m2)
COMIDA2 is an interface of COMIDA within MACCS
Revisiting inputs needed in light of more recent radioecological efforts, for example by IAEA and DOE
Revision of inputs in this project was guided by a sensitivity analysis
Notes: NUREG 6613 (1998) recommends inputs.
The recommended inputs are not incorporated in the sample input files distributed with the code
References are decades old

## Slide 4: COMIDA consequences depend on the accident date
Year after the accident
Accident 1
Accident 2
Accident 3
Accident 9
Accident 5
Accident 6
Accident 7
Accident 4
Accident 8
Start of crop growing
Harvest
Crop season
Notes: Total ACU_DOSE
The fact that doses are the same for Accident 1 and Accident 9 indicate that the first-year products are destroyed or do not contribute to the dose. The computations start after the second year.
For Accident 1, all of the production is assumed to proceed as normal. The crops are harvested as usual, but the first-year inventory is removed and it does not contribute to the dose. The amount of 1st year inventory, removed from the dose computations, is maximal. The first year the dose is computed, the dose is low.
For Accidents 3 to 8, the inventory removed corresponds to the inventory after the accident. The inventory before the accident anniversary contributes to the dose. The inventory causing a dose is older than one year.

## Slide 5: Different plant and animal product concentration with the accident date
Plant products
Animal products
Notes: Each curve represents an accident year: year 1, 2, 3, …, 9.
The jumps correlate with the start and end of the crop season. Other dates are not so important.

## Slide 6: Examination approach for inputs
Local, variation of one-at-a-time sensitivity
Each parameter varied by one order of magnitude above and below a baseline value, when possible
The one-at-a-time sensitivity was intended to characterize the mathematical structure of the model
  Physical correlations were not enforced
  Radionuclide-dependent inputs were perfectly correlated (no interest in ranking radionuclide relevance in this project)
The sensitivity analysis was intended to inform input updates
Notes: Sensitivity indices were defined as slopes of linear fits with x-domains normalized to range between −1 and 1

## Slide 7: Sensitivity index: a slope
Simple linear fit of relative dose or relative cost versus log10(variable/reference)
Slope selected as the sensitivity index to compare different variables

## Slide 8: MACCS interdiction model
Interdiction model
Suspension of farming
Food disposal
Land decontamination
Land condemnation
Population dose
Economic cost
Notes: Initially, the population dose and the economic cost coherently vary, until the individual dose exceeds a user-defined threshold, at which point the interdiction model is triggered to control the population dose at a high economic cost.
There is no absolute conservative direction for input parameters.
The interdiction model is responsible for some of the non-intuitive trends.

## Slide 9: Sensitivity to plant growth rate (ZKG)
Individual dose tends to increase with increasing ZKG, except for ZKG(pasture). Why?

## Slide 10: Individual dose decreases with increasing pasture growth rate because the time for radionuclide uptake by roots is expanded
Pasture
Start of grazing season
End of grazing season
Baseline
Active growth longer than in baseline
ZKG(pasture) (1/d)
Notes: In the baseline case, accidents after day 150 would not contaminate grass via root uptake.
Decreasing pasture growth rate, ZKG, increases the root active time and the amount of radionuclide uptake

## Slide 11: Agricultural dates
Crop season
Hay season
Grazing season
Day 365
Day 1
Notes: Same harvest day is assumed for the five crops
Some delay from production to consumption is implicit in the harvest synchronization
  Harvest is delayed in the model until all crops are ripe

## Slide 12
Accident 2
Accident 2
Accident 8
Accident 8
Accident 9
Accident 9
Start of crop season
Harvest date
Harvest date
Start of crop season
Notes: The most important dates influencing dose estimates are the start of the crop season and the crop harvest date
However, the effect of varying solely the duration of the farming seasons (crop season, hay season, grazing season) on dose estimates is relatively minor
The most important factor influencing dose estimates is whether an accident occurs near the beginning or end of a farming season
No need to spend much effort in refining dates of farming seasons for site-specific analyses
The main point is that spikes correlate with the occurrence of accidents.
I have a confusion here. The NUREG 6613 states that COMIDA2 prepares a type of lookup table with the variable assumed accident dates. Then MACCS takes the results from the closest accident to the postulated date of the accident. If such was true, some accident dates would not matter to the dose and cost results. However such appears not true. The results are affected by all accident dates. It seems to me that the NUREG 6613 description is not accurate. Rather than using results from a single accident date, COMIDA2 computes an average over all accident dates to determine the population dose and the economic cost.

## Slide 13: Individual dose can increase with holdup
Individual dose increase with increasing holdup time is an artefact of the holdup time splitting the proportion of food causing consequences in the current accident year and the next accident year
Notes: Holdup: delay from production to consumption

## Slide 14: Linear increase of dose with holdup for long-lived radionuclides
Long-lived radionuclide example: linear increase
For short-lived radionuclides, decay wins
Cs-137
t1/2=11,000 days
I-131
t1/2=8 days
Notes: Horizontal axis: holdup time (grains)
Vertical axis: accumulated population dose (grains) for a specific radionuclide
Different curves represent different accident dates
Half life of Cs-137: 10,960 days
Half life of I-132: 8.04 days
The concept of holdup may need to be revisited. My recommendation is that the holdup should not be used in the proportion of how much harvest is consumed in the current or the next accident year.

## Slide 15
Pasture growth rate
Dry to wet ratio leafy vegetables
Milk holdup time
Contamination remaining after food processing, grains
Dry to wet ratio grains
Transfer coefficient beef
Cattle feeding rate, pasture
Resuspension rate constant
Notes: Input variables that are linearly related to the individual dose or population dose were highlighted by the sensitivity analysis
  Consumption rates, production rates, dry to wet ratio
Grains are highlighted due to their high dry-to-wet ratio
  Grains are more concentrated than other food products
Leafy vegetables are highlighted due to the assumption of high translocation rates
  Radioactivity is assumed efficiently incorporated by leaves
Milk consumption is highlighted because of the assumed relatively high consumption rates

## Slide 16
Dry to wet ratio, leafy vegetables
Maximum biomass grains
Maximum biomass leafy vegetables
Weathering rate constant
Translocation rate constant grains
Plant growth rate grains
Dry to wet ratio, fruit
Notes: Input variables that are linearly related to the individual dose or population dose were highlighted by the sensitivity analysis
  Consumption rates, production rates, dry to wet ratio
Grains are highlighted due to their high dry-to-wet ratio
  Grains are more concentrated than other food products
Leafy vegetables are highlighted due to the assumption of high translocation rates
  Radioactivity is assumed efficiently incorporated by leaves
Milk consumption is highlighted because of the assumed relatively high consumption rates

## Slide 17: General comments
Plant translocation is more effective for assimilation of radioactivity than root uptake depending on inputs
  Surface processes, such as resuspension, can be important
The COMIDA food-chain model accounts for seasonal variability
  However, duration of agricultural seasons has a secondary effect compared to whether an accident occurs near the beginning or end of the crop season
  In other words, accurately pinning down specific dates for farming activities is not that relevant

## Slide 18: General comments
Approach to define the pasture growth rate should be revisited
  Considering a typical growth span of 30 days could underestimate individual doses
  Recommend to considering a lower grass growth rate based on the duration of the grazing season
The delay time of feed and food production to consumption (holdup time) should be revisited
  Should other factors than decay time be associated with the holdup?
  A holdup time is already embedded in the assumption of synchronicity of the harvests (i.e., harvest until all crops are mature)